## Slide 1
Mark Chen
Queen’s University and the Canadian Institute for Advanced Research
Summer Particle Astrophysics Workshop 2024
LiquidO
Seeing through the fog to find new physics

## Slide 2: What is LiquidO? → O is for “Opaque”
R&D towards a novel liquid scintillator detection technique that uses an opaque medium

## Slide 3: What is a Liquid Scintillator?
It’s a material that gives off light when excited by particles/radiation
inorganic crystals, organic liquids, noble gases and liquids, plastic scintillators
Right: the SNO+ neutrino detector is filled with liquid scintillator; light is detected by photomultipliers (PMTs)

## Slide 4: Light Confinement using high scattering medium (with low absorption) to preserve energy deposition information

## Slide 5: How to readout an “opaque” scintillator?
grid of wavelength-shifting fibres
X, Y info: ~1-cm fibre grid spacing (~mm imaging)
Z info: timing along fibre (~cm resolution)
SiPM fibre readout (photon counting)
(everybody ❤️ SiPMs these days)
Image: CDF central tracker
It’s like a light TPC or photon drift chamber!

## Slide 6: Scintillation light from energy deposition is confined stochastically… scattering enables imaging!
Fibres
6

## Slide 7: LiquidO Features & Advantages
spatial and temporal event ID and pattern information → powerful background rejection
relaxing the scintillator transparency requirement opens many doors for liquid scintillator design options

## Slide 8: Event Identification @MeV energies
Single Site (electrons, alphas, proton recoils)
Multi Site (gammas)
Positrons!
4 3 2 1
γ

## Slide 9: LiquidO Simulations – 2 MeV
In contrast: how do PMTs from far away see such events?
…as mostly indistinguishable large balls of light!

## Slide 10: “Energy Flow” – Time Information
LS

## Slide 11
Light “confinement” establishes strong space-time event pattern

## Slide 12: Does stochastic light confinement work? YES! μ-LiquidO
electron beam from SuperNEMO R&D

## Slide 13
:4 :2
X2.5 X1
translucent
transparent

## Slide 14
:4 :2
X2.5 X1
translucent
transparent

## Slide 15
Summary of μ-LiquidO demonstration of
opacity light confinement
in Nature’s Communications Physics (2021) 4:273

## Slide 16: Advantages of Large Volume Liquid Scintillator viewed by PMTs far away
Homogeneous volume
Low background
Fiducial volume cut to reduce external backgrounds
Passive buffer volume needed to shield from PMT radioactivity
Image: SNO+
negatives in pink
Review

## Slide 17: Advantages of LiquidO Technique readout by fibres+SiPMs
Active background rejection
Powerful single-site/multi-site discrimination
External SiPMs don’t require passive buffer
Fiducial cut includes active detector rejection of external backgrounds
Liquid scintillator can still be low background
Added background component: fibres
Image: GERDA fibre curtain
Scintillating, wavelength-shifting fibres
can be radiopure and are active
GERDA fibre curtain as an example
negatives in pink
Review
Images: Mini-LiquidO

## Slide 18: Next Steps for LiquidO
Mini-LiquidO
(has taken data)
w/fast SiPM electronics readout

## Slide 19: Mini-gamma
161 L opaque LS
1021 L transparent LS

## Slide 20: ~10-ton LiquidO at Chooz ~10,000 fibres+SiPM readout channels (GHz waveforms)
fully funded EIC project

## Slide 21: CLOUD
Chooz LiquidO Ultra-near Detector
Baseline: ~30 m
Overburden: ~3 mwe
IBD antineutrino rate:
~15 events/minute

## Slide 22: Summary
LiquidO is a novel approach for liquid scintillator neutrino detection
Exciting neutrino physics potential
EVENT ID ⊕ RELAXED LS REQUIREMENTS
Thanks!