## Slide 1: Industrialization Realizing applied opportunities
Fabrice Retiere (TRIUMF) with major inputs from Serge Charlebois (Sherbrooke)

## Slide 2: Outline
Motivation
Jargon
Examples of opportunities
Roadblocks and breakthroughs
You

## Slide 3: Motivation – value/goal mapping – 20 years ago when I moved to Canada
Value
Creativity
Achievement
Independence
Belonging
Goals
Develop experimental solutions for discovery physics
Integrate in Canadian SAP community
Ski

## Slide 4: Motivation – value/goal mapping - now
Value
Creativity
Achievement
Concern for Environment
Responsibility
Goals
Develop experimental solutions for mitigating climate change and astro-particle physics
Develop effective technology resource management solutions

## Slide 5: Technology Readiness Level

## Slide 6: Push – Pull technology

## Slide 7: Photon to Digital Converter ++
Push – TRL 1 to 8
CMOS
CMOS
p+
p
n+
n
SiO2
Poly
CMOS
p-epi
CMOS
Front side avalanche diode
Back side avalanche diode
Extended
80um
5-20um
5-50um
Ultra-thick
100-500 um
Geiger mode avalanche
VUV – Blue photon
Charged particle
Un-depleted
p-epi
depleted
Electron trajectories
Linear avalanche
Neutron or dark matter
Hole trajectories
7
Photon to Digital Converter

## Slide 8: Development timeline and update – All critical gates passed (but the last…)
2019
2023
2024
1st CMOS readout
1st 3D SPAD wafer (on fake CMOS)
Bonding on real CMOS demonstrated
Complete
PDC
2022
2nd CMOS readout wafer run
2020-21
2D SPADs and
Wafer level bonding
2018
Start at TDSI
…
2019
2023
Geiger mode testing during SPAD dev.
Wafer level SPAD testing
Large tile 8×8 dev.
2022
First functional 2×2 tile
2020
Geiger mode testing with active probe
2021
2024
System and scaling up challenges
Photon detection layer
(SPAD array) and 3D
integration
Electronics layer
(CMOS)
Notes: Two axis of development:
Top arrow - The PDC itself including both the readout electronics (top of top arrow) and the detector (bottom of top arrow)
Bottom arrow – developing the SPAD and PDC test capabilities (left most part) to system level integration in increasingly large systems

## Slide 9: Made possible by the astroparticle physics community
Definite need for a new photon detection technology
  High sensitivity and sensitive area, Low power consumption, Scalable to large area
Past Current Future Leverage
First CFI support through Carleton U. for ARGO and nEXO 1.2 M$
  Completed PDC process development and completing first production run
Engineering support from MI 437 k$
nEXO CFI grand 1.2 M$
  Maturing the PDC, producing silicon low radiation tile substrate (interposer)
Other partners: TRIUMF, UofA ~250 k$
Oak Ridge National Lab. project 902 k$ ~1.6 M$ 2.6 M$
  HEP direct support to Teledyne DALSA 350 k$
ARGO’s next CFI proposal 600 k$
Institut national d’optique / Defense R&D Canada ~1 M$
Total 6.4 M$ ~3 M$

## Slide 10: Dissimination of PDC: Creating a community of first users
Exploring (strange) properties of some to performances from large ensemble of SPADs
Single and small PDC arrays to larger PDC tiles
2×2 PDCs
50 mm
50 mm
Top

## Slide 11: A wide range of (potential) applications
Large cryogenic experiments
  nEXO, ARGO, …
Medical imaging
  Time-of-flight positron emission tomography – ToF PET
  Time-of-flight computed tomography – ToF CT
  Photon counting X-ray imaging
  Single gamma imaging
Neutron imaging
  Project with Oak Ridge NL
  Project with General Fusion
Muon imaging
Quantum information sciences
  Quantum key distribution – leverages embedded signal processing
  Future entangled photons work
LIDAR
  Ranging is a crowded field (we don’t do)
  Free space air analysis - Time-of-flight with wavelength information
Digital Single photon counting
  Enclosed air analysis for Forest fire surveillance and beyond
  Space telecommunication

## Slide 12: Push – Single Photon Air Analyser
Push – TRL 4 to 8

## Slide 13: Forest fire
It is a huge growing problem in Canada
Why isn’t there a consortium tackling this problem from all angles?
  Forestry, detection, suppression (firefighting), AI,….
  Nothing to do with astro-particle physics but has to be done!
Applying to a variety of grants
  NFRF exploration coming up
Pull – TRL 3 to 9

## Slide 14: Neutron time of flight spectrometry for General Fusion
Challenge: GHz neutron flux for 10us or so – High rate, high efficiency needed - TRL
Technology: Plastic scintillator + SiPM / PDC
Funding: MITACS Elevate for R. Underwood (former SuperCDMS PhD) and NSERC ALLIANCE (1,200k$ for 4 years)
Neutron
Fusion
Pull – TRL 3 to 8

## Slide 15: TIIGR, Therapeutic Isotope Imager with Gamma Rays
Isotope parent | Energy | Time scale | Intensity
221Fr | 218 keV | 4.9 min | 11 %
213Bi | 440 keV | 4.9 min + 46 min | 25 %
209Tl | 117 keV | 4.9 min + 46 min + 2.2 min | 1.6 %
209Tl | 465 keV | 4.9 min + 46 min + 2.2 min | 2 %
209Tl | 1,567 keV | 4.9 min + 46 min + 2.2 min | 2.1 %
225Ac decay into gamma rays
Challenge is the detection of single gamma at low rate - this is not SPECT
Our (TRIUMF + Korea) aim is to identify a compelling detection scheme by the end of 2024
If successful move towards a staged construction scheme with industrial partners
Push – TRL 2 to 7

## Slide 16: Pull – Qbit decoherence
Key issue for (most) quantum computers
Ionizing radiation (primarily from cosmic ray) affects the coherence of qubits and causes correlated errors.
Work at SNOLAB in CUTE to characterize cosmic ray impact
Emerging work on developing cosmic ray tag in cryostat
  UK – Canada grant application led by Giampa (MI/TRIUMF) and Monroe (Oxford)
Pull – TRL 3 to 5

## Slide 17: Roadblocks
Technology transfer offices – Too far from basic research
  We are not selling ice cream. The requirement of doing market assessments does not always make sense, though some grants require it (NSERC I2I, Korea)
  Risk adverse – building trust is needed but should it?
Academic administration – lack of strategic thinking
  Intellectual property - Disconnect between potential IP and “money making” IP. Most IP don’t make money and IP protection requires strategic thinking
  Research security – ad-hoc vetting for companies, more formalized for research institute but still piecemeal
  Too many grants – what should we do?
We need startup…

## Slide 18: Breakthrough
Cutting-edge technology are often compelling solutions for applied problem
  Moving technology through the TRL scale is absolutely worth doing
  Be strategic - don’t push a solution without studying the competing solutions
  Don’t worry about being “wrong”. Venture capitalist say that your drive and team is more important than your starting idea. Ability to pivot is key
Advertising our expertise is key
  Let companies come to us for solutions
  Advertisement through Linkedin and websites but also networking – Tech transfer people do a great job at that.
Many grants available though most require commercial partner matching
Drive enables technical and scientific breakthrough … And startup

## Slide 19: The end / Fin
Two related questions for all:
Should we do this, can we establish a vicious circle between basic research and applications without losing our soul?
At what TRL should we start working (not an industrialization question)?

## Slide 20: Single Photon Air Analyzer – enclosed
Laser diode
SPAD array
Beam dump
Air flow
Beam dump
SPAD array
Laser diode
Side view
Top view
Three modalities in one unit:
Scattering for smoke detection – Same wavelength as light source
Fluorescence for many molecule detection – Select wavelength
Fluorescence of specific film that react to the presence of specifc gases – select wavelength

## Slide 21: Single photon air analyser – open path
Fire laser in open air
  Backscattered light – smoke
    LIDAR for distance
  Fluorescence
    “LIDAR” for distance
  Attenuation
    For conventional attenuation SPAD not so good because high flux required
    Quantum scheme with entangled photons may reduce photon flux requirement

## Slide 22: Comparison between TRL and MRL and relevance
Plexus, https://www.plexus.com/en-us/current/articles/manufacturing-readiness-levels-aerospace-defense , 2024-08
ANSYS, https://www.ansys.com/blog/what-is-dfx, 2024-08

## Slide 23: Supporting General Fusion
Neutrons
Fusion zone
General Fusion is a company headquarter in Richmond BC (suburb of Vancouver)
Expected to produce 1GHz of neutrons (in pipe) during 10us
Extremely high rate that is very hard to deal with with analog SiPM

## Slide 24: Assisted particle imaging neutron radiography
ORNL Portable Pixelated Fast-Neutron Imaging Panel [1] Left: Multi-Anode PMT | Right: Pixelated scintillators
30 cm
30 cm
Existing solution developed by Oak Ridge National Lab.
  Multi-Anode PMT-based panel array.
  2304 pixels over 30 x 30 cm2.
  Eijen EJ-299 PSD pixelated plastic scintillators.
  100s of Watts.
M. R. Heath et al., “Development of a Portable Pixelated Fast-Neutron Imaging Panel”, DOI:10.1109/TNS.2021.3136344.

## Slide 25: From small demonstrator to Large tiles
Gamma detection demonstration 2×2 tile with scintillator and PMT
PMT R9779 Hamamatsu
Plastic Scint.
PDCs
Eu-152 (10 µCi), EJ-200 Plastic Scintillator
FPGA-based controller to setup and gather data
Development of a 8×8 tile

## Slide 26: Outside radiation instrumentation
Quantum information sciences
  Quantum key distribution – leverages embedded signal processing
Spectral LIDAR
  Time-of-flight with wavelength information
      Remote sensing of pollutants
      Remote sensing of threats
Single photon counting and high sensitivity
  Forest fire surveillance
  Space telecommunication
Few words on conventional LIDAR:
Use short infrared wavelength for eye savety
Can use low sensitivity detectors (<15%) because repeated high intensity laser source
Major industrials in this race with highly dedicated sensor design

## Slide 27: Time-bin Quantum Key Distribution
What our detectors read
What is transmitted
Interferometer convert polarisation states into time-of-arrival quantum states

## Slide 28: Time stamp classification: the power of embedded processing
Each photon is timestamped in the chip
~20ps resolution and precision
Timestamps are transmitted to the computer
The histogram shows 3 modes to the distribution corresponding to the projection of the 4 states of the qubit onto the time base (center bin holds 2 states)
Timestamps are classified inside the chip into 5 bins
Two bins for out-of-range values
Programmable bins
The provides effective data compression limiting to a 2-3 bits only the relevant information about each qubit
The two graphs show different measurements. Time variations are due to slow tuning of an interferometer for the purpose of this demonstration.
Raw time stamp data
Classified time-bins