## Slide 1
Colin Moore | Max-Planck-Institut für Physik
on behalf of the CRESST collaboration
The CRESST Experiment
Status and Outlook

## Slide 2: CRESST
~60 collaborators | 9 Institutions | 5 countries

## Slide 3: Transition Edge Sensors
Al
TES
Heater
W
Au
Thin tungsten film maintained in superconducting transition
Small change in temperature of crystal produces measurable change in resistance
Aluminum fins increase phonon collection area
Operating point maintained via gold resistive heater
Notes: Add energy range
Add TES schematic

## Slide 4: Transition Edge Sensors
Absorber
Light Detector
Two Modes:
Phonon
> 90% deposited energy
Independent of particle type
Light
< 10% deposited energy
Dependent on particle (quenching)
10.1103/PhysRevD.100.102002
NR
ER

## Slide 5: CRESST-III 2019 Results
World-leading 0.16 < mc < 1.2 GeV
10.1103/PhysRevD.100.102002

## Slide 6: CRESST-III 2019 Results
BUT
World-leading 0.16 < mc < 1.2 GeV
10.1103/PhysRevD.100.102002
Unknown background below ~200 eV “Low Energy Excess” (LEE)

## Slide 7: Effect of LEE on Dark Matter Search
Notes: Update slides from Felix

## Slide 8: Attempts to Mitigate LEE
Exchange target material
Compare commercial and self-grown crystals
Removed scintillating material from housing
Replaced scintillating sticks with clamps
Different target geometries
Notes: Not grav assist

## Slide 9: Attempts to Mitigate LEE
Exchange target material
Compare commercial and self-grown crystals
Removed scintillating material from housing
Replaced scintillating sticks with clamps
Different target geometries
Exchange target material
Compare commercial and self-grown crystals
Removed scintillating material from housing
Replaced scintillating sticks with clamps
Different target geometries
Notes: Not grav assist

## Slide 10: What We’ve Learned
Decays over time:
  Fast decay time ~10 days
  Slow decay time ~250 days
Fast component can be reset with thermal cycles
Calibrations do not affect LEE
Shape definable by power law, but different between detectors →not DM, radiological in origin
10.1140/epjc/s10052-024-13282-8
Notes: Non-identical spectral shape
Well defined by power law

## Slide 11: Low-threshold Dark Matter Results
Light detector analysed for dark matter limit
10.1103/PhysRevD.110.083038
SI
SDp
SDn
Material: Al2O3
Mass: 0.6 g
Exposure: 138 g ∙ days
Resolution: 1 eV
Threshold: 6.7 eVnr
Notes: Check Collar
Also black/grey lines are from same CRESST run

## Slide 12: Low-threshold Dark Matter Results
First observation of single photons with CRESST detector
10.1103/PhysRevD.110.083038

## Slide 13: DoubleTES Detectors
Can LEE be attributed to sensor? If so, with a second TES:
  Events in single sensor are vetoed by second → singles
  Events in bulk are observed in both sensors → shared

## Slide 14: DoubleTES Detectors
Can LEE be attributed to sensor? If so, with a second TES:
  Events in single sensor are vetoed by second → singles
  Events in bulk are observed in both sensors → shared
Does not eliminate LEE, but greatly reduced
10.1140/epjc/s10052-024-13282-8

## Slide 15: CRESST-III Current Status
5x Standard DoubleTES:
  CaWO4, 20x20x10 mm3
  Instrumented with two TES
  Standard light detector
DoubleTES Stack:
  4x Silicon-on-Sapphire, 20x20x0.4 mm3
  Instrumented with two TES

## Slide 16: Preliminary Results – CaWO4
Module | Baseline Res TES1 (eV) | Baseline Res TES2 (eV)
1 | 16 | -
2 | 5 | 5
3 | 10 | -
4 | - | 9
5 | 8 | 7
All modules have at least one working TES
Good baseline resolutions
3 TES detectors failed before data collection
Data collection on hold for He liquefier upgrade → Maintenance of affected modules

## Slide 17: Preliminary Results – Wafer Stack
Stack | Baseline Res TES1 (eV) | Baseline Res TES2 (eV)
1 | 1.4 | 1.1
2 | 1.2 | 1.0
3 | 2.6 | 1.7
4 | 1.5 | 3.9

## Slide 18: Next Steps for CRESST
Upgrade aging electronics to accommodate increased number of detectors:
Readout channels: | ~32 | 288
Active modules: | O(10) | O(100)
Notes: Will start after current scientific campaign

## Slide 19: Summary
CRESST operates cryogenic calorimeters in the search for sub-GeV dark matter, with world-leading limits below ~1.2 GeV
The LEE currently limits the sensitivity, but progress is being made
The forthcoming upgrade promises up to 3 orders of magnitude improvement in sensitivity

## Slide 21
Backup

## Slide 22: Threshold
Fuchs, D. (2023) nbn-resolving.org/urn:nbn:de:bvb:91-diss-20231004-1709800-1-3