## Slide 1: Data-driven analysis of gamma-ray spectra from the London SIGMA sensor network
Daniel Binks, Valerie Livina, Steven Bell

## Slide 2: Contents:
2
Dataset Introduction
Hospital Data
Correlations
Gaussian Processes

## Slide 3: The Data
SIGMA Data Challenge:
  NuSec and AWE pilot project
  159 gamma-ray detectors across London
  06/08/2018 – 19/12/2018
  Data stored in hdf5 files – one file per day
  Can be treated as a sensor network
3

## Slide 4: Data Format
Detector 1
Detector 2
Detector 3
HDF5
Device Status
Location
Reading
Radiation
Reading
Sensor Status
Spectrum
Time
Latitude
Longitude
  06/08/2018 – 19/12/2018
  x 139 Files
4

## Slide 5
Datasets
Groups
HDF5
File
Date
Detector Name
Spectrum, Time…
[ Date List ]
[ Detectors List ]
[ Spectrum List ]
[ Time List ]
File Reading:
H5Py
Data Handling:
pandas
DataFrame
Visualisation,
Data manipulation, etc.
5

## Slide 6: Active Detectors
Detectors in yellow (D3 SGM106813 and D3 SGM108827) are active throughout the dataset. They allow us to look at long-term trends.
Detectors in green are close to St. Thomas’ Hospital. Can look at spikes in data and short-term trends due to hospital and patient activities.
6

## Slide 7
The D3 SGM108827 is active over the 4-month period.
Look at averages and trends over long periods of time.
Can establish environmental reasoning for trends in data.
7
Monthly Average

## Slide 8: Hospital Detectors – Hourly Averages 27/11/2018
Detector: digiBASERH 16354445
Peak in counts at 10am (Orange, above)
Dip between 1pm – 2pm (Green, right)
Dip again at 6pm (not shown)
8

## Slide 9: Hospital Area Correlations
Counts / Time (s-1)
Detectors at St Thomas’ Hospital (red box) show peaks at the same hours.
Detectors around the area don’t show obvious peaks in spectra:
Detector location
Detector type
Residual peaks from 11am – 12am on 27/11/2018
9

## Slide 10: Detector Types
10
Hospital detectors are digiBASE-RH (yellow, large)
Two other digiBASE-RH detectors are underground (yellow, large)
Other detectors are D3 detectors (blue, small)

## Slide 11: Hospital Area Peaks with D3 Detectors
11
Residual peaks for D3 detectors from 10am – 11am on 27/11/2018
Counts / Time (s-1)
Yellow (left):
Area with a high and low peak in gamma-ray count
Orange (top right):
Area with medium peak in gamma-ray count
Blue (bottom right):
Area with low peak in gamma-ray count
Red (middle):
Hospital location

## Slide 12: Gaussian Processes - Explanation
12
Polynomial Regression:
Gaussian Processes Regression:
‘A Gaussian process is a probability distribution over possible functions that fit a set of points.’
Can generalise across multiple spatial dimensions (i.e. latitude and longitude) to give a distribution of peak gamma-ray counts over an area
Examples adapted from sci-kit learn.
See https://scikit-learn.org/stable/auto_examples/linear_model/plot_polynomial_interpolation.html and https://scikit-learn.org/stable/auto_examples/gaussian_process/plot_gpr_noisy_targets.htm

## Slide 13: Gaussian Processes
13
Gamma-count predictions:
Standard Deviation:
Blue: Known detectors Red: Location of hospital
Applying Gaussian Processes on residual peaks for D3 detectors from 10am – 11am on 27/11/2018
Make prediction of peak for hospital location
Hospital location is far from other sensors, expect a high standard deviation

## Slide 14: Future Work:
Fine-tune Gaussian Processes
Investigate Neural Processes
Apply physics-based techniques
14
Normalise Detectors

## Slide 15
This project was funded by the UK Government’s Department for Science, Innovation, & Technology through the UK’s National Measurement System programmes
Contact: daniel.binks@npl.co.uk