## Slide 1: EIC Workshop – Promoting Collaboration on the Electron-Ion Collider Cockcroft Institute CEA PARIS-Saclay experience and EIC
October 2020
Pierre Vedrine
CEA Saclay, IRFU/DACM
pierre.vedrine@cea.fr

## Slide 2
Overview

## Slide 3: French research organisation (nuclear, particle & astroparticle physics)
CEA
16 000 staff
4 directions
CNRS
34 000 staff
10 institutes
CNRS/IN2P3
3 300 staff
25 units
CEA/DRF
6 000 staff
11 institutes
ANR
TGIR
CNES
about 300 FTE on accelerators/magnets (incl. GANIL-CNRS) in 13 labs/institutes
about 250 FTE on accelerators/magnets (incl. GANIL-CEA) in 1 institute

## Slide 4: high technologies for accelerators
Irfu is developing and realizing particle accelerators, cryogenic systems and superconducting magnets for the scientific programs of Irfu and more widely of CEA.
Irfu develops R&D activities to support theses programs.
Irfu is involved in large scale projects in Europe, Japan and in USA.
Institute of Research into the Fundamental Laws of the Universe

## Slide 5
DACM technological infrastructures (25 000 m2)

## Slide 6: ACADEMIC AND INDUSTRIAL PARTNERS
Notes: Sigmaphi (refroidir le cyclotron du 192, programme LOTUS), Iter

## Slide 7
Competences
High Intensity Light Ion Sources
Beam Transport Lines
Beam Diagnostics
Radio-Frequency Quadrupoles
Beam Dynamics
Superconducting RF Cavities and Cryomodules
Power sources, plasma accleration, targets
Superconducting Magnets
Cryogenics
Facilities

## Slide 8: High Intensity Light Ion Sources
We are specialists of high intensity (5 – 100 mA) light ion (H+, D+) sources for accelerators
Current, emittance, species proportions, stability, reliability
Pulsed or continuous modes
IFMIF
Vert: courant sortie source (25 mA/V)
Magenta: courant en fin de ligne (20 mA/V)
Orange: cadencement
Pulsed mode: duty cycle 20%
140 mA
SILHI reliability tests during 7 days, 114 mA : 99,8 %
8 trips > 3s
SPIRAL2
40 kV, 10 mA
Permanent magnets
Cost, size
Since 1996
95 kV, 100 mA
Fraction H+ > 80 %
Source of the IPHI project
Licence Pantechnik
FAIR
Pulsed proton beam (30 ms - 300 ms @ 4Hz).
95 keV, 100 mA

## Slide 9: Low energy beam transport lines (LEBT)
Purpose of the LEBT:
House beam diagnostics
Focus the beam at the entrance of the acceleration stage
« Chop » the pulses
Challenge = keep the beam emittance small (in particular space charge effects at high intensity)
Low Energy Beam Transport Line for the FAIR proton linac at CEA Saclay
Photo P.Stroppa/CEA
Source
D+
12m
SPIRAL2 LEBT at Saclay in 2012

## Slide 10: BEAM DIAGNOSTICS
Needed to characterize the beam: current, proportions, position, profile, emittance
High intensity = high power  non interceptive beam diagnostics
2D tomographic profile
e = 0.2 π.mm.rad
0°
30°
60°
90°
120°
150°
0°
30°
60°
90°
120°
150°
Beam direction
Proportions measured by Doppler shift method
Cooled emittance-meter
with thermal screen

## Slide 11: Radio-Frequency Quadrupoles (RFQ)
DACM has the following competences:
Beam dynamics simulations
RF design
Thermomechanical studies
Cooling
Mechanical design
Ancillary equipment
Realization with industries
Assembly
Tuning
Conditioning
Design and/or fabrication and/or tuning of the RFQs for IPHI, LINAC4 and SPIRAL2
Today, RFQ for ESS: design and realization of the RFQ, tuning, RF conditioning

## Slide 12: SC cavities
Electropolishing:
Test New Electrolytes
(Better speed, surface state)
To understand and improve hydrodynamics.
Collaboration CEA-KEK :
Use of rotating cathode « ninja » (uniform polishing)
R&D BCP treatment:
Test reduction of Fluor concentration
Study Frequency Vs Chemistry
R&D Atomic Layer deposition (ALD):
Sample caracterisation of treatments HT (degassing H, N doping, ALD doping)
Tests of thermal treatments on samples and existing cavities
Magnetometer
Scanning tunnelling spectroscopy

## Slide 13: Superconducting RF technologies: from cavity design to cryomodules
Coupler assembly
Cavity train assembly
Cold mass assembly
Insertion into cryostat
Shipment
Alignment

## Slide 14: BEAM DYNAMICS codes
DACM is developing codes since 90’s. TRACEWIN is commercially distributed.
Beam dynamics codes are mandatory for accelerator optimization and commissioning
Source to target simulation of the IFMIF accelerator
160 users, 47 laboratories, 3 companies, 18 countries

## Slide 15: Power sources, plasma acceleration, target
  High-efficiency klystron with a large number of cavities
      Higher efficiency
      Working on a design at 12 GHz (70%)
      « kladistron version » of an existing klystron from Thales (TH 2166, 4.9 GHz, 50 kW, 6 cavities) to give a proof of principle.
  Enabling plasma accelerator
      Enabling multi-stage acceleration (EuPRAXIA, CILEX)
      Optimizing plasma profile
      Simulations
Target Be + PE
  R&D on Beryllium target and moderator at IPHI to produce neutrons
      Collaboration with LLB
      Target / moderator development
Time of flight

## Slide 16: Superconducting magnets
Accelerator magnets for LHC
MQ MQYY
MRI magnet: ISEULT
NbTi
FRESCA 2
Nb3Sn
Dipole and Quad for FCC
Technology development
MgB2
HTS => ReBCO
For high field magnets
For accelerator magnets
EUCARD
EUCARD2
LOTUS: radio isotope production
Conductor characterization
Other Accelerator Magnet
SARAF FAIR SuperFRS
Special magnet
WAVE: neutron diffraction=> condensed matter physics

## Slide 17: Superconducting magnets
ATLAS Barrel Toroid Magnet (LHC, CERN)
CMS Solenoid Magnet (LHC, CERN)
Large acceptance SC dipole
(R3B-GLAD GSI Darmstadt)
SACM is also developing superconducting magnets for physics detectors
MadMax Axion experiment
(MPI Munich)

## Slide 18: Cryogenics
Large coil testing facilities
R&D activities for new cooling solutions

## Slide 19
Highlights

## Slide 20: MQYY(M) Quadrupole en NbTi
MQYY (3,67 m)
MQYYM (1,35 m)
Operating Gradient | 120 T/m
Operating current | 4550 A
Bpeak at operation | 6.42 T
Manufacture of coils at the CEA
Assembly of the magnet at CERN by the CEA team with CERN/927 support
A 4 m test coil was wound by Sigmaphi and another by Elytt Energy.
The mechanical structures demonstration programme is in its final phase.
Aluminum collars
SS collars

## Slide 21: FRESCA 2 Nb3Sn dipole
14.6 T in FRESCA2, in collaboration with CERN, a niobium-tin dipole magnet with an aperture of 100 mm, tested in early August 2017 at the HFM test station at CERN.
World record, with a stored energy of 3 MJ/m and mechanical forces never before achieved in this type of magnet, with a magnetic field homogeneity of around one percent over a length of 540 mm.

## Slide 22: Dipole model toward FCC
CERN-CEA collaboration agreement to design and fabricate a single aperture block model at CEA
FCC Flared-ends Dipole Demonstrator: F2D2 => as close as possible to ECC
2D magnetic parameters | 
Iop | 10469 A
LL margin HF | 14.0 %
LL margin LF | 15.4%
Bbore | -15.54 T
Bpeak HF | 16.20 T
Bpeak LF | 11.85 T
b3 at nominal | 2.98
b3 at injection | -14.80
b5 | -0.50
b7 | -2.98
b9 | -1.46
Conductor parameters HF LF |  | 
Strand diameter | 1.1 mm | 0.7 mm
Cu/nonCu ratio | 0,8 | 2
Jc at 4.2 K and 16 T | 1200 A/mm2 | 
Cable number of strands | 21 | 34
Unreacted bare cable width | 12.579 mm | 
Unreacted bare cable thickness | 1.969 mm | 1.253 mm
HT cable thickness dim. change | 4.6 % | 4.5 %
HT cable width dim. change | 1.3 % | 
Reacted bare cable width | 12.74 mm | 
Reacted bare cable thickness | 2.06 mm | 1.31 mm
Insulation thickness at 50 MPa | 0.150 mm | 

## Slide 23: Toward HTS accelerator magnets: EUCARD
Nominal current | A | 2800
Central field wo / w SCIF (screening current induced field) | T | 5.4 / 4.7
Temperature | K | 4.2
Stocked energy | kJ | 12.5
Inductance | mH | 3.2
Temperature margin | K | 29
Load line margin | % | 47
Tested at CEA Paris Saclay and reached 5.4 T

## Slide 24
MadMax
A new QCD Dark Matter Axion Experiment
10 T NbTi coils

## Slide 25: ISEULT 11.75T WB MRI MAGNET
Iseult project magnet 11.72 T-900 mm has reached its nominal field strength
11.72 teslas on July 18, 2019.

## Slide 26: HIGH FIELD HYBRID MAGNET LNCMI-Grenoble
Objective: Exceed 42 teslas in the LNCMI Grenoble Hybrid Station
The CEA is involved in the studies and realization of the superconducting magnet outsert, the cryogenic satellite and the heat pipe. CNRS LNCMI is prime contractor for this hybrid station.
  Superconducting magnet alone 8,5 T
    8,5 T n F 800 mm n (700 kW)
  Supercond. + Bitter (9 T)
    17,5 T n F 376 mm n (12 MW)
  Supercond. + Bitter + Polyhelix (25 T)
    42,5 T n F 34 mm n (24 MW)
NbTi 8.5 T – 500 mm Outsert
Magnet manufacturing
(BNG, Allemagne)
Magnet support post
25+ 9 + 8,5 = 42,5 T

## Slide 27: NOUGAT
Insert made of 9 double pancake (ReBCO) (inner diameter of 50 mm) using an innovative MI insulation (Metal-as-Insulation)
32.5 T obtained (14,5 T created by the HTS insert with a background field of 18T @ LCNMI Grenoble)
ANR-14-CE05-0005 'NOUvelle Génération d'Aimants pour la production de Teslas'
New Generation of Magnets for Teslas Production

## Slide 28: JT60 (broader approach)
      Superconducting Tokamak JT60-SA
      Construction of 18 (+2) coils (IRFM/IRFU) – 15 tons, 4.5 K
Cryogenic tests
    Nominal conditions ( 27.5 kA)
    All steps succesful ( fast discharge, quench)
Outer Intercoil mechanical structure integration
11 coils left Saclay  NAKA

## Slide 29: Future Circular Collider
Objective: design of a p-p collider at CERN (100 TeV centre of mass, 100 km circumference, 16 T dipoles)
DACM involved in arc optics and magnet design.
Collider optics validated
Maximum fields of the magnets, protection, beam stability, ...
CDR published
Future: participation in the FCC-ee booster
Collider scheme
http://fcc-cdr.web.cern.ch/
Multi-turn injection stability (3.3 TeV)

## Slide 30: RFQ European Spallation Source
Novembre 2019

## Slide 31
Cryomodules prototype M-ECCTD ( CM00):
February 2019: Transport of the prototype M-ECCTD cryomodules to Lund after the RF and 2K power tests carried out at CEA at the end of 2018.
The M-ECCTD cryo module will be tested at ESS. It is currently installed in the test stand...
Beta = 0.67
M-ECCTD in the test bunker at Lund
CM01: 1er cryomodule medium beta series tested at Saclay
CM01 in the test bunker at Saclay
Cryomodules prototype H-ECCTD (CM30):
Assembly done, test is ongoing at Saclay
Beta = 0,86
CM30 in the assembly hall in Saclay
ESS cryomodules

## Slide 32: SPIRAL 2 Cryomodules
12 Cryomodules type A (CMA) quarter wave cavity installed by the end of 2015
1st beam at LINAC output (33 MeV): 27/11/2019
A proton beam intensity of 4.7mA at the nominal energy of 33 MeV, produces a mono energetic neutron beam at 30 MeV : 09/2020

## Slide 33: SARAF accelErator, SOREQ
Delivery of the medium-energy line, MEBT to SOREQ-Israel in August 2020
Superconducting linear accelerator, providing proton and deuteron beams of variable energy between 5 and 40 MeV with an intensity of up to 5mA for SOREQ in Israel.

## Slide 34: interest in EIC

## Slide 35: IRFU Potential interest to the EIC
DACM is interested in helping the EIC in its development.
We have clearly a number of expertise and facilities that could benefit developments for the future accelerator.
Expertise
  Beam physics and technologies
  SRF technology
  Superconducitng magnets
Facilities
  - SRF assembly and test facilities
  - Magnet assembly and test facilities
DACM welcomes future collaborations with the EIC team on the accelerator and the detectors.