## Slide 1: EIC/FCC-ee Commonalities*) of RF systems
Erk Jensen/CERN
Special thanks: K. S. Smith/BNL, R. A. Rimmer, A.-M. Valente-Feliciano/TJNAF, M. Benedikt, O. Brunner, F. Gerigk, A. Grudiev, E. Montesinos, I. Syratchev/CERN, J. Cai/ULANC
… and probably many others (sorry)
EIC Workshop – Promoting Collaboration on the Electron-Ion Collider
*) probably “Similarities” describes it better.

## Slide 2: Outline
Introduction: EIC RF systems and FCC-ee RF systems
SRF and Cryomodules
Fundamental Power Couplers
HOM Damping
RF Power Generation
Crab Cavities

## Slide 3: EIC RF systems overview
3
Electron - 591 MHz electron storage cavity
Electron - 1773 MHz 3rd harmonic cavity
Hadron Cooling - 591 MHz acceleration cavity
Rapid Cycling Synchrotron - 591 MHz acceleration cavity
Hadron - 591 MHz bunch compression cavity
Hadron – 24.5 MHz acceleration cavity
Both rings – 394 MHz crab cavity
Hadron – 49.2 MHz and 98.5 MHz bunch splitter cavity
Injector - 571 MHz bunch compression cavity
Hadron - 197 MHz bunch compression cavity
K. Smith, R. Rimmer
eSR
HSR
SHC
RCS

## Slide 4: EIC RF systems (1/4)
eSR: Total RF voltage 70 MV, , .
  Choice: 14 CMs, one 2-cell cavity/CM for 5 MV, 591 MHz, 0.8 MW/cavity – power limited.
  Requires 2 adjustable 500 kW FPCs.
  Strong HOM damping.
  Option, presently studied: 1-cell cavities, would require 28 CMs.
  Q: Would a lower frequency make things simpler? (e.g. 394 MHz – synergy with FCC) – see next slide!
Baseline eSR: 2-cell, single-cavity CM
K. Smith, R. Rimmer

## Slide 5: EIC RF systems (2/4) – eSR choice of
 | 394 | 591 | 788
#cells (eSR) | 14 | 28 | 32
#Amplifiers (eSR) | 14 | 14 | 16
impedance | least | reference | most
HOM power (kW) | 264 | 528 | 704
3H freq | 1182 | 1773 | 2364 (1572 2nd?)
Comments: | Synergy with LHC/FCC (e.g. crabs) | unique | Synergy with PERLE/FCC (e.g. crabs)
size | New cavity, cryostat, infrastructure | CDR reference design (also fits in JLAB mod. cryostat) | Fits in cryostat and infrastructure
transients | least | acceptable | most
Max bunch rate (MHz) | 394 | 197 | 788
R. Rimmer

## Slide 6: EIC RF systems (3/4)
RCS, HSR (), SHC:
  Choice: 591 MHz 5-cell cavities for 14 MV (RCS: 3, HSR: 2, SHC: 8)
  Choice 1-cavity cryomodule, 4.3 m long, 5-cell cavity, 75 kW/cavity
HSR:
  add NCRF systems at 24.6, 49.2, 98.5 and 197 MHz
  Option, presently studied: use 2-cell cavity CM’s
SHC:
  add harmonic system at 1773 MHz – 3 CMs with one 5-cell cavity each.
K. Smith, R. Rimmer

## Slide 7: EIC RF systems (4/4): 5-cell Cryomodule
591 MHz, 5-cell elliptical, operated @ 2 K
Single cavity per cryomodule
Warm beamline SiC HOM absorbers
Maximum 20 MV RF voltage
  : 15.8 MV/m
  : 35.8 MV/m
  : 69.7 mT
  : 32 W
Used in RCS (3 units), HSR (2 units) and SHC (8 units)
K. Smith, R. Rimmer

## Slide 8: FCC-ee RF systems (1/2)
8
O. Brunner
RF:
2.8 km
RF:
2.8 km
PA
PB
PC
PD
PG
PJ
29.9 km
Z | 400 MHz, 1-cell, strong HOM damping! 2 MV/cavity, 1 MW/cavity!
WW | 400 MHz, 4-cell, still substantial BL and HOM excitation, 1 MW/cavity
ZH | 400 MHz, 4-cell cavities, 370 kW per cavity (change FPC)
 | realign 400 CMs to share them for both beams, add 800 MHz, 5-cell cavities, operated at 20 MV/m, 175 kW/cavity
Z | 400 MHz, 1-cell, strong HOM damping! 2 MV/cavity, 1 MW/cavity!
WW | 400 MHz, 4-cell, still substantial BL and HOM excitation, 1 MW/cavity
ZH | 400 MHz, 4-cell cavities, 370 kW per cavity (change FPC)
 | realign 400 CMs to share them for both beams, add 800 MHz, 5-cell cavities, operated at 20 MV/m, 175 kW/cavity

## Slide 9: FCC-ee RF systems (2/2)
9
O. Brunner
 | Z | WW | ZH |  | 
Beam energy (GeV) | 45.6 | 80 | 120 | 175 | 182.5
Beam current (mA) | 1390 | 147 | 29 | 6.4 | 5.4
# of bunches | 16640 | 2000 | 328 | 59 | 48
total RF voltage (GV) | 0.1 | 0.75 | 2 | 9.5 | 10.93
400 MHz system, operated at 4.5 K: |  |  |  |  | 
RF voltage (MV) | 100 | 750 | 2000 | 4000 | 4000
#cells/cav; #cav/CM; #CM | 1;4;13 | 4;4;13 | 4;4;34 | 4;4;68 | 
Voltage/cavity (MV) | 1.92 | 14.4 | 14.7 | 15 | 
Power/cavity (kW) | 962 | 962 | 368 | 175 | 149
800 MHz system, operated at 2 K: |  |  |  |  | 
RF voltage (MV) |  |  |  | 5500 | 6930
#cells/cav; #cav/CM; #CM |  |  |  | 5;4;74 | 5;4;93
Voltage/cavity (MV) |  |  |  | 18.6 | 18.6
Power/cavity (kW) |  |  |  | 176 | 155
 | Z | WW | ZH |  | 
Beam energy (GeV) | 45.6 | 80 | 120 | 175 | 182.5
Beam current (mA) | 1390 | 147 | 29 | 6.4 | 5.4
# of bunches | 16640 | 2000 | 328 | 59 | 48
total RF voltage (GV) | 0.1 | 0.75 | 2 | 9.5 | 10.93
400 MHz system, operated at 4.5 K: |  |  |  |  | 
RF voltage (MV) | 100 | 750 | 2000 | 4000 | 4000
#cells/cav; #cav/CM; #CM | 1;4;13 | 4;4;13 | 4;4;34 | 4;4;68 | 
Voltage/cavity (MV) | 1.92 | 14.4 | 14.7 | 15 | 
Power/cavity (kW) | 962 | 962 | 368 | 175 | 149
800 MHz system, operated at 2 K: |  |  |  |  | 
RF voltage (MV) |  |  |  | 5500 | 6930
#cells/cav; #cav/CM; #CM |  |  |  | 5;4;74 | 5;4;93
Voltage/cavity (MV) |  |  |  | 18.6 | 18.6
Power/cavity (kW) |  |  |  | 176 | 155

## Slide 10
FCC SRF R&D Program structure
Parameters and Design
Coordination and Review
Integrate Baseline Design and Parameters
Define Installation and Operational Scenarios
Perform Implementation Studies (cost, powering, cooling, civil engineering, safety)
Cavity Studies
Determine the Optimum Cavity Shape, Technology and Operating Temperature (complexity, power consumption, Qo, Eacc)
Design 1-cell and 4-cell Cavities for the new CM
Complete Beam-Cavity Interactions Studies
Identify Cavity Control System (LLRF) challenges
Complete HOM Damping Schemes and Coupler Design Optimization Studies
SRF & Substrate Technologies
Improve Engineering of Cavities: New SC Materials, Improved Fabrication, Substrate Surface Preparation and Coating Techniques
Fabrication and Testing of 1-cell and 4-cell Cavities for the new CM.
Promote R&D Activities in Collaboration with international Partners
Cryomodule Development
Improved design and engineering of 400MHz cryomodule including ancillaries
Built a 2 cavity CM which can host 1-cell / 4-cells 400MHz cavities
Promote R&D Activities in Collaboration with international Partners (e.g. JLAB)
800 MHz CM: Profit from Ongoing Development @ PERLE
FPC & HOM Couplers
Improved design and engineering of the ‘LHC-type’ 400 MHz FPC
Fabrication and Testing of the improved 400 MHz FPC for the new CM
FPC R&D:
  Pave the road towards 1MW CW fixed/movable FPC operating at 400 MHz
  Design and engineering of ‘adjustable’ FPC (external large adaptation of Qext)
HOM coupler production
O. Brunner, F. Gerigk

## Slide 11: SRF and Cryomodules
FCC baseline is Nb/Cu at 400 MHz, operated at 4.5 K, (5 MV/m) and bulk Nb at 800 MHz, operated at 2 K (20 MV/m).
FCC R&D: alternative materials (A15) thin films, novel cavity manufacturing, new CM concepts.

## Slide 12: FCC-ee , bulk Nb based 802 MHz cavities
Existing collaboration with JLAB – relevant also for PERLE@ Orsay
A.M. Valente Feliciano, F. Marhauser

## Slide 13: Nb/Cu Technology – Energetic Condensation
A.M. Valente Feliciano

## Slide 14: R&D on novel cavity fabrication techniques
Spun seamless 400 MHz cavity (INFN/LNL)
Electroforming on aluminium mandrel (CERN) – very promising!
…and also: Electro-hydroforming, hydroforming

## Slide 15: Fundamental Power Couplers
Interest EIC: 500 kW power couplers 591 MHz.
FCC-ee in its different stages always requires to feed 100 MW RF in CW to the cavities. This requires hundreds of couplers!
The LHC has variable couplers capable of 500 kW CW – CERN is performing R&D and is building FPC’s for many international partners.
CERN is home to the “World-Wide FPC Meeting” of experts.

## Slide 16: 500 kW CW, Variable Couplers
16
Use existing fixed 500 kW CW coupler design.
Vary using adjustable waveguide tuner section.
Initial funding by BNL LDRD.
Testing delayed by Covid19.
K. Smith

## Slide 17: FCC-ee needs:
Power need at FCC-ee Z-pole: 1 MW/single-cell cavity.
FCC baseline: use 2x 500 kW power couplers (LHC-type)
R&D towards 1 MW CW power couplers is only starting
Complication: to use the same 4-cell cavities in FCC-ee “WW” and FCC-ee “ZH”, the coupling must be changed.

## Slide 18: LHC power couplers (400 MHz, CW – variable coupling)
variable by a factor 20.
Tested up to 500 kW CW forward.
E. Montesinos

## Slide 19: New FPC R&D Centre created in Prévessin
Mezzanine: 200 m2: Components clean storage, Test boxes, vacuum, metrology, assembly robots
Ground floor (600 m2): transport, heavy equipment, welding & brazing, machining, LLRF measurements and 1 kW processing, 1 MW processing with resonant ring
E. Montesinos

## Slide 20: HOM Damping
EIC eSR has 2.5 A beam current and short bunches(!) eSR HOM damping baseline: SiC warm beamline, HOM absorbers.
FCC-ee requires strong HOM damping in particular at the Z-pole (1.4 A), baseline requires “only” hook-type couplers.

## Slide 21: EIC eSR High-Power SiC HOM absorbers
Requirement and challenge
  High power (20 kW), broadband HOM damper
  Large size of SiC HOM damper for low frequency
Initial LDRD program on SiC HOM absorber:
  Low power test on a cavity to test effective damping bandwidth
  High power test to test the power handling capability
Results:
  Tests were delayed due to CoVID-19.
Inspiration
  Instead of one solid piece HOM damper, fabrication and RF study of piece-by-piece (tile) type HOM damper
  HOM damper suitable for various temperature environments.
SiC HOM Absorbers
eSR CM
R. Rimmer

## Slide 22: FCC-ee HOM power estimates
From https://cds.cern.ch/record/2302276/files/CERN-ACC-2018-0005.pdf :
We believe that, even for the Z-pole machine, we can achieve the required HOM damping with hook couplers (4 per 1-cell cavity). This is possible at 400 MHz thanks to a judicious combination of bunch spacing, cavity design and cavity separations.
I. Karpov

## Slide 23: HOM Damping in FCC-ee
A.M. Valente Feliciano, S. Gorgi Zadeh
See also https://indico.cern.ch/event/656491/contributions/2932265/

## Slide 24: RF Power Generation
Interest for EIC: Baseline is using IOT’s (65 kW, 591 MHz modules), but is looking at a 36 x 400 kW SSPA solution. Total RF power . eSR would need 200 of these! (interest in SSPA)
For FCC, CERN studies 400 MHz and 800 MHz High-Efficiency Klystrons as well as SSPA’s. Total RF power .
CERN’s SPS has recently been upgraded with a 200 MHz, 4.6 MW SSPA system (see above).
CERN also has relevant experience with IOT systems (SPS 800 MHz installation: see above) and 1.3 MW MB-IOTs.
CERN SPS 800 MHz IOT installation, 2x 200 kW
CERN SPS 200 MHz SSPA, 4.6 MW

## Slide 25: 400 MHz – retrofitting the LHC klystron with a “High-Efficiency” version:
Parameter | present TH2167 | CSM upgrade
Frequency | 400 | 
Beam voltage | 54 | 
Perveance, | 0.72 | 0.72
Saturated RF power | 300 | 350
Efficiency | 60 | 70
Parameter | present TH2167 | CSM upgrade
 | 400 | 
 | 54 | 
 | 0.72 | 0.72
 | 300 | 350
 | 60 | 70
CSM: “Core Stabilisation Method”
Uses 3rd harmonic cavity.
Efficiency increase 60%  70%
“Drop-in” replacement (same HV supply, same perveance, same drive).
Proof of principle for FCC!
This is only a moderate step, respecting practical constraints by the presently installed klystrons – a full optimization for an FCC 400 MHz tube, targeting has started.
I. Syratchev, J. Cai, Thales AVS

## Slide 26: FCC-ee High-Efficiency 800 MHz Klystron: 134 kV × 12.5 A × 80% > 1.3 MW
I. Syratchev, J. Cai

## Slide 27: Benchmark with PIC code
Efficiency=80%, Time cost=12h
Bz=0.07T (5xBr). Efficiency 79%
Efficiency=79%, Time cost=50h
MAGIC2D
CST3D
I. Syratchev, J. Cai

## Slide 28
MAGIC (0.07T) 2D, 79.4%
FCC#6. KlyC2D vs MAGIC
MAGIC (20T) 2D, 79.6%
The radial bunch ‘expansion’ in output cavity (MAGIC2D) practically does not affect efficiency. This validates KlyC2D as an attractive (and fast) tool.
Nz=256,Nr=4, =79.9%,Tcpu= 20 min
Tcpu = 4000 min (~1ooo ns)
Beam settings:
Saturation=97%
Nz=128,Nr=4
Convergent analysis
I. Syratchev, J. Cai

## Slide 29: EIC Scope Detail: RF1010 Building
2020: RF1010 Support Building with 14.4 MW* total SSA based high power RF, interface to IR-10 and IR-10 cryomodule layout.**
  Remarkable power densities becoming realistic for solid state power across the digital TV broadcast frequencies.
  3D model is based on one of the vendor budgetary proposals.
591 MHz, 400 kW modular amplifier unit.
36 = 18 * 2 shown.
* 14.4 MW is just the result of showing 36x 400 kW “units”. Vendor budgetary quote in this case is based on 400kW = 4x 100kW per amplifier.
** This layout is a conceptual layout to explore the space requirements for 18x single cell 591 MHz ESR cryomodules. The 18 cryomodules fit in the available IR space. The SSA power density leads to reduced building space needs.
29
K. Smith, R. Rimmer

## Slide 30: SPS 200 MHz, 4.6 MW SSPA System
Amplifier #1
1280 x 2 kW RF modules
16 Towers
300 m of 6-1/8 Lines
15 Hybrid combiners & loads
RF lines:
1200 m of 345 mm coaxial
Amplifier #2
1280 x 2 kW RF modules
16 Towers
300 m of 6-1/8 Lines
15 Hybrid combiners & loads
TWC200 Cavities (total now 6)
1st floor: Power combiners
2nd floor: 32 x 144 kW “towers”, arranged as 2 “amplifiers”
E. Montesinos, Thales/Gerac
36 m
19 m
12.5 m

## Slide 31: SSPA for FCC (? – really big, 200,000 transistors!)
Present baseline for FCC are High-Efficiency Klystrons.
CERN has also started R&D on higher power density SSPA’s new ideas of power combiners scalable to thousands of inputs, and GaN-based SSPA’s, jointly with academic and industrial partners.
… but: progress doesn’t come wandering along – one has to make it!

## Slide 32: Crab Cavities
Interest for EIC: see next slide
CERN studies 400 MHz “WOW” (Wide Open Waveguide) crab cavities for the FCC-hh (R&D WP8).
And of course the 400 MHz crab cavities for LHC – result of a very successful, international collaboration (see above map, presented by L Rossi at 4th Cost&Schedule Review, Nov. 2019).

## Slide 33: EIC Crabbing systems (1/2)
New SRF crabbing systems for both rings (eSR and HSR)
Large voltage needed for 25 mrad crossing angle
eSR system 394 MHz, 2.9 MV each side
HSR system 197 MHz, 34 MV each side
  Need second harmonic for linearization
IR 6 total 8 x 197 MHz cavities, 6 x 394 MHz cavities
Two candidates under consideration based on LHC experience, DQW and RFD
  Both meet voltage requirements
  Both can meet pressure code (even at 197 MHz)
  Both have been fabricated at 400 MHz
  Both need improved HOM damping for EIC
K. Smith, R. Rimmer

## Slide 34: EIC Crabbing systems (2/2)
DQW 394 MHz crab cavity
RFD 197 MHz crab cavity
Courtesy: Qiong Wu, Silvia Verdú-Andrés, Doug Holmes, Binping Xiao
Courtesy: Suba Da Silva, HyeKyoung Park, Jean Delayen, ODU, Jim Henry Jlab.
621
940
“WOW” crab cavity
Courtesy: Zhenghai. Li
DQW 197 MHz crab cavity
822
453
585
K. Smith, R. Rimmer

## Slide 35
The CERN crab cavities
290kg
1.4m
3
Nb/Cu:
Wide-Open Waveguide (WOW) crab cavity for FCC: Nb/Cu, 1st prototype completed in 2018
Bulk Nb:
E.g.: DQW crab cavity for HL-LHC
0.66 m
Total power loss ~ 60W
@ Q0 = 4x108 / 3 MV
Dissipated Psurf [W/m2]
B. Xiao et al, Physical Review Special Topics - Accelerators And Beams, 2015
A. Grudiev et al, Proceedings of SRF 2015.
R. Calaga, A. Grudiev

## Slide 36: Wide-Open Waveguide Crab Cavity
E-field
Details (from SRF 2019):
https://indico.cern.ch/event/832933/contributions/3644032/
https://indico.cern.ch/event/832933/contributions/3644009/
A. Grudiev, F. Avino, A. Sublet

## Slide 37: RF and engineering design studies of the cavity
FMC
HOM coupler
Impedance and HOM characterization
Multipacting analysis of the bare cavity
Coupler design and HOM damping
Pressure sensitivity
Comprehensive design study has been performed including:
Cavity design and power loss calculation using different coatings
Beam coupling impedance and HOM characterization
Preliminary design of the fundamental and HOM couplers
Multipacting simulations
RF sensitivity to pressure
Preliminary design of the coupler for cold tests
See details in DOI: 10.1103/PhysRevAccelBeams.22.072001
A. Grudiev, F. Avino, A. Sublet

## Slide 38: Fabrication of Copper cavity
Copper cavity (substrate) assembly has been finished end of 2018
Visual inspection has been done showing good RF surface state and no visible defects
A. Grudiev, F. Avino, A. Sublet

## Slide 39
Nb+
(Nb)
(Cu)
V-
V+
WOW coating challenge
Cylindrical magnetrons
  Coating surfaces at different:
  Distances (20 – 80 mm)
  Angles of incidence (0 – 90°)
How to get a void-free and defect-free film?
4
Increase the fraction of metal ions -> HiPIMS
Increase metal ions energy:
  By a negatively biased substrate
  By a positive pulse (PP)
252 mm
A. Grudiev, F. Avino, A. Sublet

## Slide 40: Summary
There are a number of “similarities” (if not commonalities) between the different versions of the FCC-ee and the EIC RF systems
Areas of common interest – possible collaboration:
  Cavity and CM design and optimisation
  Fundamental power couplers of MW class
  HOM damping
  RF Power generation (in particular SSPAs)
  Crab cavities
Synergies could be maximized when choosing similar frequencies (please reconsider 394 MHz for eSR)
CERN wishes to collaborate – it is a “win-win” scenario.
Thank you very much!