## Slide 1: Millimeter-wave undulators for compact XFELs
Liang Zhang1,3, Jim Clarke2,3, Craig R. Donaldson 1,3, Craig W. Robertson 1, Colin G. Whyte 1, and Adrian W. Cross 1,3
liang.zhang@strath.ac.uk
1Department of Physics, SUPA, University of Strathclyde
2ASTeC, STFC Daresbury Laboratory, Sci-Tech Daresbury
3The Cockcroft Institute, Sci-Tech Daresbury

## Slide 2
Wavelength of output radiation
Free-electron Laser (FEL)
[1] Bolko Beutner, Introduction to Free Electron Lasers
[2] P. G. O'Shea and H. P. Freund, 292 (5523), pp. 1853-1858, 2001.
[3] A. Ghaith, et. al, Physics Reports 937(6), 2021
[4] https://www.youtube.com/watch?v=-kdqVuJxkrs
=
peak B field of the undulator,
K is the undulator / deflection parameter
The concept was proposed in 1972
First experiment in 1977-78
Undulator

## Slide 3
X-ray Free-electron Laser (XFEL)
First X-FEL operated in 2005. Features:
  Coherent, narrow bandwidth, high energy, short duration
Applications:
  Bioscience (molecular movies of enzyme catalysis)
  Physics (understand internal structure of star core)
  Chemistry (observe form / break of bonds between molecules)
  Challenges:
  GeV-energy electron beams
  Undulator with short period
  High cost (~£5 Bn), <10 XFELs in the world
  Timeliness: UKXFEL science case made by STFC in Oct. 2020 and CDR approved 2022
Copyright: European XFEL

## Slide 4
Compact XFEL
Compact XFEL relies on
High-gradient accelerators
  Traditional accelerator: higher frequency (X, Ka-band accelerator)
    high-power source required, need to prevent microwave breakdown
  Novel concept: DLA, PWFA, LWFA
Short period undulator ()
Europe XFEL: 17.5GeV, 3.4km
Swiss XFEL: 5.8GeV, 740m
CompactLight: 5.5GeV, 480m (Conceptual Design Report)

## Slide 5: Undulators
 | SwissFEL (Aramis) | Europe XFEL
Structure | Planar hybrid | Planar hybrid
Material | NdFeB | NdFeB
K | 1.2 | 3.0
Period | 15 mm | 26 mm
Peak field | 0.85 T | 1.24 T
Gap type | Variable | Variable
Gap | 4.7 mm | 6 mm
Permanent magnet undulators
Cryogenic permanent magnet undulators
Superconducting undulators
Exotic undulators (Microwave undulator, Optical undulator)
  State-of-the-art PMU
1.7 mm period allows for generating soft X-ray radiation using a 250 MeV beam.
Moderate K value for 1.7 mm period MU mitigated by
588 periods per meter.
200MeV
300MeV

## Slide 6: Microwave undulator (MU)
[1] T. Shintake, Jpn. J. Appl. Phys. 22, 844, 1983.
[2] S. Tantawi, Phys. review letters 112, 164802, 2014.
SLAC 2014: Frequency 11.424 GHz, Q 91000, K 0.69.
Klystron power 50MW. Tunable radiation 400-600nm with 50 MeV to 70 MeV beam, and seeded coherent harmonic generation (SCHG) 160-240nm @ 120 MeV beam
NLP, Japan 1983:
Freq. 2.856 GHz, Q 7100, K 0.24.
Klystron power 300kW. 400nm @143MeV beam.

## Slide 7: Features of mmWU
Features
Shorter undulator period, lower beam energy;
Large aperture to reduce wakefield;
Fast control of polarization and magnetic field (electrical vs mechanical);
Resilient to damage by radiation (copper vs rare-earth material).
Demonstrate soft X-ray radiation using the FEBE 250MeV beam
[1] Deepa Angal-Kalinin, FEBE Users Group Meeting, 5th July 2022.
=1.7 mm @ 94 GHz;
K=0.13 @ 2.5MW drive power;
=3.57nm (348eV)@ 250MeV beam.

## Slide 8: Requirements for MU
goes to 0 when = [An overmoded structure is required, operating far from the cutoff]
Backward Wave
Forward Wave

## Slide 9: Types of MUs
[1] L. Zhang, W. He, J. Clarke, et. al, IEEE Trans. Electron Devices, 65(12), pp. 5499-5504, 2018
[2] L. Zhang, W. He, J. Clarke, et. al, Journal of Synchrotron Radiation, vol. 26, 2018
 | Cavity-type undulator | Flying-type undulator
Microwave source | Medium power, long pulse microwave source, 30 MW, 2 ms | High power, short pulse microwave source, 800 MW, 10 ns
Field stability | Excellent | Tapered field due to loss
Phase accuracy | Excellent | Require phase locking
Cavity-type undulator based on the corrugated waveguide
Flying-type undulator based on helically corrugated waveguide.
Mode coupling to generate copropagating wave to increase the effective interaction length.

## Slide 10: Ka-band MU
[1] L. Zhang, W. He, J. Clarke, et. al, IEEE Trans. Electron Dev., 66(10), p.4392-4397, 2019.
[2] L. Zhang, J. Clarke, C. Donaldson, et. al, Sci. Rep., 12, 7071, 2022.
  Design and optimize the undulator structure based on low-loss quasi-optical corrugated waveguide. Inner Diameter of 16.2mm, Length of 1m, K peak of 0.5 @50MW, 36GHz, 2ms pulse duration.
Scalable (frequency and cavity length) design for the coupler structure
Particle trajectory simulation in the MU
Zero drift distance by controlling injection phase
Small drift distance at higher beam energy (oscillator for beam energy > 1GeV)
Designed from near-field radiation pattern

## Slide 11: Manufacture of the MU
Evaluate the different methods of manufacture of a short section of MU and measure performance using a Vector Network Analyser (VNA).
(1) Electroforming
(2) Direct machining
(3) 3D printing + plating
Electroforming and direct machining are promising
[1] L. Zhang, C. Donaldson, J. Clarke, et al. Sci. Rep., 12, 7071, 2022.
Notes: 3D printing: good accuracy, seeking for the copper plating method.
Better result for the directly machining method compared with the electroforming method.
Prepare for the high frequency shorter wavelength undulator.
Problems:
  The structure was made by electroforming method.
  ~40% of the Q0 compared with simulation.
  Higher drive power is required.

## Slide 12: W-band mmWU
Bragg reflector reduces the mm-wave power leakage and maintains the large aperture.
[1] L. Zhang, et. al, J. Infrared Milli. Terahz Waves, vol. 37, no. 9, pp. 846-856, 2016.
Frequency (GHz) | 94.0 | Q factor | 47800
in free space (mm) | 3.19 | Input power (MW) | 2.5
Undulator period (mm) | 1.72 | Peak Ex on axis (V/m) | 2.43E8
Waveguide radius (mm) | 3.0 | (T) | 0.81
Min. tunnel radius (mm) | 1.80 | Electric field at wall (V/m) | 3.3E6
Corrugation period (mm) | 1.38 | K | 0.13
Overall length (mm) | 200 | output (nm) | 3.6nm (342eV)
Frequency (GHz) | 94.0 | Q factor | 47800
 | 3.19 | Input power (MW) | 2.5
 | 1.72 | Peak Ex on axis (V/m) | 2.43E8
Waveguide radius (mm) | 3.0 |  | 0.81
Min. tunnel radius (mm) | 1.80 | Electric field at wall (V/m) | 3.3E6
Corrugation period (mm) | 1.38 | K | 0.13
Overall length (mm) | 200 |  | 3.6nm (342eV)
Broadband feature enables step-tunning.

## Slide 13: W-band mmWU

## Slide 14: FEL Experimental setup
[12] Sami Tantawi, Phys. Rev. Lett., 112(16), 164802, 2014
Chiller
Phase shifter
Pre-amplifier
High-power AMP
Signal generator
Electron gun
Seed laser
Linacs
Spectrometer
Modulator
Seeded coherent harmonic generation (SCHG) setup
Self-Amplified Spontaneous Emission (SASE) can be achieved by cascading multiple MU sections
MU

## Slide 15: Driving sources
SLAC
12GHz,
75 MW,
1.6 µs @120 Hz, Eff. 55%.
Japan
170GHz,
1 MW, CW,
Eff. 45%.
Strathclyde
90GHz, ~10 MW, ~150ns, single shot, Eff. ~4%. (2D SWS)
60MW@36GHz
IAP, Russia
90GHz, 150MW, ~1ns, eff. 13%, IAP, Russia
Frequency | Sources | Specifications
X-band | Klystron | 11.424 GHz, 75 MW, 55%, SLAC
Ka-band | Gyro-klystron | 30.0 GHz, 15 MW, 40%, IAP
 | CARM | 35.7 GHz, 30 MW, 10%, IAP
 | Gyrotron | 35.0 GHz, 250 MW, 10%, NRL
W-band | Gyrotron | 94.4 GHz, 5.6 MW, 23%, pulsed mode, IAP
D-band | Gyrotron | 170 GHz, 1 MW, 45%, CW, CPI, KIT, Japan, IAP
 | CARM | 250 GHz, 20 MW, 20%, NRL
MBK
Notes: The oscillator can be used when the beam energy is large. For a low beam energy, amplifiers are preferred.

## Slide 16: Conclusion
Millimetre-wave undulator enables
  X-FELs using the 250MeV FEBE beam at Daresbury Lab
  The MW-level millimetre-wave source developed for the MU can be used for high-gradient accelerator research
  Enhances the search for axion-like-particles (ALPs) by increasing the event rate of the detection system
[1] E. Nanni, SLAC, HG 2021.
[2] G. Linde, IEEE Trans. Aerospace and Electronic Systems, 44(3), pp. 1102-1117, 2008.
[3] M. A. K. Othman, et. al, Appl. Phys. Lett. 117, 073502 (2020).
[4] L.M. Capparelli, Physics of the Dark Universe, 12 (37-44), 2016.

## Slide 17
I would like to thank the Science and Technology Facilities Council (STFC) U.K., Cockcroft Phase 4 grant ST/V001612/1 for supporting this research.
Thank you for attention!
I’d be happy to answer any questions