## Slide 1: Diamond upgrade M. Apollonio – Diamond Light Source Ltd. Institute of Physics PABG 2017 RHUL, London thanks and credits to: A. Alekou, T. Pulampong, R. Bartolini, R. P. Walker (DLS) S. Liuzzo, P. Raimondi, N. Carmignani (ESRF)

## Slide 2
  Diamond today
    ... and other facilities
  Low Emittance
    Brilliance and coherence
    From 2.7nm to < 270pm
    Constraints on new machine
  Evolution of Diamond-II low emittance lattice
    Double Double Bend Achromat (DDBA)
    Double Triple Bend Achromat (DTBA)
  Where we stand
    Optimizations
    Open issues
  Summary
Outline

## Slide 3
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions
  Diamond
  3rd generation synchrotron light source
  world class facility
  31 beamlines
    7 bending magnet BLs
    24 undulator/wiggler BLs
      2 SC wigglers BLs
  Machine parameters
    E = 3.0 GeV
    e = 2.7nm / C=0.3% / n =(0.172,0.273) / x = (1.5,2) /
    LT > 12 hrs [usergaps/Wig-on/300mA] / top-up mode

## Slide 4
MAX IV (Sweden): reached 200mA (end of 2016), first users
ESRF upgrade (France): placing contracts
magnets placed, large scale prod. 2017-mid2018;
assembly phase. Long SD end of 2018, back in op. 2020
Sirius (Brazil) under construction
APS-U (US) has passed CD1
ALS-U (US) at CD0 stage
BAPS (China) got money for R&D programmes (ready in 2022?)
SLS-II (Switzerland) and Diamond II
advanced consultations with PBSs and users in view of CDR
many labs are investigating options (SOLEIL, ELETTRA, ILSF, ...)
lattices
Others Low Emittance DDBA HMBA DTBA optimization conclusions
Notes: 4
Talk only about ESRF, Sirius, ALS U, Diamond II

## Slide 5
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions

## Slide 6
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions

## Slide 7
electron beam sizes (standard straight)
Parameter (rms values) | Diamond | Diamond-II (DTBA)
Horizontal size, x [m] | 123.5 | 23.6
Vertical size, y [m] | 3.5 | 3.5
Horizontal divergence, x’ [rad] | 24.1 | 5.1
Vertical divergence, y’ [rad] | 2.3 | 2.3
Product | 2.38 104 | 9.60 102
Electron beam brightness ratio | 1 | 24.8
The electron beam brightness is improved by nearly a factor of 25.
lattices
Diamond Low Emittance DDBA HMBA DTBA beamlines conclusions
Parameter (rms values) | Diamond | Diamond-II
Horizontal size, x [m] | 123.6 | 23.8
Vertical size, y [m] | 4.7 | 4.7
Horizontal div. x’ [rad] | 25.8 | 10.5
Vertical div., y’ [rad] | 9.5 | 9.5
Product | 1.44 105 | 1.13 104
Brightness ratio | 1 | 12.7
photon phase space at 12.4 keV (i=7)

## Slide 8
Comparison of phase space (at 1Å)
Diamond
Diamond-II
lattices
Diamond Low Emittance DDBA HMBA DTBA beamlines conclusions

## Slide 9: Brightness improvement with Diamond-II (120pm)
Soft X-rays undulators
APPLE-II for I05, I06, I08, J09, I10 ,I21
lattices
Diamond Low Emittance DDBA HMBA DTBA beamlines conclusions
Photon Energy (eV)
The improvement in brightness/coherence is approximately a factor of x3 at 100 eV and x10 at 1 keV, the main benefit coming from the reduction in horizontal source size and divergence

## Slide 10: Flux through an aperture
Flux through a 40 rad * 40 rad aperture for the Diamond CMPU in the existing ring (red) and in Diamond-II (black).
lattices
Diamond Low Emittance DDBA HMBA DTBA beamlines conclusions
Photon Energy (eV)

## Slide 11
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions
  Diamond II wish list
  Emittance: from 2.7 nm to < 270pm
  Minimal changes to present machine
    Keep tunnel / beamline structure
    Leave straight sections as they are
    Re-use hardware wherever possible (RF, magnets, …)
  Keep I09-I13 optics (mini-beta sections)
  Maintain short pulse operations
  Minimize dead-time
  Minimize technology risks

## Slide 12
  Broadly speaking, emittance reduction is achievable with usual approach, i.e.
  Increase n. of dipoles
  Increase Jx with combined function dipoles
  MBA solutions with longitudinal gradient dipoles
  However, reducing emittance may not be the only target
  increase ratio of straight_sections / C
  This twofold request leads to the Double DBA concept (DDBA)
  - a 4BA cell with a central straight for an extra ID
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions

## Slide 13
  The Double Double-Bend Achromat concept (DDBA) is a modification of the standard Diamond DBA cell, where the central region has been “cleared” to host a new insertion device (VMX)
  It is a modified 4BA with a 10x emittance reduction factor and 2x n. of possible beamlines
  Baseline design for Diamond-II
  until the end of 2015
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions

## Slide 14
  at present one DDBA cell has been installed in Diamond and has been commissioned
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions

## Slide 15
DDBA cell installation (16/11/2016)
beam accumulation in the SR
(17/11/2016)
Beam current = 300mA
(24/11/2016)
8/3/2017
Ib = 300mA
C = 0.27%
LT ~ 12hrs
New tune point
Wigglers ON
Emi = 3.06  2.8nm (Low-Eta lattice)
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions
J02 – undulator
March 2017
shut-down
installation

## Slide 16
  There were few reasons to go beyond the DDBA concept:
    a request from beamlines for a more aggressive scheme: 20x reduction in emittance
    Challenges in the optimization of Lifetime, Dynamic Aperture
  Point (1) led to a 6BA-like approach, where the 7BA ESRF cell (HMBA) was modified to create a central ID straight
  Collaboration with ESRF very fruitful in overcoming some design difficulties
  Emittance  140 pm
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions

## Slide 17
ESRF-HMBA
Sextupoles located at large hx dispersion bumps
Central DQ2 removed
Drift spaces kept equal
Magnet lengths shortened thanks to
reduced gradient (6GeV  3GeV)
DII-DTBA
~ (3p,p) phase advance
C2
ESRF - HMBA
E: 6 GeV
Cell lenghts: 26.4m
C: 844m (32 cells)
DII - DTBA
E: 3 GeV
Cell lenghts: 22.6m
C: 561m (24 cells)
Porting the ESRF-HMBA concept into Diamond SR:
by scaling magnet lengths while keeping the same
inter-distances
by shortening cells to fit Diamond length constraints
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions
Notes: Sextupoles @ dispersion bumps, more effective, weaker  less geometric aberrations

## Slide 18
There are indeed two kinds of cell, C1 and C2, used to reproduce the SP-6 structure of the present lattice (1long / 3 short straights):
-C1 C2 C2 C1
C1 is an asymmetric cell: +1.5m w.r.t. C2
a modified C1 is needed as
injection cell (Cinj)
ID_C
ID_B
2 x ID_A
2 x ID_A
2 x ID_A
ID_B
ID_B
ID_B
ID_C
long straight
short straight
new straight
DII-SuperPeriod
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions

## Slide 19
DA@C2 independent from beta@injection
DA@Cinj grows with beta@injection
MA larger with no inj cell
courtesy of A. Alekou
no CINJ
no CINJ
no CINJ
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions
Notes: DA at different positions. When at C2 the DA is small and independent from the beta chosen at injection. Instead the DA at injection is directly connected to the beta chosen by varying the entry quadrupole.
MA for the different cases. Hard to see, but without injection cell (better symmetry) the MA increases (and therefore the LT)

## Slide 20
Optimizing the lattice:
  Matching technique
    Analytic cancellation of non-linear driving terms
      Cell-length adaptation
        Injection Cell
          MOGA (DA, LT, InjEff ...)
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions

## Slide 21
cell matching technique:
- bx @ IDs
by,ay at central SF sextupoles
jx,y advance between sextupoles [3p/p]
jx,y advance in the cell
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions
bx @ IDs  ex
by @ sext  ex, xx
ay @ sext  dQy/dy
jy advance between sextupoles  dQx/dy
These parameters have been:
kept fixed when changing cell length (HMBA  DTBA)
scanned when tuning quads during DTBA optimization (later)
varied with Multi-Objective Genetic Algorithm (MOGA) optimizer
Notes: Fast …

## Slide 22
MOGA optimization(*) on the whole set of parameters
(bx, by, ay, K4, jx,y)  (t,DA) [keep x=(2,2)]
Promising improvement, BUT still errors to be included
(*) 24xC2 ring
Ib = 300mA
Nb = 900
Bl = 1.71 mm
C = 1.0%
With a DA of 11 mm and a lifetime of 3.2hr the DTBA is a promising candidate for Diamond II.
Most of the design effort is concentrating on this lattice
lattices
Diamond Low Emittance DDBA HMBA DTBA optimization conclusions
sextupoles / octupoles
chromaticity control (2,2)
(t,DA) optimization
MOGA improvement in DA [no change in t]
Injection Efficiency optimization  DTBA lattice with InjCELL
(t,IE) optimization
 IE~85%, t ~ 1.1hr
IE parameters
Npart = 1e3
Nturns = 512
ex = 150nm
InjGap = 6.8mm
HHC cavities for bunch lengthening considered
to increase Touschek lifetime

## Slide 23
lattices
Low Emittance DDBA HMBA DTBA open issues conclusions
Issues : integration of present features into new lattice
I09 / I13 straight @ mini-b
I21 strong focussing section
Short-pulse
improve performance @ BL
mini-b straights critical, with low by and virtual focussing
present proposed solution under study for mini-b cases
250m
I13: coherence
imaging

## Slide 24
lattices
Low Emittance DDBA HMBA DTBA present situation conclusions
STR Q-Q: 4.88m straight section
mini-b
courtesy of T. Pulampong
Notes: Check better newer plots

## Slide 25
lattices
Low Emittance DDBA HMBA DTBA present situation conclusions
courtesy of T. Pulampong
LT ~ 0.44 hr (!)
|DA| > 5mm
courtesy of T. Pulampong
MOGA optimization
2351-0.44hr
1754 – 0.3hr
Notes: Check newest results with TP

## Slide 26
lattices
Low Emittance DDBA HMBA DTBA present situation conclusions
Initial consideration on layout, engineering
Integration, girders, beamline layout, etc.
courtesy of R. Bartolini

## Slide 27
lattices
Low Emittance DDBA HMBA DTBA present situation conclusions
Diamond is considering a development to reduce emittance by a factor 10x to 20x
Following the DDBA concept, and the expertise developed at ESRF the DTBA concept emerged, which should double the n. of beamlines
Initial studies suggest a DTBA cells organized in 6-fold SP could fulfil the 20x emittance reduction
However optimization process is underway to ensure:
  Good LT/DA are achievable
  Non linearities can be controlled
  Present machine requirements are met
  (mini-b / short-pulse operations)

## Slide 28
Thanks for your attention