## Slide 1: Caustic Analysis in Accelerators
Tessa Charles
University of Liverpool
Cockcroft Institute

## Slide 2
The envelope of trajectories forms the caustics lines.
2

## Slide 3
Surface of water
J.F. Nye “Natural Focusing and Fine Structure of Light: Caustics and Wave Dislocations”, (Taylor & Francis, Philadelphia, 1999).
3
Caustics lines are an envelope of trajectories, or the projection of that envelope on another surface.

## Slide 4
Surface of water
J.F. Nye “Natural Focusing and Fine Structure of Light: Caustics and Wave Dislocations”, (Taylor & Francis, Philadelphia, 1999).
4
Caustics lines are an envelope of trajectories, or the projection of that envelope on another surface.

## Slide 5: Outline
Introduction of caustics
Current horn suppression
MAX IV experimental measurements
Longitudinal Phase Space manipulation in recirculating machines
Microbunching instability
5

## Slide 6: Outline
Introduction of caustics
Current horn suppression (example of the usefulness of caustics)
MAX IV experimental measurements
Longitudinal Phase Space manipulation in recirculating machines (example of the usefulness of caustics)
Microbunching instability (example of the usefulness of caustics)
6

## Slide 7
z (µm)
Position (m)
0
2
4
6
8
150
75
0
-150
-75
Electron trajectories in a bunch compressor:
Where there are caustics, there will be current spikes.
tail of bunch
head of
bunch
Optical caustics example:
tail
head
Current
z (µm)
7
Intensity
Distance from caustic
caustic

## Slide 8
Caustics are singularities in the density of families of trajectories.
8

## Slide 9: Caustics fall into catastrophe theory
Figure: EC Zeeman (1976) Catastrophe Theory in Scientific American.
z
x
y
9

## Slide 10: Longitudinal phase space evolution through a bunch compression
z (fs)
head
tail
Fractional
energy spread
z (ps)
z (ps)
z (fs)
10
dipole
magnet

## Slide 11: Longitudinal phase space dist. at bunch compression exit
BC2_1
BC2_2
BC2_3
BC2_4
BC2_5
λ = linear charge density
Energy spread induced by Coherent Synchrotron Radiation (CSR):
Current spikes are problematic, leading to CSR-induced emittance growth.
z (fs)
-λ
11

## Slide 12: Caustic expression:
T.K.Charles et al. Phys. Rev. Accel. Beams, (2016) 19, 104402
Initial phase space distribution:
12

## Slide 13: Caustic expression for a chicane
R56 = -10 mm
Caustic expression (red)
13

## Slide 14
E.g. MAX IV
[S. Thorin et al. FEL2010,
WEPB34]
T566 =16.1 mm, U5666 = 2.6 m
E.g. single spike bunch compression [S. Huang et al, Phys. Rev. AB (2014) 17 120703]
T566 = 18.1 mm, U5666 = -24 mm
E.g. LCLS
[Y. Ding et al. Phys. Rev. AB 19, 100703]
T566 = 16.4 mm, U5666 = -11.4 mm
Fold
Cusp
Butterfly
14

## Slide 15: A closer look…
3 types of catastrophes, but all described by the same parametric expression.
15
These 3 cases give us an idea of how we might be able to sculpt electron trajectories to our benefit.

## Slide 16
Current horn suppression
Example of the usefulness of caustics

## Slide 17: LSLC’s experience - current spikes diminish FEL performance
Before collimation
After collimation
FEL power increased from ~3.5 mJ to 4-5 mJ.
17
Y. Ding et al. (2016) Phys. Rev. AB 19, 100703

## Slide 18: Current horn suppression - an S-band FEL Linac example
Elegant simulations of longitudinal phase space and current profile at the end of Linac2.
18

## Slide 19: Caustic condition
19
Point (a) is the working point of the S-band linac example

## Slide 20: Caustic condition

## Slide 21: Caustic current horn suppression - S-band FEL linac
Octupole added to BC1 to vary U5666.
21

## Slide 22: Caustic current horn suppression - S-band FEL linac
Octupole added to BC1 to vary U5666.

## Slide 23: Caustic current horn suppression
With octupole:
Without octupole:
63% reduction in the CSR-induced emittance growth.
T.K.Charles et al. Phys. Rev. Accel. Beams, (2017) 20, 030705
23

## Slide 24
Experimental results from MAX IV
with Andrea Latina (CERN), Sara Thorin (MAX IV), Jonas Björklund Svensson (MAX IV)

## Slide 25: MAX IV
25
3 GeV
1.5 GeV
Linac
SPF

## Slide 26: MAX IV Linac
Thermionic RF gun
Photo cathode RF gun
BC1 @ 260 MeV
Extraction 1.5 GeV
Extraction 3 GeV
BC2 @ 3 GeV
SPF
Photocathode and thermionic electron guns
2 double achromat bunch compressors (BCs)
RF frequency 2.998 GHz
26

## Slide 27: MAX IV Bunch Compressors
Double achromat bunch compressors:
positive fixed R56 (energy chirp from falling RF slope)
natural T566 used for linearization, self-linearizing
weak sextupoles at the center of each achromat used for fine tuning T566
dipole
quadrupole
sextupole
corrector
27

## Slide 28: Zero-crossing method
Extraction 3 GeV ring
BC1 @ 260 MeV
Extraction 1.5 GeV ring
L2A
L2B
L1B
L0
TG
PG
BC2 @ 3 GeV
SPF
L2B
L19B
RF phase at 40º
Screen
(after first dipole)
Sextupole strengths varied
28

## Slide 29: Zero-crossing method
Extraction 3 GeV ring
BC1 @ 260 MeV
Extraction 1.5 GeV ring
L2A
L2B
L1B
L0
TG
PG
BC2 @ 3 GeV
SPF
L2B
L19B
RF phase at 40º
Sextupole strengths varied
29

## Slide 30: Experimental results – linearly ramped current profiles
1.0
7.0
13.0
19.0
25.0
31.0
Sextupole strengths
[m-3]:
37.0
30

## Slide 31: Caustic expression:
Illustration of compressed bunches
Distance between peak and origin.
The origin is found as being the distance from one bunch edge to the position within the bunch where the accumulated integrated charge equals half of the total charge.
(Same expression as shown on slide 11, simply re-arranged)
31

## Slide 32: Mapping out caustic lines
Offset due to the combined effects of wakefields and curvature of the phase space distribution.
32
Caustic expression (red)
Offset removed

## Slide 33: Mapping out caustic lines
Where the caustic expression is undefined, the longitudinal phase space is considered well linearized, resulting in a short bunch with a symmetrical current profile.
Offset of 14 micrometers removed
33
T.K.Charles et al. IPAC19, WEYYPLS2

## Slide 34
Longitudinal Phase Space manipulation in recirculating machines
Example of the usefulness of caustics
with
Dave Douglas, JLAB
Peter Williams, Cockcroft Institute

## Slide 35: A UK recirculating FEL concept
35
with
Dave Douglas, JLAB
Peter Williams, Cockcroft Institute

## Slide 36: Caustic exclusion plots for each arc of a recirculating machine during acceleration
Non-caustic region
Region of single fold caustic (single current spike)
Region of two fold caustics (multiple current spike)
12345678
Arc no.
36

## Slide 37: Caustic exclusion plots for each arc of a recirculating machine during acceleration
12345678
Arc no.
Non-caustic region
Region of single fold caustic (single current spike)
Region of two fold caustics (multiple current spike)
37

## Slide 38: Bunch distributions at various positions around the accelerator
Bunch Distribution from gun:
Distribution after lasing:
Distribution at end of arc 8:
With thanks to Julian McKenzie (Daresbury, UK) for this distribution.
38

## Slide 39: Caustic exclusion plots for each arc of a recirculating machine during deceleration
Arc no.
9
101112131415
16
Non-caustic region
Region of single fold caustic (single current spike)
Region of two fold caustics (multiple current spike)
39

## Slide 40: Caustic exclusion plots for each arc of a recirculating machine during deceleration
Arc no.
9
101112131415
16
40
Non-caustic region
Region of single fold caustic (single current spike)
Region of two fold caustics (multiple current spike)

## Slide 41: Caustic exclusion plots for each arc of a recirculating machine during deceleration
Arc no.
9
101112131415
16
Non-caustic region
Region of single fold caustic (single current spike)
Region of two fold caustics (multiple current spike)
41

## Slide 42: Caustic exclusion plots for each arc of a recirculating machine during deceleration
Arc no.
9
101112131415
16
Non-caustic region
Region of single fold caustic (single current spike)
Region of two fold caustics (multiple current spike)
42

## Slide 43: Bunch distributions at various positions around the accelerator
Distribution after lasing:
Distribution at dump:
43
T.K.Charles et al. IPAC18, WEYGBE2

## Slide 44
Microbunching instability
Example of caustics

## Slide 45: Micro-bunching caustics
A caustic expression can also be derived for micro-bunching. Each line shows where a current spike will be seen.
45

## Slide 46: Caustic nature leads to bifurcated current peaks
46

## Slide 47: Micro-bunching with higher-order effects
47
Hyper-caustics = ‘caustics of caustics’
grey: T566 = 0, U5666 = 0 mm
red: T566 = -30 mm, U5666 = 0 mm
grey: T566 = 0, U5666 = 0 mm
red: T566 = 0, U5666 = -2 m

## Slide 48: CSR with microbunching
48
Numerically hazardous!
The caustic nature of microbunching results in sharp peaks in the linear charge density function, 𝜆(z), which means the numerical evaluation of d𝜆/dz is risky. Making matters even more difficult, this numerically problematic data set is then convolved with a function that also contains a singularity, 1/z1/3.

## Slide 49: Conclusions ...
With octupole:
Without octupole:
Current horns (often seen in FELs) can be suppressed by considering the underlying caustics, resulting in 63% reduction in the CSR-induced emittance growth.
Caustics are commonplace in optics, they are ultilised in electron microscopy, and they are also seen in accelerator physics.
Applied to accelerator physics, we can explore the high-order focusing.
Fold
Cusp
Butterfly
Phys. Rev. Accel. Beams, (2016) 19, 104402
Phys. Rev. Accel. Beams, (2017) 20, 030705
Caustics are a useful way that we can look at various types of focusing.

## Slide 50
Longitudinal phase space manipulation in recirculating & energy recovery machines
Experimental demonstration of linearly-ramped current profiles and caustics!
14 𝜇m offset removed
Microbunching is also a caustic phenomenon and can be used to better model microbunching.
Conclusions
Bifurcated current peaks
Exclusion plots identify regions where caustics of different codimension exist
Caustic expression
IPAC18, WEYGBE2
IPAC19, WEYYPLS2
Caustics are a useful way that we can look at various types of focusing.
Caustic exclusion plots can be used to pair down viable parameter space.
Linearly-ramped current profile achieved through T566 variation.

## Slide 51: Acknowledgements
With acknowledgments and thanks to the people who have supported and contributed to this work:
  Sara Thorin and Jonas Björklund Svensson (MAX IV)
  Andrea Latina and Frank Zimmermann (CERN)
  Rohan Dowd (Australian Synchrotron)
  David Paganin (Monash University)
  Mark Boland (Canadian Light Source)
  Peter Williams (Daresbury Laboratory)
  Dave Douglas (J-Lab)
Thank you
51

## Slide 52: Back up slides

## Slide 53: Final bunch slice properties
With octupole: 
Without octupole: *
53

## Slide 54: What about chromatic and geometric aberrations?
54

## Slide 56: MAX IV Bunch Compressors
dipole
quadrupole
sextupole
corrector

## Slide 57
Illustration of compressed bunches
Distance between peak and origin.
The origin is found as being the distance from one bunch edge to half of the accumulated charge,
The light grey portion of the distribution will be mapped to a smaller x value, lengthening out the bunch on the screen.
57

## Slide 58: Current profile analytical expression
= analytical expression
= histogram, particle tracking data
58
non-caustic region
caustic region

## Slide 59: Current profile analytical expressions – caustic region
59
Piecewise analytical functions (orange) can model the caustic current profiles.
(These are mono-energetic, longitudinal plane only.)

## Slide 60: X-band linac example
Without octupole:
With octupole:
Without CSR:
With CSR:
Non-caustic region
Region of single fold caustic (single current spike)
Region of two fold caustics (multiple current spike)

## Slide 61: X-band linac example
Without sextupole:
With sextupole:
Without CSR:
With CSR:
Non-caustic region
Region of single fold caustic (single current spike)
Region of two fold caustics (multiple current spike)

## Slide 62: X-band linac example
X-band Linac
Bunch Compressor 2
Bunch Compressor 1
Bunch Compressor 2

## Slide 63: X-band linac example
With octupole & sextupole:
Without octupole & sextupole:
T. K. Charles et al. (2017) Phys. Rev. AB, 30, 030705
49% reduction in the CSR-induced emittance growth.
X-band Linac

## Slide 64: FEL, X-band linac

## Slide 65: X-band linac, final bunch slice properties
X-band linac
Without octupole: 
With octupole: +
With octupole and sextupole: *