## Slide 1: Development of gas-jet based diagnostics at the CI
Hao D. Zhang, N. Kumar, A. Salehilashkajani, O. Sedlacek, O. Stringer, C. P. Welsch (Univ. Liverpool / CI) M. Ady, T. Lefevre, S. Mazzoni, I. Papazoglou, A. Rossi, G. Schneider, K. Sidorowski, R. Veness (CERN) P. Forck, S. Udrea (GSI)
haozhang@liverpool.ac.uk

## Slide 2: Diagnostics: Beam profile monitors
BIF monitor
Residual gas based IPM monitor
Scintillating screen
Credit: B. Walasek-Höhne, GSI and G. Kube, DESY
Credit: U. Iriso and F. P´erez, ALBA
Wire scanner or slits
Credit: B. Dehning et al., CERN
Intercepting method
phosphor
YAG, etc.
Non-Invasive method
Credit: D. Morris, et al., TRIUMF
OTR
SR
Credit: P. Fork, GSI
Resolution, S/N ratio
Long integration time!
Credit: P. Fork, GSI
Notes: Diagnostics are sensing organ of the accelerators. Today I will mainly focus on the beam profile monitors.
Traditionally, the intercepting methods were used for example S-screen such as YAG or phosphor screen, wire scanner or slits, OTR screen. These methods are normally used in LINAC or commissioning of high intensity machines. Non-intercepting method are preferred due to their robustness. SR is one of the good example but not every beam is energized enough to product SL. There are two monitor based on interaction between the charged particle beam and the residual gas. The IPM collect ions or electrons while the BIF detect the fluorescent photon. Due to usage of the residual gas, they tent to have low resolution, low S/N ratio which normally means long integration time. Here we need a way to increase the signal level without sacrifice the vacuum.

## Slide 3: Gas jet based beam profile monitors
Principle
Advantage
  Non-Invasive
  Minimum vacuum interference
  2D profile with high resolution
  Versatile
  Not affected by space charge (Neutral emitter)
Using a supersonic gas jet curtain
Notes: The solution is to use a supersonic gas jet. The principle is simple, you generate a supersonic gas jet curtain, which interact with the primary beam the same way as the residual gas and detect the secondaries the same way as the IPM or BIF. Due to the finite thickness of the gas curtain, the profile you got will be 2D.
The advantage will be it is an invasive method, with minimum vacuum interference. It give 2d profile with high resolution due to the low temperature of the gas jet molecule. It is very versatile to change the curtain size. If a neutral emitter is chosen, there will be no space charge effect.

## Slide 4: Gas jet monitor setup
Notes: To generate the such a curtain, 5bar nitrogen or neon flow through a 30 um nozzle to form a supersonic gas jet. then this jet is be shaped through 2 conical skimmers and a rectangular skimmer. The skimmers divide the vacuum volume into differential pumping stages to maintain the pressure in the beam pipe. the jet flow through will dumped to the final pumping station. To prevent back flow, a 4th skimmer slightly larger than the jet is applied.

## Slide 5: Curtain simulation and verification
Continuous flow:
Quitting surface + analytical formular
Molecular flow:
Particle ray tracing
Gas jet density distribution verified at 264 mm from nozzle:
    Nozzle : 30 μm; 1st Skimmer I : 180 μm; 2nd Skimmer: 2mm
FWHM = 13.6 mm
FWHM = 15.8 mm
FWHM = 12.5 mm
FWHM = 13.3 mm
Neon
Nitrogen
X
Y

## Slide 6: Beam profile Measurement
IPM mode (See Narender’s talk)
BIF mode
σ(cross section, N2, 391 nm) | 9.2*10-19 cm2
I (electron current) | 0.66 mA
n (gas jet density) | 4×1015 m-3
d (jet thickness) | 0.7 mm
Optical parameter | 2.9×10-4
Photon rate estimation | 49 ± 39 s-1
Photon rate measured | 18.0 ± 0.3 s-1
Photon number
A. Salehilashkajani, H. D. Zhang, et al. Appl. Phys. Lett. 120, 174101
E-beam:
0.66mA, 5keV
Image:
200 frames with
2s exposure time each
Verified with OTR
Measurement

## Slide 7: Design a monitor for LHC
Generate a uniform gas jet with 20 mm
Old configuration
  30 μm nozzle
  180 μm 1st skimmer
  2 mm 2nd skimmer
  9*0.7 mm2 3rd skimmer
New configuration
  30 μm nozzle
  400 μm 1st skimmer
  2 mm 2nd skimmer
  9*0.7 mm2 3rd skimmer
Vacuum behaviour (when jet in on)
Nozzle chamber | Skimmer chamber I | Skimmer chamber II | Interaction chamber
5.56×10-3 mbar | 1.13×10-5 mbar | 1.52×10-6 mbar | <5×10-9 mbar
Nozzles testing
Convergent-Divergent (CD) Nozzles
Credit: A. Cherif
Replace TMP with NEG
For high B-field applications
Simulation
Experiment
Convolution

## Slide 8: Noise reduction and stray photon estimation
Chamber blackening to reduce stray photons
 | Amorphous carbon | LESS (Dundee) | Multilayer sputtering (Polyteknik) | Carbon nanotubes (Vantablack)
Copper | ≈ 13% | ≈ 2% | ≈ 0.2% | 
Steel | ≈ 14% | ≈ 2% | ≈ 0.2% | ≈ 0.15%
Reflectivity test at neon wavelength 584nm
Beam
Imaging system
Amorphous carbon
Multilayer coating
Stray photons from cathode and Synchrotron light
Molflow simulation
Credit: Noah Jens
Cathode
Electron lens test stand for HEL
Imaging system
for gas jet monitor
Conclusion:
α-C coating used in the copper liner and the vacuum chamber with reflection of 10-15%
Multi-layer optimized coating used under the interaction point with reflection of < 0.2%

## Slide 9: Gas jet monitor delivered to CERN
LHC installation in later YETS
(Gas jet generation and dump chambers)
V3 gas jet monitor in CI
See Oliver's poster for more details.
LHC installation during LS2
(interaction chamber and optics)
Measure beam profile using residual gas
& fluorescence cross section with 6.8 TeV beam
Standalone lab space in CERN
Validate CI result and vacuum compatibility test
Electron beam test stand for HEL in Sep.
Measure hollow electron beam (test v4 concept)

## Slide 10: Ongoing work
Gas jet v4 for HLLHC (hollow electron lens)
qHAM & QuantumJet
Credit: T. Reisinger, S. Eder, et.al
JetDose (see Narender’s talk)
Gas jet monitor

## Slide 11: Conclusion
Gas jet based diagnostics has
  Developed over a decade at the CI from a lab test equipment to an accelerator module.
  Been equipped with simulation and experimental tools for versatile design to meet different beam environment.
  Expanded to wider applications such as Medical and Microscopy.
Monitor for keV beams
HLLHC prototype
HLLHC compatible instrument

## Slide 12: Acknowledgment
I would like to thank the whole BGC team.
Any Questions?
This work is supported by the HL-LHC-UK phase I & II project funded by STFC under Grant Ref: ST/T001925/1 and the STFC Cockcroft Institute core grant No. ST/G008248/1.