## Slide 1: First proton beam measurements with gas jet in-vivo dosimeter for medical applications
Narender Kumar

## Slide 2: Overview
Motivation and clinical benefits
Background and R&D
Measurements at UoB's Scanditronix MC40 cyclotron
IOP PABG Annual Conference, Liverpool 25th-26th July 2022

## Slide 3: Hadron beam therapy
Clear healthcare benefits for certain cancer types;
Significant investment through NHS and private facilities in the UK;
Optimization of Medical Accelerators (OMA) network identified key R&D challenges:
  Significant time goes into Q&A
  New technology solutions needed for novel treatment modalities such as FLASH
  Desirable machine operation modes not currently possible due to lack of non-invasive (online) diagnostics
CNAO Synchrotron, image courtesy CNAO.
IOP PABG Annual Conference, Liverpool 25th-26th July 2022

## Slide 4: Existing diagnostics
High resolution
Reliability
Validity
Interceptive
Ongoing calibration
Beam perturbation
Limited live feedback
B. Walasek-Höhne, GSI and G. Kube, DESY
S. Giordanengo & M. Donetti, arXiv:1803.00893
IOP PABG Annual Conference, Liverpool 25th-26th July 2022

## Slide 5: JetDose - Novel diagnostics solution
No beam perturbation
Online monitoring
Superior error detection
1
Minimally invasive
Enabling technology for FLASH and Mini-Beam treatments
Active machine regulation based on live feedback becomes feasible
3
Novel treatments and improved operation
No mechanical parts interact with the beam
All key parameters monitored remotely
Significantly reduced maintenance
2
Significantly reduced calibration time
1
2
3
USP
N. Kumar, C.P. Welsch, et. al, Physica Medica 73, p 173-178 (2020).
S. Jolly, C.P. Welsch, et al., “Technical challenges for FLASH proton therapy“, Phys Med 2020 – Galileo Galilei Award, best paper in 2020
“Non-Invasive Gas Jet In-Vivo Dosimetry for Particle Beam Therapy”, contributed talk at IPAC21
IOP PABG Annual Conference, Liverpool 25th-26th July 2022

## Slide 6: Building up on previous developments
Gas jet shaping
MCP
Phosphor screen
Detector
Ionization
Ion extraction
Visible light
IOP PABG Annual Conference, Liverpool 25th-26th July 2022

## Slide 7: Measurements with protons at UoB's Scanditronix MC40 cyclotron
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
Beam Parameters
Beam Species: Protons
Beam Energy: 28 MeV
Beam Current: 150-750 nA (on FC1)
Beam Collimator Area: 4-100 mm2
Interaction chamber
125 µm
Ti foil
125 µm
Ti foil
Beam
dump
Proton
beam
(in vacuum)
Beamline
(ending with Ti foil)
Proton
beam
(in vacuum)
Proton
beam
(in air)

## Slide 8: Measurements with protons at UoB's Scanditronix MC40 cyclotron
Beam collimator Area= 100 mm2
Integration time = 1second
Gas Pressure in Interaction chamber = 1.2 ×10-5 mbar
σ = 5.4mm
Beam current at FC1= 150nA
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
Beam collimator Area= 4 mm2
Integration time = 20seconds
Gas Pressure in Interaction chamber = 1.2 ×10-5 mbar
σ = 6.4mm
Beam current at FC1= 150nA

## Slide 9: Measurements with protons at UoB's Scanditronix MC40 cyclotron
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
Beam collimator Area= 4 mm2
Integration time = 20seconds
Gas Pressure in IC= 1.2 ×10-5 mbar
σ = 6.6mm
Beam current at FC1= 750nA
GEANT4 simulations

## Slide 10: Updated design
IOP PABG Annual Conference, Liverpool 25th-26th July 2022
Nozzle Chamber
Skimmer Chamber
Interaction Chamber
Port for Laser Interferometry measurements
More flexible design for nozzle skimmer assembly and tuning
Compact system: total length ≈ 1m

## Slide 11: Summary
First measurements were done with a proton beam. Good agreement was found with results from simulation.
It was shown that 1 s integration time is sufficient for having a density equivalent to 10-5 mbar gas pressure.
System integration is subject to optimization; considering direct coupling to existing system.
R&D into increasing gas jet density at the interaction point is ongoing.
IOP PABG Annual Conference, Liverpool 25th-26th July 2022

## Slide 12: Thank you for your attention
Special thanks to
I. Maltusch, O. Stringer, J. Wolfenden, H. Zhang, T. Price, C.P. Welsch