## Slide 1
Terahertz-driven electron bunch manipulation for advanced accelerators
Particle Accelerator and Beams Conference | 29-30th June 2023
Morgan Hibberd | STFC Ernest Rutherford Fellow | The University of Manchester
Terahertz Acceleration Group @ The Cockcroft Institute | www.THzAG.uk

## Slide 2
Dan Lake
Christopher Shaw
Laurence Nix
Connor Mosley
Beatriz Higuera Gonzalez
Darren Graham
Sergey Siaber
Joseph Bradbury
Morgan Hibberd
Graeme Burt
Steven Jamison
Rob Appleby
Terahertz Acceleration Group @ The Cockcroft Institute
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 1/13
www.THzAG.uk

## Slide 3
Why do THz techniques complement other advanced accelerators?
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 2/13
Advanced accelerators use THz frequency fields
Wakefields driven by lasers, electrons or protons
Plasma frequency ranges from 0.1 – 10 THz
E. Gschwendtner et al. Symmetry 14,1680 (2022)
THz-driven bunching
Ultrashort duration
Temporal locking
Bunch trains at THz rep rates
For AWAKE
External injection schemes
The Advanced Wakefield Experiment (AWAKE)
Proton beam-driven wakefield
Plasma frequency ≈ 0.25 THz
RF ≈ 3 GHz
THz pulse ≈ 0.1-10 THz
Image of modulated proton bunch
In this talk

## Slide 4
Why do THz techniques complement other advanced accelerators?
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 2/13
Advanced accelerators use THz frequency fields
Wakefields driven by lasers, electrons or protons
Plasma frequency ranges from 0.1 – 10 THz
E. Gschwendtner et al. Symmetry 14,1680 (2022)
THz-driven bunching
Ultrashort duration
Temporal locking
Bunch trains at THz rep rates
For AWAKE
External injection schemes
The Advanced Wakefield Experiment (AWAKE)
Proton beam-driven wakefield
Plasma frequency ≈ 0.25 THz
Image of modulated proton bunch
…+
THz bunching
In this talk
Run 1

## Slide 5
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 3/13
Why are terahertz pulses ideal for bunch manipulation?
High electric field strengths
100 MV/m to >GV/m possible
Laser and THz pulse shaping
Bandwidth and frequency tuning
Polarisation modes
Laser timing synchronisation
THz sources generated by drive laser
Synchronise to the fs-scale
Compact mm-scale structures
Minimal beam-line footprint
High-charge throughput (>100 pC)
C. D. W. Mosley et al. Opt. Express 31,4041 (2023)
Periodically-poled lithium niobate wafer stack source
Dielectric lined THz waveguide structure

## Slide 6
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 3/13
Why are terahertz pulses ideal for bunch manipulation?
High electric field strengths
100 MV/m to >GV/m possible
Laser and THz pulse shaping
Bandwidth and frequency tuning
Polarisation modes
Laser timing synchronisation
THz sources generated by drive laser
Synchronise to the fs-scale
Compact mm-scale structures
Minimal beam-line footprint
High-charge throughput (>100 pC)
Optimal frequency for manipulation
Short enough field cycle for fs control
Long enough for ps-scale bunch lengths

## Slide 7
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 3/13
Why are terahertz pulses ideal for bunch manipulation?
High electric field strengths
100 MV/m to >GV/m possible
Laser and THz pulse shaping
Bandwidth and frequency tuning
Polarisation modes
Laser timing synchronisation
THz sources generated by drive laser
Synchronise to the fs-scale
Compact mm-scale structures
Minimal beam-line footprint
High-charge throughput (>100 pC)
Optimal frequency for manipulation
Short enough field cycle for fs control
Long enough for ps-scale bunch lengths

## Slide 8
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 3/13
Why are terahertz pulses ideal for bunch manipulation?
High electric field strengths
100 MV/m to >GV/m possible
Laser and THz pulse shaping
Bandwidth and frequency tuning
Polarisation modes
Laser timing synchronisation
THz sources generated by drive laser
Synchronise to the fs-scale
Compact mm-scale structures
Minimal beam-line footprint
High-charge throughput (>100 pC)
Optimal frequency for manipulation
Short enough field cycle for fs control
Long enough for ps-scale bunch lengths

## Slide 9
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 3/13
Why are terahertz pulses ideal for bunch manipulation?
High electric field strengths
100 MV/m to >GV/m possible
Laser and THz pulse shaping
Bandwidth and frequency tuning
Polarisation modes
Laser timing synchronisation
THz sources generated by drive laser
Synchronise to the fs-scale
Compact mm-scale structures
Minimal beam-line footprint
High-charge throughput (>100 pC)
Optimal frequency for manipulation
Short enough field cycle for fs control
Long enough for ps-scale bunch lengths

## Slide 10
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 4/13
How does terahertz-driven bunching work?
Energy
Time
THz energy modulation
R56 compression
Induce an energy chirp (or modulation) followed by compression
Analogous to standard RF-based zero-crossing compression
Higher THz frequency makes interaction more efficient
And… makes multi-bunch generation possible
Dipole magnets
Lower energy
Higher energy
Magnetic chicane
Or a dog-leg
Multi-cycle THz pulse
Short electron bunch
Longer chirped electron bunch
Micro-bunch train

## Slide 11
Beam Area 1
Experiments on CLARA @ Daresbury Laboratory
CLARA
Compact Linear Accelerator for Research and Applications
Bunch parameters
Energy: 35.5 MeV
Charge: 2 – 100 pC
Duration: 0.2 – 6 ps
Spot size: 100 µm
Rep. rate: 10 Hz
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 5/13
Interaction chamber
Energy spectrometer
Optical breadboard

## Slide 12
Laser and THz optics outside chamber
THz-electron interaction point inside vacuum chamber
Experimental setup
Laser parameters
Wavelength: 800 nm
Pulse length: 50 fs
Chirped to 750 fs
Pulse energy: 300 mJ
≈150 mJ on THz source
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 6/13
THz parameters
Frequency: 0.4 THz
Bandwidth: 40 GHz
10 cycles each 2.5 ps
Pulse energy: ≈100 μJ
<20% coupling
1.2m x 0.9m

## Slide 13
Terahertz-driven multi-cycle energy modulation
Energy modulation demonstrated experimentally
Chirped (>4 ps rms) bunches interact with multiple THz field cycles
Can tune THz field strength and injection timing to control energy modulation
Varying THz field strength
Varying THz injection timing
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 7/13
M. T. Hibberd et al. Nature Photonics 14,755-759 (2020)

## Slide 14
Terahertz-driven multi-cycle energy modulation
Energy modulation demonstrated experimentally
Chirped (>4 ps rms) bunches interact with multiple THz field cycles
Can tune THz field strength and injection timing to control energy modulation
Varying THz field strength
Varying THz injection timing
Longitudinal phase space diagnostic
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 7/13
Now just need magnetic compression to convert into micro-bunches
Can model this using our experimental data for now

## Slide 15
Terahertz-driven micro-bunching
THz off
THz on (sharpest energy peaks)
After R56 compression
4.4 ps rms
75 fs rms
WTHz ≈ 2 μJ
Eacc ≈ 3 MV/m
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 8/13
Notes: R56 = - 6.8 ps/MeV = 7.2 cm

## Slide 16
Terahertz-driven micro-bunching
THz off
After R56 compression
45 fs rms
WTHz ≈ 20 μJ
Eacc ≈ 10 MV/m
THz on (largest peak splitting)
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 9/13
4.4 ps rms
Notes: R56 = - 3.1 ps/MeV = 3.3 cm

## Slide 17
Terahertz-driven bunching
After R56 compression
THz on
<10 fs rms
Duration, spacing and number of micro-bunches controlled by:
THz source frequency
THz field strength
Electron bunch chirp
Electron bunch length
Magnitude of R56 compression
kA peak current
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 10/13
50 MV/m THz fields
4 keV uncorrelated energy spread
Single bunch compression
≈ 10 fs rms
From experimental measurements
Shorter (< 1 ps) input bunch
Injected into a single THz cycle
Notes: R56 = - 2.5 ps/MeV = 2.7 cm
R56 = - 2.4 ps/MeV = 2.6 cm

## Slide 18
Terahertz-driven bunching – temporal locking
THz-induced energy and timing jitter reduction
  Energy jitter on the initial electron bunch
  THz-induced energy modulation observed to be more stable
Energy spectrometer with THz on and off
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 11/13
  Micro-bunches locked to the THz pulse (laser) timing
  Experimental data indicates 4x reduction in timing jitter
≈ 400 fs
≈ 100 fs
L. Zhao et al. Phys. Rev. Lett. 124,054802 (2020)
Shanghai group – compression and timing jitter reduction

## Slide 19
Opportunities at AWAKE
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 12/13
THz injection time delay
THz source
Laser
THz waveguide
150 MeV electron beam
Vacuum chamber
Optical breadboard
Key features for AWAKE
Ultrashort bunches for injection
Temporal locking between witness bunch and wakefield
Bunch trains matched to wakefield
  Multi-bunch injection + acceleration
  Pump-probe wakefield dynamics
Longitudinal diagnostic for witness
Located between injector and dog-leg
E. Gschwendtner et al. Symmetry 14(8),1680 (2022)

## Slide 20
Summary
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 13/13
THz-driven electron bunch manipulation
Ultrashort bunches with phase-locked timing jitter
  Optimised injection
Bunch trains at THz repetition rates
  Multi-bunch injection
  Pump-probe wakefield dynamics
Energy-modulation for longitudinal bunch diagnostics
  Measure bunch length and chirp
Thank you for listening!
Any questions?
Further advanced accelerator applications
  Wakefield drivers
  Free-electron lasers
  Ultrafast electron diffraction
Acknowledgements
Terahertz Acceleration Group
Steven Jamison Connor Mosley
Darren Graham Daniel Lake
Graeme Burt Sergey Siaber
Rob Appleby Laurence Nix
Christopher Shaw
Joseph Bradbury
Beatriz Higuera-Gonzalez
STFC staff
Thomas Pacey
James Jones
David Walsh
+ CLARA operators
Job advert!
2x PDRA positions in the Terahertz Acceleration Group
Links can be found at: www.THzAG.uk
Deadlines 10th and 14th July

## Slide 21
Terahertz-driven bunch de-chirper
De-chirping controlled by the THz injection timing
Reduce initial spread by a factor of 7 from 148 keV to 21 keV
Final energy spread <0.06% of the 35.5 MeV bunch energy
THz frequency is 100-1000x higher than RF-driven injectors
Allows for RF compression followed by efficient THz de-chirping
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 14/15
Potential benefits for AWAKE
Energy spread (0.2% ≡ 300 keV) removal to improve beam focusing at wakefield injection
Achieve challenging beam size parameters
R. Ramjiawan et al. Nucl. Instrum. Methods Phys. Rev. A 1049,168094 (2023)

## Slide 22
Terahertz-driven transverse streaking
Map the longitudinal coordinate to a transverse coordinate
Analogous to RF-driven transverse deflecting cavity (TDC)
Measure bunch length and time-of-arrival with fs-scale resolution
Simulation
Morgan Hibberd | Terahertz-driven electron bunch manipulation for advanced accelerators | 15/15
100 keV electrons
Potential benefits for AWAKE
Absolute measurement of sub-ps bunches from injector
Combine with energy spectrometer for full LPS extraction
Same THz structure  Just switch THz mode and frequency
R. K. Li et al. Phys. Rev. Accel. Beams 22,012803 (2019)
Demonstrated at SLAC with 3 MeV electron beams