## Slide 1
Hybrid Electromagnet-Permanent Magnet Tunable Optics for Low Emittance Storage Rings
Alex Hinton, Ben Shepherd (STFC Daresbury Laboratory)
Abolfazl Shahveh (Diamond Light Source)
Tadej Milharcic, Mirko Kokole, Jure Počkar (Kyma S.p.A.)
Particle Accelerators and Beams Conference, Strathclyde
29/06/2023

## Slide 2
Fourth generation synchrotron light sources make use of multi-bend achromat lattices to reduce beam emittance and increase radiation brightness.
Lattices require combined function dipole-quadrupole (DQ) magnets.
Diamond-II upgrade will require 48 DQ magnets drawing 2.3 kW each.
Can permanent magnets achieve the same purpose with negligible power?
Introduction

## Slide 3
Hybrid Electromagnet-Permanent Magnet Tuneable Optics (HEPTO).
Dipole = 0.7 T, Gradient = 33 T/m.
Effective length = 0.870 m.
Main source of field = NdFeB permanent magnet blocks
Dipole and gradient fields require independent tuning of ±2.5% for commissioning purposes.
Field tuning achieved by air-cooled trim coils.
Yoke and poles made from XC06 low-carbon steel.
Design Overview
831 mm
320 mm
400 mm

## Slide 4
Pole tip design optimised in Opera 2D.
Pole shaping algorithm used to minimise multipole errors [1].
Required field quality ΔB/B < 5x10-4.
Pole Shape Optimisation
[1] G. Le Be, J. Chavanne and P. N'gotta, “Shape optimization for the ESRF II magnets,” in IPAC 2014: Proceedings of the 5th International Particle Accelerator Conference, 2014.

## Slide 5
Integrated field quality assessed in Opera 3D.
Pole tips curved to follow beam trajectory and give constant dipole field.
Effective length of quadrupole shorter than dipole.
Central gradient increased and pole profile adjusted slightly to give target field integrals.
Trim coils reduce integrated sextupole, octupole terms.
3D Field Quality

## Slide 6
Permanent magnet strength decreases with increased temperature.
FeNi shunts used to provide improved thermal stability.
Shunt has negative temperature coefficient; as temperature increases, saturation polarisation decreases.
Dipole thermal stability from -0.131% / degree without shunt to +0.004% / degree with shunt
0.01% variation typical in electromagnets due to power supply fluctuation.
Thermal stability
Flux vectors
Permanent magnet
FeNi shunt
Steel yoke

## Slide 7
Air cooled coils used to independently trim dipole and quadrupole fields by ±2.5%.
Currents limited to 5 A to allow air cooling.
Tuning is inefficient due to permanent magnets in magnetic circuit.
Required tuning range cannot be achieved with air-cooled coils.
Tuning Range
Main coil
Auxiliary coil

## Slide 8
Main and auxiliary coils cannot achieve independent field tuning in isolation.
Lateral movement of magnet can tune on-axis dipole independent of gradient without coil currents.
Auxiliary coil used to tune sextupole field component.
Main coil used to tune gradient.
With ±1mm lateral movement of magnet in-situ, required tuning can be achieved with air-cooled coils.
Mechanical Tuning

## Slide 9
Required field quality ΔB/B < 5x10-4.
Sextupole component < 10-3.
Machining and assembly tolerances will negatively impact field quality compared to nominal magnetic design.
Auxiliary coil can trim undesired sextupole component introduced by tolerances.
Modelling shows required machining tolerances of ±20 μm on main pole, ±40 μm on auxiliary pole.
Displacement tolerances < 200 μm.
Tolerance Studies

## Slide 10
Coils wound from solid insulated copper wire.
Air cooled coils – no need for water cooling infrastructure.
Some current expected at nominal operation to trim fields (account for magnetisation and machining tolerances).
Nominal power dissipation of equivalent electromagnet = 2.3 kW.
Bipolar power supply required for field tuning.
Final Coil Design
Yoke
Coil cross-section

## Slide 11
Large attractive magnetic forces between permanent magnet blocks and steel yoke.
Forces need to be considered during assembly of magnet to prevent injury or damage to the magnet.
Forces between poles in assembled magnet could cause deformation and hence reduced field quality.
Movement of components must be prohibited.
Assembly and Forces
30 kN
30 kN
40 kN
5 kN
0.3 kN
0.7 kN

## Slide 12
Conceptual mechanical design for assembling and mounting magnet produced by Kyma.
Aluminium C-shape support frame.
Device can be inserted around vacuum chamber.
Gap spacers control separation of poles subject to attractive forces.
Support base allows adjustment of displacement and angular alignment.
Can in-situ lateral adjustment be achieved?
Mechanical Design Overview

## Slide 13
Magnetic design is complete.
Mechanical design being finalised.
Nominal power requirement per magnet (for field trimming) < 2 W.
Maximum power requirement per magnet (5 A per coil) = 150 W.
Equivalent electromagnet requires 2.3 kW + water cooling.
Next steps: procurement of materials for building prototype magnet.
Testing and magnetic measurements of prototype magnet to compare performance with electromagnets.
Conclusions and Future Planning

## Slide 14
Thank you
Facebook: Science and Technology Facilities Council
Twitter:@STFC_matters
YouTube: Science and Technology Facilities Council
Acknowledgements:
Ben Shepherd (STFC)
Alfie Shahveh (Diamond Light Source)
Tadej Milharcic, Mirko Kokole, Jure Počkar (Kyma)