## Slide 1: Upgrades to the Injector Complex for Diamond-II
Ian Martin
On behalf of the Diamond-II design team
IoP PABG Annual Conference
29/30 June 2023

## Slide 2: Diamond Light Source and Diamond-II Upgrade
Diamond Light Source is the UK’s national synchrotron radiation facility located on Harwell Campus, Oxfordshire
Currently engaged in a major facility upgrade, Diamond-II:
Objective #1: Optimise the science enabled at Diamond
Objective #2: Maximise the impact it has for researchers both in universities and in industry
Objectives achieved through several means:
New Modified Hybrid 6-Bend Achromat (M-H6BA) storage ring
  Lower emittance to increase brightness and coherence
  Double number of straight sections to increase capacity
Raise energy from 3 GeV to 3.5 GeV to increase flux and brightness above 10 keV
Upgrade insertion devices, new flagship beamlines
Improved data handling/computation, automation, ...
Technical Design Report published in October 2022:
https://www.diamond.ac.uk/Diamond-II.html
 | Diamond-I | Diamond-II
Lattice Type | DBA | M-H6BA
Circumference | 561.6 m | 560.561 m
Straight Sections | 24 | 48
Energy | 3 GeV | 3.5 GeV
Energy Spread | 0.096 % | 0.094 %
Natural Emittance | 2.7 nm.rad | 161 pm.rad
Emittance with IDs | 3.1 nm.rad | 120 pm.rad

## Slide 3: Storage Ring Injection
Injection into the Diamond-II storage ring will be more demanding than for the existing ring:
Compact, high gradient lattice small bore magnets narrow vacuum chambers
Strong quadrupoles + small dispersion strong sextupoles small dynamic aperture
 | Existing booster | Target
Energy | 0.1 - 3.0 GeV | 0.1 - 3.5 GeV
Emittance | 134 nm.rad | <30 nm.rad
Bunch length | 100 ps | <40 ps
Max. SB charge | ~0.2-0.4 nC | ~5 nC
Max. MB charge | ~1-2 nC | ~15 nC
Diamond
Diamond-II
38 mm
89 mm
20 mm
Factor 4 reduction in aperture horizontally
Factor 6 reduction in aperture vertically
Consequences:
Need to reduce horizontal separation between stored and injected beams
Need to reduce the dimensions of the beam extracted from the booster
Expected dynamic aperture

## Slide 4: New Booster Synchrotron
Parameter | Booster-I | Booster-II
Energy Range | 0.1-3.0 | 0.1-3.5
Circumference | 158.4 | 163.847
Tunes | [7.18, 4.27] | [12.41, 5.38]
Emittance | 134 nm.rad | 17.4 nm.rad
Energy Spread | 0.073 % | 0.086 %
Bunch Length | 100 ps | 38 ps
Energy Loss / Turn | 580 keV | 947 keV
Design for Booster-II:
Racetrack structure (fit in existing tunnel)
Unit cells built from combined-function magnets
Two dispersion-free straight sections
Quadrupole triplets in straights for tune control
Distributed trim sextupoles to counter eddy-currents and allow fine-tuning of the chromaticity

## Slide 5: Booster-II Hardware
RF Fingers
Venting slots
Bellows
Ion pump port
Vacuum gauges port
Electron beam path
OTR screen
YAG screen
Mirror
Camera
Modular end
Central body
Pumping port
Tapers
Folded conductor
Integrated bellows
Diagnostic Screens
Magnet | Number | L (m) | B (T) | G (T/m) | S (T/m2)
BB | 4 | 1.25 | 0.95 | - | -
BD | 38 | 1.3 | 0.99 | -8.24 | -44.0
BF | 36 | 1.3 | 0.42 | 11.2 | 36.0
Quad. | 20 | 0.45 | - | 30 | -
Sext. | 44 | 0.05 | - | - | 300
Magnet Parameters at 3.5 GeV
Pumping / Bellows Assembly
Injection / Extraction Kickers
BD Dipole
BF Dipole

## Slide 6: Prototyping for Booster-II
Prototyping of components to check:
Vessel stiffness / clearance from magnet poles
Material thickness (1 mm stainless steel)
Assembly procedure / ease of access to bolts
Functionality of pumping cross / bellow assembly
Robustness of RF fingers
Vessel supports / alignment

## Slide 7: Transfer Line Modifications
Linac-To-Booster (LTB)
New dipole
Replacement septum and kicker
New quadrupole
New booster
Existing booster
Booster-to-Storage Ring (BTS)
New dipole
Relocated dipoles
Relocated quadrupoles
Replacement septa
Replacement septum

## Slide 8: BTS Diagnostics Improvements
The BTS will be upgraded to improve its diagnostics capabilities:
OTR screen
Quads used for emittance measurement
Extra BPM and steerers
Dispersion-free emittance measurement for the beam extracted from booster
Increase control of the beam position / angle at storage ring injection septum
Space retained for BTS Test Stand
R&D:
Pepper pot for single-shot emittance measurement
Cavity BPMs
Cherenkov Diffraction Radiation monitors
…

## Slide 9: Storage Ring Septum Magnets
8.3 mm
2.7 mm
Diamond
Diamond-II
3 mm septum plate
1 mm septum plate
135 nm.rad injected beam
17 nm.rad injected beam
Parameter | Value
Length | 330 mm
Peak Field | <0.6 T
Bend angle | ~1 degree
Septum blade thickness | 1 mm
Pole gap | ±5 mm
Pulse shape | Full-sine
Pulse duration | 10 μs
Peak magnet current | <6 kA
Leakage field (pulsed) | <3 µT
Storage ring septum magnet will have several sections:
Investigating PM designs for first two modules
Final section pulsed magnet, with 1 mm plate to reduce separation between stored and injected beams
Short pulse duration to minimise leakage field
Active copper conductor
Passive copper conductor (shield)
Mumetal shielding
Iron powder yoke
Injected beam
From booster
Storage ring
Septum #1
Septum #2
Thin Septum
Stored beam

## Slide 10: Storage Ring Septum Magnets
Parameter | Module 1 | Module 2
Length | 1400 mm? | 200 mm?
Peak Field | <1.5 T | <0.6 T
Bend angle | ~6.9 degree | ~0.6 degree
Septum blade thickness | - | 1 mm (4 mm gap)
Pole full gap | 10 mm | 8 mm
Leakage field (static) | - | Below 1 mT
Pulsed Septa
PM Septa
PM designs for main septa under study:
PM septum reduces shot-to-shot jitter for injected beam position and angle
Storage ring main septum has two modules, each optimised for leakage field and bend angles
Booster extraction septum challenging due to larger aperture requirements
Permendur pole and shielding
SmCo
Steel
Iron
Good field region
4mm
PM septa module 2 – end section
Stored beam region
Tracked beam centroid

## Slide 11: Project Status
Acknowledgements (partial!)
DLS: Jonas Kallestrup, Filip Malinowski, Ben Nicholson, Walter Tizzano, Vitalii Zhiltsov
ASTeC/DL: Alex Bainbridge, James Jones
JAI/Oxford: Riyasat Husain
Milestone | Planned Date
Treasury approval for the Diamond-II Project and start of funding | July / August 2023?
Start of dark period | 1st December 2027
Start of booster commissioning | 1st June 2028
Start of storage ring commissioning | 1st December 2028
End of dark period / start of regular beamline x-ray commissioning | 1st June 2029
First operational beamline | 1st September 2029
End of Diamond-II project | 1st March 2030

## Slide 12
Extra Slides

## Slide 13: Booster-II Simulated Performance (WIP!)
Beam dynamics studies are ongoing:
Dynamic aperture including field and alignment errors, vacuum chamber eddy currents, etc.
Impact of magnet fringe fields and saturation effects
Intra-beam scattering
Short and long range wakefields
Transfer efficiency and loss locations
So far, so good!
Average dynamic aperture vs energy
Betatron tunes vs energy
Electron beam parameters during the ramp for 100 MeV injection / zero chromaticity
Initial beam blow-up at injection from wakefields
Beam loss at injection for high-charge bunches
Losses reduced for small positive chromaticity
Intra-beam scattering increases bunch size at extraction
Dynamic aperture
Physical aperture