## Slide 1: An Optimisation Framework for Underexpanded Jets
Particle Accelerators and Beams 2023 Conference
O. Stringer, H. Zhang, C. Welsch

## Slide 2: Contents
Underexpanded jets and their applications
Monte-Carlo underexpanded jet model
Multi-Objective Genetic Algorithm optimisation
Future work

## Slide 3: Gas Jets Applications
Underexpanded jet of gas
Beam profile monitors – Ionisation Profile Monitors
Plasma wakefield injectors
Nuclear targets
Ion engine propulsion
Figure 1: SpaceX Raptor engine test [1].

## Slide 4: Monte-Carlo Jet Simulation
A Monte-Carlo particle tracking code was previously developed to simulate the density and distribution of the gas jet.
It uses ideal gas laws and a calorically perfect isentropic expansion model and has been shown to accurately simulate the jets behaviour.
Figure 2: Animation of the Monte-Carlo gas jet principal.

## Slide 5: Multi-Objective Genetic Algorithm
Non-dominated Sorting Genetic Algorithm (NSGA-II)
Optimisation technique that simulates “Survival of the Fittest” in biological evolution.
Parameter space of 10 variables, 5 design variables
50,000,000 geometric solutions, varying skimmer distance and aperture of all 4 skimmers.

## Slide 6: Injection Optimisation
Nozzle
1st Skimmer
2nd Skimmer
3rd Skimmer
IP
0.00
1.00 – 10.00 mm
6.58 – 48.49 mm
174.94 – 241.11 mm
294.94 mm
Figure 3: Schematic of the injection parameter space used for the optimisation study.
4th Skimmer
346.13 – 409.94 mm
d: 500 – 7,500 um
d: 30 – 10,000 um
a
b
a: 50 – 2,000 um
b: 2 – 60 mm
a: 50 – 10,000 um
b: 2 – 100 mm
d
d
a
b

## Slide 7: Design Space
Design Parameter |  | Justification | Target
Number density | - | Proportional to signal received | 
Length of jet | - | Maximum beam profile size | 
Width of jet | - | Determines spatial resolution, signal yield and beam losses | 
Density variation | - | Uniform profile measurement | 
Background Pressure | - | Minimise beam losses | 
Design Parameter |  | Justification | Target
Number density | - | Proportional to signal received | 
Length of jet | - | Maximum beam profile size | 
Width of jet | - | Determines spatial resolution, signal yield and beam losses | 
Density variation | - | Uniform profile measurement | 
Background Pressure | - | Minimise beam losses | 

## Slide 8: Results
Figure 7: Surface plot of density as a function of skimmers 1 and 3 positions.
Figure 8: Surface plot of width as a function of skimmers 1 and 3 positions.
Density / # m-3 | Curtain Length / mm | Curtain Width / mm | Variation in centre / % | BG Pressure / mbar
 | 31.14 | 0.25 | 9.61 | 
Density / # m-3 | Curtain Length / mm | Curtain Width / mm | Variation in centre / % | BG Pressure / mbar
 | 31.14 | 0.25 | 9.61 | 

## Slide 9: Conclusions and Future Work
A high speed optimisation framework for underexpanded jets has been developed.
A best geometric solution has been shown.
Validating analytical background calculations with experimental data
Validate final chosen simulations using MolFlow

## Slide 10: Additional Slides

## Slide 11: Beam Gas Fluorescence
Beam path
Jet path
Photon yield [4]:
Concentrate a higher number density in a small region to minimise losses.
Orientating a thin sheet 45o will allow X & Y profiles of beam to be reconstructed.
Circular Jet
45o Jet Curtain
Figure 1: Beam induced fluorescence in chamber background gas
Figure 1: Beam induced fluorescence using circular jet
Figure 1: Beam induced fluorescence using 45 degrees jet
Notes: ****Non-invasive, within energy spread****
Sigma – fluorescence cross-section (a function of beam energy & size)
Omega – solid viewing angle of camera
T – Transmittance of the imaging system
I – Beam current
n – gas curtain number density
d – gas curtain thickness

## Slide 12: Beam Gas Curtain
Injection
Interaction
Dump

## Slide 13: BGC measurements
Pixels
Pixels
Number of photons
Number of photons
Beam Path

## Slide 14: Hollow Electron Beam

## Slide 15: Key Performance Criteria (Required)

## Slide 16: Adaptive Background Pressure
Notes: Mdot = mass flow rate
Delta mdot jet = mass flow rate of jet that does not pass a skimmer (mdot jet in – mdot jet out)
Delta mdot effusion = mass flow rate of effusion between chambers (mdot effusion in – mdot effusion out) – a result of different chamber pressures and entropy.
Mdot pumping = mass flow rate of volume being pumped.
Rho = density (of jet, unless subscript BG which is Background)
V = velocity of jet.
Delta A jet = difference in area of jet (jet 2D area at skimmer – skimmer area)
Q effusion = flow rate of effusion
S = pumping speed.
Delta P = difference in pressure between two chambers
A = area of skimmer
NA = Avogadro’s constant
M = molar mass of gas
R = Gas Constant
T = Temperature of background.

## Slide 17: Effusion
2nd Law of Thermodynamic - two connected reservoirs at a pressure differential will eventually converge to equal pressure.
 | BG pressure N2 / mbar | BG pressure Ne / mbar
Jet loss | 0 | 0
Effusion | 1.64E-8 | 2.86E-8
Experimental | 1.14E-8 | 3.60E-8
Notes: BG – number density of background pressure in chamber (# m^-3)
Jet loss – density of the jet (# m^-3)
v Jet loss – velocity of the jet (m s^-1)
A Jet loss – area of the jet remaining in the chamber at the skimmer (size jet – size of skimmer) (m^2)
Delta P – pressure different between two chambers (Pa)
A – Aperture of skimmer (m)
NA – Avogadro’s Number
M – Molar mass of gas
R – Gas constant
T – Temperature of BG (K)
S – Pumping speed of TMP (m^3 s^-1)
𝜌 BG – number density of background pressure in chamber (# m^-3)
𝜌 Jet loss – density of the jet (# m^-3)
v Jet loss – velocity of the jet (m s^-1)
A Jet loss – area of the jet remaining in the chamber at the skimmer (size jet – size of skimmer) (m^2)
Delta P – pressure different between two chambers (Pa)
A – Aperture of skimmer (m)
NA – Avogadro’s Number
M – Molar mass of gas
R – Gas constant
T – Temperature of BG (K)
S – Pumping speed of TMP (m^3 s^-1)

## Slide 18: Dynamic Background Check
V3, Neon injection @ 5 bar, Skimmers: 400um, 2mm, 0.3x9mm and 7x31mm.

## Slide 19: References
[1] SciNews, Raptor engine test. [Online]. 2016. [Accessed 23 June 2023]. Available from: https://www.youtube.com/watch?v=e7kqFt3nID4&ab_channel=SciNews