## Slide 1: Novel emittance diagnostics: utilising optical radiation for single-shot measurements
C. Swain1,2, J. Wolfenden1,2, T. Pacey3, C. Welsch1,2
1 University of Liverpool, UK
2 Cockcroft Institute, Warrington, UK
3 ASTeC, Warrington, UK

## Slide 2
Overview
Traditional emittance measurements are generally invasive and often destructive.
Low energy or high space charge beams can be difficult to measure.
Replicating traditional methods utilising optical radiation to make them minimally invasive.
  Currently optical transition radiation (OTR).
  Future plans for optical synchrotron radiation (OSR) would make these methods non-invasive.
This will be of interest to many facilities, but is currently being developed for AWAKE, where emittance is generally 2 – 5 mm mrad[1].
These all-optical methods will be a compact, high resolution, single-shot alternative.
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
1

## Slide 3
Traditional emittance measurements
[3] M. Zhang, "Emittance Formula for Slits and Pepper-pot Measurement", FERMILAB-TM-1988, Oct. 1996
Emittance measurement methods being replicated are slit/pinhole scans, and pepperpots.
Metal plates are placed in the path of the beam, with holes etched to let ’beamlets’ through.
Beamlets are imaged and analysed, and emittance calculated.
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
2
xj
σj
nj
jth beamlet intensity
Beam
Mask
Beamlets
Screen
Notes: Benefit of pepperpot is you gain x and y emittances simultaneously
Pepperpot also good for space charge dominated beams, small beamlets each have low charge – ATHOUGH it is still affected
Beam passes through plate, to scintillator screen (or similar), and light is imaged
Equation uses number and position of slits/pinholes, number of particles, position and divergences of beamlets

## Slide 4
Micro Lens Array
MLA is array of lenses, in this setup with a pitch of 150 μm[4].
Two cameras are used to image spatial and angular components simultaneously.
Will allow for imaging of x and y emittances simultaneously.
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
3
Pre-MLA
Post-MLA

## Slide 5
Digital Micro-mirror Device
DMD is an array of individually controllable mirrors, here with 7.56 μm pitch and angular control of ±12°[5].
Pinholes or slits are created on the DMD, with one section of the reflection imaged for spatial information, and the other for angular information.
DMD masking is very flexible, meaning it can be adjusted for different beam specifications or facility needs.
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
4

## Slide 6
Laser benchmarking: laser ‘emittance’ theory
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
5
When combined with Gaussian laser spot size equations:
Notes: 4 is because omega^2 is 4<x^2>, because omega is the 1/e^2 width
w^2 = w0^2 + (lambda/4pi)^2 z^2
Gaussian laser equations include Rayleigh length

## Slide 7
Laser benchmarking: laser ‘emittance’ measurement
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
6
[6] https://github.com/scottprahl/laserbeamsize
[7] J. Wolfenden, "Optical Pepper-pots: Developing single-shot emittance diagnostics", in Proc. IPAC'23, Venezia.
Notes: - Laser 1 is from the MLA setup, 2 is from the DMD

## Slide 8
Laser benchmarking: MLA resolution
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
7

## Slide 9
Laser benchmarking: DMD resolution
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
8
Theoretical PSF spot size for varying apertures was calculated.
Experimental verification of results will be carried out.
Increasing pinhole radius decreases the PSF.
This means images with larger pinholes will have less contribution from diffraction through the aperture.
Therefore, larger pinholes give higher diffraction resolution.

## Slide 10
Experimental plans for CLEAR
In October, both setups will be taken to CLEAR.
Here we hope to gain proof of concept measurements for the divergence resolution of both systems.
Utilising OTR both systems will image simultaneously.
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
9
MLA setup
OTR
BS
MLA
e- beam
Window
OTR
To DMD setup
To MLA setup
Beamsplitter
OTR target
DMD setup
OTR
DMD
Mirror
Mirror

## Slide 11
Summary
Two systems for all-optical emittance measurements have been tested at CI.
Diffraction resolution limits of the two have been compared.
Plans for experimental testing at CLEAR scheduled for October 2023.
Next steps include simulating different radiation sources, e.g non-invasive OSR.
Future plans for testing at FEBE on CLARA.
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
10

## Slide 12
Thanks for listening, any questions?
For any further questions, email:
catherine.swain@liverpool.ac.uk
[1] S. Kim, et. al., (2020), “Commissioning of the electron injector for the AWAKE experiment”, NIM-A, vol. 953
[3] M. Zhang, "Emittance Formula for Slits and Pepper-pot Measurement", FERMILAB-TM-1988, Oct. 1996
[4] https://www.thorlabs.com/newgrouppage9.cfm?objectgroup_id=2861
[5] https://www.ti.com/product/DLP6500FLQ
[6] https://github.com/scottprahl/laserbeamsize
[7] J. Wolfenden, et. al., (2023), "Optical Pepper-pots: Developing single-shot emittance diagnostics", 14th Int. Particle Acc. Conf., pg 3874 - 3877
This work is supported by the AWAKE-UK phase II project funded by STFC grant no. ST/T001941/1, the STFC Cockcroft core grant no. ST/V001612/1.

## Slide 13
Additional slides
This work is supported by the AWAKE-UK phase II project funded by STFC grant no. ST/T001941/1, the STFC Cockcroft core grant no. ST/V001612/1.

## Slide 14
Emittance calculations – M. Zhang (1996)
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
A1
M. Zhang, (1996), Emittance Formula for Slits and Pepper-pot Measurement, Emittance Formula for Slits and Pepper-pot Measurement

## Slide 15
CLEAR test stand
C. Swain (catherine.swain@liverpool.ac.uk)
IOP PAB conference 28/06/2023
A2
Diagram courtesy of Pierre Korysko (CLEAR, CERN).