## Slide 1: CARP Development of a new tool for modelling medical radionuclide production
Duncan Mayhem
11th June 24
Not protectively marked
Notes: Name
Role
How long
Background

## Slide 2: Acknowledgements
Not protectively marked
This work was partially undertaken within the SECURE project funded by the European Union under grant agreement No. 101061230.
“Strengthening the European Chain of sUpply for the generation medical RadionuclidEs”
Sustainability of medical isotope production
Focus on irradiation target and production route developments

## Slide 3: Presentation Contents
Not protectively marked
What is CARP?
How does CARP work? (ish)
Example inputs and outputs
Verification & Validation work
Intended uses and future work

## Slide 4: What is CARP
Not protectively marked
New tool for modelling the nuclide composition of irradiated target materials
Inputs:
  Target information (geometry, composition, mass etc.)
  Irradiation conditions
Outputs
  Stepwise evolution of the target nuclide inventory
  Inc. parameters of interest e.g per nuclide contributions to alpha, beta and gamma emissions
  Nuclide agnostic
Computational Assessment of Radionuclide Production
Notes: Irradiation conditions can be as variable as you like incl cooling
Outputs @ user specified irradiation and cooling times incl reirradiation, recooling…
Nuclide agnostic – unlike some other tools, CARP isn’t preferential towards a set desired nuclide. All desired nuclides and undesirable byproducts are treated the same

## Slide 5: What is CARP?
Not protectively marked
Aims:
To produce a flexible, batch operable, and easy to use tool for the quick assessment and optimisation of radionuclide production routes by incident particle beams.
To produce simple, human readable and flexible outputs to advise on the pitfalls and benefits of production routes.
To produce a collaborative tool for research purposes to support the medical radionuclide production community, and accelerator system and research reactor beam communities.

## Slide 6: How does CARP work?
Not protectively marked

## Slide 7: How does CARP work? - FISPIN
Not protectively marked
So what is FISPIN?
UK nuclear fuel inventory code – used for validation of UK reactors, reprocessing facilities etc.
In development since the 70’s, FISPIN 10 (90’s/00’s) was used for various reactor validation cases throughout Europe
New version FISPIN 11 – acts as a calculation kernel – not constrained to reactors – can model incident particle scenarios
0 dimensional…
Notes: FISPIN 10 – quite a crude method for estimation of Bateman equation solutions using the infamous LEVEL parameter – due to CPU constraints
- 556 nuclides
FISPIN 11 – no longer has these constraints, calculates definitively
- 2609 nuclides
- allows explicit declaration of the incident particle flux, and (multi) particle type definition
Beam and target geometries must be introduced via the x-sec libs – MCNP/Serpent

## Slide 8: How does CARP work? – MCNP -> CARP
Not protectively marked
Energy dependent neutron spectrum
Incident neutron reaction cross- section database
FISPIN format cross-section library
Uses recommended NJOY equations to emulate continuous neutron flux – as in ORIGEN
Translates beam and target information into a FISPIN usable format
TENDL-2017, 2021, ENDFB-VIII
Energy bin agnostic
Notes: Convolve
This process makes CARP energy binning structure agnostic

## Slide 9: How does CARP work? - Summary
Not protectively marked
MCNP generates a beam specific particle spectrum across the target
This particle spectrum is cross-referenced against a cross-section database to produce a FISPIN cross-section library containing the beam data
The FISPIN kernel calculates the stepwise inventories of the target using this data, producing inventories at the user specified timesteps
A number of behind the scenes calculations e.g. activity, mass
  Visualised into a user friendly excel file

## Slide 10: Example inputs/outputs - Input
Not protectively marked
Target information
Beam information
Calculation times
MCNP file
Nuclide and reaction files
Cross-section libraries

## Slide 11: Example inputs/outputs - Output
Not protectively marked

## Slide 12: Example inputs/outputs - Output
Not protectively marked

## Slide 13: Verification & validation work – EK data
Not protectively marked
Acquired V&V data from EK under the EU SECURE project:
  EK run the Budapest Research Reactor (BRR)
  Multiple beam lines
  Irradiating samples for medical radionuclide production research
  Gamma scan data and FISPACT modelled data made available
Notes: EK – Energiatudomanyi Kutatokozpont – Centre for energy research (CER)
Explain about the EU SECURE programme
Explain about EKs BRR reactor

## Slide 14: Verification & validation work – EK data
Not protectively marked
Three target types irradiated in three beam lines for 30-60 mins, cooled for ~4-6 days
Gd diluted Al foil  Tb-161
Lu diluted Al foil  Lu-177
Pt diluted Al foil  Au-199
Notes: EK – Energiatudomanyi Kutatokozpont

## Slide 15: Verification & validation work – EK data
Not protectively marked
Chart: Tb-161
| ch17 | ch47 | ch72
FISPACT | 41.28 | 218 | 417.7
Gamma spec | 38.4977 | 170.0326 | 351.4868
CARP | 39.5044 | 210.6484 | 395.6969
Chart: Lu-177
| ch17 | ch47 | ch72
FISPACT | 125000 | 524000 | 855000
Gamma spec | 119000 | 399351.2035 | 723205.7882
CARP | 131138.3066 | 543757.6803 | 892134.2037
Chart: Au-199
| ch17 | ch47 | ch72
FISPACT | 19200 | 39979 | 45293
Gamma spec | 16469.6827 | 34456.1489 | 32285.5834
CARP | 18455.506 | 39590.8914 | 45844.7979
Notes: After discussion with EK, they say their ch17 beam model is their most confident, and ch47 and 72 require additional work

## Slide 16: Verification & validation work – EK data
Not protectively marked
Two further target types irradiated in a single beam line for 20-30 mins, cooled for 8 and 41 days
Gd2O3  Tb-161
Lu2O3  Lu-177
Product nuclide | FISPACT (Bq) | Gamma spec (Bq) | CARP (Bq)
Tb-161 | 3.79E+06 | 2.87E+06 | 3.74E+06
Lu-177 | 7.26E+07 | 5.12E+07 | 6.87E+07

## Slide 17: Verification & validation work
Not protectively marked
We hope to receive further reactor beam validation data from other SECURE partners
Verify against FISPACT
Always on the search for more!
  Accelerator beam scenarios
  Alternative particle types
    (Where nuclear data is available…)

## Slide 18: Intended uses and future work
Not protectively marked
Future developments
  Batch mode
  User defined thresholds
  Mid process separation
Intention is to use CARP in collaborative work
  Optimising existing experiments
  Modelling novel and/or complex scenarios
And to collaborate in understanding what CARP should do!
Notes: EK – Energiatudomanyi Kutatokozpont

## Slide 19: Thank you!
Duncan Mayhem
Nuclear & Reactor Physics Team
NNL
duncan.mayhem@uknnl.com
This work was partially undertaken within the SECURE project funded by the European Union under grant agreement No. 101061230.