## Slide 1: Crystal experiments and recent measurements at CERN
K.A. Dewhurst, on behalf of the NDC (Non-linear Dynamics and Collimation) Section
12 June 2024

## Slide 2: Contents
Why use bent crystals?
Crystals for collimation of the lead ion beam
The TWOCRYST experiment
Channelling efficiency measurements
Summary

## Slide 3: Why use bent crystals?
Charged particles follow the lattice structure of the silicon crystal. Holders clamp the silicon crystal sheet into a bent position. With bent crystals, particle trajectories can be bent in a short distance.
Crystal lattice
Channel particles
Bend trajectory
Critical angle
V. M. Biryukov et al., 1997 doi: 10.1007/978-3-662-03407-1.
No bending
1 GeV/cm
2 GeV/cm

## Slide 4: Crystals for collimation
LHC
Collimators
IR7 – main collimation region (betatron cleaning)
IR3 – momentum cleaning

## Slide 5: Crystals for collimation
A hierarchy of collimators scatter, and eventually absorb particles from the beam halo. Works for the LHC!
Projected collimation performance at the HL-LHC: OK for proton beams! Not OK for lead ion beams 

## Slide 6: Crystals for collimation
Area of interest

## Slide 7: Crystals for collimation
IR7 Standard collimation
IR7 Crystal collimation
3.9e-14 m-1
2.9e-13 m-1
The first comparisons of cleaning the LHC 6.8 Z TeV lead ion beams with crystal collimation was carried out in 2022/2023.
The crystal collimators are located in IR7.
Cleaning efficiency was improved in every case. Empirical comparisons indicate gains with a factor >5 for the best crystals!
Find out more, read the paper:
D’Andrea et al., Operational performance of crystal collimation with 6.37 𝑍 TeV Pb ion beams at the LHC, Jan 2024 https://doi.org/10.1103/PhysRevAccelBeams.27.011002

## Slide 8: Contents
Why use bent crystals?
Crystals for collimation of the lead ion beam
The TWOCRYST experiment
Channelling efficiency measurements
Summary

## Slide 9: Physics Beyond Colliders: IR3 experiment
Final PBC double-crystal experiment
Aim: To measure the magnetic and electric dipole moments of rare baryons (Λc).
Run 4 HL-LHC 2029 +
Proof-of-principle (PoP) test stand
Aims: To gain operational and technical experience.
To characterise the IR3 crystals. To measure crystal channelling efficiency at TeV energies.
Run 3 LHC 2025 +
Crystals in the LHC
Collimation crystals are already installed in IR7.
Crystal prototypes for IR3 are being manufactured and tested.
Run 3 LHC 2023 (today)
🚩
TWOCRYST
ALADDIN
An Lhc Apparatus for Direct Dipole-moments INvestigation

## Slide 10: The final PBC experiment: ALADDIN double-crystal setup – high intensity operation
Protons impact the collimator (TCP in IR7) – some particles form a secondary halo
Intercept halo particles with a first bent crystal (CRY1) directing them towards a fixed target
Fixed target at safe distance from beam Proton interactions produce rare baryons
A second bent crystal enforces precession of the rare baryons
Detector including spectrometer: measure precession + decay products
Collimators: safely absorb residuals of the channelled halo
TCCS
TCCP

## Slide 11: A Proof of Principle experiment: TWOCRYST low intensity operation at TeV energies
One goal on the journey: find the channelling efficiency of crystal 2 (TCCP)
Align CRY1 with the edge of the main beam (~5σ) to produce channeling – one spot on pixel detector Align CRY2 (linear and angular position) to produce double-channelling – second spot on pixel detector Measure intensity of double-channelled halo spot on the detector, to find the channelling efficiency of CRY2. For a prediction from simulations see IPAC paper doi: 10.18429/JACoW-IPAC2024-TUPC64.
Beam ➡
Crystal 1 TCCS
Pixel detector PIX 1
Absorber
TCLA
1 m
Target TGT retracted
Crystal 2
TCCP

## Slide 12: TWOCRYST to be installed this year
Visit to IR3 in February 2023 to check component positions and space requirements. Components will be installed in the Year-End-Technical-Stop (YETS) of 2024/2025. Measurements will take place in 2025.
Crystal 1 at 6775 m
Space available
Crystal 2 at 6655 - 6675 m
Plenty of space available

## Slide 13: Contents
Why use bent crystals?
Crystals for collimation of the lead ion beam
The TWOCRYST experiment
Channelling efficiency measurements
Summary

## Slide 14: The TWOCRYST crystals: TCCS and TCCP
The TCCS and TCCP were delivered to CERN in summer 2023. Single-pass experiments were carried out to measure the single-pass channelling efficiency.
TCCS (crystal 1) TCCP (crystal 2)
Prototype

## Slide 15: 3. The TWOCRYST crystals
Crystal 1 (short)
Anodic-bonded crystal
Crystal 2 (long)
Crystal properties:
Length 4 mm
Material Silicon
Bend radius 80.0 m
X dimension 2 mm
Y dimension 35 mm
Crystal properties:
Length 70 mm
Material Silicon
Bend radius 10.0 m
X dimension 2 mm
Y dimension 8 mm
Crystal properties:
Length 70.5 mm
Material Silicon
Bend radius 5.3 m
X dimension 2 mm
Y dimension 22.5 mm

## Slide 16: The TWOCRYST crystals: TCCS and TCCP
H8 experiment
θin
θout
T2
Crystal
T3
Single-pass experiments were carried out in Aug 2023 in the CERN North Area (beamline H8) to measure the single-pass channelling efficiency. Results soon to be published.
Preliminary results: cut at half of the critical angle
Crystal and data cut point | Ch. Eff. expected from simulation | Whole crystal Ch. Eff. H8 data | Central 2.5 mm Ch. Eff. H8 data | Bend angle H8 data
Crystal 1 (TCCS) (+/- 7.7 µrad) | ~77 % | 59.7 % | 63.4 % | 48 µrad (aim 50)
Crystal 2 (TCCP) (+/- 7.3 µrad) | ~36 % | 8.0 % | 13.0 % | 6915 µrad (aim 7000)
Anodic-bonded crystal (+/- 7.0 µrad) | ~ 30 % | 10.0 % | 12.4% | 13280 µrad (expected 13302)

## Slide 17: Summary
Why use bent crystals? - For collimation: the bend angle does not vary with the mass-to-charge ratio. - For spin-precession: short-lived particles can traverse a short (cm-length) crystal before they decay.
Crystals for collimation of the lead ion beam - Have been show to improve the cleaning efficiency
The TWOCRYST experiment - Components will be installed in the upcoming YETS - Measurements in the LHC will take place in 2025 - Single-pass channelling efficiency measurements have been carried out in the North Area

## Slide 18: Thank you. Read the IPAC 2024 papers: https://doi.org/10.18429/JACoW-IPAC2024-TUPC64 https://doi.org/10.18429/JACoW-IPAC2024-TUPC65 https://www.jacow.org/ipac2024/doi/jacow-ipac2024-frxn3/index.html
Kay Dewhurst | Crystal experiments and recent measurements at CERN