## Slide 1: Electron beam jitter suppression and diagnostic using terahertz-induced modulation
Joseph T. Bradbury
3rd year PhD student
joseph.bradbury-2@manchester.ac.uk
Terahertz Acceleration Group @ The Cockcroft Institute www.THzAG.uk

## Slide 2: THz Acceleration Group @ www.THzAG.uk
Sub-relativistic acceleration
Recent publication
Relativistic acceleration
1/10
Our research group
Novel terahertz (THz)-based techniques for electron beam acceleration and manipulation.
Higher driving frequency compared with conventional RF accelerators.
THz source development.
M. T. Hibberd et al. “Acceleration of relativistic beams using laser-generated terahertz pulses” Nature Photonics 14,755-759 (2020)
Dan Lake
Christopher Shaw
Laurence Nix
Connor Mosley
Beatriz
Higuera Gonzalez
Darren Graham
Sergey Siaber
Joseph Bradbury
Morgan Hibberd
Graeme Burt
Steven Jamison
Rob Appleby
L. J. R. Nix et al. “Terahertz-driven acceleration of subrelativistic electron beams using tapered rectangular dielectric-lined waveguides” Phys. Rev. Accel. Beams 27 041302 (2024)
Poster by me on this topic

## Slide 3
About this talk
2/10
Coming up…
I will present experimental results and supporting simulations showing how THz energy modulation can be used to diagnose and suppress jitter from other accelerator systems.
Motivation
Diagnosing and suppressing jitter in electron beams using THz is an active research area.
Using ultra-short fs duration bunches requires excellent timing stability.
Laser-synchronised bunches with fs-scale jitter are key for
  Pump-probe experiments.
  Time-resolved electron diffraction imaging.
  External injection into e.g. PWFA and FELs.
Content
Longitudinal phase space diagnostic using THz energy modulation
Compression and bunching
Jitter modelling and extraction using THz energy modulation
Jitter suppression
L. Zhao et al. “Femotosecond Relativistic Electron Beam with Reduced Timing Jitter from THz Driven Beam Compression” Phys. Rev. Letters 124, 054802 (2020)
E. C. Snively et al. “Femtosecond Compression Dynamics and Timing Jitter Suppression in a THz-driven Electron Bunch Compressor” Phys. Rev. Letters 124, 054801 (2020)
Y. Song et al. “MeV electron bunch compression and timing jitter suppression using a THz driven resonator” Nucl. Instrum. Methods Phys. Res. Sect. A, 1047, 167774 (2023)

## Slide 4
Laser-generated narrowband 0.4 THz pulses using periodically-poled lithium niobate (PPLN) wafers stacks (Poster by Patrick Dalton)
Stack of PPLN wafers for producing laser-generated THz radiation.
DLW installed in the vacuum chamber.
3/10
Introduction to the experiment
C ompact
L inear
A ccelerator
R esearch
A pplications
Beam parameters
35.5 MeV
6 ps FWHM
Chirped bunches
100 pC
THz pulse and electron beam injected into dielectric-lined waveguide (DLW)
Electron energy measurement using dipole spectrometer

## Slide 5
4/10
Introduction to the experiment
Laser and THz optics outside the vacuum chamber
THz-electron interaction point inside the vacuum chamber
Beam Area 1
Interaction chamber
Energy spectrometer
Optical breadboard

## Slide 6
Uncorrelated energy spread
Chirp
ΔE
Energy spikes are separated in time by one THz cycle.
T = 2.5 ps (0.4 THz)
Chirp ≈ 73 keV ps-1
ΔE
The width of energy spikes indicate the slice uncorrelated energy spread
σE = 8 keV
Overmodulation
Compression
60 fs FWHM
5/10
Compression
Accurate longitudinal phase space reconstruction
THz-frequency train of < 100 fs, 5 pC micro-bunches.
Short single bunch compression is also possible.
Magnetic chicane
Initial bunch phase space from CLARA
0.4 THz wave
Electrons receive a longitudinally dependent energy change
Interaction strength is optimised for diagnostics by producing sharp energy peaks
THz phase scans allow time-slice properties to be diagnosed which are otherwise complex / inaccessible
2.5 ps THz period allows sharp features in the phase space to be exploited
Increased THz field strength
Curved phase space from non-linear chirp
Example compression using moderate THz field

## Slide 7
6/10
Sources of jitter
Bunch arrival time jitter
Jitter in injection time into the linac.
RF amplitude jitter
RF field strength can vary.
RF phase jitter
RF phase affects the initial bunch energy and chirp.
THz arrival time jitter
Alters the phase of the energy modulation imposed on the bunch

## Slide 8
Each source of jitter produces a unique effect in the energy spectrum, and can therefore be extracted independently.
7/10
Jitter modelling and extraction
RF amplitude jitter
Bunch arrival time jitter
RF phase jitter
THz arrival time jitter
Chirp profile is of underlying bunch is changed
THz off LPS has different curvature
THz off
ΔEd
ΔEc
ΔEc > ΔEd
THz phase alters the energies where LPS is flattened
Chirp profile of underlying bunch unchanged
Phase space moved vertically in energy
ΔEa
ΔEb
ΔEa = ΔEb
ΔEf
ΔEe
ΔEe ≈ ΔEf
Phase space remains overlapped
Bunch profile arrives at a different time
Bunch profiles
Peaks are locked
ΔEa
ΔEb
Pedestal shifted
Equal energy shift to each peak
Pedestal is shifted
Peaks remain at fixed energy
THz off spectrum (norm.)
Peaks are shifted along the underlying phase
Pedestal is still fixed to the energy of THz off beam
ΔEc
ΔEd
Energy shift to peaks depends on local chirp
ΔE = 0

## Slide 9
8/10
Jitter modelling and extraction
Measured energy spectra of
50 consecutive THz-modulated bunches.
A best fit to the energy spectrum extracts the phase space.
Values for each source of jitter are found shot-by-shot.
(Units chosen for convenient simulation)
< M. A. Johnson, J. K. Jones, P. H. Williams,
‘Jitter Tolerance for the FEBE Beamline on
CLARA’, IPAC 2023, JaCoW Publishing
Jitter source | Bunch arrival time | RF phase | RF amplitude
RMS jitter extracted from fitting (rel. to THz drive laser) | 157 fs | 211 fs | 5.3 keV
By converting the units, we find the extracted jitter compares well with previous work on CLARA.

## Slide 10
δt = 11 fs rms
δt = 144 fs rms
Bunch from CLARA
Compressed bunch with THz
9/10
Jitter suppression
50 shots
Base beam from CLARA (black) - 144 fs rms jitter
Corresponding compressed bunch trains with THz on (red) - 30 fs rms jitter
R56 – 3.46 ps/MeV
The compressed bunch train becomes locked to the laser.
Timing jitter relative to the laser is reduced by a factor of up to 5.
δt = 29 fs rms
δt = 38 fs rms
δt = 43 fs rms
δt = 33 fs rms
δt = 144 fs rms
Long bunches for diagnostics,
shorter bunches for compression…
1.5 ps FHWM
Lower chirp
1.5 x higher THz field
R56 – 2.44 ps/MeV
Jitter relative to the laser is reduced by a factor of 13 x.

## Slide 11
10/10
Summary
LPS diagnostic using THz modulation
Jitter from upstream accelerator components can be diagnosed using THz modulation.
THz modulation experiments using CLARA
THz-modulated / chirped bunches can be compressed into micro-bunch trains or ultra-short single bunches.
The compressed bunches can be locked to the THz drive laser, with rms jitter of 11 – 30 fs.
A directly scalable technique…
Jitter suppression can be readily improved be increasing the THz field and using a lower value of R56, bringing bunches with fs-scale duration and synchronisation within reach.
δt = 11 fs rms
δt = 144 fs rms
Bunch from CLARA
Compressed bunch with THz
Thank you for listening!

## Slide 12
Thanks for listening! Any questions?
Thanks to all the people involved
Morgan T. Hibberd1,2, Christopher T. Shaw1,2, Daniel S. Lake1,3, Connor D.W. Mosley1,3, Sergey Siaber1,3, Beatriz Higuera Gonzalez1,2, Thomas H. Pacey1,4, James K. Jones1,4, David A. Walsh1,4, Robert B. Appleby1,2, Graeme Burt1,3, Darren M. Graham1,2, and Steven P. Jamison1,3
joseph.bradbury-2@manchester.ac.uk
Terahertz Acceleration Group @ The Cockcroft Institute - www.THzAG.uk
1
2
3
4