## Slide 1: ISIS Upgrade: 40 Years of the ISIS Neutron and Muon Source
B. Kyle
PAB 2024, Cumbria
11/06/2024

## Slide 2: Outline
Introduction to ISIS
  The ISIS Facility
  40 Years of ISIS: Milestones and Major Upgrades
Neutron Sources
  Types of Neutron Sources
  Applications of Neutron Sources
  Spallation Neutron Sources
Recent ISIS Upgrades
  Tank 4 Replacement
  Synchrotron RF Upgrade
  Target Station 1 Upgrade
Upcoming ISIS Upgrades
  EPICS Migration
  Q-Kicker Damping System
  MEBT
  Novel RF Plasma Source
ISIS-II
  Design Options
  Studies Underway
  FETS FFA

## Slide 3: Introduction to ISIS

## Slide 5: The ISIS Facility
H- source (RFQ + DTL)
800 MeV RCS
Target Station 1
Target Station 2

## Slide 6: The ISIS RCS
Mean Radius | 26 m
Beam Energy | 70 – 800 MeV
Intensity | ~3e13 ppp
Repetition Rate | 50 Hz
Lattice Periodicity | 10 SP
Injection | 220 μs, 130 turns (charge exchange)
Painting | Dispersive horizontal, injected beam position scanned vertically
Extraction | Single turn, vertical
Betatron Tune | (Qx, Qy) = (4.31, 3.83), programmable
Beam Losses | Injection: 2%, Trapping: <3%, Acceleration/Extraction: <0.5%
RF System | 6 × fundamental (h=2) @ 160 kV/turn, 4 × 2nd-harmonic (h=4) @ 80 kV/turn
Extraction
Injection
TS2
TS1

## Slide 7: ISIS@40
ISIS celebrates its 40th birthday this year. Major milestones and achievements include:
First neutrons Dec 1984
Regular runs from Jan 1985 (25 Hz, 10 µA, 550 MeV)
Operational phase began in 1986 (50 Hz, 30 µA, 550 MeV)
First muons 1987
Design energy and current achieved 1994 (50 Hz, 200 µA, 800 MeV)
Most powerful pulsed neutron source in the world in 2004 (now surpassed)
Longest operational lifetime of any UK accelerator
ISIS named for Egyptian goddess of re-birth, as well as the traditional name of the River Thames as it flows through Oxford:
Linac originally commissioned as injector upgrade for Nimrod
RCS constructed in the hall of the old Nimrod accelerator
Re-used many components of Nimrod and NINA accelerators

## Slide 8: ISIS@40: Statistics
Over the last 40 years, the ISIS RCS has delivered 8×1023 protons to the neutron targets.
This corresponds to:
½ a teaspoon of protons (assuming H atom volume)
100 coronavirus virions (assuming nuclear volume in close-packing regime)
1.3 mol of ionised hydrogen
Looking at installation and operational costs of the ISIS facility, £1 will purchase 2×1014 800 MeV protons
Over the last 40 years, approximately 28.5 GWh of energy has been deposited on the targets
In order to produce that proton beam power, approximately 0.9 MT CO2 has been emitted (from wall-plug power)

## Slide 9: ISIS@40: Major Upgrades
1987: 6 fundamental RF cavities operational; new extract septum
1989: orbit correction system
1991: new extraction kickers
1993: diagnostic chopper, betatron Q-control system, MPS (BLM trips)
2001: move to tantalum-coated tungsten target material
2002: collimation system; new extract septum
2004: CW generator replaced with RFQ; 2nd-harmonic RF
2008: Target Station 2 first neutrons

## Slide 10: Neutron Sources

## Slide 11: Types of Neutron Sources
Many types of sources, of varying size:
Radioisotope devices (e.g spontaneous fission, alpha-emitters, photo-neutron)
  Typically capsule sized, filled with powder
  Unstable nuclei, sometimes mixed with secondary light nuclei
  Integrated fluxes ~ 106 – 109 n s-1
Plasma-based devices (e.g. Z-pinch, inertial electrostatic confinement)
  Table-top devices
  Exploit nuclear fusion reactions
  Z-pinch devices can be pulsed (single-shot, ~1012 – 1014 n/pulse)
Nuclear reactor sources
  Most ubiquitous source of research neutrons
  Very high continuous flux (1014-1015 n s-1cm-2), very reliable
  Very large installations
Spallation Neutron Sources
  Pulsed, high rep-rate
  Very large installations
  Very high flux (1016 – 1018 n s-1)
  High(ish)-energy proton accelerator driver
Cf-252 source
IEC fusor
Advanced Test Reactor core
Institut Laue-Langevin
ISIS Synchrotron
European Spallation Source
China Spallation Neutron Source
Notes: Can make a little joke here about not needing to explain what a neutron is
Alpha-emitter sources use secondary interactions with light nuclei to generate neutrons
Photo-neutrons are from high energy gamma collisons with lighter nuclei (typically Be)
Z-pinch is the self-confinement of axial plasma current by own mag field

## Slide 12: Applications of Neutrons
Industrial Uses
  Non-destructive materials testing and analysis (neutron radiography)
  Stress analysis
  Oil and gas exploration
  Silicon doping for semiconductor manufacturing
Research
  Nuclear fuel development
  Materials science
  Biomedical research
  Cultural heritage
  Neutron activation analysis
  Condensed matter research
Medical
  Cancer therapy (NCT)
  Medical imaging
  Radioisotope production
Agriculture and Environment
  Soil moisture and nutrient content
  Trace element analysis
  Crop breeding and genetics
  Nuclear waste analysis
Notes: Introduce as four main areas – maybe don’t
1.1 e.g. weld-quality, general quality control
1.4 widest adopted

## Slide 13: Spallation Neutrons
High energy proton hits a heavy nucleus, generating neutrons as debris from collision
Image credit: J Thomason

## Slide 14: Spallation Neutron Sources
ISIS Neutron and Muon Source
800 MeV proton beam
200-250 µA
50 Hz
2 Target Stations
Short pulse
Also produces muons for spectroscopy
2e16 n s-1
SNS
1 GeV proton beam
1.4 mA
60 Hz
Short pulse
1e17 n s-1
J-PARC
3 GeV proton beam
300-400 µA
25 Hz
Short pulse
Also produces muons for spectroscopy
1e17 n s-1
SINQ
590 MeV proton beam
2.3 mA
Continuous beam
Also produces muons for spectroscopy
1e17 n s-1
ESS
Still under-construction
2 GeV proton beam
62.5 mA
14 Hz
Long pulse
Will be the most powerful source in the world – 5 MW
1e18 n s-1
Honourable mentions:
CSNS
LANSCE
n_TOF

## Slide 15: Recent ISIS Upgrades

## Slide 16: Tank 4 Replacement
ISIS linac is re-purposed from Nimrod:
50 → 70 MeV injector upgrade (never realised for Nimrod)
Tanks 2 & 3 re-purposed from the Proton Linear Accelerator (PLA)
Tanks 1 & 4 constructed in 1970s (based on Fermilab design)
New Tank 4 installed during 2021 long shutdown.
Direct “plug-in” replacement of original tank
Increased reparability with new maintenance hatches
Sections bolted together (originals welded)
New drift-tube design improving TTF
Image Credit:
[1] Atomic Energy Research Establishment Harwell Photographic Group, courtesy AIP Emilio Segrè Visual Archives, Physics Today Collection
[2] Letchford, A. “UPGRADES AND DEVELOPMENTS AT THE ISIS LINAC”, LINAC2022
[3] ISIS
[1]
[2]
[2]
[2]
[3]
[3]

## Slide 17: Synchrotron RF Upgrade
Fundamental RF high-power drives (HPDs) replaced during 2021 long-shutdown
Old HPDs use pair of Burle valves: concern over obsolescence and sourcing of replacements
New HPD runs off single Thales valve
2nd-harmonic systems to receive similar update at next long shutdown
Image Credit: ISIS

## Slide 18: Target Station 1 Upgrade
Target reflector and moderator (TRAM) assembly also upgraded in 2021 long shutdown.
New TRAM provides:
Extended lifetime for TS1
Improved neutron flux, due to solid Be reflector
Easier remote handling capability
Simplified decommissioning
Commissioning began 4 Nov 2022, fully commissioned 2023
Image Credit:
[1] Coates, D. “ISIS Target Station One Upgrade Project – An overview of the
development work being undertaken to improve the Target,
Reflector and Moderator (TRaM) support systems”, J. Phys.: Conf. Ser. 1021 012059, doi :10.1088/1742-6596/1021/1/012059
[2] ISIS
[1]
[1]
[2]

## Slide 19: Ongoing and Upcoming Ugrades

## Slide 20: EPICS Migration
Current VSYSTEM-based control software has been running since the 90’s
Instrumentation has been using EPICS-based (IBEX) since 2018
Migration to EPICS currently underway:
Easy interfacing with custom python scripts
Opportunity to revisit/redesign accelerator controls and add functionality
Facilitates easy-access to time-series data of set/read values and measurements
Removal of obsolete/unused control screens

## Slide 21: Q-kicker Damping System
Head-tail instability is a significant limit on ISIS intensity.
Vertical displacement oscillation
Mode structure longitudinal
Driven by characteristic ring impedance
Multi-pronged effort to:
Characterise the instability
Diagnose the source impedance
Develop methods for mitigation
The Q-kicker is a ferrite-loaded electromagnetic kicker, already installed on ISIS, used for tune measurements.
A feedback system using a ring beam position monitor and the Q-kicker are under development, with the aim of damping vertical oscillations.
Initial tests demonstrate reduction in instability, but not fully commissioned for 50 Hz operations
Image Credit: Pertica, A. “EXPERIMENTAL DAMPING SYSTEM WITH A FERRITE LOADED
KICKER FOR THE ISIS PROTON SYNCHROTRON”, IBIC2017

## Slide 22: MEBT Installation
Currently, no matching performed between RFQ and DTL:
Limit injector efficiency (lower energy losses)
Limit injection efficiency (70 MeV losses)
Medium energy beam transport (MEBT) section planned installation during next long shutdown
Addition of quadrupole focusing, rebunching cavity, diagnostics, and electrostatic chopper
6-dimensional matching into DTL
Better operational tuning of injector
Longitudinal matching of pulse train to synchrotron RF acceptance
Image Credit:
[1] Wood, T. et. al. “The ISIS pre-injector reconfiguration”, Rev. Sci. Instrum. 87, 02B121, doi:10.1063/1.4934658
[2] Speed, J. et. al. “PRACTICAL DESIGN AND MANUFACTURING
OF THE NEW ISIS MEBT CHOPPER”, IPAC2024
[1]
[2]
[2]

## Slide 23: RF Ion Source
Current ISIS ion source is Penning-type caesiated surface-plasma H—source
Caesium limits lifetime (typically ~ 2-3 weeks):
Significant technical effort to maintain hot spares
Limits availability to neutron users
Can pose limit on machine optimisations
Examining possibilities of upgrade to a volume-plasma RF-driven source:
Significantly improved lifetime
No requirement of caesium
Potential to increase synchrotron current through longer pulse length
Required spec:
30 mA H- current
4-rms emittance < 1.5 π mm mrad
200 µs pulse length
The RF ion source installed and operating at full duty cycle. Visible components
include filter magnets (a), plasma light visible through translucent plasma chamber and cooling
jacket (b), main support housing (c), RF coil (d), cooling jacket connection manifold (e) and
ignition gun (f).
Image and text sourced from:
Lawrie, S. et. al. “Plasma commissioning in a high power external RF-coil volume-type H− ion source”, J. Phys.: Conf. Ser. 2244 012033

## Slide 24: ISIS-II

## Slide 25: ISIS-II Megawatt Upgrade
Europe (incl. UK) is a world leader in neutron-based science
Decommissioning of reactor sources of neutrons
Potential European “neutron drought”
ISIS-II vital to maintain European competitiveness with Japanese (J-PARC) and American (SNS) short-pulse neutron sources
2019
2021
2027
2031
2040
Phase 1
Phase 2
Feasibility, design studies and R&D
Integrated facility technical design
ISIS-II construction
Phase 1.1
Physics design
Small-scale prototypes
Phase 1.2
Physics design
Large-scale prototypes
Phase 3
ESFRI Neutron Scattering Facilities in Europe Report (2016)
“…by far the most cost effective solution would therefore be to build a MW-class short pulse facility at ISIS, reusing existing infrastructure and facilities as well as drawing upon on-site competences. The current facility could operate until the new facility is operational with its initial suite of instruments.”
Sentiment echoed in UKRI Infrastructure Opportunity Report (2023)
ISIS-II Working Specifications
1.25 MW proton accelerator
1.2 GeV beam on target
0.1% beam-loss
Conventional Ring (RCS, AR) and FFA options being explored
Special focus on
Sustainability of the future machine
Ensuring health of the neutron user community during construction phase

## Slide 26: ISIS-II “Conventional” Rings
Completed exploratory designs Feb 2022
  2 x Rapid Cycling Synchrotron
  2 x Accumulator Rings
New sustainability-focussed designs under investigation
Lattice Design
Working Point
Injection Straight & Foil Temperature
Closed Orbit Correction
Collimation Simulations
Longitudinal Simulations
3D Simulations
Life-Cycle Analysis

## Slide 27: ISIS-II “Conventional” Rings R&D
Understanding loss mechanisms key to success of ISIS-II design
Reliable prediction of loss (~0.01%)
Understanding of beam halo dynamics
Origin of losses
Likely need to develop custom beam dynamics and design codes
Benchmark against other codes
Benchmark against measurement
Tune Plane Measurements
Measured
ORBIT
Transverse Profiles
  Frozen space charge halo
Chromaticity
  Non-linear components
Beam Instability Studies

## Slide 28: ISIS-II FFA Option
FFA-option aims for
Sustainability
Reliable operation
Capacity
Capability
Currently, proof-of-concept machine under development (FETS FFS)
Platform for development of ISIS-II FFA driver
Experimental study of injection painting, orbit correction, resonances, collimation, etc.

## Slide 29: ISIS-II FFA R&D: FETS FFA
3 – 12 MeV
4 – 4.4 m radius
50 Hz beam repetition
3x1011 protons per bunch
30 W power
Space charge tune shift ~-0.35
Still a work in progress
Completion of CDR by March 2025
HV-testing underway for RF cavity magnetic alloy and ferrite cores
Prototype BPM and wire scanner tests at KURNS

## Slide 30: ISIS-II FFA R&D: Beam Stacking
Beam stacking is a method for increasing the circulating current in FFA
Inject, accelerate, and de-cohere beam at top energy
Inject and accelerate second beam
Stack in longitudinal phase space
Experimental verification of beam stacking at KURNS FFA:
Schottky analysis of incoherent signals
Determine energy and energy spread stacked beams
Potential use at ISIS as diagnostic tool
Studies underway to repeat experiment on the ISIS RCS

## Slide 31: Summary
ISIS has seen many changes over 40 years
  Numerous challenges encountered
  Numerous upgrades
  Lots of re-purposed equipment
  Huge collaborative effort
ISIS is still one of the most productive neutron sources in the world
Continued development and refurbishment are aimed at extending ISIS’ operational lifetime
ISIS (along with FETS) will be the test-bed upon which ISIS-II is developed
Several design options still under consideration for ISIS-II, each with its own challenges and research questions