## Slide 1: Emittance Measurements and Beam Optics Matching for CLARA
ASTeC Accelerator Physics Group STFC Daresbury Laboratory mark.johnson@stfc.ac.uk
Mark Johnson | IOP Particle Accelerators and Beams Conference 2025

## Slide 2: Outline
CLARA Overview
Software Development
Emittance Measurements
Outlook & Conclusions

## Slide 3: CLARA Key Parameters
High-brightness linear accelerator at STFC Daresbury Laboratory, with a total length of ~80 m
Among the most advanced medium-energy electron beam facilities in Europe when complete
Dedicated shielded Full Energy Beam Exploitation (FEBE) user area, with access to 250 MeV/c electron beam and 100 TW laser
Parameter | Low Charge | High Charge
Beam momentum pz [MeV/c] | 250 | 
Bunch Charge Q [pC] | 5 | 250
RMS Bunch Length σt [fs] | 50 | 100
RMS Energy Spread σE [%] | < 1 | < 5
RMS Spot size σx,y [µm] | 20 | 100
Emittance εx,y [mm mrad] | 2.0 | 5.0
Above: Nominal “day one” CLARA beam parameters for user experiments at the FEBE interaction points
Below Left: Schematic of the CLARA accelerator (not to scale)

## Slide 4: CLARA Status
CLARA is currently undergoing technical commissioning with beam at its nominal momentum (250 MeV/c)
  Testing of RF, diagnostics, and controls,
  Commissioner training,
  High-level software development
Beam commissioning and machine optimisation during the second half of 2025
All results shown here are PRELIMINARY
CLARA Commissioning Talk Tom Pacey Wednesday 14:40

## Slide 5: CLARA Key Dates (2025)
March 17th First beam since CLARA shutdown (2022 – 2024)
April 2nd Beam threaded to nominal momentum (250 MeV/c)
June 6th First beam accelerated using Linac 1
June 19th Bunch compression demonstrated using the VBC and transverse deflecting cavity (TDC)

## Slide 6: CLARA Software
Significant software development activity during the recent CLARA shutdown (2022 – 2024)
Updated python-based tools underpin most scientific software:
  CATAP Accelerator middle layer, used for directly interacting with machine hardware
  CLARA Software Tools High-level interface with standardised procedures and analysis for physics measurements
Hardware-based
Physics-based
Operators
Accelerator Middle Layer (CATAP)
High-level Interface (CLARA Tools)
EPICS-Based Control System
Below: Block diagram showing the various layers of the CLARA software environment

## Slide 7: High-Level Software
CLARA tools is a high-level python package designed to support physics measurements on CLARA. It includes:
Standardised code for common procedures:
  Quadrupole scans,
  Trajectory correction,
  RF cresting,
Utilities for experimental data handling,
Analysis functions for common data types
Above: Reference documentation for the CLARA Tools python package

## Slide 8: Beam Optics Measurements
A range of beam optics measurements will be critical for CLARA beam commissioning:
  Optimisation of the emittance,
  Matching to the machine’s design optics,
  Phase space reconstruction, for accurate simulations and model validation
Standardised high-level software for:
  Quadrupole scans
  Twiss calculations
  Beam optics matching
Increasing Phase Space
Resolution
Simple Quadrupole Scans
Multi-magnet Quadrupole Scans
Machine Learning Methods
Phase Space Tomography

## Slide 9: Simple Quadrupole Scans
Single-magnet quadrupole scans offer the fastest, simplest measurement of the beam optics.
Measure the RMS beam size at a YAG screen while varying the quadrupole strength
Large emittance uncertainty (typically ≳ 10%) due to small beam sizes at the focal points

## Slide 10: Multi-Magnet Quadrupole Scans
Vary several quadrupoles to maintain a fixed beam size while constraining the transverse phase space [1, 2]
Multi-quadrupole scans can offer significantly smaller emittance uncertainties
Sensitive to transverse coupling in the beam’s 4D covariance matrix
[1] E. Prat and M. Aiba, Phys. Rev. Accel. Beams 17, 052801 (2014)
[2] A. Wolski et al., Phys. Rev. Accel. Beams 23, 032804 (2020)

## Slide 11: Multi-Magnet Quadrupole Scans
Vary several quadrupoles to maintain a fixed beam size while constraining the transverse phase space [1, 2]
Multi-quadrupole scans can offer significantly smaller emittance uncertainties
Sensitive to transverse coupling in the beam’s 4D covariance matrix
[1] E. Prat and M. Aiba, Phys. Rev. Accel. Beams 17, 052801 (2014)
[2] A. Wolski et al., Phys. Rev. Accel. Beams 23, 032804 (2020)

## Slide 12: Beam Substructure
Analysis based solely on the beam size neglects information about the beam substructure.
Phase space tomography uses full beam images to reconstruct the charge distribution in 4D phase space (x, px, y, py)
Recent machine learning advances [1, 2] have led to faster, higher resolution tomography methods
[1] A. Wolski et al., Phys. Rev. Accel. Beams 25, 122803 (2022)
[2] R. Roussel et al., Phys. Rev. Accel. Beams 27, 094601 (2024)
Above and Left: Recent CLARA beam images showing significant substructure

## Slide 13: Machine Learning Methods
Generative Phase Space Reconstruction (GPSR) is a new technique developed by Ryan Roussel and others [1, 2]
It uses differentiable simulations [3] to train a neural network and “learn” a phase space from experimental beam images
GPSR reconstructs high resolution phase spaces for later use in simulations
Below: Diagram showing the GPSR method for reconstructing phase space distributions from experimental data. Adapted from [2]
[1] R. Roussel et al., Phys. Rev. Lett. 130, 145001 (2023)
[2] R. Roussel et al., Phys. Rev. Accel. Beams 27, 094601 (2024)
[3] J. Kaiser et al., Phys. Rev. Accel. Beams 27, 054601 (2024)

## Slide 14: CLARA Reconstructed Phase Space
4D phase space (x, px, y, py) reconstructed from 64 beam images at the end of the CLARA straight-on line
  Momentum: 172 MeV/c
  Bunch charge: 30 pC
Significant beam substructure due to sub-optimal machine setup without Linac 1
Reconstructed emittances: εn,x = 1.7 µm, εn,y = 5.0 µm
Below: Projections of the 4D transverse phase space reconstructed from CLARA beam images
We have already demonstrated GPSR using real CLARA data!

## Slide 15: Reconstructed Beam Profiles
EXPERIMENTAL
PREDICTED
Trained Neural Network
Reconstructed Phase Space
Simulation New Quadrupole Settings
Q1
Q2
Q3
Q4
Q5
Q6
Q7
YAG
Predicted Beam Image(s)

## Slide 16: Conclusions
CLARA is currently undergoing technical systems commissioning with beam
The development of standardised software should lead to rapid progress during beam commissioning
We are deploying advanced ML techniques for high-resolution phase space measurements
Special Thanks To…
Alex Brynes, James Jones, Matt King and Euan Gepp ASTeC, STFC Daresbury Laboratory, UK
Andy Wolski Department of Physics, University of Liverpool, UK

## Slide 18: Backup Slides

## Slide 19: CLARA Beam Parameters
Parameter | Commissioning |  |  | Machine Development | 
 | Low Charge | High Charge |  | Low Charge | High Charge
Beam momentum pz [MeV/c] | 250 |  |  | 250 | 
Bunch Charge Q [pC] | 5 | 250 |  | 5 | 250
RMS Energy Spread σE [%] | < 1 | < 5 |  | 0.1 | 1
RMS Bunch Length σt [fs] | 50 | 100 |  | ≪ 50 | < 50
RMS Spot size σx,y [µm] | 20 | 100 |  | ~ 1 | 50
Emittances |  |  |  |  | 
εn,x [mm mrad] | 2.0 | 5.0 |  | < 1 | < 5
εn,y [mm mrad] | 2.0 | 5.0 |  | < 1 | < 1
Above: Expected CLARA beam parameters at the FEBE interaction points (IP). Parameters are shown for initial commissioning, and those targeted following required periods of machine development [1].
[1] E. W. Snedden et al., Phys. Rev. Accel. Beams 27, 041602 (2024)