Title
Photon detection
with CMOS sensor
for fast imaging
PSD 2008, Glasgow, September 1-5
Jerome Baudot, IPHC Strasbourg
in collaboration with IPN-Lyon
R.Barbier, E. Chabanat, P. Depasse,
W. Dulinski, N. Estre, M. Winter
CMOS sensors for Min.Ion.Part.
Single photon with EBCMOS
First tests for biology

---
Basic principle of CMOS sensors
Technology
  - Industry standard for ICs
  - Require an “epitaxial layer”
    10-20 mm thick
Monolithic sensors
  - Tow layers in a single object: sensing + reading-out
  - Many integration advantages
[Speaker Notes: About Mimosa serie : > 30 chips produces]

---
Basic principle of CMOS sensors
Developments since 1999
  - Originated in IPHC-Strasbourg
  - >30 sensors produced
  - Including ~MegaPixels sensors
    of few cm2
“Standard” performances for Single charge particle detection
  - Analog readout of each pixel
  - Techno. AMS 0.35 um OPTO
    - Noise ~ 10-15 e-
    - Signal/Noise (MIP) > 15
    - Efficiency ~ 100%, fake rate ~ 10 -5/pixel
    - Spatial resolution
      ~ 1 um (10 um pitch) -> 3 um (40 mm pitch)
  - Room temperature operation
Technology
  - Industry standard for ICs
  - Require an “epitaxial layer”
    10-20 mm thick
Monolithic sensors
  - Tow layers in a single object: sensing + reading-out
  - Many integration advantages
[Speaker Notes: About Mimosa serie : > 30 chips produces]

---
Readout possibilities
Readout speed
  - Analog readout limited ~ ms
    for MegaPixels sensors
  - Column parallel readout
    - ~100-200 ns / column
      readout ~100 ms for 1000 rows
    - Requires discrimination/ADC
    - Digital readout

---
Readout possibilities
Readout speed
  - Analog readout limited ~ ms
    for MegaPixels sensors
  - Column parallel readout
    - ~100-200 ns / column
      readout ~100 ms for 1000 rows
    - Requires discrimination/ADC
    - Digital readout
Digital Mimosa serie: M8, 16, 22
  - Mimosa 22 (2007)
    - 576x128 pixels, 18.4 mm pitch
    - 100 ms readout time
  - Suze 01 (2007)
    - Zero-suppression logic only
    - 64 columns treatment in 160 ns
    - Validated with test patterns
PRELIMINARY
results from SPS beam test

---
Sensitivity
Low energy particles
  - Electrons of few keV,
    Visible photons
  - Short range in IC material:
    can't reach the sensitive volume !
  - Back-thinning (industrial process)
    + Post-processing of sensitive volume back-plane
  - back-illumination

---
Sensitivity
Low energy particles
  - Electrons of few keV,
    Visible photons
  - Short range in IC material:
    can't reach the sensitive volume !
  - Back-thinning (industrial process)
    + Post-processing of sensitive volume back-plane
  - back-illumination
Back-thinned Mimosa 5
  - MegaPixel sensor with 17 mm pitch
  - Back-tinning within SUCIMA project
  - HV accelerated electrons bombarding
  - applications for electron imaging not covered here
G.Deptuch

---
Photon detection
g rays
  - No efficiency, bu seeable
X rays
  - > 10 keV: no efficiency
  - Few keV range
    - % level efficiency
    - Energy resolution ~ %
55Fe, 5.9 keV
Mimosa 18

---
Photon detection
g rays
  - No efficiency, bu seeable
X rays
  - > 10 keV: no efficiency
  - Few keV range
    - % level efficiency
    - Energy resolution ~ %
Visible photons
  - Std camera applications for visible light
  - For much less intense source:
    back-illumination
    - Back-thinned Mimosa 5
    - In-pixel focused infrared led (1063 nm)
Still looking for applications
55Fe, 5.9 keV
~900 e-
Back-thinned Mimosa 5
Mimosa 18

---
Single photon detection: EBCMOS
A new hybrid photo-detector:
Electron-Bombarded CMOS Sensor
  - Use back-thinned Mimosa 5
    - 1024x1024 pixels, 17 mm pitch
    - Readout time 27 ms (~30 frames/sec)
  - Combined with photocathode S20-type
    - QE @ 532 nm ~ 15%
  - Vacuum tube integration by PHOTONIS,
    first prototypes june 2007
EBMIMOSA-5

---
EBCMOS performances
Characterization @ IPN-Lyon
  - Optical bench: focalized laser diode
  - Photon-counting calibration
  - PSF studies
Performances
  - Dark count rate 100 Hz/mm @ 10 C
  - Spatial resolution 11.6 mm (@ 540 nm)
  - Dynamic 1-30 photo-electrons/pixel

---
EBCMOS performances
Characterization @ IPN-Lyon
  - Optical bench: focalized laser diode
  - Photon-counting calibration
  - PSF studies
Performances
  - Dark count rate 100 Hz/mm @ 10 C
  - Spatial resolution 11.6 mm (@ 540 nm)
  - Dynamic 1-30 photo-electrons/pixel
Known problems
  - Ion feed-back
  - Back-scattering ~ 18%
  - Low to moderate quantum efficiency
    (restricted wavelength bandwith)

---
Fluorescence microscopy
In life sciences
  - Image cells/molecules
    in 3D+time dynamics
  - Use fluorescent (all colors) proteins on defined targets
  - Detector used:
    - CCD: 2D but sensitivity limited
    - EMCCD: 2D+single photon but speed limited (~30 frames/sec)
    - PMT: single photon but not 2D
Confocal
microscopy
Epifluorescence
microscopy,
if no pinhole

---
Fluorescence microscopy
In life sciences
  - Image cells/molecules
    in 3D+time dynamics
  - Use fluorescent (all colors) proteins on defined targets
  - Detector used:
    - CCD: 2D but sensitivity limited
    - EMCCD: 2D+single photon but speed limited (~30 frames/sec)
    - PMT: single photon but not 2D
Where can EBCMOS helps ?
  - for single photon sensitivity
  - for fast 2D imaging
    from 50 and beyond 1000 images/sec
    - Decrease photodamage & photobleaching
    - Observe a fast dynamic
    - Build real-time 3D pictures
Confocal
microscopy
Epifluorescence
microscopy,
if no pinhole
Spinning disk
microscope

---
EBMIMOSA-5 tests with biologists
Biological samples from
  - EBMIMOSA-5 operation by IPNL & IPHC
  - IGBMC-Strasbourg, Angela Giangrande & Jean-Luc Vonesh
    - Lilly root cells
    - Latex beads (~100 nm)
  - ENS-Paris, Maxime Dahan
    - Quantum dots fixed on membranes of hela cells

---
EBMIMOSA-5 tests with biologists
Biological samples from
  - EBMIMOSA-5 operation by IPNL & IPHC
  - IGBMC-Strasbourg, Angela Giangrande & Jean-Luc Vonesh
    - Lilly root cells
    - Latex beads (~100 nm)
  - ENS-Paris, Maxime Dahan
    - Quantum dots fixed on membranes of hela cells
zoom+filtering
Sensitivity / contrast
  - Better than CCD
  - Similar to EMCCD (for green fluorescence)
Spatial resolution
  - s of distribution after 30 frames and after microscope magnification
  - 275 nm for EBMIMOSA-5
    ( 145 nm with CCD of 6.5 mm pixel pitch)
3 indivual beads
ZOOM

---
On-going developments
CMOS sensor
  - New chip LUCY fabricated in 2007
    - 400x800 pixels, 10 mm pitch
    - Analog readout on 8 outputs
      readout time 1 ms (1000 frames/sec)
    - Std version OK (from 55Fe test), noise~8 e-
    - Back-thinned version expected Sept.08
Vacuum tube for EBCMOS
  - Work on photocathode by Photonis to ↗QE
  - Reduced gap ~ 600 mm
    to improve spatial resolution
Data acquisition
  - 1 MegaPixels @ 40 frames/sec ~ 300 Mbits/s !
  - IPN-Lyon develops on-board (hit) analysis
    + Gbits/s PC-connection
  - Goal: 1000 frames/sec on 320 kPixels (0.3 cm2)
Data analysis
  - Various image treatments
    to be evaluated
    - Filters
    - Tracking

---
Summary & outlooks
CMOS sensors from single charged particle tracking
  - Offer various sensitivity for photon imaging
    - Low efficiency for X-rays but few% energy resolution @ few keV
    - Single-photon when back-thinned + hybridized with a photocathode
  - Offer fast readout with on chip signal treatment
First applications expected:
  - Single photon positionning with EBCMOS
    for fluorescence microscopy in biology
  - Proof of principle passed
  - Real measurement to come this year

---
Thanks to
IPN -Lyon
  - Sylvain Vanzetto / Georges Maurelli / Rodolphe Della Negra / Cyrille Guérin / Didier Bon / Pierre-Yves Solane
IPHC-Strasbourg
  - Andrea Brognia / Auguste Besson / Claude Colledani / Rita De Masi / Guy Doziere / Christina Dritsa / Andrei Dorokhov / Gilles Clauss / Jean-Charles Fontaine / Mathieu Goffe / Abdelkader Himmi / Christine Hu / Kimo Jaaskelainen / Michal Koziel / Mathieu Goffe / Alexandre Merlin / Frederic Morel / Nicolas Pillet / Alexandre Shabetai
PHOTONIS SA
  - Henk Verboom / Patrick Clauzel /Carlo Kayser / Nicolas Laurent

---
! BACKUP SLIDES !

---
CMOS charge collection principle

---
CMOS analog readout principle

---
EBCMOS characterization at IPN-Lyon
50X LWD Mitutoyo
XYZ
ebcmos

---
EBCMOS contrast study / EMCCD
From R.Barbier & N.Estre
EBMI5 Tint=27 ms
Cascade 2 / EMCCD Tint=30 ms : Gmax=1000
C3
C3
C2
C2
C1
C1
C= (Imax-Imin)/(Imax+Imin)
Imean = 7400
Imax=9400 Imin= 7300 C= 0,13
Imax=18000 Imin= 8000 C= 0,38
SNRmean = 30
C3
SNRmax=48 SNRmin= 28 C= 0,26
C2
SNRmax=175 SNRmin=45 C= 0,59
C1

---
Fluorescence microscopy applications
where 2D localization of single photons
is required
PhotoActivated Localization Microscopy
E.Betzig, Science vol 313, 2006