## Slide 1: LHC Detectors overview Emphasis on ATLAS
Beniamino Di Girolamo
CERN

## Slide 2: Outline
The LHC experiments and their sub-detectors
The details: I had to make a choice
  Emphasis on vertex detectors and intermediate trackers
  Little on data acquisition and trigger, computing
    Extensive bonus material to cover some of these extremely important aspects
  Trying to show intriguing aspects. More classical performance in many talks in this conference
Chose to show a few physics results to illustrate how well the detectors are functioning
Few words on future upgrades
Conclusions
What did not fit here you can be found in the Bonus Material

## Slide 3: A variety of technologies
The aim of this talk is to give a feeling of the LHC detector performance, but…
…also show you how many different solutions have been found using a variety of technologies for Position Sensitive Detectors and more
LHC instruments could easily fit all detectors described in instrumentation books
At the end we will also see what is foreseen in future and no surprise: exploiting even more techniques
  And even more acronyms

## Slide 4: The LHC experiments
TOTEM
LHCf

## Slide 5
ATLAS

## Slide 6: Requirements
ATLAS and CMS to be as “general purpose” as possible and as hermetic as possible
  All possible physics channels from known to unknown
  The dream of measuring everything with a surrounding sphere
ALICE measuring on a MeV to GeV dynamic range
  Heavy ions focus
  Paying attention to material budget
LHCb dedicated to b physics
  A forward detector
TOTEM and the ATLAS forward detectors
  Looking at luminosity, diffractive physics
LHCf looking at p0 to calibrate high energy cosmic rays experiments
  A nice example of variety of technology: two almost identical detectors

## Slide 7: General purpose detectors
A closer look

## Slide 8: The dream of full coverage

## Slide 9: ATLAS
44 m
25 m
7000 tons

## Slide 12: CMS
15 m
12500 tons
ECAL
HCAL
21.6 m
TRACKER
Muon System Endcap
(CSC+RPC)
IRON YOKE
3.8T Solenoid

## Slide 13: Specialized detectors
A closer look

## Slide 14: ALICE
16 m wide
26 m long
10000 t

## Slide 15: Main facts about ALICE
Many sub-detectors!
Design evolved with time and knowledge from running HI physics detectors
Measurements from MeV to GeV
  Low material budget!
Need of particle identification
Need of muon tracking with a fancy absorber
Extremely light supporting structure for the detectors inside the 0.5 T magnet

## Slide 16: LHCb

## Slide 17: Main facts about LHCb
B and D physics at the LHC are forward/backward
  The interacting partons have different x
  The produced pair are boosted forward or backward, together
    The detector can look only at one side, and get both b, very useful as we have both the signal b and the tagging b in the acceptance
Single arm spectrometer
  Very good vertex detector
  Dipole magnet for accurate
  momentum measurement
  Good particle ID over a large
  momentum range
  Should fit in an existing LEP cavern...

## Slide 18: A typical LHCb event
The concept works!

## Slide 19: Forward detectors
A closer look

## Slide 20: ATLAS Forward
10.6 < | η | < 13.5
| η | > 8.3
5.6 < | η | < 5.9
2.1 < | η | < 3.8
SciFi tracker
W+quartz rods calorimetry
Cherenkov rad.
Scintillators

## Slide 21: ATLAS: ALFA detector
4m
~ 237m
left & right
overlap detectors
Roman Pot
main detector
station
system – 4 stations, 2 (A-side) + 2 (C-side)
each station – 2 Roman Pots approaching the beam vertically – from below and above
1 main detector and 2 overlap detectors in each Roman Pot; tracker-type detectors

## Slide 22: ATLAS: ALFA results
Results from data taking at b* = 90 m optics, detectors at 10 s from the beam (~ 7 mm)

## Slide 23: TOTEM
~14 m
CMS
T1: 3.1 < |h| < 4.7
T2: 5.3 < |h| < 6.5
10.5 m
T1
T2
HF
Inelastic Telescopes:
Roman Pots:
RPs220
RPs147
Same scheme on both sides of IP5
T1: CSCs
T2: GEMs
Si strips

## Slide 24: TOTEM: Elastic pp scattering
TOTEM Note: CERN-PH-EP-2011-101
Differential cross section for pp scattering
Confirmed the move of the diffractive dip at increasing √s
  First look at pp since ISR time
  B increases in exp(-B|t|)
  Power law confirmed for higher t
Higher the t: deeper the look inside the proton
It differs from models
  Getting really interesting

## Slide 25: LHCf
W sampling shower calorimeters (44 X0 and 1.7 l)
At ± 140 m from IP1 in TAN absorbers, only neutral particles
Tungsten and scintillator layers
Position sensitive layers
  Scintillating fibers with MAPMT readout on one side and Si sensors on the other

## Slide 26: Vertex detectors
A lot of Silicon

## Slide 27: Vertex detectors
Silicon has been the choice of the experiments
Large pixel detectors are used in ALICE, ATLAS, CMS
A strip detector is used by LHCb: the Vertex LOcator
Silicon strip layers are deployed at larger radii
  ATLAS uses a straw-tubes tracker as intermediate tracker before calorimetry
Concentrating on Pixel: hybrid pixels for all
Requirements:
  Radius for the innermost layer and radii of the rest
  Number of layers
  Readout electronics
  Granularity
  Radiation tolerance
  Material budget (for all, but ALICE has special needs)

## Slide 28: The Pixel + VELO detectors

## Slide 29: The Pixel master table
Even though it seems IBL would have less material than ALICE Pixel, in reality ALICE has done an enormous effort to reduce material on services. ALICE has 13 X0 up to the end of the TPC!
The type of sensors differ, p-in-n for ALICE, n-in-n for ATLAS and CMS and LHCb VELO (with one n-in-p module installed)
All using 250 nm CMOS ASICs
The operating temperatures (0C) are +25 (ALICE), -20 (ATLAS), +18 (CMS), -5 (VELO)
* IBL: decided to aim at using two technologies: planar sensors (200 mm) and 3D sensors (230 mm)
 | Pixel size |  | Sensor Thickness (X0) | ASIC Thickness (X0) | Layers |  | beam-pipe inner radius | spatial resolution
 | z [mm] | rf [mm] | [mm] (%) | [mm] (%) | [#] | radii [mm] | [mm] | [mm]
ALICE | 425 | 50 | 200 (0.21) | 150 (0.16) | 2 | 39-76 | 29 | 100 (z) 12 (rf)
ATLAS | 400 | 50 | 250 (0.27) | 180 (0.19) | 3 | 50.5-88.5-122.5 | 29 | 115 (z) 10 (rf)
IBL | 250 | 50 | 200 (0.21)* | 100 (0.11) | 1 | 33.25 | 23.5 | 79 (z) 10 (rf)
CMS | 150 | 100 | 285 (0.30) | 180 (0.19) | 3 | 44-73-102 | 29 | ~ 15

## Slide 30: The outer layers
CMS has a full silicon inner detector: 2 tons!
ATLAS decided to invest in particle identification with straw tubes and radiators for transition radiation measurement
  Advantage of inclusive isolated electron measurement, powerful tool for electron and photon studies in conjunction with e.m. calorimetry
ALICE added silicon drift detectors between pixel and strips: need of extend 2-dim measure in radius
Overall the biggest Inner Detectors ever built

## Slide 31: ATLAS Inner Detector
2 T solenoidal magnetic field
Acceptance ||<2.5 (transition radiation tracker ||<2)
Momentum resolution (pT)/pT = 0.05% pT [GeV/c]  1%
Impact parameter resolution (0.25<||<0.5) (d0) = 10 m 140 m / pT [GeV/c]

## Slide 32: CMS Strip tracker
Tracker Inner Barrel (TIB ): 4 layers: 2 Rf (2D), 2 Rf-Stereo (3D)
Tracker Outer Barrel (TOB): 6 layers, : 4 Rf (2D), 2 Rf-Stereo (3D)
Tracker Inner Disks (TID ): 3*2 disks, : 1 Rz (2D), 2 Rz-Stereo(3D)
Tracker EndCap (TEC): 9*2 disks, : 4 Rz (2D), 3 Rz-Stereo(3D)
Modules:
  3112 + 3024 Thin modules (ss +ds)
  5496 + 3600 Thick modules (ss +ds)
Silicon:
  6,136 Thin sensors = 48m2
  18,192 Thick sensors = 162m2
210 m2 of silicon microstrip sensors
FE Electronics:
75,376 APV chips
9,648,128 strips  electr. Channels
Each Track has at least
10 high precision measurements for Pt and 4 in Q
Coverage: | h | < 2.5

## Slide 33: ALICE ITS
ITS: 3 different silicon detector technologies
Strip Drift Pixel
Material budget measured with  conversions

## Slide 34: The silicon detectors master tables
 | Strips | Layers |  | spatial resolution
 | pitch [mm] | [#] | radii [mm] | [mm]
ALICE | 95 | 2 | 380-430 | 830 (z) 20 (rf)
ATLAS | 80 | 4 | 299 to 514 | 580 (z) 17 (rf)
CMS | 80-183 | 3 | 255 to 1080 | 23-52 (rf)
 | Pixel | Drift | Strips |  | Pixel | Drift | Strips
 | Area [m2] |  |  |  | # channels [x 106] |  | 
ALICE | 0.2 | 1.3 | 5 |  | 9.8 | 0.13 | 2.6
ATLAS | 1.8 |  | 61 |  | 80.4 |  | 6.3
CMS | 1 |  | 198 |  | 66 |  | 9.3
VELO |  |  | 0.2 |  |  |  | 0.17

## Slide 35: ATLAS Pixel having fun with tracks
Secondary vertices map for hadronic interactions
  Imaging of the detector
Detector drawing
How data describes the reality!

## Slide 36: dE/dx in Silicon: ATLAS Pixels

K
p
d
K+K-
Mass determination inverting Bethe-Bloch energy loss relation
s ~ 12%

## Slide 37: PID in ALICE
‘stable’ hadrons (p, K, p): 100 MeV < p < 5 GeV (several 10 GeV)
  dE/dx in silicon (ITS) and gas (TPC) + time-of-flight (TOF) + Cherenkov (HMPID)
decay topologies (K, L, WD)
  K and L decays beyond 10 GeV
leptons (e, m), photons h,p0
  electrons TRD: p > 1 GeV, muons: p > 5 GeV, p0 in PHOS, EMCAL: 1 < p < 80 GeV
PHOS, EMCAL

## Slide 38: ALICE TPC: dE/dx
10 bit ADC: Dynamic range up to 26×MIP. s ~ 5%

## Slide 39: ATLAS TRT: transition radiaton at work
Barrel shown here, same for endcaps
ALICE has equally nice results

## Slide 40: A quick look at results
“It will be hard to make everything work quickly”

## Slide 41: ATLAS status
Chart: 
| Pixel | SCT | TRT | Lar EM Calo | Tile Calo | Had End-Cap Lar | Forward Lar | LVL1 Calo Trigger | LVL1 Muon RPC Trigger | LVL1 Muon TGC Trigger | MDT Muon | CSC Muon | RPC Barrel Muon | TGC End Cap Muon
Channel Live Fraction | 0.969 | 0.991 | 0.975 | 0.995 | 0.979 | 0.996 | 0.998 | 0.999 | 0.995 | 1 | 0.998 | 0.985 | 0.97 | 0.984

## Slide 42: ATLAS data taking efficiency
Max inst lumi. : 2.37x1033 cm-2 s-1
Delivered luminosity: 2.68 fb-1
ATLAS ready recorded: 2.55 fb-1
Preliminary uncertainty on 2011 luminosity 4.5%
Fraction of good quality data per detector
Data taking efficiency: ~95%

## Slide 43: ATLAS pile-up
Average Pile Up in 2011 : 6.0 Coll/BC
Max Pile Up : 10-12 Collisions/BC
Issue for:
  Missing energy
  Lepton Isolation (mainly calorimetric)
  Jet Energy Scale and resolution
  Vertexing
  CPU time and event size
Event with 11 vertices and 1 Z

## Slide 44: Few event displays

## Slide 46: CMS ECAL, photon and electron performance
Di-electron mass spectrum

## Slide 47: CMS tracking and muon performance
Thanks to high flexibility of trigger system!
Excellent tracking resolution and alignment shows in resolution of Mmm

## Slide 48: ATLAS: SM cross-sections

## Slide 49: ATLAS Higgs cross-sections

## Slide 50: ATLAS: H->gg
Cleanest channels for very low Mass Higgs and simple signature
Needs:
  Good di-photon mass resolution
  Determination of primary vertex
  Good Photon Id.
  g/Jet, g/p0 discrimination
Need to understand backgrounds with high precision with Data Driven techniques
  QCD gg production
  g-Jet and Jet-Jet production
No indication of significant excess, therefore limits on SM Higgs production cross-section

## Slide 51: ATLAS Higgs combination
The combined upper limit on the SM Higgs boson s divided by the SM expectation vs. mH indicated by the black solid line
SM mH excluded at 95% C.L.:
146 < mH < 232 GeV
256 < mH < 282 GeV
296 < mH < 466 GeV
Fun just starting!

## Slide 52: Thinking about the future
Yes, already

## Slide 53: LHC upgrades and how detectors follow

## Slide 54: ATLAS: IBL in Phase0
The major project of Phase0
  Installation of a reduced diameter beam pipe (47 mm) and the innermost Pixel layer: the Insertable B-Layer
Improvement of b-tagging capabilities and redundancy to cope with future occupancies and radiation damage

## Slide 55: ATLAS IBL
Innovative
  Reduced thickness for sensor and ASIC
  Planar and 3D silicon sensors

## Slide 56: Upgrades in Phase 1 and 2
ATLAS and CMS: increase in interaction rates and keeping an eye on physics results
  Phase 1
    ATLAS: Muon system, L1&2 trigger, Calorimetry
    CMS: Pixel, trigger, DAQ, beam instrumentation and luminosity, infr.
  Phase 2
    ATLAS: Trigger, some Muon chambers, endcap and forward calorimetry, calorimeter readout for trigger, new Inner Detector
    CMS: new Inner Detector, readout of Muon system, calorimetry readout, trigger electronics
ALICE and LHCb: enlarge measuring capabilities
  ALICE: Inner Tracker, Muon Forward Tracker, new forward calorimetry, particle identification improvement, TPC readout upgrade, trigger and DAQ
  LHCb: move to 40 MHz readout, new VELOPIX, new Si tracker, PID improvements at low momenta, calorimeter readout
  Both aiming at Phase 1

## Slide 57: When being puzzled is good
30 March 2010
6 December 2009
We did again, √s = 7 TeV
I thought we we’re getting used to it
I was worrying for few moments then all went fine
Switching on 80M Pixel for the first time, √s = 0.9 TeV
Is that so simple?
I looked clearly worried to see beam effects
ATLAS channels increased by one order of magnitude

## Slide 58: Conclusions
I’m greatly indebted to the Organizing Committee
  Preparing such a talk is very challenging, but extremely interesting
I’m greatly indebted to all LHC experiment colleagues
  Many provided tons of material, impossible to mention all (already too many slides)
Lessons learned: we were too worried that between switching on and getting results too much time was needed
  It went much smoother
  We’re getting lots of results
LHC performed really well and our DAQ, Trigger and Computing have been following well the challenge
Now: waiting for even more results!

## Slide 59: ATLAS&CMS looking forward

## Slide 60
Higgs in ATLAS

## Slide 61
Higgs in CMS