## Slide 1: Development of the Balloon-Borne sub-MeV Gamma-ray Compton Camera Using an Electron-Tracking Gaseous TPC and a Scintillation Camera
Tetsuya Mizumoto
Department of Physics, Graduate School of Science, Kyoto University
contents
About SMILE experiment and the Electron Tracking Compton Camera (ETCC)
(30 cm)3 prototype ETCC
New readout circuit of the scintillation camera for SMILE-II

## Slide 2: Motivation (sub-MeV/MeV gamma-ray astronomy )
Nucleosynthesis
SNR : Radio-isotopes
Galactic plane : 26Al・60Fe
Annihilation
Acceleration
GRB, Jet (AGN) : Synchrotron
+ Inverse Compton
Strong Gravitational Potential
Black Hole : accretion disk, p0
Etc.
Gamma-ray Pulsar, solar flare
The observation of continuum component is also important.
Where are MeV gamma-ray objects?
There are many background events which obstruct the observations.
Requirements for
the next-generation detectors are …
Wide-band detection
Large Field of View
Background rejection
Sensitivity
Astro-H
1mCrab
EGRET
Air
Cherenkov
Fermi
～１°
Good
Bad
erg / (cm2 sec)
Obs. Time : 106 sec

## Slide 3: Electron-Tracking Compton Camera (ETCC)
1 photon  direction + energy
Large fielf of view (~3str)
Kinematical noise rejection (a)
Gaseous TPC : Tracker
track and energy
of recoil electron
Scintillator : Absorber
position and energy
of scattered gamma
Reconstruct Compton scattering
event by event
a
with electron tracking
(ETCC)
without electron tracking
(COMPTEL)
Schematic view of ETCC
Notes: 我々は、電子飛跡検出型コンプトンカメラを開発した。
We developed the Electron-Tracking Compton Camera. This detector

## Slide 4: Sub-MeV gamma-ray Imaging Loaded-on-balloon Experiment (SMILE)
10cm cube camera @ Sanriku (Sep. 1st 2006)
30cm cube camera
Operation test @ balloon altitude
Observation of
diffuse cosmic/atmospheric gamma
~400 photons during 3 hours
(100 keV~1MeV)
Checking the imaging performance
by observing gamma rays from Crab/Cyg X-1
40cm cube camera
50cm cube camera
Long duration observation with super pressure balloon
Adding pair-creation mode
All sky survey (load on a satellite)
Sub-MeV ~ MeV
SMILE-I
SMILE-II

## Slide 5: Gaseous TPC (micro-TPC)
micro PIxel Chamber(m-PIC)
sliced proportional chambers
2D readout (400 mm pitch)
Large detection area : (30cm)2
Gas : Ar 90% + C2H6 10% 1atm, sealed
Gain : ~106
Drift velocity (4 cm/msec)
position resolution: 400μm
Pressure Vessel
Drift Cage
cosmic muon
recoil electron
Data of (10 cm)3 ETCC
Electric Field

## Slide 6: Scintillation Camera
137Cs
Position imaging map
GSO 8×8 pixels
H8500
5cm
Scintillator : GSO(Ce)
Pixel size : 6x6x13 mm3
Photo readout : multi anode PMT H8500
(Hamamatsu Photonics)
4 channels readout with resistor chain
Absorber Unit
8×8 anodes
30cm
30cm
14cm
6×6 units

## Slide 7: (30 cm)3 prototype ETCC

## Slide 8: Imaging performance
137Cs : 662keV, 1MBq (X,Y,Z) = (5, 5, -52) [cm]
54Mn : 835keV, 1MBq (X,Y,Z) = (-5, -5, -52) [cm]
40cm
(30cm)3 Gaseous TPC
Scintillation Camera
(6×6 absorber units)

## Slide 9
SPD: 147[deg]
ARM: 9.8[deg]
DE/E: 12.3%
(FWHM) @662keV
183[deg]
17.7[deg]
14.3%
SMILE-I
SMILE-I
SMILE-I
(30 cm)3 ETCC
(30 cm)3 ETCC
Angular and energy resolutions
SPD
ARM
ARM : Angular Resolution Measure
SPD : Scatter Plane Deviation
SMILE-I
(30 cm)3 ETCC

## Slide 10: New readout circuit of the scintillation camera for SMILE-II

## Slide 11
Use resistor chain to reduce the power consumption.
••• 192 anode outputs -> 4channel
Power consumption of the readout system
••• 1.71 W/channel
Energy resolution :
••• 11% (FWHM, at 662 keV)
Typical dynamic range :
••• 80keV – 800keV
Readout System of Scintillation Cameras for SMILE-I
readout circuit for SMILE-I.
for SMILE-II, we need
resistor chain
192 channels -> 4 channels
Wider dynamic range
192anodes/4ch -> 64anodes/4ch
Saving the power consumption
Use recent power saving electrical components
The same or higher energy resolution.
To meet these requirements,
we developed the new readout system.

## Slide 12
New Readout System of Scintillation Cameras for SMILE-II
2×3PMTs
Readout
Circuit
• Use the resistor chain
(64 anodes /4 channels)
• Power consumption
0.41 W/channel
• 2×3 PMTs can be attached to one readout circuit.
• Use the output of the last dynode for the generation of the trigger of DAQ.
We developed the new readout circuit of scintillation cameras with ClearPulse Co. Ltd.
resistor chain
64 anodes -> 4 channels
The trigger delay and its change
are small enough for SMILE-II

## Slide 13: Performances of the new readout circuit
•Reconstructed Image of absorption points is good.
•Peak-to-valley ratio 10:1 well separated
•Energy Resolution : 10.3±0.9% at 662keV.
It’s enough for SMILE-II.
•Energy dynamic range : 81 keV – 1332keV.
(SMILE-I dynamic range : 80 keV-800 keV).
Fig.1 : reconstructed
2-dimensional histogram (137Cs)
Fig.2 : x-projection of a row (red circle) in Fig.1
Fig.3 : typical energy spectrum
of one pixel (137Cs)
Fig.4 : Energy Resolution
(10.3±0.9% at 662keV )
We checked the performance of the new readout circuit with a PMT (HV = -900V)
by using several irradiation sources.

## Slide 14: conclusion
Developing the ETCC for MeV gamma ray astronomy.
Used a (10 cm)3 ETCC in SMILE-I (2006).
As the next step, we have been developing the (30 cm)3 ETCC
for SMILE-II.
Constructed a prototype (30 cm)3 ETCC, and checked its performance.
Developed a new low-power readout system of scintillation cameras
for SMILE-II, and checked its performance.
Power consumption ••• 0.41 W/channel
Dynamic range ••• 81keV - 1333 keV
Energy Resolution ••• 10.3 ± 0.9 % at 662 keV
And the future work is …
Available for SMILE-II
SPD: 147[deg]
ARM: 9.8[deg] @662keV
DE/E: 12.3% (FWHM)

## Slide 15: Future work
Development and performance study of the (30 cm)3 prototype ETCC
with bottom and side scintillation cameras (108 absorber units).
We will begin changing to the new readout system for the scintillation camera.
Side scintillation cameras
(3 × 6 absorber units per one face)
Bottom scintillation cameras
(6 × 6 absorber units)
Development of the (30 cm)3 flight-model ETCC for SMILE-II experiment.

## Slide 16: Future work
Effective area
×50
sensitivity
SMILE-I
SMILE-II
To observe gamma rays from the Crab nebula at a 5 sigma confidence level in the 5 hour SMILE-II measurement, we are developing the (30cm) 3 flight-model ETCC using the result of the prototype ETCC.
In SMILE-II, we will use 216 absorber units for the (30 cm)3 ETCC .
estimated effective area : 0.5cm2.
(50 times larger than that of (10 cm)3 ETCC for SMILE-I)

## Slide 17
End

## Slide 18: Motivation
Nucleosynthesis
SNR : Radio-isotopes
Galactic plane : 26Al・60Fe
Annihilation
Acceleration
Jet (AGN) : Synchrotron
+ Inverse Compton
Strong Gravitational Potential
Black Hole : accretion disk, p0
Etc.
Gamma-ray Pulsar, solar flare
Observation of MeV gamma-ray will provide us…
The observation of continuum component is also important.
Where are MeV gamma-ray objects?
There are many background events which obstruct the observations.
Requirements for
the next-generation detectors are …
Wide-band detection
Large Field of View
Background rejection
Sensitivity
Astro-H
1mCrab
EGRET
Air
Cherenkov
Fermi
～１°
Good
Bad
erg / (cm2 sec)
Obs. Time : 106 sec

## Slide 19: MeV gamma-ray imaging
Collimator + position-sensitive detector
 OSSE (CGRO)
Coded Aperture Imaging
 BAT (SWIFT), SPI (INTEGRAL)
Laue Lens
Compton imaging
 COMPTEL (CGRO)
PSD
source
narrow FOV
background from collimator
Energy < 1MeV
Low-Z
High-Z
Single Compton
wide Energy band
only event circle
no background rejection
A new method with satisfying requirements
wide FOV & good angular resolution
photons from outside of mask are background
imaging of the spread sources is difficult
Energy < 1MeV
narrow FOV & good angular resolution
mono-energy

## Slide 20: COMPTEL (CGRO:1991～2000)
E0
φ
E1
E2
Using Compton Scattering
energies of scattered gamma
and recoil electron
Energy of incident gamma
Scattering angle
Compton scattering point
& Absorption point
Direction of scattered gamma
Restrict the direction of incident
gamma-ray to a circle
The source position is determined fully
by piling up circles
require 3 g at least
ignore the direction of recoil electron
Liquid scinti.
NaI(Tl)

## Slide 21: Background of COMPTEL
G.Weidenspointner, et.al. (A&A, 2001)
A：external g
B：internal g
C：two g
D：random coincidence
E: proton-induced g
Other background
  neutron
  electron
  gamma from atmosphere
TOF of 2 detectors
COMPTEL has rejected such background by the measurement of the Time Of Flight between 2 detectors.
Background rejection was not complete
Bad S/N
0
10
-10
[nsec]
-20
Intrinsic
background
forward
backward

## Slide 22: Comparison with the usual Compton method
150 events
Electron-Tracking Compton
Usual Compton Imaging
600 events
Using the electron tracks
complete direction within
sector form error region
only event circle within
ring form error region
-15
-15
15
15
X [cm]
Y [cm]
-15
-15
15
X [cm]
15
Y [cm]
Not using the electron tracks
2 sources were
separated clearly
Hard to separate
2 sources
137Cs(1MBq)2, usual Compton
137Cs(1MBq)2, Advanced Compton
Simply overlay
Simply overlay
(ETCC)
(COMPTEL)

## Slide 23: Electron-Tracking Compton Camera (ETCC)
1 photon  direction + energy
Large FOV (~3str)
Kinematical background rejection
Gaseous TPC : Tracker
track and energy
of recoil electron
Scintillator : Absorber
position and energy
of scattered gamma
Reconstruct Compton scattering
event by event
Eg : Energy of scattered gamma-ray
Ke : Kinematic energy of recoil electron
mec2 : Rest mass of electron
g : unit vector of scattering direction
e : unit vector of recoil direction

## Slide 24: SMILE-I gondola
Regulator
Battery
Battery
Ballast
GA
Bessel
TPC
GSO
scinti.
preamplifier
Plastic scinti.
FPGA encoding
board
VME module
CPU
ADC
telemetry
scaler
NIM module
Shaper
DAC
Size : 1.451.21.55m3
Weight : 397 kg
Power : ~250 W
No posture control !!

## Slide 25: 1st Flight SMILE
Balloon
B100 (100,000m3)
Weight 816kg
Buoyancy 888.2kg
Gondola size: 1.451.21.55m3
Gondola weight: 397kg
Bessel: f11.4m3
Power: ~350W
  in Bessel：220W
In Bessel (1 atm)
Detector, DAQ system, Storage, Thermometer,
Pressure gauge,
GPS, Clinometer
Out of Bessel
Battery & Regulator,
Thermometer,
Pressure gauge,
GPS antenna,
Geomagnetic aspectmeter
Flight Control
Telemetry,
Transponder,
Buoy, Radiosonde,
GPS, Thermometer,
Pressure gauge, etc.
TPC
GSO
ASD
NIM
VME
encoder
1.4m
f~1m

## Slide 26: 1st Flight SMILE
Balloon
B100 (100,000m3)
Weight 816kg
Buoyancy 888.2kg
Gondola size: 1.451.21.55m3
Gondola weight: 397kg
Bessel: f11.4m3
Power: ~350W
  in Bessel：220W
In Bessel (1 atm)
Detector, DAQ system, Storage, Thermometer,
Pressure gauge,
GPS, Clinometer
Out of Bessel
Battery & Regulator,
Thermometer,
Pressure gauge,
GPS antenna,
Geomagnetic aspectmeter
Flight Control
Telemetry,
Transponder,
Buoy, Radiosonde,
GPS, Thermometer,
Pressure gauge, etc.
TPC
GSO
ASD
NIM
VME
encoder
1.4m
f~1m
Regulator
Battery
Battery
Ballast
GA
Bessel

## Slide 27: 1st Flight SMILE
Balloon
B100 (100,000m3)
Weight 816kg
Buoyancy 888.2kg
Gondola size: 1.451.21.55m3
Gondola weight: 397kg
Bessel: f11.4m3
Power: ~350W
  in Bessel：220W
In Bessel (1 atm)
Detector, DAQ system, Storage, Thermometer,
Pressure gauge,
GPS, Clinometer
Out of Bessel
Battery & Regulator,
Thermometer,
Pressure gauge,
GPS antenna,
Geomagnetic aspectmeter
Flight Control
Telemetry,
Transponder,
Buoy, Radiosonde,
GPS, Thermometer,
Pressure gauge, etc.
TPC
GSO
ASD
NIM
VME
encoder
1.4m
f~1m
Regulator
Battery
Battery
Ballast
GA
Bessel
1.55m
1.45m
1.20m

## Slide 28: Sensitivity of X/Gamma-ray observations
Sensitivity
Astro-H
1mCrab
EGRET
Air
Cherenkov
Fermi
～１°
goal
Good
Bad
erg / (cm2 sec)
SMILE-I
Obs. Time : 106 sec

## Slide 29: GEM
Gas
Electron
Multiplier
Kapton
(d=50mm)
Cupper
(d=5mm)
F.Sauli, CERN
F.Sauli
70mm
140mm
10cm