## Slide 1
Proton tracking for medical imaging and dosimetry
J.Taylor,
P.Allport, G.Casse, N.A.Smith, I.Tsurin
For the PRaVDA Consortium

## Slide 2
Background
Silicon detectors at Liverpool University Physics Dept.
PRaVDA setup and microstrip tracker
Detector design and testing
Sensor & ASIC design
Preliminary results with charged particles
Simulation work
- Simulating efficiency
GEANT4 simulation and tracking
Summary and further work
Talk Overview

## Slide 3
The LHCb VErtex LOcator

## Slide 4
LHCb VELO Module as Beam Halo Monitor
LHCb Back-to-Back Sensor Module
Clatterbridge Centre for Oncology
Proton Therapy Facility
With thanks to Andrzej Kacperek

## Slide 5
Thin n-in-p
RD50
Thin detectors can be present in the beam for doses up to 5 x 1015 n eq/cm2 without requiring re-calibration due to radiation damage effects.
Radiation hardness studies
CERN RD50 collaboration has shown radiation hardness of thin n-in-p detectors up to at least 1016 n eq/cm2.
This allows design of detectors that are very rad hard for applications with clinical beams.

## Slide 6
System Overview
24 CMOS detectors
100 – 200 MeV protons
Range Telescope
4 sets of 3 strip detectors
Beam stop during treatment mode
x - outputs
x - outputs
x - outputs
x - outputs
u - outputs
u-outputs
v - outputs
v-outputs
Each 150um thick silicon detector has 2048 strips, 1024 read out on each side of the detector.
Each station of strip modules has three detectors crossed at 60o in an (x,u,v) configuration to resolve ambiguities at high particle rate.

## Slide 7
Operating Modes
Treatment Mode
(High Current)
Field size: 5cm collimated treatment beam
Energy: 60 - 191 MeV
Flux: ~107 protons/cm2/s
Use Strip Tracker to..
Check beam profile – reconstruct 1D & 2D histograms
Measure dose
Requirements:
- Proton counting
- 1D histograms
- 2D beam profile
Patient Imaging Mode
(Low Current)
Field size: 10cm (max.)
Energy: 191 MeV
Flux: ~105 protons/cm2/s
Use Strip Tracker to..
Track individual protons in (x,u,v) layers
Use Range Telescope to..
Measure positions and energies of each proton
Requirements:
- Accurate Tracking
- High Efficiency

## Slide 8
Sensor & ASIC Design
ASIC design carried out by ISDI CMOS Ltd. Binary chip allowing:
Treatment Mode: Read out all strips every 100us for 1D & 2D beam profile histograms and dosimetry map
Two thresholds per channel allow for high occupancy
Patient Imaging Mode: Read out up to 4 strips per ASIC with signal over threshold possible at 26MHz
(beam spill repetition rate at iThemba)
ASIC was fabricated in August 2014, testing now underway
Hybrid design by N.A. Smith at Liverpool
Designed by I.Tsurin, P.Allport, G.Casse, J. Taylor produced by Micron Semiconductor Ltd.
93 mm
96 mm

## Slide 9
Sensor & ASIC Design
1cm x 1cm x 150um silicon strip detector with 128 channels and 80um strip pitch
Sensor wire bonded to rad-hard BEETLE ASIC (LHCb experiment) with 40 MHz clock
ALiBaVa readout motherboard capable of much slower 300 Hz readout using scintillator trigger behind sensor
191 MeV protons (typical proton energy before phantom)
Proton cluster width vs threshold

## Slide 10
Sensor & ASIC Design
1cm x 1cm x 150um silicon strip detector with 128 channels and 80um strip pitch
Sensor wire bonded to rad-hard BEETLE ASIC (LHCb experiment) with 40 MHz clock
ALiBaVa readout motherboard capable of much slower 300 Hz readout using scintillator trigger behind sensor
60 MeV protons (typical proton energy after phantom)
Proton cluster width vs threshold

## Slide 11
RHEA ASIC
Rapid high-speed extended ASIC (RHEA)
Commercially designed ASIC from ISDI Ltd.
Binary chip with two tunable thresholds:
Threshold range 1: 2,000 – 10,000 e-
Threshold range 2: 20,000 – 160,000 e-
Expected equivalent noise charge 700e-
128 channels with a bonding pitch of 60um
Diced chips will be ready this month for testing and wire bonding to the PRaVDA sensors (18 currently available)

## Slide 12
PRaVDA Sensor
Silicon microstrip sensor using 150µm thick n-in-p technology developed for the ATLAS Experiment at the High Luminosity LHC
Left and right sides each contain 1024 strips with a pitch of 90.8um. Each station of strip modules will have three planes crossed at 60o in an (x,u,v) configuration to allow high particle rate.
12 strip modules will be used to make 4 tracking stations, 2 before and 2 after the patient
PRaVDA module mock-up for bonding trials and RS exhibit

## Slide 13
Sensor QA
Chart: IV curve for PRaVDA p-spray n-in-p sensor
| 1.0 | 11.0 | 21.0 | 31.0 | 41.0 | 51.0 | 61.0 | 71.0 | 81.0 | 91.0 | 101.0 | 111.0 | 121.0 | 131.0 | 141.0 | 151.0 | 161.0 | 171.0 | 181.0 | 191.0 | 201.0 | 211.0 | 221.0 | 231.0 | 241.0 | 251.0 | 261.0 | 271.0 | 281.0 | 291.0 | 301.0 | 311.0 | 321.0 | 331.0 | 341.0 | 351.0 | 361.0 | 371.0 | 381.0 | 391.0 | 401.0 | 411.0 | 421.0 | 431.0 | 441.0 | 451.0 | 461.0 | 471.0 | 481.0 | 491.0 | 500.0
I(uA) | 0.52766 | 2.5258 | 2.7897 | 2.8692 | 2.9197 | 3.0051 | 3.2048 | 3.4396 | 3.7291 | 4.0176 | 4.3037 | 4.5987 | 4.9197 | 5.2395 | 5.4964 | 5.6733 | 5.8355 | 6.0251 | 6.2255 | 6.4085 | 6.6157 | 6.8442 | 7.0726 | 7.2891 | 7.5276 | 7.7684 | 8.032 | 8.2433 | 8.4904 | 8.7245 | 9.0041 | 9.3046 | 9.5778 | 9.9352 | 10.2842 | 10.756 | 11.3135 | 12.3383 | 13.5708 | 15.0468 | 17.008 | 20.1667 | 25.4672 | 31.9836 | 38.659 | 44.1497 | 48.9138 | 54.6251 | 62.283 | 71.863 | 81.8861
QA on detectors carried out using manual and automatic probe stations to measure global IV and then to measure individual strip characteristics.
Leakage currents for sensors are typically a few uA even at several times depletion voltage.
Depletion voltage

## Slide 14
Sensor QA
Measurements with probes:
Parameter | Measured value | Spec. value
Polysilicon bias resistor | 6 MΩ | >2 MΩ
Coupling capacitance | 122 pF | 125 pF
#1
#2
#3
#1
#3
#2

## Slide 15
Sensor QA
Using an LCR meter and an automatic probe station we can probe the complex impedance for all strips on both sides of a detector
Detectors show at least 99% good strips per side.

## Slide 16
Wire-bonded 256 strips (12.5% of total detector) which allows a beam size of up to ~20 mm to be studied (and laboratory source measurements)
Readout using BEETLE ASIC (LHCb) and ALiBaVa DAQ
Thin beam entrance and exit windows to prevent degrading of energy before detector and backscatter after it
Test setup for charged particles
Beta Source test
Clatterbridge
With thanks to Andrzej Kacperek

## Slide 17
Testing the sensor with MIPs
Threshold on all strips set to 5.5ke-
1 strip clusters: 90.2%
2 strip clusters: 9.3%
3 strip clusters: 0.5%

## Slide 18
Testing the sensor with 60 MeV protons
1 strip clusters: 69%
2 strip clusters: 30.6%
3 strip clusters: 0.4%
3 mm collimator
Threshold on all strips of 10 ke-
7 mm collimator

## Slide 19
Simulating the Efficiency of the (x,u,v) configuration
How efficient is the tracker at distinguishing hits in a multi-hit environment in both Treatment and
Patient Imaging mode?
For a strip detector with orthogonal strips and N hits, there are: N2 - N ‘Ghost-hits’ or ambiguities generated

## Slide 20
Simulating the Efficiency of the (x,u,v) configuration
A smaller stereo angle would reduce the ambiguities further, but doesn’t offer same resolution in all directions
Tracker module design
Tilt planes of strips at a (stereo) angle w.r.t other planes to prevent strip from one plane crossing all strips in the next plane.
Each station has strips
crossed at 60o to one
another in (x,u,v)
configuration allowing
higher particle rate.
x - outputs
x - outputs
x
v
u

## Slide 21
Simulated Efficiency in Treatment Mode
Determine efficiency of (x,u,v) configuration in treatment mode using simple Monte Carlo
A concave distribution is a good test of how well we can reconstruct the beam profile without introducing artifacts
Events/Frame | Ambiguity Rate | >1 hit per strip | >2 hits per strip
30 | 8.1% | 4.7% | 0.0%
60 | 62.1% | 10.5% | 0.3%
120 | 811.1% | 18.1% | 1.2%
Pacman Input Distribution
Ambiguity rate = total ambiguous hits/ total real hits

## Slide 22
60 protons/frame 1D & 2D output distributions
Output Distribution
(x,u,v) Output Distributions
Simulated Efficiency in Treatment Mode

## Slide 23
120 protons/frame 1D & 2D output distributions
Proton counting and 1D histogramming – Possible up 120 protons/frame with only small error in calculated dose since 2 thresholds and only 1.2 % > 2 hits per strip.
2D proton beam profile – Large distortions in a concave beam profile appear at 120 protons/frame
(x,u,v) Output Distributions
Output Distribution
Simulated Efficiency in Treatment Mode

## Slide 24
Events/Frame | Ambiguity Rate | >1 hit per strip | >2 hits per strip
5 | 0.6% | 0.8% | <0.1%
10 | 1.6% | 1.4% | <0.1%
Flux in patient imaging (pCT) mode is 100 times less than treatment mode therefore ambiguity rates are very low (at iThemba only expect 0.04 events/frame)
High Efficiency – The detector is highly efficient for patient imaging with >99% hits unambiguous at well over 10 times planned iThemba pCT mode rates
Ambiguity rate = total ambiguous hits/ total real hits
Simulated Efficiency in Patient Imaging Mode

## Slide 25
S.Jeyasugithtan & S.Peterson UCT, T.Price UoB
iThemba beamline code used as input for GEANT4 simulations of silicon strip tracker
(x,u,v) triplets of 150um Si with 90.8um strip pitch simulated
Simulation provided output for detector/ASIC design and (soon) output for CT reconstruction codes written by University of Surrey
iThemba GEANT4 Simulation

## Slide 26
GEANT4 Simulation of tracker
GEANT4 Simulation of the tracker uses the iThemba beamline simulation on the previous slide as an input. The tracker simulation consists of:
There are 8 planes before and after the phantom:
- 6 silicon planes arranged into two (x,u,v) modules
- 2 air planes used to provide truth information
Each plane uses G4VDigitizerModule to store sensitive detector information into strips
Charge sharing is implemented to provide realistic cluster width distributions for comparison with measured distributions and input to tracking algorithm
Range Compensator
Phantom
Calorimeter

## Slide 27
Simulated dE/dx distributions

## Slide 28
GEANT4 validation
Measured data agrees with GEANT4 simulation to within <10%

## Slide 29
Tracking algorithm
The uncertainty on the projected track depends on its length, ie the distance to the phantom surface.
Ellipses indicate 1,2 & 3 sigma values for reconstructed position – truth position

## Slide 30
Summary
The PRaVDA system will enable proton CT and real-time beam monitoring with dosimetry making proton therapy safer and more accurate
A tracker has been designed for the PRaVDA system using 150µm thick silicon microstrip sensors with radiation-hard n-in-p technology developed for the ATLAS Experiment at the High Luminosity LHC
The tracker is capable of fast and precise proton tracking for Patient Imaging and accurate dosimetry up to the high beam currents used during Patient Treatment
Preliminary data has been taken with 150um silicon strip strip detectors and charged particles of varying energies
Simulation together with preliminary measurements has been used to inform design of a new silicon sensor, ASIC, hybrid and DAQ
Tracking software and analysis algorithms are currently under development using simulated data from GEANT4 which has been validated with measurments
Full system to be assembled early next year for beam tests at iThemba LABS, South Africa

## Slide 31
Thanks for Listening!
And many thanks to:
P.Allport, G.Casse, N.A.Smith, I.Tsurin
and..