## Slide 1: Deep Science at Boulby Underground Laboratory
Emma Meehan
LRT – 20/05/2019
1

## Slide 2: Boulby Mine
A working polyhalite and rock-salt mine in the North East of England.
Owned by Israel Chemicals Ltd. (ICL-UK)
Major local employer - ~700 direct and many indirect employment.
Middlesborough
Whitby
Staithes
York
Deepest mine in Britain: 1100m
Polyhalite
2
Source: http://www.icl-uk.uk/product/polysulphate

## Slide 3: Boulby Underground Laboratory
The UK’s deep underground science facility
1.1km depth (2805 mwe). With low background surrounding rock-salt
Operated by the UK’s Science & Technology Facilities Council (STFC) in partnership with the mine operators ICL
Factor ~106 reduction in cosmic ray flux
vs. surface
New Lab open since 2017
Permian Evaporites
3

## Slide 4: Boulby Geology & Mining
Mine Shafts
New Lab
(2017)
Excavations are in Salt (NaCl), Potash (KCl) and Polyhalite (K2Ca2Mg(SO4)4).
Permian Evaporite layers left over from the Zechstein Sea.
Over 40 km of tunnel can be mined each year
Long-lived roadways in Salt
4

## Slide 5: Boulby Geology & Mining
Typical Boulby Salt Roadway
By San Jose and Drdoht, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=19014943
5

## Slide 6: Underground Science
DRIFT-II
BUGS: Ultra-low background material screening (for LUX-ZEPLIN and Super-K-Gd and more)
CYGNUS: Directional Dark Matter Search
ERSaB: Environmental gamma spectroscopy
Deep Carbon: Muon Tomography for CCS (etc)
SELLR: Life in Low background radiation
BISAL: Geomicrobiology / Astrobiology studies
MINAR: Space Exploration Tech. Development
Misc. Geology / Geoscience
Etc... (More to come)
6

## Slide 7: Facility Details
The World’s Underground labs
• The UK’s deep underground science facility. One of 4 in EU. ~10 in the world.
• Supports work of 9 collaborative projects (astrophysics to climate, geology, environment etc), 20 institutions, > 70 scientists and students.
Facility funded and operated by the Science and Technology Facilities Council (STFC).
Operations, H&S & science programme managed by 6 (+4) onsite staff and supported by Rutherford Appleton Lab (PPD).
Mine operators ICL-UK provide wide-ranging operational & higher level support.
How does Boulby compare?
Lowest Radon levels (3 Bq/m3)
Most diverse science prog.
Science and Industry partnership
7

## Slide 8
Working alongside
mining at Boulby…
ICL support us:
Keep the mine operating and safe
Emergency H&S
Materials transportation
Misc. Facility maintenance
Our responsibility:
Safety
Operations Impact
Outreach & Media
8

## Slide 9: What’s New?
Plenty has been going on since the last LRT meeting
A few highlights over the next few slides
  MINAR/MEDSALT
  What is coming up
  Preparing for the future – data data data
9

## Slide 10: MINAR (Mine Analog Research) VI/VII
Another hugely successful workshop was held in September 2019
  Mars rover deployment
  MEDSALT student training school
10

## Slide 11: Mars Rover
11

## Slide 12: MEDSALT
MedSalt Training School on the Deep Hypersaline Biosphere
Aim to train early-stage researchers in the multidisciplinary areas of geomicrobiology, biogeochemistry and astrobiology.
  How to sample aseptically from experimental brine ponds for microbiological analysis
  How to measure methane flux in these brines.
12

## Slide 13: MEDSALT
13
Also included a programme of surface lectures from both students and teachers
https://twitter.com/MedSalt/status/1040227625728450560

## Slide 14: What Is Coming?
14

## Slide 15: WATCHMAN
15
Objectives:
Remote monitoring of small fission reactors (~40 MWth) via detection of antineutrino emissions.
Initial project goal is to observe reactor on/off states at approximately 10 – 30 km distance from reactor.
Prototype Design Features:
  Medium scale (~1 ktonne fiducial mass) water-based gadolinium-loaded anti-neutrino detector
  Initial prototype to demonstrate monitoring of a single known reactor site
  Rationale is to develop a detector design that can be scaled to larger masses for smaller reactors and larger standoff distances

## Slide 16: WATCHMAN
16

## Slide 17: The World in Anti-neutrinos
17
Source: The National Geospatial-Intelligence Agency

## Slide 18: The World in Anti-neutrinos
99% Geophysical
1% Anthropogenic
Source: Usman, S.M. et al. AGM2015: Antineutrino Global Map 2015. Sci. Rep. 5, 13945; doi: 10.1038/srep13945 (2015)

## Slide 19: Boulby As a Site for WATCHMAN
WATCHMAN required a site that:
  Could host an underground laboratory
  Was 10-30 km from an active nuclear reactor
Boulby chosen as site in 2017

## Slide 20: Boulby As a Site for WATCHMAN
This will require the largest excavation to date underground at Boulby (25m dodecagon)
Represents a step change in underground lab space in the uk
Team at Boulby is expanding to meet this exciting new challenge
Will prove the UK capable of hosting large scale underground experiments
25m

## Slide 21: Boulby As a Site for WATCHMAN
Hartlepool has 2 cores.
  Sometimes they run together, sometimes alone
2 Cores
1 Core

## Slide 22: Preparing for WATCHMAN
WATCHMAN will require clean facilities for construction
WATCHMAN will want to monitor radon levels
WATCHMAN will require stable environment
  Temperature, Pressure, Humidity
WATCHMAN will require “clean” power
Our current lab acts as a testbed to show that we can achieve these requirements
22

## Slide 23: Airborne Particle (dust) monitoring
TSI 6510 samples at 1 CFM
TSI 6510

## Slide 24: Radon Monitoring
We have started long term monitoring of radon at Boulby
2.2 Bq/m3 Average

## Slide 25: Radon Monitoring
Complemented by additional 3x RAD7 detectors
To be deployed in various locations (including surface)

## Slide 26: Power Monitoring
Panel mounted system installed to monitor incoming power to the lab
Working to understand what we are seeing
  i.e. none of us have an electrical background
Currently only really used to monitor frequency and duration of power outages.

## Slide 27: Surface Particle Monitoring
Recently acquired a PartSens surface monitor from PMT-GB
Measures surface particles > 2.0 um
Sample area of 5 mm x 7mm
Suitable for use on multiple surfaces
This will be used to monitor surfaces used for sample preparation in BUGS as well as in WATCHMAN construction

## Slide 28: Stay connected
Fascination
STFC’s digital in-house magazine, packed full of our latest, most exciting science and technology stories.
www.stfc.ac.uk/fascination
STFC Impact Report
A showcase of how STFC science delivers real economic and societal benefits to the United Kingdom
www.stfc.ac.uk/2550