## Slide 1: Noble gas purification for LZ and other rare event searches
Eric Miller
LRT – Jaca, Spain
May 20 2019

## Slide 2: LZ Detector
Z position from S1 – S2 timing
X-Y positions from light pattern
Reject gammas by S2/S1 ratio
Expect > 99.5% rejection
Notes: Time Projection Chamber

## Slide 3: LUX-ZEPLIN (LZ) detector
7.0 T active LXe
5.6T fiducial
17 tonnes Gd-LS Outer Detector
50 kV cathode high voltage
Instrumented Xe skin detector
Technical Design Report, arXiv:1703.09144.
Lower PMT cable conduit
LXe supply & return
Neutron conduit

## Slide 4: Backgrounds uniform in LXe
Solar neutrinos
Contamination of the xenon by:
  Non-noble gases, eg 3H
  Long-lived noble gases, eg 85Kr, 39Ar
  Short-lived noble gases, eg 222Rn

## Slide 5: Backgrounds uniform in LXe
Solar neutrinos
Contamination of the xenon by:
  Non-noble gases, eg 3H
  Removed by Getter
  Long-lived noble gases, eg 85Kr, 39Ar
  Removed before experiment start
  Short-lived noble gases, eg 222Rn
  Mitigated by materials screening
  Removed while experiment is running

## Slide 6: LZ Circulation

## Slide 7: Circulation Getter
LZ’s full 10 tonnes purified every 2.3 days
Saes hot zirconium getter removes electronegative impurities
  O2, N2, etc.
  Critical for detector performance
Getter also removes 3H
  Eliminates this background

## Slide 8: LZ – Radon Control
Radon emanates from materials in contact with Xe
Screening
  Around 100 materials/components screened for LZ
  Warm end of PMT cables potentially significant

## Slide 9: LZ – Radon Control
Radon emanates from materials in contact with Xe
Screening
  Around 100 materials/components screened for LZ
  Warm end of PMT cables potentially significant
In-line removal system
  Impractical to purify 500 SLPM circulation
  Practical to purify problematic areas

## Slide 10: LZ – Radon Control
Radon emanates from materials in contact with Xe
Screening
  Around 100 materials/components screened for LZ
  Warm end of PMT cables potentially significant
In-line removal system
  Impractical to purify 500 SLPM circulation
  Practical to purify problematic areas
Projected Rn level:
  <2 μBq/kg

## Slide 11: LZ Circulation

## Slide 12: LZ – In-line radon removal
Remove radon from subset of circulation flow
  0.1% of Xe flow, but significant Rn contribution
Strategy: charcoal chromatography
  Radon passes through charcoal slower than xenon
  Design system to trap radon for many half-lives (3.8 days)
Radon Removal system in development at the University of Michigan:

## Slide 13: LZ – In-line radon removal
Critical that charcoal remove more radon than it produces!
  Identify low-emanation; high adsorption charcoal
Charcoal | Density (g/cm3) | Surface area (m2/g) | Spec. activity (mBq/kg) | Price ($/kg)
Shirasagi | 0.45 | 1,240 | 101 ± 8 | 27
CarboAct | 0.28 | 1,000 | 0.23 ± 0.19 | 15,000
Saratech | 0.60 | 1,340 | 1.71 ± 0.20 | 35
Saratach (HNO3) | 0.60 | 1,340 | 0.51 ± 0.09 | 135
provided by Carter Hall
Saratech
CarboAct
Shirasagi

## Slide 14: Any worry about cosmic-ray activation of xenon?
Cosmic ray interactions produce radioactive byproducts in xenon cylinders at the Earth’s surface
Many of these are solids, and will not enter experiment
3H will be removed by getter
127Xe
  36-day half-life reduces impact
  Production rate too low to be significant background
133Xe
  5.2 day half-life reduces impact
We have the luxury of purifying Xe at the surface
Cosmogenic activation of xenon and copper, Baudis et al., Eur. Phys. J. C (2015) 75: 485

## Slide 15: Kr Removal with Chromatography
Remove via gas charcoal chromatography (with helium carrier gas)
  Kr has a faster flow rate through activated charcoal than Xe

## Slide 16
400 kg Charcoal Column
Vacuum Pump
Storage Compressor
Bottles of Xenon
Freezer
Cold Charcoal
Trap
Circulation Pump

## Slide 17: LZ Kr Removal - Chromatography
400 kg Charcoal Column
Cold Charcoal
Trap
Circulation Pump
Vacuum Pump
Storage Compressor
Bottles of Xenon
Freezer
Clean He

## Slide 18: LZ Kr Removal - Chromatography
400 kg Charcoal Column
Vacuum Pump
Storage Compressor
Bottles of Xenon
Freezer
Xenon with ppb Kr
Clean He
Cold Charcoal
Trap
Circulation Pump

## Slide 19: LZ Kr Removal - Recovery
400 kg Charcoal Column
Vacuum Pump
Storage Compressor
Bottles of Xenon
Freezer
Clean He
Cold Charcoal
Trap
Circulation Pump

## Slide 20: LZ Kr Removal - Storage
400 kg Charcoal Column
Vacuum Pump
Storage Compressor
Bottles of Ultrapure Xenon
Freezer
Ultrapure Xe
Cold Charcoal
Trap
Circulation Pump

## Slide 21: LZ – Krypton Removal
Employ 2 columns to clean xenon twice as fast!
LZ system to process 16 kg slugs every two hours
Plan to purify 10 tonnes over 6 months
R&D system reduced Kr content to 0.06 ppt
LZ system designed to achieve 0.015 ppt (15 ppq)
  Subdominant to solar neutrinos
  LZ requires < 0.3 ppt
  Currently commissioning system

## Slide 22: Centrifuge Purification - EXO
Enriched Xenon Observatory (EXO-200) searched for neutrinoless double-beta decay in 136Xe
Centrifuges used to enrich heavy isotopes of Xe
  136Xe fraction increased from 8.9% to 80.6%
Other lighter elements also removed by this process
  Including 85Kr and 39Ar
Kr concentration reduced to 16.3 ± 1.9 ppt
The EXO-200 detector, part I: detector design and construction, EXO Collaboration. Journal of Instrumentation 7 (05), P05010, 2012

## Slide 23: Cryogenic Distillation: Krypton
Employed by XMASS, XENON100, XENON1T, PANDAX…
Distillation tower for XENON1T
Operates at -98 C;
Vapor pressure of Kr is 10.8x greater than of Xe
High-Kr gas extracted from the top
Low-Kr liquid extracted from bottom
Achieved lowest reported Kr level:
  < 17 ppq
Removing krypton from xenon by cryogenic distillation to the ppq level, XENON Collaboration, Eur. Phys. J. C (2017) 77: 275

## Slide 24: Cryogenic Distillation: Radon
Demonstrated on XENON100
  Installed in series with circulation system
Operates at -96 C;
Low-Rn gas extracted from the top
Rn decays in liquid at bottom
See also talk by Hardy Simgen later this session!
Online 222Rn removal by cryogenic distillation in the XENON100 experiment, Eur. Phys. J. C (2017) 77: 358

## Slide 25: Kr purity achieved
Experiment | Technique | Purity Achieved (ppt g/g)
Panda X | Distillation | <30
XENON1T | Distillation | <0.017
XMASS | Distillation | 2.1 ± 0.7
EXO-200 | Centrifuge | 16.3 ± 1.9
LUX | Chromatography | 3.5
LZ R&D | Chromatography | 0.06
Thanks for listening!

## Slide 26: Bonus Slides

## Slide 27: WIMP backgrounds summary
Projected WIMP Sensitivity of the LUX-ZEPLIN (LZ) Dark Matter Experiment, LZ Collaboration, arXiv:1802.06039, 2018
5.6 tonnes x 1000 days; ~1.5 to ~6.5 keV