## Slide 1
Final results of the CUPID-0 Phase I experiment
Mattia Beretta
On behalf of the CUPID-0 collaboration

## Slide 2: CUPID-0
82Se
Qββ = (2997±0.3) keV
The first enriched scintillating bolometer ββ experiment
0νββ
2νββ
Sum of two e- energy
2νββ
0νββ:
Performing resolution
At the Q value
Low Background
Few counts expected

## Slide 3: CUPID-0 Detector
O. Azzolini et al. (CUPID), Eur. Phys. J. C 78, 428 (2018), arXiv:1802.06562
26 ZnSe crystals
  24 enriched in 82Se (95%) + 2 naturals
Total mass= 10.5 kg
  82Se mass =5.17 kg (3.8∙1025 ββ emitters)
Scintillating Zn82Se crystals.
Heat signal:
bolometric high resolved output
Light signal:
particle identification
Bolometric Ge Light detectors
NOSV Copper
Surface cleaned
Vikuiti Reflector
More collected light

## Slide 4: CUPID-0 Time-line
Phase I
560 d with 74% of livetime
June 2017 – December 2018
Commissioning
2017
2019
Preparation of Phase II
ββ physics
Exposure: 9.95 kg·y
AmBe source
βγ Shape Characterization in the ROI
System manteinance
232Th Energy Calibration
Chart: 
 | 74 | 12 | 10 | 3 | 1
74%
1%
12%
10%
3%
56Co Energy Calibration

## Slide 5: Calibrations
232Th Energy Calibration
Periodic Bolometer calibration and light detector intercalibration
Response function: Double Gaussian
  Also observed in other bolometers
56Co Energy Calibration
82Se
Check of the energy reconstruction
Evaluation of FWHM energy resolution @ 82Se Q
FWHM @ Qββ
(20.0±0.6) keV
CUPID-0 Preliminary

## Slide 6: 0νββ search
Basic Selections
Rejection of “non-particle-like” events through pulse shape on thermal pulses
Total Background spectrum
0νββ ROI
Multiplicity (M)
Anti-coincidence between crystals (ΔT=20ms)
CUPID-0 Preliminary
CUPID-0 Preliminary

## Slide 7: Background – Alpha Rejection
Light Signal depends on particle type
α events
β/γ events
Selection based on light shape parameter
CUPID-0 Preliminary

## Slide 8: Background – Delayed coincidences rejection
Delayed 212Bi-208Tl (α/β) coincidences
Veto for 7 half-life
α events
β/γ events
Selection of 212Bi α events
α pulse shape
2.0 MeV<Energy<6.5MeV
  Degraded tag

## Slide 9: Background – Delayed coincidences rejection
Total cut efficiency:
(86±1)%
Lowest background ever measured with a calorimeter
No evidence of 0νββ signal
@90% C.I.
CUPID-0 Preliminary

## Slide 10: Background Model
EXPERIMENTAL DATA
BACKGROUND SOURCES
A complete model of the background sources
Analysis
Monte Carlo Simulations
Reproduction of measured activity
Bayesian fit to data
Predictions
Comprehension
O. Azzolini et al. (CUPID), (2019), arXiv:1904.10397 [nucl-ex].

## Slide 11: Experimental data for the model
M1 α – β/γ
M2 / M2 sum (Σ2)
M>3 (to constraint Muons)
Multiplicity (M)
Crystals triggered in 20ms
Divided according to multiplicity and particle type
Background source identification
O. Azzolini et al. (CUPID), (2019), arXiv:1904.10397 [nucl-ex].

## Slide 12: Background sources
Radiation type
Monte Carlo simulations
Localization in the detector
Depth of contamination
Bulk
Surface
Exponential profile
Natural Chains
Fathers + saecular equilibrium breaking points
Single isotopes
40K, 54Mn, 65Zn, 60Co, ...
Muons
O. Azzolini et al. (CUPID), (2019), arXiv:1904.10397 [nucl-ex].
Generation
Detection

## Slide 13: Additional informations
MODEL
33 background sources
Linear combination
Coefficients = Activities
PRIORS
Experimental signatures
  α/α coincidences
Previous contamination measurements
  Reflective foil
222Rn
τ1/2 = 3.82 d
218Po
τ1/2 = 3.11 m
214Pb
τ1/2 = 26.8 m
238U (226Ra →210Pb)
232Th (224Ra →208Pb)
224Rn
τ1/2 = 3.66 d
220Rn
τ1/2 = 3.11 m
212Pb
τ1/2 = 10.64 h
216Po
τ1/2 = 0.145 s
α
α
α
α
α
Daughter/parent gives a prior on surface vs bulk contaminations
Depends on source localization
O. Azzolini et al. (CUPID), (2019), arXiv:1904.10397 [nucl-ex].

## Slide 14: Reconstruction results: M1 Spectra
Full spectrum reconstruction
Peaks and continuum are well modelled
The α – β/γ separation allows to disentangle the different contributions
O. Azzolini et al. (CUPID), (2019), arXiv:1904.10397 [nucl-ex].
M1 β/γ
M1 α

## Slide 15: Reconstruction results: M2 spectra
ffff
Both α and β/γ regions are well modelled in peaks and continuum
  The surface/bulk prior is a key ingredient
Some differences on the Bi-Po pileup
Imperfect reconstruction of the deposited energy
214Bi→218Po
212Bi→212Po
O. Azzolini et al. (CUPID), (2019), arXiv:1904.10397 [nucl-ex].
M2
M2 sum (Σ2)

## Slide 16: Result: Beta/Gamma spectrum
Possibility to perform detailed study on this decay
232Th is dominant, because no delayed cut is applied
Muons give 44% of residual background
2νββ is a dominant contribution
In the ROI
Delayed coincidences
O. Azzolini et al. (CUPID), (2019), arXiv:1904.10397 [nucl-ex].

## Slide 17: Phase II upgrade
μ are the main residual background
  Installation of μ-veto
No reflective foil
  Sensitivity to M2 α events
New clear Cu Shield
  Thermalization
  Additional shielding
NOW COOLING

## Slide 18: CUPID 0: current results and future perspectives
CUPID-0 is the first large array of enriched scintillating bolometers
We reached the lowest background level achieved with bolometric experiments:
A complete background model has been developed
  Major ROI background (208Tl β events) is reduced with delayed cut
  Muons give 44% of residual counts
Phase II upgrade focused on background improvement
  Muon veto installed
  No Reflective foil: M2 alpha events direct tagging
  Additional shielding

## Slide 19
BackUp Slides

## Slide 20: Double beta decay (ββ)
0νββ
2νββ
Performing resolution
At 2-3 MeV (Qvalue of different isotopes)
2νββ:
(A,Z) → (A,Z+2) + 2e-+2ν
Predicted and detected
0νββ:
(A,Z) → (A,Z+2) + 2e-
Prohibited in the Standar Model (∆L=2)
Limits: T0ν1/2 > 1024 -1025 y
Measuring the two electron energy
Low Background
Observing few counts above background

## Slide 21
Experimental search for 0νββ
Experimental sensitivity
Maximum measurable half-life at a given C.L.
Crytical experimental parameters:
Isotope Mass (M)
FWHM energy resolution (Δ)
Background (B)
Mass scalability at low cost and high isotopic abundance
Δ of few % at Qvalue to avoid the 2νββ induced background
Ratio 0νββ signal/2νββ background
High purity materials
(< ppb radioactive contaminations)
Rejection techniques

## Slide 22: CUPID-0
Demonstrating achievable Background rejection
Precision measurements on 82Se ββ
Heat:
bolometric high resolved output
Light:
particle identification
82Se - Qββ = (2997±0.3) keV
The first enriched scintillating bolometer ββ experiment

## Slide 23: Zn82Se crystals
O. Azzolini et al. (CUPID), Eur. Phys. J. C 78, 428 (2018), arXiv:1802.06562
26 ZnSe crystals
  24 enriched in 82Se (95%) + 2 naturals
Total mass= 10.5 kg
  82Se mass =5.17 kg
  3.8∙1025 ββ emitters
Fist large mass Zn82Se enriched crystals ever grown.

## Slide 24: Material surrounding the crystal
NOSV ultra–pure copper
Cleaning procedure vs surface contaminations
O. Azzolini et al. (CUPID), Eur. Phys. J. C 78, 428 (2018), arXiv:1802.06562
Copper structure
Vikuiti Reflector
Enhances the light output
Low Th/U contaminations measured
SiO2 anti-reflective coating
Sensible to few keV energy deposition
Ge Bolometric Light Detector

## Slide 25: The Cryostat
Oxford 1000 3He/4He diluition cryostat (CUORE-0)
Radially divided by the Roman Lead shield:
  CryoExt, RomanPb, CryoInt
The cryostat contamination have been evaluated from experimental data

## Slide 26: Detector Performances
Detector response function
Double Gaussian
(deviation from simple gaussian observed in other bolometers)
232Th Energy Calibration
Bolometer calibration and light detector intercalibration
Response function evaluation
82Se

## Slide 27: Detector Performances
FWHM @ Qββ
(20.0±0.6) keV
Major contribution is the crystal quality
(average baseline FWHM ~5 keV)
56Co Energy Calibration
Check of the energy reconstruction
Evaluation of FWHM energy resolution @82Se Q
82Se

## Slide 28: Shape parameters cut
Remove energy-dependency of
the shape parameters for
energy-independent cuts
Efficiency and signal/noise as figure of merit to choose cut level

## Slide 29: Evaluation of efficiency
Heat
Fit of 65Zn Line before/after cuts applied
Light
Cut on events with M>6
  Muonic showers, almost pure beta/gamma sample

## Slide 30: 0νββ search
Basic Selections
Rejection of “non-particle-like” events through pulse shape on thermal pulses
Anti-coincidence between crystals (ΔT=20ms)
  Multiplicity selection
65Zn: cosmogenically activated
40K and 208Tl: natural radioactivity
2νββ is the dominant background
2νββ
ROI for 0νββ

## Slide 31: Background – Alpha Rejection
Light Signal depends on particle type
Selection based on light shape parameter
α events
β/γ events

## Slide 32: Background – Delayed coincidences rejection
Selection made
Delayed α coincidence 212Bi-208Tl rejection
Veto any event succeeding a 212Bi α event in a 7 half-life window
α pulse shape
2.0 MeV < Energy < 6.5 MeV
  Both peak and surface events
α events
β/γ events

## Slide 33: Background model
A full model is needed to undestand the background components
BACKGROUND SOURCES
ZnSe crystals
Bulk
Surface
O(10mm)
O(10nm)
Reflective Foil
Bulk
Surface
O(10nm)
Cryostat
Bulk
Cu Holder
CryoInt
Roman Lead
Cryo Ext
Muons
High Multiplicity
Combined with a Bayesian analysis
Particle type
α events
β/γ events
EXPERIMENTAL DATA
Multiplicity (M)
Crystals triggered in 20ms

## Slide 34: Shape cut for Background Model
α events
β/γ events
yi = filtered light pulse
A = maximum amplitude
Si = filtered average pulse
iM = position of the maximum and
wr = right width at half maximum of Si
Optimized cut:
SP = μα (E)-3 x σα (E)
Parameter calculates for SP>6 (pure beta gamma)

## Slide 35: Total Fit Results
Bulk
Surface
Exponential profile

## Slide 36: ROI contaminations
After time veto of 7 livetimes

## Slide 37: Alpha vs Bulk
Different impact on the continuum