## Slide 2: TE3530 Development and Optimization of Kicker Systems for LIU-Projects
A. Ferrero, T. Kramer

## Slide 3: What is a kicker magnet?
Fast pulsed dipole magnet for beam deflection.
Used to kick incoming beam to the circulating orbit (injection kicker);
also used to kick the beam out of an accelerator (extraction kicker);
or to merge two beams into one single line. (recombination kicker).
e.g. injection process

## Slide 4: How does a kicker magnet work?
The magnet filed is switched on only when it is needed to inject, extract or recombine a beam within a particle free gap  Pulsed magnet hence important parameters are:
  rise & fall time
  flat top quality
Since it is a “fast” pulsed magnet, transmission lines theory must be applied.
Possible issues: Reflections due to line mismatches.
Limitations: Bandwidth defined by system design.

## Slide 5: Planned LIU Kicker upgrade
Under the LHC Injector Upgrade project, some kicker systems must be upgraded to allow for future 2.0 GeV beam transfer.
Specification for rise & fall time and maximum system ripples must be respected.
Improvement possibilities had to be identified using analogue circuit simulations.

## Slide 6: Methodology
Simulations based on Orcad Pspice tool.
Measurements done during technical stop (02/09/15)
Started with brainstorming, interviews of senior engineers (identification of improvement possibilities)
Development and verification by simulation
Validation with real measurements taken in the PS tunnel

## Slide 7: Some results
Less flat top ripple.
Less ringing at the rising edge.
Less post-pulse ripple.

## Slide 8: Outlook
Test & measurement campaign foreseen for some of the KFA-45 improvements during upcoming YETS.
Meanwhile started: Optimization of the recombination kicker KFA-10.
Planned: Analysis of fast 100ns MKP-S kicker upgrade (SPS injection).
  Old kicker model obtained.
  Model update and optimization needed.
  Hardware measurements on test stand foreseen.

## Slide 9: Thank you