## Slide 1: Radiation hard electronics for ATLAS and CMS pixel detector upgrades
Luis Miguel Jara Casas
Supervisor: Jorgen Christiansen
PH-ESE-ME
Physics department, Electronics Systems for experiments section, Microelectronics group.

## Slide 2: Outline
RD53 collaboration
Pixel Readout
Readout cables
Results and status
Next steps

## Slide 3: 1.RD53 Collaboration:
Present hybrid pixel detector: success, with a new technology on a unprecedented scale. In operation at LHC for tracking the particles.
Extrapolation for the HL-LHC: major challenges for the pixel readout integrated circuits:
  Smaller pixels.
  Higher hit rates (1-3 GHz/cm2).
  Unprecedented radiation tolerance (10MGy)
    10.000 x space electronics.
  Higher output bandwidth.
  Mass and space constraints.
Collaboration to develop the pixel readout chips for the ATLAS and CMS Phase 2 pixel upgrades.
Notes: Smaller pixels to resolve tracks in boosted jets.
Minimize mass: in order to minimize scattering and energy loss of the particles being measured (not disturb the experiment).

## Slide 4: 2.Pixel readout:
WHAT WE HAVE:
High read-out rates (factor 100 compared to LHC).
Very high radiation levels.
Significant material contribution.
WHAT WE NEED:
Minimize material (scattering, energy loss)
Signal integrity.
Data must be converted into high rate optical links.
Notes: Only for the layers L1 and L2, the layers L34 OD have less radiation 1/8.
Unprecedent radiation levels and space constraints make imposible to envisage optical conversion directly on the pixel modules.
Electrical links from the readout chips to the opto conversors in the modules located in the vecinity of the pixel detector. LPGBT to this conversion.

## Slide 5: 3.Readout cables:
Trying to obtain a balance between mass and signal integrity, taking into account all the constraints (space, radiation, bit rate…)
Several proposals to simulate:
 | Kapton flat cable, Aluminum | Kapton flat cable, Aluminum, meshed ground | Cu cladded Al twisted pair, polymide isolation.
Wire resistance | 11.5 | 11.5 | 4
Mass (g/m) | 0.29 | 0.14 | 0.1
Mass for 3500 cables | 2.0 kg | 1.0kg | 0.7kg

## Slide 6: 3.Readout cables:
Different loss effects to take into account in simulations:
1.SKIN EFFECT:
Tendency of alternating current to become distributed within a conductor near the surface.
2.DIELECTRIC LOSS TANGENT:
dissipation of electromagnetic energy (heat) inside the dielectric layer.
3.DC RESISTANCE:
2m cables, dc resistance begins to be an important factor.
 | Conductivity (siemens/m)
Cu | 5.8·107
Al | 3.8·107
F(Hz)

## Slide 8: 4.Results and status:
Chart: Single ended Cu and Al Eye Amplitud vs Wire length
| 0.25 | 0.5 | 1 | 2
Cu Air thick trace | 478.2559 | 456.8002 | 415.6984 | 344.1224
Cu Air thin trace | 462.4469 | 427.4697 | 364.2198 | 266.0949
Cu Isolator+Kapton Thick trace | 477.3782 | 455.3311 | 413.3431 | 340.1142
Cu Isolator+Kapton thin trace | 460.3277 | 423.763 | 356.7624 | 253.7188
Al Air thick trace | 473.266 | 447.0203 | 397.5223 | 315.984
Al Air thin trace | 448.4638 | 401.957 | 321.7158 | 207.5405
Al Isolator+kapton thick trace | 472.6685 | 446.0045 | 396.1402 | 312.9729
Al Isolator+kapton thin trace | 444.3883 | 394.526 | 313.3357 | 195.0581

## Slide 9: 5.Next steps:
Develop simulations for the rest of the models proposed.
Study other effects: crosstalk, wire bundles…
Preemphasis.
Eye diagram before and after preemphasis
Manufacture the better models.
Measure S parameters.
Compare measurements with simulations and improve them.
Crosstalk depending on the distance between differential pairs

## Slide 10: Thank you for your attention!

## Slide 11: Extra-slides

## Slide 12
Chart: Differential pairs and single ended Amplitud vs Wire length
| 0.25 | 0.5 | 1 | 2
Differential Pair Cu | 937.2312 | 876.5875 | 763.8593 | 586.7417
Differential Pair Alu | 923.6556 | 850.8501 | 720.9436 | 528.1177
Single ended Cu | 477.3782 | 455.3311 | 413.3431 | 340.1142
Single ended Al | 472.6685 | 446.0045 | 396.1402 | 312.9729

## Slide 13
Chart: Twisted pair, differential pair and single ended Amplitud vs Wire length
| 0.25 | 0.5 | 1 | 2
Differential Pair Cu | 937.2312 | 876.5875 | 763.8593 | 586.7417
Differential Pair Alu | 923.6556 | 850.8501 | 720.9436 | 528.1177
Single ended Cu | 477.3782 | 455.3311 | 413.3431 | 340.1142
Single ended Al | 472.6685 | 446.0045 | 396.1402 | 312.9729
Twisted Pair Cu | 965.758 | 931.942 | 873.629 | 749.0362
Twisted Pair Al | 957.7655 | 916.6891 | 837.9092 | 696.7831