## Slide 1
Development of Electronics for Solid State Detectors R&D
The upgrade of the LHC experiments requires the development of highly specialized solid-state detectors. The CMS silicon based inner tracking detectors and the CMS HGCAL calorimeter silicon sensors are two prominent examples.
My task is to support the physicist developing and characterizing these detectors by designing and implementing customized electronics for data acquisition and calibration of their systems as well as the corresponding readout and control software.
CERN - CIEMAT
  This work has been funded by CERN
  under Spanish trainee program with number PH3472 Development of electronics for Radiation and Solid State Detectors R&D
Joaquín B. González
Telecommunications engineer
TCT+: TCT (Transient Current Technique)
eTCT: TCT (Transient Current Technique)
EP-DT-DD: SSD
Solid State Detectors
I-DLTS (Current Deep Level Transient Spectroscopy)
A totally new thermomechanical design
Optimized and more robust fixation, keeping the same cooling power
The new box was successfully tested. Minimum temperature of -20 ºC was reached
Detector is now mounted on its own PCB, without any electronics, just connectors
Copper plate built at CERN, compatible with all sample PCBs in the lab
eTCT cooling
Mechanical design
14 parallel loops
Up to 200 controls-indicators
12 semaphores (work managers)
~0.6 s per measurement (was~4 s)
  Even less avoiding to read the temperature each measurement
  Down to 0.04 s in special case (timing)
Independent time control for each worker (ctrl loop) and watchdogs for communications
TCTPlus_basic
Software development
Interface
Math Data manipulation Algorithm
Instrument control
TCT v0.4 to v0.9
(original)
Interface
Math Data manipulation Algorithm
Instrument control
TCT v1.0.2 to v1.0.5b
Interface
Math Data manipulation Algorithm
Instrument control
TCT v1.0.0 to v1.0.1
Hot swapping coding!!!
Safe space for long term data storage
Fully adapted and integrated within external infrastructure
Software design intrinsically parallel and scalable
Software package ready for being integrated for the control software of all the setups
Automatization of all the backing up processes. Virtual machines 24/7 in Openstack to optimize the performance
  Alarm system implemented
Safe copy processes over RSA to cross check
New features for safe file storing
  External sharing
  Automatization of the dataset
  Fully integrated with CERN-wide services (EOS platform) like WebDAV, Cernbox, SFTP, etc.
Backer Up Tool
Infrastructure design and Software development
Cooling to 10K
TSC (Thermally Stimulated Currents)
-70C to 180C
CCE (Charge Collection Efficiency)
Skiroc Calibration
Setup design, and DAQ calibration
Skiroc2CMS is the next iteration for Skiroc family
Design and building up of a calibration setup
  Acquiring knowledge on Skiroc and training of students
  Developing systematic calibration for parameters such as SNR, Noise, common mode error and other parameters relevant for normal operation of the device (HL-LCH run 1)
Setup and tools designed for Skiroc2 Dev board. Tools developed to be scalable and to repeat the studies with Skiroc2CMS, for a much bigger number of acquisition channels
HGCAL testbeam backend
Design of communication and data handling infrastructure
Hardware and protocol design to fit with CERN network standards
Entire 2017 beam test season very successful
Test beam in H2 (North area) with particles from SPS
8.8Gbps (peak) during 5s (one spill). 2 spills/1min
Zero DAQ-related down time
EP-CMX: HGCAL tb
Testbeam team
Kick-off meeting
Start desing Electronics
Feb
Mar
Apr
May
Start Production
Start Software
…
Nov
Star data taking
Data analisys
2017
Entire project under my responsibility: Development of a new setup to measure SiPMs (for CMS HCAL)
Involves design of two new PCBs, new cooling block, new setup and new software
SiPM@Susi
Electronic and Mechanical design. Software development
  Presently, data is being analysed, and prepared for publication
  Joaquin.Gonzalez@cern.ch