## Slide 1
Development, implementation and deployment of a drive for electric motors in harsh environments*
Abstract
Introduction
When commercial stepper motors drives are connected through long cables to its motor, the current control is degraded due to the undesirable effect of transmission lines [1]. This issue has been solved by developing a DSP based custom drive (Fig. 1).
Conclusions
A powerful DSP based drive has been developed to control electric motors connected through long cables. The capabilities of this drive have been extended to allow for closed loop control, safe operation, trajectory planning/tracking, autotuning and remote upgrade of firmware among many other features.
This drive can be very useful especially in harsh environments, such as nuclear plants, underwater applications, etc.
1 CERN, Engineering department, STI group, Switzerland
2 Ciemat, Spain
References
[1] R. Picatoste, PhD ‘Modelling and Control of Stepper Motors for High Accuracy Positioning Systems Used in Radioactive Environments’, 2014.
[2] M. Butcher, A. Massi, M. Martino, A. Tacchetti, ‘Implementation and tuning of the Extended Kalman Filter for a sensorless drive working with arbitrary stepper motors and cable lengths’, IEEE.
  *This work has been funded by CERN/Ciemat
  †[ jorgesome@hotmail.com ]
Jorge Sola Merino12†, Mark Butcher1, Ricardo Picatoste Ruilope1, Alessandro Masi1
Stepper motors are widely used for open-loop positioning applications. Highly radioactive environments lead to the use of long cables, where commercial motor drives tend to have poor performance or fail completely.
A full custom stepper motor drive has been designed to work with long cables of up to 1 km and with emphasis on reliability and self diagnostic capabilities. More features have been added to enhance the overall system performance.
Trajectory planning and tracking
Fig 3: Auto generated trapezoidal speed profile
Improved diagnostics
The main motor signals can be constantly monitored to predict machine degradation and perform preventive maintenance work.
A post-mortem feature allows to trace back the cause of a problem, its effects and the absolute timestamp when it happened (Fig.5).
The drive is able to generate constant speed and constant acceleration profiles, as well as tracking any kind of motion profile, defined by an array of positions and timestamps (Fig. 3 and 4).
Fig 5: Post mortem analysis shows power supply error
Fig 1: Developed stepper motor drive to work with 1km cables
The drive is capable of closed loop operation by means of an encoder signal or sensorless control, allowed by an integrated Extended Kalman Filter [2] (Fig. 2). A closed to open loop real time switch in the case of sensor failure allows for safe and seamless operation.
Closed loop operation
Fig 2: Transition from closed to open loop operation. Top: position, bottom: speed
Fig 4: User defined profile tracking
Time (s)
Position (deg)
Speed (steps/sec)
Time (s)
Position (turns)
Current (A)
Voltage (V)
Time (s)
Measured phase currents
Supply Voltage
Cause of error