## Slide 2: Power Electronics System Testing and Commissioning
Guillermo Navarro Patrón
Konstantinos Papastergiou
Technology Department
- Electric Power Conversion Group
- Medium Power Converters Section
FTEC 2017 2nd Workshop

## Slide 3
Introduction
Power converter
Tester features
Hardware integration
Software implementation
Conclusion
Outline

## Slide 4
Introduction
150 Converters
  TT2
  Booster Transfer Line
  East Area

## Slide 5
SIRIUS main configurations
  SIRIUS – S SIRIUS – 2P SIRIUS – 4P
Power converter
Parameter | SIRIUS – S | SIRIUS – 2P | SIRIUS - 4P
Output Current | 200ARMS / 450APEAK | 400ARMS / 900APEAK | 800ARMS / 1800APEAK
Output Voltage | 450V | 450V | 450V
Input Power | 3x400V / 50Hz. 32ARMS | 3x400V / 50Hz. 63ARMS | 3x400V / 50Hz. 125ARMS

## Slide 6
Power converter
  Power brick front side
SIRIUS 2P prototype
  Power brick rear side
  Main brick rear side

## Slide 7
Flexibility.
  One tool for all SIRIUS configurations.
  Automation of test tasks
  No need for CERN control electronics.
User friendly and intuitive.
  Operated by non-qualified personnel.
  Standard connections.
  Tests performed automatically and easily.
Safe. Low voltage operation.
Portable.
Tester features

## Slide 8
Hardware integration
  PXI
  Interface board
  Power source output
  HMI +
  Interface
  connections

## Slide 9
  Execution of steps/instructions.
  Execution of User Interfaces.
  Monitoring variables.
  TestStand
  LabVIEW
  Sequence manager.
  Synchronization of steps.
  Customization of steps.
Test implementation

## Slide 10
  LabVIEW: Interface board
  Single PWM Generation
  Analog signals readout
  Digital outputs command
  Full H-Bridge PWM Generation
  Digital inputs status readout
Test implementation

## Slide 11
  LabVIEW: Power Source (ActiveX controls)
  Three/Single-phase configuration
  Power source initialisation
  Current level setup
  Output activation
  Output protection configuration
  Output Voltage Mode
Test implementation

## Slide 12
  Main sequence:
  · Main configuration
  · Calls every test.
  · Clean up.
  · Main GUI call
  Test sequences:
  · One per test.
  · Calls every VI.
  · Test GUI.
  TestStand
Test implementation

## Slide 13
Current status
  Hardware assembled.
  Correct operation of Converter – Tester verified.
  Developing test sequences.
  Validating test platform with power converter in the workshop.
What’s next?
  Finishing the implementation and integration software.
  Preparation of the performance qualification tests.
  Factory visit and training of test personnel in Romania.
  Coordination of the teams in the test platform.
Conclusion