## Slide 1: Integration Tests and Commissioning of the Upgrade of the ATLAS Liquid-Argon Calorimeters Trigger Readout

## Slide 2: Outline
Introduction
  ATLAS Liquid Argon Calorimeter (LAr)
  LAr measurement
LAr Phase 1 readout electronics upgrade
  Higher granularity for Trigger
  LAr Phase 1 trigger readout upgrade
  Phase 1 Back End System
  My role in the past 4 months
  LDPB temperature & power monitoring
  LTDB pulse on local monitoring PC
  LArC + 2 LATOME in USA15
  My work - injector/checker for devkit
  Future work

## Slide 3: ATLAS Liquid Argon calorimeter
Main goal: measure path and energy of electrons, photons and jets
Lead / Liquid Argon sampling with accordion geometry
Total of 180k calorimeter cells
3k Trigger Towers: group of cells in (η,Φ) of size 0.1 x 0.1
4000 tons
Liquid Argon (LAr) calorimeters cells
0
1
2
3
Trigger Tower
12m
8m

## Slide 4: LAr measurement
LAr calorimeter
LAr ionization pulse
Energy calculation
coeff.
ADC
sample
Incoming particles create a shower
Electrons in shower ionize Liquid Argon
Ionization electrons create a current

## Slide 5: Higher granularity for Trigger
Upgrade
LAr Phase 1
Simulation of electron with 70 GeV of transverse energy
Current Trigger Tower: provide limited performance → similar results despite event rate increase
Improvement: Trigger Tower → Super Cells (lateral + longitudinal segmentation)
  Higher trigger resolution → enhanced rejection algorithms → higher quality data
Super Cells
Trigger Towers
10 times finer granularity

## Slide 6: LAr Phase 1 trigger readout upgrade
Current system:
Analog Trigger
3000 TT
Upgrade system: Digital Trigger
30000 SC

## Slide 7: Phase 1 Back End System Test
MGT
LVDS
TTC
partition
Notes: Full proof of the complete chain working
LATOME: large and cumbersome FPGA (Altera Arria 10). Contains the intelligence of the operating @ 40MHz
LArC: reconstruct of E (∑▒〖𝑎_𝑖 𝐴_𝑖 〗)
TDAQ function: windows
FEX: It search or trigger objects.

## Slide 8: My role in the past 4 months
Participate in the developments needed to integrate BE readout with real data coming from a LTDB prototype
BE readout validation tests in laboratory:
  Power & temperature monitoring
  LTDB pulse recorded in local monitoring PC
Report progress in meetings
Firmware development (VHDL, Python)
  Improve TTC block and TTC testbench (ongoing)
  Injector/checker for Development Kit (ongoing)
Elaboration of documentation
BE system crate

## Slide 9: LDPB power & temperature monitoring
LArC of reference
3 LArC fully loaded: 5 LATOME v2 + 7 LATOME v3

## Slide 10: LTDB pulse on local monitoring PC

## Slide 11: LArC + 2 LATOME in USA15
LArC + 2 LATOME installed in USA15
  Since last week up and running
When will the BE demonstrator start taking real data?
  Solve bugs in LATOME firmware
  Validate that all ADC values are correctly recorded in local monitoring PC
ATCA crate in USA15

## Slide 12: My work – injector/checker for devkit
TTC VME
TTC @ 1.28Gb
IPBUS (rd/wr registers)
Power supply
(12 V)
TX
RX
LATOME firmware (Super Cell)
pattern generator (injector) + FEX (checker)
LATOME
LATOME test
Arria 10 Development Kit
RX
TX
CLK @ 160 MHz
MTP to LC
Power supply
(12 V)
QSFP
DIN
SMA
3
4
8
1 GbE
Notes: On the other hand, I am working in a project to allow other developers to debug LATOME firmware without a TTC partition, a crate or a Felix, LArC or FEX boards.
The Arria 10 Development Kit with a FPGA of the same family as the LATOME, receives the TTC signals using a custom protocol @ 1.28 Gb/s from the LATOME test board.
The LATOME test board can receive the TTC signals from a TTC VME partition or generate them internally.
The Arria 10 devkit board runs an injector/checker firmware. It injects physics data (Super Cell values) to the LATOME board, reads back generated data by the LATOME and checks if the 𝑬_𝑻 calculations are correct.

## Slide 13: Future work
Continue with the development of the injector/checker project for Arria-10 Development Kit
Continue with the developments needed to integrate the BE readout
Firmware development for LATOME board
Validate demonstrator in USA15 during 2018 p-p run
Full system installation & commissioning in 2019-2020. In run 3 the system operation is mandatory because of the expected higher luminosity

## Slide 16: ATLAS detector
Multi-purpose detector with Forward-Backward symmetric cylindrical geometry
Designed to study elementary particles and their interactions
Tracking system
Solenoidal and Toroidal Magnets
Electromagnetic and Hadronic calorimeters
Muon chambers
Overall weight: 7000t

## Slide 17: Phase-1 Back End System

## Slide 18: LTDB

## Slide 19: My work - TTC testbench
Testbench to generate Timing and Trigger Control (TTC) signals
What are TTC signals? Provide information of the time and type of the trigger events
Clock (LHC @ 40 MHz)
L1A: Level 1 Accept (up to 100 kHz)
BCR: Bunch Crossing Reset (~80 us)
ECR: Event Counter Reset (~30 s)
TType: Triger Type (8bit)
0
ECR counter
3564
1
2
3
4
…
25 ns
BCID: Bunch Crossing ID [0, 3663]
8 bit
L1A counter
24 bit
Event ID:
18

## Slide 20: Summary on power & temperature
With final setup with 12 LATOME, running full code (+ baseline corr.)
  Total current: 23.7 A → 284 W (max. allowed 400 W)
  Temperature LArC: 36 °C (max. allowed 70 °C)
  AMC1 : 5.5 A, 76 °C (max. allowed 6.7 A, 85 °C)
  AMC2 : 5.4 A, 72 °C
  AMC3 : 5.1 A, 62 °C
  AMC4 : 4.55 A, 52 °C
The temperature and power requirements are fulfilled
Similar results as the test with the ET firmware after improving the cooling
  Removed the rails to host 8 compact-sized AMC connectors that slow the air flow
1
2
3
4