## Slide 1: 8Th FTEC Workshop | CERN
BE-BI-SW
Jordi Ustrell Garrigos
18/05/2020

## Slide 2: Outline
    Introduction to ALPS/SPS
    Development of Expert GUI for ALPS:
      Phase-r application
      Scaling factors manager
    Maintenance and upgrade of the web application FESA WEB

## Slide 3: Introduction to ALPS/SPS
ALPS is the new orbit measurement system for the SPS.
SPS is the second-largest machine in CERN’s accelerator complex ( ͌7 km. in circumference).
It takes particles from the Proton Synchrotron and accelerates them to provide beams for the Large Hadron Collider, and others experiments.

## Slide 4: Introduction to ALPS/SPS
Digital
Back-end
(VFC)
Digital
Back-end
(VFC)
FESA
(Front-end
Software Architecture)
A
B
BPM
SPS
BA1
BA3
BA2
SPS is divided into 6 sectors (from BA1 to BA6).
Each sector has:
  40 Position monitors
  10 VFC
  1 FESA Device

## Slide 5: Introduction to ALPS/SPS (BMP)
Digital
Back-end
(VFC)
Digital
Back-end
(VFC)
FESA
(Front-end
Software Architecture)
A
B
BPM
SPS
BA1
BA3
BA2
Position monitors types:
Inside the BPM:
The BMP can detect:
Horizontal plane
Vertical plane
Both
Horizontal
plane
Vertical plane
Electrodes B
Electrodes A
Each electrode detects a signal that is sent to three acquisition chains to obtain three sensibilities:
High
Mid
Low

## Slide 6: Introduction to ALPS/SPS (VFC)
Digital
Back-end
(VFC)
Digital
Back-end
(VFC)
FESA
(Front-end
Software Architecture)
A
B
BPM
SPS
BA1
BA3
BA2
VFC is an Acquisition Hardware with 4 acquisition channels.
Each channel process 1 BPM.
Firmware decides which sensitivity channel, received from the BMP, to use (Hi, Mid, Lo)
* BPM with 2 planes (horizontal and vertical) use 1 channel of the VFC for each plane.

## Slide 7: Introduction to ALPS/SPS (FESA)
Digital
Back-end
(VFC)
Digital
Back-end
(VFC)
FESA
(Front-end
Software Architecture)
A
B
BPM
SPS
BA1
BA3
BA2
FESA servers are created using the FESA framework, developed by CERN. This is the standard way to develop real-time software for accelerator controllers using C++.
Each sector has one instance of this FESA server and is used to obtain real-time data and update the settings in the hardware.

## Slide 8: GUI for ALPS – Phase-r Introduction
The Phase-r application is used to align*:
  the data in time from each electrode due to the different electronic circuits,
  the received turn clock flag with the actual turn start for each BPM,
  the injection trigger to all BAs due to the different cable lengths.
* It is important to note that when we say "align", what we are actually doing is synchronizing, but the ALPS team call it alignment.

## Slide 9: GUI for ALPS - Phase-r Evolution
Turn Clock alignment is cycle dependent
Turn Clock alignment implemented and tested
Injection Trigger alignment implemented and tested
Minor changes in the GUI
Import/Export data to CSV file
Minor bugs fixed

## Slide 10: GUI for ALPS – Scaling Factors Introduction
The Scaling Factors Manager is an application used to check if the configuration of the ALPS devices inside the SPS is correct.
To do this, it compares the configuration of the devices with the data of multiple CSV files obtained from the database.
Each CSV file contains the configuration of a specific channel of a device, each device has 40 channels.

## Slide 11: GUI for ALPS - Scaling Factors Status
GUI created with some minor bugs to fix.
Obtain the configuration data of the devices.
Read the data from a test CSV file.
Display a label for each field in the tables with the value of the data base.
Indicate which data is the same on the device and in the database.
To be implemented
Obtain data from the data base.
Display all the data of a device in the corresponding window.
Check if the device data matches with the CSV file.
Display the data in the main window.

## Slide 12: Many thanks.
Questions?