## Slide 1: 10th FTEC Workshop Cryogenics for the HL-LHC IT String
Óscar Durán Lucas
TE-CRG-ME - A. Perin (supervisor), G. Rolando, M. Sisti, A. Wanninger, J. Mouleyre, J. Metselaar
CERN, 18th May 2020
INDICO: 915648

## Slide 2: Outline
Overview of the HL-LHC IT String
Cryogenic system for HL-LHC IT String
Update on technical tasks
Update on management tasks
Upcoming activities

## Slide 3: Overview of the HL-LHC IT String
View of LHC and IP5 with location of IT magnets
Integration of IT String in SM18
The final focusing superconducting inner tripplet (IT) magnets of ATLAS and CMS of LHC will be replaced during LS3.
HL-LHC IT String will be installed in SM18 facilitiy for testing the collective behaviour of magnets and systems, get information to speed up the commissioning in the LHC tunnel and configuration of IP5L.
*Images from CRG-TM presentation,
INDICO 797080

## Slide 4: Cryogenics system for HL-LHC IT String
Pressure relief during quenches
Ultimate heat load capacity of bayonet heat exchangers
Main functionalities of the cryogenic system:
Representative of tunnel configuration
Controlled cool-down & warm-up
Magnet operation in He II (1.9 K)

## Slide 5: Cryogenics system for HL-LHC IT String
*Images from TCC presentation,
INDICO 891644
SQXL
Magnet cryostat
SQXL
Cold Box
Cold Compressor Unit
String Valve Box
Cryogenic transfer lines
Layout of equipment in SM18

## Slide 6: Technical tasks
Dimensioning of cryogenic control valve on pumping line
Pressure model of the system to calculate the pressure drop requirements of the valve
Selection of a Kv able to regulate all operation modes
Safety system dimensioning for overpressure scenarios in the 5 process lines:
Lose of insulation vacuum (LIV) → Heat load to He → Pressure increase → He release through Safety valves
Safety valves on String Valve Box → Verification of pressure upstream
LIV
Safety
Valve
Calculation of the volume of the system for purge requirements
Control Valve
Chart: Relative valve travel h (%)
| 0 | 5 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Kv 170 m3/h Valve curve | 1 | 1.2589 | 2.5119 | 3.9811 | 6.3096 | 10 | 15.8489 | 25.1189 | 39.8107 | 63.0957 | 100
Operation modes | 24.1176 | 63.1 | 4.2471 | 17.0588 | 70.5882 | 20 | 48.2353 | 30 | 95.2941

## Slide 7: Management tasks
Completion of Product Breakdown Structure
Data base including complete cryogenic distribution of the project
~900 items, MS Excel Pivot Table
Reference document for instrumentation procurement, control architecture, naming convention
Dashboard of progress
Follow-up of the project
List of approvers
Follow-up of document approval process
Continue with other management tasks
Meeting organization and minutes
Update project sharepoint webpage
Project diagrams
Block Diagram
Update of Process Flow Diagram

## Slide 8: Upcoming activities
Heaters unit
Valves dimensioning
Technical Specification for heaters and heater vessel
Risk analysis
Management tasks
Finalization of Product Breakdown Structure
Follow-up of the project (Dashboard, list of approvers, work breakdown structure, purchase)
Meeting organization and minutes
Update and improve project sharepoint webpage
Others

## Slide 9: Thanks for your attention! Questions?
Ó. Durán Lucas, 10th FTEC Workshop, 18.05.2020