## Slide 1: Validation and verification of industrial control systems (FTEC2019-11)
Ignacio David López Miguel (BE-ICS-AP)
Beams - Industrial Controls and Safety Systems – Applications
Supervisor: Jean-Charles Tournier

## Slide 2: Context
BE-ICS develops Industrial Control and Safety systems.
2
Examples
LHC Cryogenics control systems
Cooling and ventilation control systems
LHC, SPS and PS Access control and Protection systems
Safety Instrumented Systems (SM18, FAIR)
These systems use PLCs (Programmable Logic Controllers) as a control device
Improve reliability and guarantee that programs are compliant with specifications
  Using formal methods (model checking)
Goal
How

## Slide 3: When should/could we use Formal Methods?
3
Is it worth to use Model Checking to PLCs?
Not without tool support
  Damage to the environment, the installation, people
Safety critical systems
  Damage to the reputation of the company/organization
Software library used in many systems
Ariane 5 explosion
Floating-point division error
  Hide complexity
  Compatibility
PLCverif1
1 B. Fernández Adiego, D. Darvas, E. Blanco Viñuela, J-C. Tournier, S. Bliudze, J. O. Blech, V. M. González Suárez: Applying model checking to industrial-sized PLC programs. IEEE Transactions on Industrial Informatics, Vol. 11, Issue 6, pp. 1400-1410, 2015. [Paper on IEEExplore]

## Slide 4: Applying model checking to PLC programs
4
…
If Output1 is FALSE
then Output2 is TRUE
AG (!Output1 → Output2)
Requirements
Formalized requirements
Control Flow Automata
Intermediate Model
PLC program
Model checking algorithms

Property failed
Trace leading to the violation

Property OK

## Slide 5: FTEC tasks
Migration to Java 11
Complete support for TIA portal
PLCverif open source
Support for other model checkers
Support on a real verification case
Solving issues
SPS