## Slide 1: Characterisation of Bunch-by-Bunch Tune Shift Effects in the CERN SPS
Ingrid Mases Solé (BE-ABP-INC)
Special thanks to: H. Bartosik, C. Zannini and M. Schenk
22/06/2022

## Slide 2: Motivation of the project
  Number of transverse oscillations that the particles describe during one revolution in the accelerator (frequency of the transverse oscillations)
Definition of TUNE, Q
Qx = 20.13
Qy = 20.18
Beam stability and beam losses depend on the tune
Avoid values of tune that make de beam unstable due to resonances

## Slide 3: Motivation of the project
LHC Injectors Upgrade, LIU [1]
High intensity of bunches in the SPS
Strong bunch-by-bunch tune shift effect from impedance
Why is bunch-by-bunch tune measurement and correction important?
It is necessary to measure the horizontal and vertical bunch-by-bunch tunes and correct the average tunes in order to:
    Stabilise the beam
    Ensure good beam transmission (reduce losses)

## Slide 4: OUTLINE
Introduction
Experimental measurements
PyHEADTAIL simulations
Comparison of measurements and simulations
Additional tasks and IPAC 2022
Outlook

## Slide 5: INTRODUCTION
Tune shift grows for the trailing bunches as the wakefield builds up along the train
SINGLE BUNCH TUNE SHIFT [2] due to narrowband impedances
MULTITURN TUNE SHIFT due to broadband impedances
The tune shift depends on:
The intensity per bunch
The total intensity of the beam, through:
  The number of bunches
  The number of trains of bunches (batches)

## Slide 6: INTRODUCTION
Obtain a method to predict the tune shift depending on the beam configuration (number of bunches, number of batches and intensity per bunch).
OBJECTIVE
MEASUREMENTS
(at different intensities)
SIMULATIONS
(For both single-bunch and multi-bunch beams)

## Slide 7: OUTLINE
Introduction
Experimental measurements
PyHEADTAIL simulations
Comparison of measurements and simulations
Additional tasks and IPAC 2022
Outlook

## Slide 8: RESULTS FROM MUTLI-BUNCH MEASUREMENTS
LOW INTENSITY
HIGH INTENSITY
Horizontal (top) and vertical (bottom) bunch-by-bunch tunes measured through the LHC prototype Beam Position Monitors (LHCBPMs) in the SPS, for low intensity of 0.8 x 1011 p/b (left) and high intensity of 2.0 x 1011 p/b (right).
Measurements done with 4 trains of 72 bunches (Standard Beam)
We compute Q: the tune shift of the fourth train with respect to the first train (relative tune shift along the bunch trains)
Measurements done at different intensity values
Tune shift increases with intensity
Q
Q

## Slide 9: OUTLINE
Introduction
Experimental measurements
PyHEADTAIL simulations
Comparison of measurements and simulations
Additional tasks and IPAC 2022
Outlook

## Slide 10: PyHEADTAIL SIMULATIONS
Horizontal (top) and vertical (bottom) bunch-by-bunch tunes obtained with PyHEADTAIL, for low intensity of 0.8 x 1011 p/b (left) and high intensity of 2.0 x 1011 p/b (right).
LOW INTENSITY
HIGH INTENSITY
Q
Q
Impedance induced tune shifts are simulated with the PyHEADTAIL [3] macroparticle tracking code
SPS impedance model with wall and kickers contributions
Simulations done under the same conditions as the measurements
Electron cloud effects are NOT included in the simulations

## Slide 11: OUTLINE
Introduction
Experimental measurements
PyHEADTAIL simulations
Comparison of measurements and simulations
Additional tasks and IPAC 2022
Outlook

## Slide 12: COMPARISON MEASUREMENTS AND SIMULATIONS
Relative tune shift of the fourth train with respect to the first train comparing measurements with simulations (vertical plane).
 | Vertical Plane | Horizontal Plane
Single-Bunch Beams |  | 
Multi-Bunch Beams | Low intensities High intensities | 
For single-bunch beams, simulations are successfully benchmarked with measurements
For multi-bunch beams:
  More impedance contributions need to be included in the simulations model to solve the discrepancies at high intensities in the V plane
  E-cloud effects are needed to solve discrepancies in the H plane

## Slide 13: OUTLINE
Introduction
Experimental measurements
PyHEADTAIL simulations
Comparison of measurements and simulations
Additional tasks and IPAC 2022
Outlook

## Slide 14: COMPLEMENTARY WORK
M. Schenk (BE-OP) maintainer of the app.
APPLICATION FOR TUNE MEASUREMENT AND CORRECTION IN THE SPS (CCC)
PARTICIPATION IN THE
SPS SCRUBBING RUN
From 19.03.2022 to 10.04.2022
After a long shutdown, scrubbing is needed to reduce electron cloud inside the beampipe [4]

## Slide 15: Contribution to IPAC 2022 (International Particle Accelerator Conference, from 12-17 June, ipac22.org)
POSTER PRESENTATION
PAPER PUBLICATION
Link to poster
Link to paper

## Slide 16: OUTLINE
Introduction
Experimental measurements
PyHEADTAIL simulations
Comparison of measurements and simulations
Additional tasks and IPAC 2022
Outlook

## Slide 17
FUTURE WORK
Include electron cloud effects in the PyHEADTAIL simulations
Include more contributions to the SPS multi-bunch impedance model
Perform more measurements to have more experimental data
Study the impact of the tune shift on the emittance and losses

## Slide 18: References
[1] J. Coupard et al., “LHC Injectors Upgrade, Technical Design Report, Vol. I: Protons”, LIU Technical Design Report (TDR), CERN-ACC-2014-0337.
[2] C. Zannini, H. Bartosik, G. Iadarola, G. Rumolo, and B. Salvant, “Benchmarking the CERN-SPS Transverse Impedance Model with Measured Headtail Growth Rates”, in Proc. IPAC’15, Richmond, VA, USA, May 2015, pp. 402–405. doi:10.18429/JACoW-IPAC2015-MOPJE049
[3] https://github.com/PyCOMPLETE/PyHEADTAIL
[4] G. Iadarola et al., “Detailed Studies of Beam Induced Scrubbing in the CERN-SPS”, in Proc. IPAC'15, Richmond, VA, USA, May 2015, pp. 3908-3910. doi:10.18429/JACoW-IPAC2015-THPF091

## Slide 19
THANK YOU VERY MUCH FOR YOUR ATTENTION!

## Slide 20: EXTRA SLIDES: COMPLEMENTARY WORK
PARTICIPATION IN THE
SPS LIU MD’s
(Machine Development sessions)
Check the high-intensity beams that will be delivered to the LHC during Run3:
  Standard Beam (trains of 72 bunches)
  BCMS Beam (trains of 48 bunches)
Emittance measurements
Q-26 OPTICS
SINGLE BUNCH REFERENCE MEASUREMENTS
IN THE SPS
Headtail mode 0 instability GROWTH RATE as function of chromaticity [5]
Together with E. de la Fuente
19th, 20th May and 13th, 14th June

## Slide 21
EXTRA SLIDES
Single-bunch tune shift measurements in the SPS
Good agreement of
measurements
and simulations