## Slide 1: Engineering and design of interface systems to integrate the new 250-tonne high-granularity calorimeter into the CMS detector
Speaker: Diego García Robles (EP-CMX-SCI)
Supervisor: Tristan Loiseau (EP-CMX-SCI)
FTEC-2021-09
Workshop 22/06/2022

## Slide 2: Introduction
Diego G. Robles
Present endcap calorimeter
HGCAL design
Integrate a brand-new calorimeter in an existing 20-year-old structure
Need to design interface systems and components.

## Slide 3: Back flange. Introduction
Diego G. Robles
The function of the back flange is to be the direct link between HGCAL and the detector’s structure.
The back flange is mounted on the support tube, which rests the whole weight of HGCAL (250 tons) and connected by 18 brackets all around to withstand the moment created by the cantilevered calorimeter.
New elements
Existing elements

## Slide 4: Back flange. Design decision.
Diego G. Robles
Previously, 2 design options
Fixed solution
Multilayer Elastic Ring
1.18 mm
Top
Bottom
Elastic solution reduce the displacement on the top area compared to the fixed solution by around 1mm.
Tilting of the HGCAL assembly is higher with the flexible solution.
Elastic ring solution induce a drop of 2.4 mm in Y direction compared to the fixed solution.
Decision taken in internal CMS reviews

## Slide 5: Back flange. Final design
Diego G. Robles
The back flange will be attached to the support tube by the fixed interface:
The 3 sections of the back flange will be assembled by 8 pins and 72 screws:

## Slide 6: Back flange. Installation of HGCAL on the detector
Diego G. Robles
Installation
Shimming system
Shims for filling gap
Y axis shims (+5mm/-3mm)
Back pusher piece to receive the displacement of the support tube
Z axis shims for compensation
(+3.5mm/-3.5mm)

## Slide 7: Brackets
Diego G. Robles
The brackets will be reused.
Stresses on the brackets are recalculated considering the new load case.
We are studying the brackets in detail, and we will probably manufacture some new ones for the most solicitated positions.
18 brackets

## Slide 8: ME1/1 shielding
Diego G. Robles
The radiation shielding is located around ME1/1, attached to the interface tube, YN1 and the bottom part of the back flange.
Consisting of lead and borated polyethylene.
Back flange
ME1/1
Interface tube
Nose YN1
Shielding
The old shielding fixed to the back flange
will be removed in the extraction of the calorimeter.
New back flange has different design.
Need to design a new shielding piece.

## Slide 9: Project status
Diego G. Robles
Back flange status:
3D models finalized including the fixed interface and shimming system
Overall simulation completed
Check of the interface with support tube completed
Next steps:
Manufacturing 2D drawings on going
General check with HSE
drawings
simulation
ME1/1 shielding status:
ME1/1 team doing radiation simulations
Design of the new shielding
Brackets status:
Overall simulations completed
Test the material of the brackets in the detector to identify it.
Searching for an adequate material
Decide how many manufacture

## Slide 10
Thank you
for your attention
Diego G. Robles