## Slide 1: Engineering and design of interface systems to integrate the new 250-tonne high-granularity calorimeter into the CMS detector
Speaker: Diego García Robles (EP-CMX-SCI)
Supervisor: Tristan Loiseau (EP-CMX-SCI)
FTEC-2021-09
Workshop 18/01/2023

## Slide 2: Introduction
Diego G. Robles
Present endcap calorimeter
HGCAL design
Integrate a brand-new calorimeter in an existing 20-year-old structure
Need to design interface systems and components.

## Slide 3: Introduction. Components for HGCAL
Diego G. Robles
New elements
Existing elements
New components for HGCAL
designed by me:
  Back flange
  ME0 shielding
  ME1/1 shielding

## Slide 4: Back flange - Introduction
Diego G. Robles
The function of the back flange is to be the direct link between HGCAL and the detector’s structure.
The back flange is mounted on the support tube, which rests the whole weight of HGCAL (250 tons) and connected by 18 brackets all around to withstand the moment created by the cantilevered calorimeter.
Wedges interface:
Brackets interface:
Back flange
Brackets
Wedges
Absorbers
Support
Tube

## Slide 5: Back flange - Design
Diego G. Robles
Installation
Right
section
~2.3t
Left
section
~2.3t
Central
section
~8.4t
Assembly:
~13.2t
72 Screws M30x70 [BUMAX 88]
72 Washers 30x56 [BUMAX 88]
8 Pins D50 [INCONEL 718]
The design was done considering the Eurocode 3 standard for structural components.

## Slide 6: Back flange - Calculations
Diego G. Robles
All components of the back flange were analyzed using FEM.
All the screws and pins were verified according to Eurocode 3 requirements.
EDMS: 2741425

## Slide 7
IP
NIP
Radiation shieldings
IP
NIP
GEM
ME0
ME1/1
ME0
Radiation shielding
Muon chambers
7
Diego G. Robles

## Slide 8: Radiation shielding
Diego G. Robles
The design for the radiation shielding consists in different layers of lead and borated polyethylene.
The layers are joined together with screws.
The shielding is fixed to the back flange by bolts.
All the FEM studies and analytical calculations show satisfactory results.
The manufacturing drawings are finished.
The design was done considering the corresponding safety standards (for lead and polyethylene).
And Eurocode 3 standard for structural components.
EDMS: 2723199

## Slide 9: Project status
Diego G. Robles
Design is finished.
Calculations are finished.
Manufacturing drawings are ready.
November 1st
Engineering Design Review (EDR)
Committee of experts at CERN
Approved the design
(very good feedback)
https://indico.cern.ch/event/1210794/
Ready for manufacturing

## Slide 10: New projects I’m working on:
Diego G. Robles
Assembly table for HGCAL
Adjustment table for Tooling C

## Slide 11: Adjustment table for Tooling C
Diego G. Robles
This table will have 6 degrees of freedom.
Allowing movements and rotations in all 3 axis.
Riser
Adj. table
50mm
50mm
± 2.5⁰

## Slide 12
Thank you
for your attention
Diego G. Robles