## Slide 1
The use of Geant4 simulations for training a DNN to perform the NeuLAND data analysis
1/16
28 Februari 2017
C. A. Douma
24 April 2019

## Slide 2
2/16
Machine Learning & DNNs
Deep artifical Neural Network (DNN)  Can learn any math. function/alogorithm
if network is complex enough
 Ideal for complex data analysis
BES-III detector
NeuLAND detector:
ID incoming neutrons
 Our case!
Resolve individual tracks in drift chamber in magnetic field.
H. de Vries, MSc thesis, RUG (upcoming).
Other applications…?

## Slide 3
Pre-acceleration
Primary accelerator
Fixed primary target
Selection of exotic fragments
 Radioactive Beam
R3B experiment
 Measure nuclear structure of the beam
3/16
R3B Experiment in a nutshell

## Slide 4
Pre-acceleration
Primary accelerator
Fixed primary target
Selection of exotic fragments
 Radioactive Beam
R3B experiment
 Measure nuclear structure of the beam
3/16
R3B Experiment in a nutshell
Full kinematic reconstruction of nuclear Reactions with Radioactive Relativistic Beams
Incoming radioactive
beam
In-beam detector for diagnostics
Fixed target + gamma spectrometer (CALIFA) & proton tracker
GLAD (bending magnet)
Outgoing fragment
 Detected by TOF wall & wire chambers
Protons (detected inside chamber)
Vacuum chamber
neutrons
Neutrons are detected by NeuLAND  Neu(=new) Large Area Neutron Detector)
R3B phase 0

## Slide 5
5/16
NeuLAND neutron detection
neutron
Scintillator bars: 50 bars per plane, 30 hor. planes & 30 vert. planes;
PMT on both ends of the bar

## Slide 6
2/19
NeuLAND neutron detection
neutron
5/16
Scintillator bars: 50 bars per plane, 30 hor. planes & 30 vert. planes;
PMT on both ends of the bar

## Slide 7
2/19
NeuLAND neutron detection
Measured PMT signals
Reconstruct (t,x,y,z,E) from TDC & QDC
5/16

## Slide 8
2/19
NeuLAND neutron detection
Our data: NeuLAND digis:
(t,x,y,z,E) signals
What we need:
Target
NeuLAND
Beam
Reaction (t,x,y,z): measured by tracking detectors
neutron
First hit (t,x,y,z)
of neutron
Reconstruct neutron momentum vector
From Reaction & First Hit.
Which one is the First hit?
5/16

## Slide 9
2/19
NeuLAND neutron detection
Our data: NeuLAND digis:
(t,x,y,z,E) signals
What we need:
Target
NeuLAND
Beam
Reaction (t,x,y,z): measured by tracking detectors
neutron
First hit (t,x,y,z)
of neutron
Reconstruct neutron momentum vector
From Reaction & First Hit.
Or how about?
5/16

## Slide 10
2/19
Use of Machine Learning
Our data: NeuLAND digis:
(t,x,y,z,E) signals
6/16
Given a set of (t,x,y,z,E)-signals:
How many first hits do they contain? (What is the multiplicity?)
Which of those signals are the first hits? (Which are the neutrons?)
Use Geant4 Monte Carlo simulations to generate data.
Feed it to a DNN for training.
But what if simulations do not represent reality?
We need accurate Geant4 physics lists!
neutrons

## Slide 11
2/19
Benchmarking of Physics Lists
7/16
SAMURAI dipole magnet
Ion TOF hodoscope
Ion-beam
Ion-beam
NEBULA detector
SAMURAI setup: T. Kobayashi
et al., NIMB 317, 294 (2013)
NeuLAND demonstrator
(8x50 bars, 4 double planes): K. Boretzky et al., MU-NUSTAR-NR-12,
GSI report 2014
Simulation done by: J. Mayer, Ph.D. thesis, Universität zu Köln (2018)
 Benchmark single-neutron detection efficiency

## Slide 12
2/19
Benchmarking of Physics Lists
8/16
Energy deposition threshold in full NeuLAND [MeV]
Single-neutron detection efficiency [%]
BERT: Bertini cascade model & quark-gluon string model with low E neutron physics
BIC: same, but uses Binary Cascade model
INCL++: same, but uses Liege Intranuclear Cascade model & N-reactions A≤18
Our observation:
Exp ≈ ½ (BERT+INCL++)
What causes the diff. between phys. lists?
Consequences for DNN?

## Slide 13
2/19
Shower developement
9/16
 Study in the simplest configuration
250 MeV neutrons
One single NeuLAND scintillator: 5x5x250 cm
CH2 material & Al-foil
Study PDG & scat. angles of strictly sec. tracks
Phys. List | Interactions:
QGSP_INCLXX_HP | MC: 7.15% Det: 4.75%
QGSP_INCLXX | MC: 7.22% Det: 4.81%
FTFP_INCLXX_HP | MC: 7.20% Det: 4.79%
QGSP_BERT_HP | MC: 7.21% Det: 3.88%
QGSP_BIC_HP | MC: 7.21% Det: 4.48%
QBBC | MC: 7.15% Det: 4.45%
ShieldingM | MC: 7.17% Det: 3.89%
106 events simulated  ≈0.1% stat. inaccuracy.
MC: #events where sec. tracks were created.
Det: #events where both PMTs fired.
Interaction rate is ≈ same.
Diff. in detection rate due to what?

## Slide 14
2/19
10/16
QSGP_BERT_HP
QSGP_BIC_HP
QBBC
QSGP_INCLXX
Energy deposition
FTFP_INCLXX_HP
QSGP_INCLXX_HP
Protons
Deuterons
Tritons
Alphas
Other
Only INCL++ has significant (d,t,a) contributions
Deposited Energy [MeV]
Deposited Energy [MeV]
Deposited Energy [MeV]
Deposited Energy [MeV]
Deposited Energy [MeV]
Deposited Energy [MeV]
Deposited Energy [MeV]
ShieldingM

## Slide 15
2/19
Particle tracks
11/16
Behaviour is ≈ same for all physics lists
Height is slightly different due to number of protons
ShieldingM & BERT produce less protons than the others
Scattering behaviour is ≈ same
 Differences are: nr. of produced protons & presence of (d,t,a) tracks.
Protons

## Slide 16
2/19
Particle tracks
11/16
The produced deuterons also deposite (a lot) more energy for INCL++.
INCL++ has more deuterons & they are slightly more forward boosted.
Deuterons

## Slide 17
2/19
Particle tracks
11/16
Scattering behaviour is ≈ same as for deuterons (just less particles).
Edep is also ≈ same for non-INCL++ models
Tritons

## Slide 18
2/19
Particle tracks
11/16
Low energy deposition is ≈ same.
Few a-particles at higher energies, except for INCL++.
Number of a-particles differs.
Scattering behaviour is ≈ same.
Alphas

## Slide 19
2/19
Comparing the contributions
12/16
250 MeV neutrons:
NeuLAND demonstrator
4 double planes @ 11m
Geometry & event generator are slightly different from J. Mayer, Ph.D. Thesis
 So no benchmarking to exp. data (still working…)
We need: exp ≈ ½ (BERT + INCL++)
We see: |BERT – INCL++| = 50% due to (d,t,a) tracks
= 25% due to nr. of prod. protons
= 25% other/indirect causes
NB: probably not realistic to have (almost) no (d,t,a) Energy deposition (CH2 scintillators).

## Slide 20
2/19
Physics list effects on DNN
13/16
High neutron detection efficiency
Low neutron detection efficiency
Single neutron detection efficiency @ 250 MeV & 4 double planes:
20% – 32% (dep. on Ethres) & |BERT – INCL++| ≈ 8%
DNN uses neighbouring relations to find primaries
M. Polleryd, M.Sc. thesis, Chalmers University (2017)
Physics list effects could be significant.
DNN is still under development
Use classical methods to estimate effects

## Slide 21
2/19
Physics list effects
14/16
Traditional Method for multiplicity determination:
Simulate INCL++ & BERT
exp ≈ ½ (BERT + INCL++)
30 double planes
for NeuLAND @
14 m distance
SEdep
#clusters
 | 200 MeV | 600 MeV | 1000 MeV
0n | 77±4% | 74±1% | 74±1%
1n | 73±8% | 79±2% | 80±1%
2n | 62±11% | 65±1% | 71±1%
3n | 58±10% | 56±1% | 61±1%
4n | 46±8% | 52±3% | 54±3%
5n | 57±8% | 61±2% | 62±4%
Physics lists errors are larger at lower energies
Relative errors: larger at higher multiplicities
NeuLAND is designed to detect high multiplicities
1n
2n
3n
4n
5n

## Slide 22
2/19
Physics list effects
14/16
Traditional Method for multiplicity determination:
Simulate INCL++ & BERT
exp ≈ ½ (BERT + INCL++)
 | 200 MeV | 600 MeV | 1000 MeV
0n | 77±4% | 74±1% | 74±1%
1n | 73±8% | 79±2% | 80±1%
2n | 62±11% | 65±1% | 71±1%
3n | 58±10% | 56±1% | 61±1%
4n | 46±8% | 52±3% | 54±3%
5n | 57±8% | 61±2% | 62±4%
Physics lists errors are larger at lower energies
Relative errors: larger at higher multiplicities
NeuLAND is designed to detect high multiplicities
Physics list errors grow when detector gets smaller.
200 MeV | 600 MeV | 1000 MeV
82±2% | 82±1% | 83±1%
43±32% | 63±3% | 63±1%
57±5% | 51±1% | 52±1%
43±15% | 42±1% | 44±1%
49±12% | 41±2% | 37±1%
35±15% | 48±5% | 50±1%
Full NeuLAND detector: 30 double planes
Partial NeuLAND detector: 12 double planes

## Slide 23
2/19
Conclusion
15/16
NeuLAND detects fast neutrons: 100 MeV – 1000 MeV.
Benchmarking revealed: exp ≈ ½ (QGSP_BERT_HP + QGSP_INCLXX_HP)
for single-neutron detection efficiency.
Diff. = 50% due to (d,t,a) tracks, 25% due to nr. of prod. protons & 25% other.
Effects are <2% at higher energies, but very significant at lower energies.
These differences prevent us from properly training our DNN.
 A new physics list is needed with:
- Edep from (d,t,a) tracks & nr. of prod. protons between BERT & INCL++.
- neutron detection eff. (Edep in CH2 scintillators): ½ (BERT + INCL++).
- implement with special attention at lower neutron energies.

## Slide 24
16/16
Thank you!