## Slide 1: ExpertRoot. A GEANT4 and FairRoot based Sim and Reco framework for experiments at ACCULINNA2 and SuperFRS facilities
Mikhail Kozlov1,5; Sergey Belogurov1,2; Vratislav Chudoba1,3; Andrey Fomichev1; Elvira Gazeeva1; Alexander Gorshkov1; Sergey Krupko1; Bakytbek Mauey1; Ivan Muzalevskiy1,3; Egor Ovcharenko1,4; Anh Mai Quyn1; Ilyas Saityshev1; Vitaliy Schetinin1,5
1 - JINR, Dubna; 2 - NRNU MEPhI, Moscow; 3- Silesian University, Opava; 4- Uni. Giessen; 5 - BMSTU, Moscow

## Slide 2: Outlook
Introduction
Architecture
Event based workflow
Example of an experiment
Simulation “step by step”
Real data handling
Event reconstruction
Summary and plans
G4 feedback

## Slide 3
ExpertRoot is a FairRoot based framework for simulation of detector`s response, event reconstruction and real data analysis in low energy nuclear physics with radioactive beams
ExpertRoot is used for the EXPERT1 project at SuperFRS@FAIR and for the experiments at ACCULINNA-2 fragment-separator in JINR
er.jinr.ru
1 EXPERT - EXotic Particle Emission and Radioactivity by Tracking
Introduction

## Slide 4
Gadast
NeuRad
Si
OTPC
Gadast – GAmma Detectors Around Secondary Target
NeuRad – NEUtron RADioactivity
OTPC – Optical TPC
Si – microstrip Si-detector
Introduction: EXPERT

## Slide 5
E-station
E-station
Veto-station
QTelescope
Introduction: ACCULINNA-2, part of the current setup

## Slide 6: Architecture

## Slide 7: Event-based workflow
common format of the output data,
so the same reconstruction algorithms are used!

## Slide 8: Example of an experiment
On each step in sensitive volume energy losses are summed up for every particle via ROOT interface to Geant methods
Information about generated primary tracks and daughter secondary particles are stored in MCTrack class object
Target
MWPC-2
MWPC-1
QTelescope-2
Triton
Helium-3
neutron
Helium-6
Tracks
QTelescope-1

## Slide 9: Ion mixture generator
Ion
Ion’s occurring probability
P
0.55
0.1
0.2
0.15
ToF-dE
0.15
0.1
0.2
0.55
ToF
Denomination:
An arbitrary count of mixed particles;
Probability of ion occurring is normalized related to main ion in mix;
The same magnetic rigidity ;

## Slide 10: User defined interactions architecture

## Slide 11: An interaction on the target
Calculation of the material thickness among the trajectory length ;
Normalization of the probability relatively to maximal material thickness on the particle path;
Exponential distribution on the interval

## Slide 12: Work with process stack example
+ → + - theoretical cross-section
→ + + - TGenPhaseSpace
Erase primary track: gMC->StopTrack()
is not pushed into track stack
Add track to the stack of processes: gMC->GetStack()->PushTrack(1, He6TrackNb, fH3->PdgCode(),
lvH3->Px(),lvH3->Py(),lvH3->Pz(),
lvH3->E(), curPos.X(), curPos.Y(), curPos.Z(),
gMC->TrackTime(), 0., 0., 0.,
kPDecay, h3TrackNb, fH3->Mass(), 0); where is He6TrackNb - track number, fH3 – triton ion object, lvH3 – triton four-vector, curPos – current particle position.

## Slide 13: Detector simulation
Point object is created for each particle in every sensitive volume:
“In” and “out” coordinates
“In” and “out” momentum
PDG,
“In” time
Other detector specific information.
Parameter
container

## Slide 14: Detector geometry parameterization
BeamDet
QTelescope
BeamDet.xml
QTelescope.xml
Spreadsheets
(MS Excel at present time)
Medium

## Slide 15: Digitization
Digitization – task consists of summing up energy deposited by all the particles in the sensitive volume, application of energy and time spread corresponding to the resolution of the detector, taking into account inefficiency of various nature (e.g. dead time) and discretization.
Digi – object contains the characteristics of the detector response.
Digi object is created for each particle in every sensitive volumes:
R/O channel number,
Energy response, recorded to the channel,
Timestamp
Other detector specific information.

## Slide 16: Digitization
  Birks quenching
  Position sensitivity obtained by limiting lengths of a point to 2 [cm],
  Exponential lighting emission kinetics
  light attenuation
  quantum efficiency
  dinode system modeling:
    using special distribution of photoelectron amplitude
    using user-defined function of photoelectron signal shape
    delay and jitter
    signal creation as a sum of signals from single electrons
Example: NeuRad - neutron detector with scintilating fibers along the path of neutron

## Slide 17: Real data handling

## Slide 18: Event reconstruction
Coordinates
Angle distributions
Four-vectors

## Slide 19: G4EMCalculator in reconstruction

## Slide 20: Summary and plans
ExpertRoot framework is developed for simulation and reconstruction of the experiments with low energy exotic beams.
A full lifecycle functionality is implemented for the 5H and 7H experiments and can be easily extended to other examples.
The framework helps to combine efforts of physicists, detector experts and IT specialists
Plans:
Implement more usecases and make the framework more userfriendly
Develop a cloud service using Jupyter Notebook interface to Root
Extend interface to theoretical generators. In particular interpolate multiparticle output between the provided energies observing the momentum and energy conservation and phase space factor and introduce realistic background

## Slide 21: G4 feedback
Limitation:
Calling G4EmCalculator->GetDeDx() requires full initialization of Geant4 in VMC:
TG4RunConfiguration initialization
TGeant4 initialization
Fake processing of first event for initialization of other environment
Desire:
Possibility to use the G4EmCalculator without initializing the entire Geant4 simulation would be extremely convenient.