## Slide 1
photo: J. Wenninger
Work supported by the European Commission under the HORIZON 2020 projects EuroCirCol, grant agreement 654305; EASITrain, grant agreement no. 764879; iFAST, grant agreement 101004730, FCCIS, grant agreement 951754; E-JADE, contract no. 645479; EAJADE, contract number 101086276; and by the Swiss CHART program
http://cern.ch/fcc
Frank Zimmermann, CERN
on behalf of FCC collaboration & FCCIS DS team
warm thanks to S. Atieh, B. Auchmann, M. Benedikt, R. Kersevan, S. Mazzoni, and R. Ruprecht
FCC Accelerator R&D
“FCC Day - Spain”, 7 October 2024

## Slide 2: FCC-ee main machine parameters
F. Gianotti
Parameter | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
beam current [mA] | 1270 | 137 | 26.7 | 4.9
number bunches/beam | 11200 | 1780 | 440 | 60
bunch intensity [1011] | 2.14 | 1.45 | 1.15 | 1.55
SR energy loss / turn [GeV] | 0.0394 | 0.374 | 1.89 | 10.4
total RF voltage 400/800 MHz [GV] | 0.120/0 | 1.0/0 | 2.1/0 | 2.1/9.4
long. damping time [turns] | 1158 | 215 | 64 | 18
horizontal beta* [m] | 0.11 | 0.2 | 0.24 | 1.0
vertical beta* [mm] | 0.7 | 1.0 | 1.0 | 1.6
horizontal geometric emittance [nm] | 0.71 | 2.17 | 0.71 | 1.59
vertical geom. emittance [pm] | 1.9 | 2.2 | 1.4 | 1.6
vertical rms IP spot size [nm] | 36 | 47 | 40 | 51
beam-beam parameter xx / xy | 0.002/0.0973 | 0.013/0.128 | 0.010/0.088 | 0.073/0.134
rms bunch length with SR / BS [mm] | 5.6 / 15.5 | 3.5 / 5.4 | 3.4 / 4.7 | 1.8 / 2.2
luminosity per IP [1034 cm-2s-1] | 140 | 20 | ≥5.0 | 1.25
total integrated luminosity / IP / year [ab-1/yr] | 17 | 2.4 | 0.6 | 0.15
beam lifetime rad Bhabha + BS [min] | 15 | 12 | 12 | 11
Improvements:
x10-50 on all EW observables
up to x 10 on Higgs coupling (model-indep.) measurements over HL-LHC
x10 Belle II statistics for b, c, τ
indirect discovery potential up to ~ 70 TeV
direct discovery potential for feebly-interacting particles over 5-100 GeV mass range
Design and parameters to maximise luminosity at all working points:
allow for 50 MW synchrotron radiation per beam
.
Independent vacuum systems for electrons and positrons
full energy booster ring with top-up injection, collider permanent in collision mode
Up to 4 interaction points
 robustness, statistics, possibility of specialised detectors to maximise physics
3 years
2 x 106 H
5 years
2 x 106 tt pairs
2 years
> 108 WW
LEP x 104
4 years
5 x 1012 Z
LEP x 105

## Slide 3
Same two-cell RF cavities for Z, WW and ZH operation with constant cavity coupling thanks to reverse phase operation: (1) experimentally verified w high beam loading at KEKB (Y. Morita et al., 2009), (2) Baseline solution US EIC
No longer any 1-cell 400 MHz cavities
Reduced installation time
Reduced commissioning effort
Fast switching between Z, WW and ZH operation
RF waves
LEP
400 MHz cryomodule, ~12 m long
400 MHz 2-cell cavity
Niobium thin film on Copper,
Operation at 4.5 Kelvin
Max. accel. gradient Eacc = 13 MV/m
Quality factor Q0 = 3.3 x 109
Z, W, ZH
X 264
X 66
400 MHz cavities
cryomodule
400 MHz SRF progress – one system for 3 energies

## Slide 4
Beam switching between (Z, W) and ZH operation
  RF section: ES separators + magnetic field to not emit SR towards RF cavities
  Allows quasi “instantaneous” switching between Z, W, ZH
33 CM
Beam 1
Beam 2
33 CM
33 CM
33 CM
400 MHz
400 MHz
400 MHz
400 MHz
ZH
Z, W
E&M
sep.1
E&M
sep. 2a
E& M
sep. 2b
Collider RF integration at point H
(Z, WW and ZH operation)
extra year of operation thanks to single RF system
Beam crossing and combination
at RF section in point H
SRF integration and beam switchyard

## Slide 5
RF system R&D is key for increasing energy efficiency of FCC-ee
Nb on Cu 400 MHz cavities, seamless cavity production, coating techniques
Bulk Nb 800 MHz cavities, surface treatment techniques, cryomodule design
RF power source R&D in synergy with HL-LHC.
400 MHz cavity production
in coll. w German industry
800 MHz cavity and CM design collaborations with JLAB and FNAL
high-efficiency klystron R&D
in collaborations with THALES & CANON
~7 m
monoblock prototype
800 MHz segmented design, based on PIP-II
RF R&D activities

## Slide 6
C. Pira
Move from Nb @2K to Nb3Sn @4.5 K would reduce cryogenic power by a factor of 3
Nb3Sn on Cu coating
Equivalent to a Q of 9*109 @5 MV/m @4.5 K
Almost 1 order of magnitude better than LHC !
Room for improvement
4.5 K
QPR Nb3Sn
FCC 1 cell
QPR Nb3Sn
G=216 Ω
4.5 K
Nb on Cu coating
(FCC baseline)
Seamless production
SEM micrograph of the film cross section
SRF: seamless cavities & thin film coating

## Slide 7
.
GHC https://journals.aps.org/prab/abstract/10.1103/PhysRevAccelBeams.19.111005
LCC https://indico.cern.ch/event/1326738/timetable/#45-alternative-optics-and-vari
Average betas ~ 105m
Peak betas ~ 175m
Average betas ~ 85m
Peak betas ~ 120m
K. Oide, UNIGE; P. Raimondi, FNAL; S. Liuzzo, S. White, ESRF; K. Andre, M. Hofer, G. Roy, CERN
Local Chromatic Correction (LCC)
Global Hybrid Correction (GHC)
FCC-ee optics baseline & alternative
FODO lattice, many -I sext pairs; periodic unit cell length 520 m
hybrid FODO lattice,
with few sext. families,
periodic unit cell length300 m
5 sext.s per final focus, modular
“1.5” sext.s per final focus,
asymmetric

## Slide 8
Arc cell optimisation – 80 km total system length, dedicated working group active
Including support, girder and alignment systems, shielding systems
vacuum system with antechamber + pumps, dipole, quadrupole + sext. magnets, BPMs,
cabling, cooling & technical infrastructure interfaces.
Safety aspects, access and transport concept,
FCC-ee arc half-cell mock up
arc layout and integration optimisation
A. Piccini, F. Carra, et al.

## Slide 9
Twin-dipole design with 2× power saving
16 MW (at 175 GeV), with Al busbars
Twin F/D arc quad design with 2× power saving
25 MW (at 175 GeV), with Cu conductor
prototype
prototype
even more efficient alternative magnet designs are being explored
FCC-ee low-power arc magnets - baseline
A. Milanese, Efficient twin aperture magnets for the future circular 𝑒+/𝑒- collider, Phys. Rev. Accel. Beams 19, 112401
CDR: 5800-8700 dipoles, 2900 quads
& 4700 sextupoles for collider arcs
FCC-ee magnet contributions from Spain?
design, prototyping …

## Slide 10
Key topics:
SC IR magnet system & cryostat design
3D integration
IR mock-up / INFN
Q1 prototype tested at cold in SM18 (CERN), October ‘23
M. Koratzinos, PSI
M. Boscolo, F. Palla, INFN
J. Seeman, SLAC
P. Tavares, CERN
FCC-ee machine detector interface
cryostat experts at CIEMAT or elsewhere in Spain?

## Slide 11
K. Andre, Y. Dutheil, M. Hofer R. Ramjiawan, CERN; P. Hunchak, CLS & U Saskatchewan
Off-axis top-up injection challenging at Z due to large orbit excursion and slow damping. SR intercepted by the last mask 0.2mJ/Xing compared 0.8µJ/Xing from colliding beam
preference for longitudinal injection
top-up injection from full energy booster into collider rings
expertise, tests or studies at ALBA/CELLS (?)

## Slide 12
FCC-ee beam diagnostics: X-HNFS at ALBA,… BPMs IFMIF
X-ray Heterodyne Near Field Speckles
M. Siano et al., Proc. IBIC’21 (2021)
M. Siano et al., PRAB 25, 052801 (2022)
M. Siano et al., Proc. IPAC’23 (2023)
U. Iriso, M. Siano,
S. Mazzoni, et al.
Targets will be tested in NCD beamline (undulator radiation) early 25.
Tests in FE21 beamline starting 2nd half of 2025
ALBA developing FE21 speckles beamline with 23.7 KeV, 1% monochromator BW dipole radiation
Uni Milan developing nanostructured, High Z targets for tests at ALBA in 2025.
world leading beam diagnostics
- an asset for the FCC !

## Slide 13
Mid-term review recommendations to reduce gradients and repetition rate  new linac optimization in terms of cost and power density
  Overall power consumption (for linacs) is reduced by more than a factor 3 by means of:
    new accelerating structures with higher shunt impedance;
    lower gradient (29.5 MV/m  22.5/20.5 MV/m);
    lower repetition rate (200/400 Hz  100 Hz).
  Repetition rate of 100 Hz with 4 bunches per rf pulse
  New layout: Damping Ring at higher energy 2.86 GeV, no common linac with 2x repetition rate.
Optimized injector concept and parameters
synergies with ALBA or S-band linac developments in Spain

## Slide 14
Installation works at SwissFEL progressing smoothly during SwissFEL shutdowns (3 per year):
    Parts of dedicated extraction line and HV klystron-modulator system accommodated in the tunnel
    Procurement and assembly of most accelerator and diagnostics components on schedule
    Operation of the HTS solenoid successfully demonstrated at PSI (up to 18 T)
    Radiation tests on dedicated HTS solenoid in the beamline of the PSI cyclotron under discussion.
Start of operation with e+ expected in 2026.
Status of PSI Positron Production experiment (P3)

## Slide 15
polarization transmission 90% (Z), 60%(W), 15%(H) and 0 (top) for different error seeds and lattices
booster errors assumed
Z. Duan, IHEP
Z. Duan, IHEP
J. Heron et al., CERN
polarization preserved in the booster
pre-polarized injection increases availability
injecting polarized pilot bunches ?

## Slide 16
nonlinear collimation – gift from Spain to SuperKEKB
2006
2024
nonlinear collimation options for FCC-ee not yet studied
– does Spain jump into the breach ?

## Slide 17
past Spanish efforts & expertise in collider design
1992
1993
1996

## Slide 18
FCC-ee monochromatized s-channel Higgs production

## Slide 19
FCC-ee monochromatization optics & performance
Monochromatization at 125 GeV
create opposite-sign
D*x
D*y
So far best performance is obtained with ttbar lattice based “mix” mode, which reaches ye< 2.9*ye(SM) in the Higgs-electron Yukawa coupling
A. Faus-Golfe, Z. Zhang, P. Raimondi, K. Oide, F. Z.
optional running mode for FCC-ee enabled by Spanish expertise; e- Yukawa coupling is “the main reason to build the FCC-ee” (prominent CMS physicist”)

## Slide 20
F. Gianotti
Formidable challenges:
high-field superconducting magnets: 14 - 20 T
power load in arcs from synchrotron radiation: 4 MW  cryogenics, vacuum
stored beam energy: ~ 9 GJ  machine protection
pile-up in the detectors: ~1000 events/xing
energy consumption: 4 TWh/year  R&D on cryo, HTS, beam current, …
Formidable physics reach, including:
Direct discovery potential up to ~ 40 TeV
Measurement of Higgs self to ~ 5% and ttH to ~ 1%
High-precision and model-indep (with FCC-ee input)
measurements of rare Higgs decays (𝛄𝛄, Z𝛄, µµ)
Final word about WIMP dark matter
With FCC-hh after FCC-ee: significantly
more time for high-field magnet R&D
aiming at highest possible energies
parameter | FCC-hh | HL-LHC | LHC
collision energy cms [TeV] | 84 - 120 | 14 | 14
dipole field [T] | 14 - 20 | 8.33 | 8.33
circumference [km] | 90.7 | 26.7 | 26.7
arc length [km] | 76.9 | 22.5 | 
beam current [A] | 0.5 | 1.1 | 0.58
bunch intensity [1011] | 1 | 2.2 | 1.15
bunch spacing [ns] | 25 | 25 | 25
synchr. rad. power / ring [kW] | 1100 - 4570 | 7.3 | 3.6
SR power / length [W/m/ap.] | 14 - 58 | 0.33 | 0.17
long. emit. damping time [h] | 0.77 – 0.26 | 12.9 | 12.9
peak luminosity [1034 cm-2s-1] | ~30 | 5 (lev.) | 1
events/bunch crossing | ~1000 | 132 | 27
stored energy/beam [GJ] | 6.3 – 9.2 | 0.7 | 0.36
Integrated luminosity/main IP [fb-1] | 20000 | 3000 | 300
FCC-hh main machine parameters

## Slide 21
Cos-theta
Blocks
Common coils
Swiss contribution
Canted
Cos-theta
H2020
INFN
CEA
CIEMAT
PSI
LBNL
FNAL
FCC-hh: EuroCirCol 16 T dipole design activities & options
M. Benedikt, Granada, May 2019

## Slide 22
CIEMAT is producing correctors MCBXH/V for HL-LHC
In ‘ISAAC’ assembly, coils fabricated at CERN will be assembled into a common-coil layout end of Q1/25. The mechanical design was made by CIEMAT.
CIEMAT high-field demonstrator magnet ‘DAISY’ should be tested in 2026.
new laboratory
CIEMAT high-field magnet development for FCC-hh
CIEMAT as one of the global leaders in HFM

## Slide 23
Hybrid REBaCuO-Cu Coating for the FCC-hh Beam Screen
HTS coated FCC-hh beam screen
G. Telles et al., Institut de Ciència de Materials de Barcelona (ICMAB – CSIC), ALBA Synchrotron Light Source, Universitat Politècnica de Catalunya (UPC), CERN
objectives: good field quality, low impedance
world leading beam screen
developments for the FCC-hh !
first proposed by L.Rossi,
CERN-ATS-2012-23

## Slide 24
FCC-hh beam screen & photon desorption
F. Perez, M. Gil Costa, R. Kersevan, R. Ruprecht, et al.
design effort (EuroCirCol 2015-2019) was spearheaded by ALBA/CELLS

## Slide 25
FCC beam screen test-bench experiment (BESTEX)

## Slide 26
Installation of test chamber at KARA BESTEX
whole test chamber with ancillary diagnostic equipment being moved by the crane
total time to change sample ~5 days

## Slide 27
Next step: FCC-ee beam pipe prototype for BESTEX
Spain back on board?

## Slide 28
other FCC-ee science applications under study
for example:
FCC-ee booster as diffraction limited storage ring with coherent synchrotron radiation down to 0.1 Å
FCC-ee injector as the world’s ultimate positron source for material studies and paving a path towards the first Bose-Einstein condensation of Ps (511-keV gamma-ray laser)
using beamstrahlung for radionuclide production
e- beam driven neutron source
etc.
S. Casalbuoni
M. Calviani,
C. Duchemin
M. Doser,
B. Rienäcker
→ Workshop on “Other Science Opportunities at the FCC-ee”
28-29 November at CERN, https://indico.cern.ch/event/1454873/
input and ideas welcome!
please contribute

## Slide 29
opportunities for Spain – a few ideas in a nutshell
magnets for collider or booster
arc vacuum system
support structures, survey & alignment systems
beam diagnostics – beam size, beam loss & beam position monitors
IR magnet cryostat
collimators and design of nonlinear collimation system
high-field magnets
lower-field HTS magnets for FCC-ee
top-up injection
optics design ?
other science applications at FCC-ee including photon science
beam tests at ALBA/CELLS

## Slide 30: FCC overall organigram
whom to contact …

## Slide 31
from the Habsburg empire
FCC Day Spain 2024
FCC Week 2025
Hofburg Palace, in Vienna, Austria, Monday 19 to Friday 23 May 2025
Come & join !
to the FCC

## Slide 32
muchas gracias por su atención

## Slide 33
spare slides

## Slide 34
beam-beam performance @ HZ
design luminosity
PIC code, nonlinear lattice
soft Gaussian, nonlinear lattice
PIC code, linear optics
soft Gaussian, linear optics
design bunch charge
K. Ohmi, KEK
beam-beam codes & approximations validated ; design performance reached & exceeded

## Slide 35
beam-beam performance @
K. Oide, UNIGE
vert. emittance w/o collision
beam lifetime
equilibrium emittance in collisions
SAD simulation
need for a small vertical “lattice emittance” ; ~50% blow up in collision;
beam lifetime dominated by burn-off (not included here)

## Slide 36
CDR arc lattice
HTS option proposal
CDR: 2900 quads & 4700 sextupoles
Normal conducting, ~50 MW @ ttbar
3 different types of short straight sections
“HTS4” project within CHART collaboration
Nested SC sextupole and quadrupole.
HTS conductors operating at around 40K.
Cryo-cooler supplied cryostat
Produce a 1m prototype by 2026
“LCC” arc optics
Power saving
Relaxed tolerances
No longer twin magnets
M. Koratzinos, B. Auchmann
options for FCC-ee arc quads and sextupoles
P. Raimondi
Modified CDR optics – same from Z to ZH
Higher filling factor, less cables
Reduced cost
More operational flexibility in 1st phase
C. Garcia, R. Tomas,
F. Zimmermann
Combined Function magnets
Higher filling factor
C. Garcia, R. Tomas

## Slide 37
regular arc
interaction region
FODO lattice, many -I sext pairs; periodic unit cell length 260 m
hybrid FODO lattice,
with few sext. families,
periodic unit cell length300 m
5 sext.s per final focus, modular
“1.5” sext.s per final focus,
asymmetric
K. Oide
K. Oide
P. Raimondi
P. Raimondi
C. Garcia,
R. Tomas, et al.
optimisation goals:
reduced power consumption
lower SR energy loss
increased momentum acceptance
relaxed tolerances
larger dynamic aperture
simplified powering schemes
FCC-ee optics baseline & further evolutions

## Slide 38
FCC-ee accelerator R&D focus
key items, cost drivers & energy efficiency:
  SRF system – SC cavities, cryomodules, power source
  arc magnets – dipoles quad’s, sext’s for collider & booster
  arc vacuum chamber with photon stops, shielding, NEG…
  support structures, survey & alignment systems
  arc beam diagnostics – beam loss & beam position monitors
  ..
special & challenging components
  IR elements, SC IR magnet system, IR supporting structures
  special diagnostics: polarimetry, beamstrahlung monitors,…
  collimators