## Slide 1
Quantum Computing
May 5th 2022, Madrid
Philippe Chomaz
Scientific and Program Director of CEA Basic Research
With the help of Florent Staley

## Slide 2: Quantum computing
”Nature isn’t classical, dammit !
if you want to make a simulation of Nature,
you’d better make it quantum mechanical”
Richard Feynman at the conference on "simulating physics with computer" on May 1981
Quantum Computing is the use of quantum-mechanical phenomena such as superposition and entanglement to perform computation of a new kind.
Richard Feynman's post-Nobel lecture at CERN, 1965

## Slide 3
Quantum 1.0 and the Digital Revolution
1

## Slide 4: Quantum Revolutions
Quantum 1.0 and the digital revolution:
Macroscopic quantum systems of bosons or fermions with quantized energies have revolutionized information technology:
computing, sensing, communication.
lasers
micro electronic
“Invention” of quantum mechanics:
Matter, light and interactions composed of particles
governed by a wave mechanics.
2 wave packets
Many others

## Slide 5: Quantum Revolutions
Quantum 1.0 and the digital revolution:
Macroscopic quantum systems of bosons or fermions with quantized energies have revolutionized information technology:
computing, sensing, communication.
lasers
micro electronic
“Invention” of quantum mechanics :
Matter, light and interactions composed of particles
governed by a wave mechanics.
2 wave packets
Many others

## Slide 6: Quantum 1.0: Revolution of information treatment
Electronic et photonic
the revolution in information and communication technologies
1959 Jack S. Kilby handling the first integrated circuit
1947 First Transistor at Bell Laboratories

## Slide 7: Quantum 1.0: Revolution of information treatment
Ordinateur classique
Processed with logic gates
(transistors)
NOT and a single 2 bit gate (as XOR) are enough => Universal Turing
Machine
Classical computers
2020
Are reaching the limit of one atom per bit
Elementary information:
Bit: 0 or 1
1959 Jack S. Kilby handling the first integrated circuit
1947 First Transistor at Bell Laboratories
0 or 1
0 or 1
0 or 1
0 or 1
0 or 1

## Slide 8
Quantum 2.0 and the disruption of information technology
2

## Slide 9: Quantum 2.0 : Mastering individual quantum “objects”
Same quantum degrees of freedom
but
going from a macroscopic ensemble
to individual states
Huge paradigm shift
for the accessible space of possibilities
=> access to the huge space of quantum states
(Hilbert/Fock space)
=> access the "strangest" quantum phenomena
  Superposition
  Non-locality
  Entanglement
Single photon source
Quantum 2.0: Opens a new world
Mastering individual quantum “objects”
ie individual quantum degrees of freedom
Single photon source
Matrices de µLEDs
Microlaser en GeSn
Germanium laser
Quantum 1.0: Reaching its end
Manipulating macroscopic quantum systems
ie with many quantum “objects”

## Slide 10: Superposition & Entanglement
Superposition of states :
  Example of an object with 2 states : quantum bit or Qubit
Entanglement :
  Superposition of states of several objects,
  ex 2 objects with 2 states
I01> = I0>*I1>
I11> = I1>*I1>
I00> = I0>*I0>
I10> = I1>*I0>
I 1 >
I 0 >
An infinity of states “simultaneously" 0 and 1 : I state > = a I 0 > + b I 1 >
N “objects” => 2N dimensions space, ex 2 qubits : I state > = a I00> + b I01> + g I10> + d I11>
Coupled quantum objects cannot be thought individually
Example : I00> + I11>  (aA I0> + bA I1>) * (aB I0> + bB I1>)
Superposition => Entanglement
Coupled quantum objects cannot be thought individually => they are entangled
access to the huge space with 2N dimensions of entangled states
2N evolutions of all the solutions « at the same time »

## Slide 11: Superposition & Entanglement
I0>
I1>
I0>
I00> + I11>
I1>
Particle A
Particle B
Measure A
Measure B
“simultaneously" I00> and I11>
Entanglement far beyond the classical world
New York Times, May 4th 1935
Quantum entanglement — a "spooky action at a distance" as Albert Einstein famously called it
W. Mittig et al, EPR and Bell’s inequalities with protons
A. Aspect et al, EPR and Bell’s inequalities with photons
  Quantum information beyond classical one,
  ie no hidden variables,
  access to a huge space of entangled states
  Particle A and particle B are correlated at a distance
  Measurement on particle A affects (projects) particle B
1982, John Bell

## Slide 12: Quantum 2.0: the promised disruptions for ICT
Mastering individual quantum “objects”: ultimate sensitivity
Entangling distant “objects”: inviolable and disruptive communications
Massive entanglement: unprecedented massive computing capabilities

## Slide 13: Quantum 2.0: Major difficulties
Fabrication challenges:
  Even more difficult then the 1st quantum revolution
1947, 1st Transistor
2020, 54 milliard transistors
1971, 2 300 transistors.
Sources of
decoherence
I 1 >
I 0 >
I 1 >
I 0 >
Loosing coherence
Coupling to environnement
Quantum cohérence
Coupling to environment is destroying coherence: Superposition & entanglement
  Error correction codes needed
  => thousands of physical Decoherence
  qubits to protect a single
  logical qubit
  Or new robust qubits
  protected from decoherence
13
Quantum is probabilistic: the measure destroys the superposition
I 1 >
I 0 >
a0 I 0 > + a1 I 1 >
State I i > with probability IaiI2
Measure
Example. Electron waves and probabilistic measure on screen
.

## Slide 14: 2022 International competition and collaboration
Public investments
2022 Data

## Slide 15
Quantum computing for nuclear, particle and astro physics
3

## Slide 16: Different quantum computing strategies
Quantum simulation
  |y(t)> = Û(0,t) |y(0)>
  Quantum evolution
  analogue computing
Quantum annealing
  |y> => |y0>
  Looking for ground states
  adiabatic optimization
  exploring many paths
  using tunnel effects
Quantum digital computing
  |y(NDt)> = ÛN(Dt) … Û1(Dt)|y(0)>
  Gate based evolution

## Slide 17: Many possible technologies/degrees of freedom
Quantum “objects”/degrees of freedom
Electrons pairs / superconducting curent
  Quantronium - transmon
Photons
Spin
  Electrons or holes in semiconductors (AsGa, Si, Ge, …)
  NV centers in diamond (Nitrogen vacancy)
Ions
Atoms
Molecules
New quantum degrees of freedom / quantum materials
  Flying qubits, surface states, leviton, pseudospin, Skyrmions, spin-orbite, 2D systems, topological materials, Majorana fermions, anti/multi-ferroïc …

## Slide 18: Main classes of quantum algorithms
Quantum Fourier transforms (QFT)
such as Shor's algorithm for factorization (&Bitcoin)
  Exponential acceleration
Cryptography
Optimization
searching equilibrium point of a complex system
such as neural network and optimal path (PCA)
  Exponential acceleration
Image processing
Market evolution
Quantum simulation and variational approach
Quantum many body problems
Resolution of linear differential equations (HHL)
  Exponential acceleration
Weather broadcast
Molecules
Search
based on Deutsch-Jozsa, Simon and Grover's algorithms
  Polynomial acceleration
Exploring graphs and data bases
Classical versus Quantum acceleration
Notes: To date, four main categories of quantum algorithms are available, which we will detail below:
Search algorithms based on Deutsch-Jozsa, Simon and Grover's algorithms.
Algorithms based on quantum Fourier transforms (QFT), such as Shor's algorithm for integer factorization,
Algorithms that seek an equilibrium point of a complex system as in neural network training, optimal path search in networks or process optimization.
Algorithms for the simulation of quantum mechanisms which are used to simulate the interactions between atoms in various molecular structures, both inorganic and organic.

## Slide 19: Quantum algorithms for nuclear, particle and astroparticle
Quantum Fourier transforms (QFT)
such as Shor's algorithm for factorization (&Bitcoin)
  Exponential acceleration
Optimization
searching equilibrium point of a complex system
such as neural network and optimal path (PCA)
  Exponential acceleration
Quantum simulation and variational approach
Quantum many body problems
Resolution of linear differential equations (HHL)
  Exponential acceleration
Search
based on Deutsch-Jozsa, Simon and Grover's algorithms
  Polynomial acceleration
Signal treatment
frequency decomposition
Image and data analysis
Advance treatment (AI, statistical analysis)
Theory and simulation
Many-body problem and field theory,
Data mining
pattern recognition, Graph analysis
Notes: To date, four main categories of quantum algorithms are available, which we will detail below:
Search algorithms based on Deutsch-Jozsa, Simon and Grover's algorithms.
Algorithms based on quantum Fourier transforms (QFT), such as Shor's algorithm for integer factorization,
Algorithms that seek an equilibrium point of a complex system as in neural network training, optimal path search in networks or process optimization.
Algorithms for the simulation of quantum mechanisms which are used to simulate the interactions between atoms in various molecular structures, both inorganic and organic.

## Slide 20: First quantum calculation of a deuteron Dumitrescu, McCaskey, Hagen, Jansen, Morris, TP, Pooser, Dean, Lougovski, Phys. Rev. Lett. 120, 210501 (2018)
Hamiltonien
  Pionless effective field theory at leading order
  fit to deuteron binding energy;
  constructed in harmonic-oscillator basis of 3S1 partial wave
  [à la Binder et al. (2016); Aaina Bansal et al. (2017)]
Ab initio approach
  Low-depth version of the unitary coupled-cluster ansatz
Use the variational quantum eigensolver algorithm
On 2 (and 3) Qubits IBM QX5 and Rigetti 19Q computers
Deuteron ground-state energies from a quantum computer compared to the exact result, E∞=-2.22 MeV
Rigetti 19Q
Unitary operator entangling 2 (and 3) orbitals
Notes: N=nb qbit
Gaute Hagen Oak Ridge National Laboratory Quantum computing and scientific research: state of the art and potential impact in nuclear physics CEA, Saclay, June 13th, 2019

## Slide 21
https://quantum.cern.ch
A strong quantum initiative @ CERN

## Slide 22: Areas of Research
Computing
Sensing
Communications
Theory
Simulation
Reconstruction
Classification
QKD infrastructures
Quantum Internet
Quantum Field Theory
Low-energy experiments, quantum states measurements, nano-technologies
https://doi.org/10.1140/epjst/e2015-02607-4
Lattice QCD
https://cds.cern.ch/record/2703396
Future HEP Detectors

## Slide 23: Scientific Publications (2021)
More than 20 projects in all four quantum areas
18 papers
  8 on peer-reviewed journals
More than 20 talks and presentations at conferences and workshops

## Slide 24: Scientific Publications (2021)
More than 20 projects in all four quantum areas
18 papers
  8 on peer-reviewed journals
More than 20 talks and presentations at conferences and workshops

## Slide 25: Scientific Publications (2021)
More than 20 projects in all four quantum areas
18 papers
  8 on peer-reviewed journals
More than 20 talks and presentations at conferences and workshops

## Slide 26: Many initiatives: 2 examples
QuantHEP a QuantERA project in EU
  Portugal
  Italy
  Latvia
QC2I an IN2P3 project in France
  IJCLab – Orsay
  LPC – Clermont-Ferrand
  LLR – Palaiseau
  LPNHE – Paris
  CC-IN2P3 – Lyon
  APC – Paris
  LPSC – Grenoble
  LUPM – Montpellier

## Slide 27: Many initiatives: 2 examples
QuantHEP a QuantERA project in EU
  Portugal
  Italy
  Latvia
QC2I an IN2P3 project in France
  IJCLab – Orsay
  LPC – Clermont-Ferrand
  LLR – Palaiseau
  LPNHE – Paris
  CC-IN2P3 – Lyon
  APC – Paris
  LPSC – Grenoble
  LUPM – Montpellier

## Slide 28: Many initiatives: 2 examples
QuantHEP a QuantERA project in EU
  Portugal
  Italy
  Latvia
QC2I an IN2P3 project in France
  IJCLab – Orsay
  LPC – Clermont-Ferrand
  LLR – Palaiseau
  LPNHE – Paris
  CC-IN2P3 – Lyon
  APC – Paris
  LPSC – Grenoble
  LUPM – Montpellier

## Slide 29: Quantum – HPC hybrid platforms
HPCQS
European initiative to couple Quantum computing/simulation with HPC
  Julich in Germany
  Bruyère le Châtel in France
More than 100 Qubits operational in 2022-2023
A five year project – 23M€ budget
Providing potential end-users with a full programming environment and diverse hardware for developing proof of concept projects
Allowing academic and industrial research aimed at enhancing the capabilities of existing technology
Three axes that closely match the objectives
  Deployment (QPU integration, HPC integration, cloud access, Languages, optimization, certification)
  Applications:
    Optimization and machine learning
    Simulation of physical systems
  Exploration
    Noise characterization and mitigation
    Quantum links for secure computation
French node – national quantum-HPC hybrid platform
Hardware: 3 quantum machine in 2022-2023
  Analog quantum computers (eg Atoms)
  Gate-based QPUs (eg superconducting/trapped ions)
  Early stage innovative QPUs (eg. photonic, carbon nanotubes, cat qubits, self-stabilized architectures)
23M€ to develop usage of QPU
Notes: After the latter example it is obvious that a lot can already be done with a hybrid computer ….

## Slide 30: Quantum – HPC hybrid platforms
French node – national quantum-HPC hybrid platform
Hardware: 3 quantum machine in 2022-2023
  Analog quantum computers (eg Atoms)
  Gate-based QPUs (eg superconducting/trapped ions)
  Early stage innovative QPUs (eg. photonic, carbon nanotubes, cat qubits, self-stabilized architectures)
23M€ to develop usage of QPU
WP4: Simulation of physical systems
  Ab initio calculation of nuclei
  Quantum chemistry
  Entanglement in solid state physics
  Phase transitions in quantum materials
  Partial differential equation
  Academia: CEA, CNRS, INRIA, IPP, Paris-Saclay, Sorbonne, UGA
  Industry: ATOS, PASQAL, Qubit Pharmaceuticals
  Deployment
    WP1: QPU integration, HPC integration, cloud access
    WP2: Software environment
  Applications
    WP3: Optimization and machine learning
    WP4: Simulation of physical systems
  Exploration
    WP5: Noise characterization and mitigation
    WP6: Quantum links for secure computation
Notes: After the latter example it is obvious that a lot can already be done with a hybrid computer ….

## Slide 31
Conclusion: a revolution to come
3

## Slide 32: Quantum computing in its enfancy

## Slide 33: Reduction of quantum errors needed before any applications
202x
20xx

## Slide 34
Thank you for your attention