## Slide 1
Caterina Michelagnoli michelagnolic@ill.fr
Nuclear Structure studies using
high-resolution techniques
26/01/2023
Master Interuniversitario IEM-CSIC

## Slide 2
Table of contents
Introduction: main challenges in Nuclear Physics, why g spectroscopy
 Nuclear Structure and Astrophysics
Why high resolution and how
   HPGe detectors and related technologies
   Array of HPGe detectors, facilities (in-beam g-ray spectroscopy)
   Performance, back-ground reduction and selectivity
   Angular correlations, polarization and lifetimes
Advanced g-ray tracking
 Basics
 The AGATA project
Notes: Table of Contents – Synthetic overview – I will go through, not necessarily ok order

## Slide 3
(Main) bibliography of today’s lecture
G.F. Knoll "Radiation Detection and Measurement"
F. Recchia and C. Michelagnoli, in Lec. Notes in Phys. (Euroschool Vol. VI)
C. Michelagnoli, PhD Thesis, Univ. of Padova (2013) (and refs therein  )

## Slide 4
Advances in g-ray spectroscopy
156Dy
super-deformation in 156Dy
major/minor axis = 2:1
Sensitivity = inverse of the weakest channel reaction cross-section that can be measured over total cross-section

## Slide 5
New generation HPGe arrays
Tracking Arrays based on
Position Sensitive Ge Detectors
Gamma Arrays based on Compton Suppressed Spectrometers
e ~ 50 — 25 %
( Mg=1 — Mg=30)
e ~ 10 — 5 %
( Mg=1 — Mg=30)
GAMMASPHERE
EUROBALL
GRETA
AGATA

## Slide 6
From conventional Ge to g-ray tracking
q ~ 8º
q ~ 3º
q ~ 1º
eph ~ 10%
Ndet ~ 100
eph ~ 50%
Ndet ~ 1000
eph ~ 50%
Ndet ~ 100
 ~40%
 ~80%
Compton-shielded Ge
Ge sphere
Ge tracking array
Using only conventional Ge detectors, too many detectors
are needed to avoid
summing effects and keep the resolution to good values
Efficiency is lost due to the solid angle covered by the shield; poor energy resolution at high recoil velocity because of the large opening angle
Use detectors in a non-conventional way 

## Slide 7
The g spectroscopy dream
Cover the whole detection solid angle by germanium and track the path of the g rays inside the detector medium
segmented detectors
digital electronics
timestamping of events
analysis of pulse shapes
tracking of g rays
4 time more efficient than standard arrays, also for high g multiplicity
(28 % Mγ=30)
High count rate capabilities
(100s KHz)
Study of nuclei in extreme conditions of angular momentum and neutron/proton asymmetry
“perfect” Doppler correction
(6 keV @ 1 MeV, β=50%)
new accuracy and sensitivity for
nuclear level lifetimes
g linear polarization
g
source
“continuous” angular distributions of the g interaction points (θ~1o)

## Slide 8
Position resolution used to limit Doppler broadening of gammas emitted in flight
scarce
good
Definition of the photon direction
Doppler correction capability
Detector
Segment
Pulse shape analysis
+
tracking g
Energy (keV)
v/c = 20 %

## Slide 9
Tracking of radiation
in High Energy Physics
in Nuclear Spectroscopy
“continuous tracks” from very energetic particles
huge detectors for “one” experiment
Physics ← the study of “complete” events
“many” low energy (0.01 -- 10 MeV) neutral transitions with low density of energy deposition
“general-purpose” detectors for a large variety of experiments
Physics ← large number of incomplete events

## Slide 10
Position-sensitive operation mode and g-ray tracking
highly segmented
HPGe detectors
Event by event:
how many gammas,
for each gamma: energy, first interaction point, path
digital electronics to record sampled waveforms
Pulse Shape Analysis of the recorded waves
Identified
interaction points
(hits)
(x,y,z,E,t)i
reconstruction of γ-rays from the hits
(tracking)

## Slide 11
Aim of g-ray tracking
e1, x1, y1,z1
e2, x2, y2,z2
…………………..
en, xn, yn,zn
E1, (θ,φ)inc,1,(θ,φ)sc,1. …
E2, (θ,φ)inc,2,(θ,φ)sc,2. …
………………………………
Ei, (θ,φ)inc,i,(θ,φ)sc,i
deposited energies and the positions of all the interactions points
of an event in the detector
reconstruct individual photon trajectories and write out photon energies,
incident and scattering directions
discard events corresponding to incomplete energy release
e1
e2
Doppler correction
Linear polarization

## Slide 12
Forward tracking implemented for AGATA
Create cluster pool => for each cluster, Eγ0 = ∑ depositions in the cluster
Find most probable sequence of interaction
points, test the 3 mechanisms
  do the interaction points satisfy the Compton scattering rules ?
  does the interaction satisfy photoelectric conditions (e1,depth,distance to other points) ?
  do the interaction points correspond to a pair production event ? E1st = Eγ – 2 mec2
3. Select clusters based on χ2
D.Bazzacco, Padova - A. Lopez-Martens, Orsay [NIMA 533 (2004) 454]

## Slide 13
Performance of the Ge shell
Idealized configuration to determine maximum attainable performance.
1.33 MeV | Mγ = 1 | Mγ = 30
εph (%) | 65 | 36
P/T(%) | 85 | 60
27 gammas detected -- 23 in photopeak 16 reconstructed. -- 14 in photopeak
Eg = 1.33 MeV
Mg = 30
A high multiplicity event
Reconstruction by Cluster-Tracking
Packing Distance: 5 mm
Position Resolution: 5 mm (at 100 keV)

## Slide 14: Fundamental Effects limiting the performance
Interaction position  position of energy deposition
Bremsstrahlung
Rayleigh scattering  change incident direction (relevant at low energy & end of track)
Momentum profile of electron  change scattering direction (relevant at low energy & end of track)
Fortunately (?) these effects are masked by the poor position resolution of practical Ge detectors
e-
g’
g
gbr

## Slide 15: Practical Effects limiting the performance
uncertainty in position of interaction: (position & energy dependent)
position resolution
energy threshold
energy resolution
dead materials ...
x
x
x
x
x
x
x

## Slide 16
Efficiency of Ge shell vs position resolution and g multiplicity
Standard shell; Eγ = 1.33 MeV; Packing=Smearing;
Energy independent smearing
The biggest losses are due to multiplicity (mixing of points) not to bad position resolution
5 mm is the standard
“realistic” packing and smearing assumption
If positions inside segments are not known, performance
is a factor 2 worse
Sub-segment position resolution is needed

## Slide 17
Pulse Shape Analysis (PSA)
8 AGATA Triple Clusters (24 detectors)
@ GANIL
“captured” during an experiment
Reconstruction of the interaction points (hits)

## Slide 18
Detector = p-i-n diode
Near intrinsic bulk (ND~1010cm-3)
Highly doped thin contacts
NA ~ 1018cm-3 ND ~ 1018cm-3
B ~ 3 mm Li ~ 0.5 mm
Radiation creates carriers in bulk
Carriers swept out by field  signal
Reverse bias (-HV on p+ contact) depletes bulk
generates high electric filed
-HV
h
e

## Slide 19
Pulse shapes in a co-axial HPGe
On “true” coaxial detectors, the shape depends on initial radius

## Slide 20
Segmented detectors
When one of the electrodes is (electrically) segmented, the motion of charges within one segment induces a transient signal also in the neighboring electrodes
Contrary to the segment where the interaction takes place (the charge is released), the total collected charge in the neighboring electrodes is null
The amplitude of the induced transient signals provides a convenient way to locate the interaction with sub-segment precision
Segmentation of an AGATA detector

## Slide 21
Pulse Shape Analysis concept
Interaction occurred in segment 4 (net charge signal)
Interaction is closer to segment 3 (larger amplitude than segment 5)
Sub-segment precision … but not enough to efficiently perform tracking!
➔ Pulse Shape Analysis

## Slide 22: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
791 keV deposited in segment B4
measured

## Slide 23: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,10,46)
791 keV deposited in segment B4
measured calculated

## Slide 24: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,15,46)
791 keV deposited in segment B4
measured calculated

## Slide 25: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,20,46)
791 keV deposited in segment B4
measured calculated

## Slide 26: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,25,46)
791 keV deposited in segment B4
measured calculated

## Slide 27: Pulse Shape Analysis concept
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,30,46)
791 keV deposited in segment B4
measured calculated

## Slide 28: Pulse Shape Analysis concept
Result of Grid Search Algorithm
B4
B5
B3
C4
C5
C3
CORE
A4
A5
A3
C4
D4
E4
F4
A4
B4
x
y
z = 46 mm
(10,25,46)
791 keV deposited in segment B4
measured calculated

## Slide 29
Scan setup
The interaction point is located by requesting a coincidence between the germanium detector and a second, narrowly collimated detector
Scanning the whole crystal is a time-consuming procedure!

## Slide 30: Signal Formation
Signal is due to the motion of charge carriers inside the detector volume.
Calculations based on the weighting field method derived by Ramo’s theorem, which is based on
Green’s reciprocity theorem that says: given two systems consisting of a distribution of charges and electrodes, charges and voltages are related by

## Slide 31
1 V
0.5 V
0 V
4000 V
2000 V
0 V
Weighting potential is calculated by applying 1 V on the segment collecting the charge and 0 V to all the others (Ramo’s Theorem).
It measures the electrostatic coupling (induced charge) between the moving charge and the sensing contact.
(1)
(2)
Real potential
Weighting potential
Current of electrode k
Weighting potential

## Slide 32
Position resolution for AGATA
F. Recchia et al., NIMA 604 (2009) 555
P-A. Soederstroem et al., NIMA 638 (2011) 96
Method = Doppler correction capability in an in-beam experiment
Energy [channel]
Simulation of reaction + detector response
F. Recchia et al., NIMA 604 (2009) 555

## Slide 33: Doppler correction capabilities
F
O
N
C
B
Be
α
Li
No Dopp Corr
Crystal Centers
Segment Centers
PSA+Tracking
16O
TKE (MeV)
dE (MeV)
Inelastic scattering 17O @ 20 MeV/u on 208Pb
F.Crespi, Milano
AGATA Demonstrator at LNL
46

## Slide 34
AGATA as a big (and expensive) Compton camera
F. Recchia et al., NIMA 604 (2009) 60
Far Field Backprojection
Near Field Backprojection
All 9 detectors
One detector
All 9 detectors
One detector
Source at 51 cm ➔Dx ~Dy ~2 mm Dz ~2 cm

## Slide 35: AGATA (Advanced-GAmma-Tracking-Array)
180 hexagonal crystals 3 shapes
60 triple clusters all equal
inner radius 24 cm
amount of germanium 374 kg
solid angle coverage 79 %
6480 segments
efficiency at 1MeV: 39% (Mg=1), 25% (Mg=30)
Peak/Total: 53% (Mg=1), 46% (Mg=30)
High efficiency.
Good position resolution on the individual g interactions.
Capability to stand a high counting rate.
High granularity.
Capability to measure the Compton scattering angles of the g-rays within the detectors.
Coupling to ancillary devices for added selectivity.
the “g-ray spectroscopy dream”
E. Farnea, NIMA 621 (2010) 331
Geant4 Montecarlo simulations
Notes: Ultimate dream
Full coverage, no spaces
All hits recorded

## Slide 36
GRETA vs. AGATA
120 hexagonal crystals 2 shapes
30 quadruple-clusters all equal
Inner radius (Ge) 18.5 cm
Amount of germanium 237 kg
Solid angle coverage 81 %
4320 segments
Efficiency: 41% (Mg=1) 25% (Mg=30)
Peak/Total: 57% (Mg=1) 47% (Mg=30)
Ge crystals size:
Length 90 mm
Diameter 80 mm
180 hexagonal crystals 3 shapes
60 triple-clusters all equal
Inner radius (Ge) 23.5 cm
Amount of germanium 362 kg
Solid angle coverage 82 %
6480 segments
Efficiency: 43% (Mg=1) 28% (Mg=30)
Peak/Total: 58% (Mg=1) 49% (Mg=30)

## Slide 37: “realization of the dream”: AGATA the nomadic detector
Demonstrator at the Legnaro National Lab.,
Italy
2009-2012
AGATA @ GSI
Germany
2012-2014
AGATA@GANIL,
2014-2020
22

## Slide 38
AGATA is today at LNL

## Slide 39: AGATA Crystals
Volume ~370 cc Weight ~2 kg
(the 3 shapes are volume-equalized to 1%)
80 mm
90 mm
6x6 segmented cathode

## Slide 40
Asymmetric AGATA Triple Cryostat
Challenges:
- mechanical precision
- heat development, LN2 consumption
- microphonics
- noise, high frequencies
- integration of 111 high resolution
spectroscopy channels
- cold FET technology for all signals
Courtesy P. Reiter
A. Wiens et al. NIM A 618 (2010) 223–233
D. Lersch et al. NIM A 640(2011) 133-138

## Slide 41: Analogue vs Digital Electronics
Detector
(Germanium)
Shaping Amplifier
CFD
DAQ
E
t
ADC
TDC
Standard Arrays
Notes: 1/26/23 10:36 AM
© 2007 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.
41

## Slide 42
Performance comparable to best analog electronics.
Higher count rate capabilities
FADC
MWD
DCFD
Filters
DAQ
E
t
PSA
Tracking
E
t
x,y,z
E
t
AGATA
Segment
Detector
Array
Detector
(Germanium)
Analogue vs Digital Electronics

## Slide 43
1)
2)
3)
Digital processing of signals
The energy is obtained via trapezoidal filter (or Moving Window Deconvolution, MWD)
A.Georgiev and W. Gast, IEEE Trans. Nucl. Sci., 40(1993)770 V.T.Jordanov and G.F.Knoll, Nucl.Instr.Meth., A353(1994)261
Signal amplitude = value at the top –
value of the baseline

## Slide 44: Signal processing at high counting rates
time [10ns]
30 kHz "nominal"
(front) segment
core

## Slide 45: Signal processing at high counting rates
time [10ns]
30 kHz "nominal"
core
MWD amplitude:
risetime 5us
risetime 2.5us

## Slide 46: Singles rates and shaping time
60Co - fixed
137Cs – 6 positions
6 different rates x 4 trapezoid risetimes x 6 BLR lengths
F. Recchia

## Slide 47: Singles rates and shaping time
60Co - fixed
137Cs – 6 positions

## Slide 48: Structure of Data Processing Local Level Processing

## Slide 49: Structure of Data Processing Global Level Processing
Ancillary Producer/Filter
(Merger)

## Slide 50
Data preparation to the PSA: energy calibrations
Calibration of traces: from calibrations of amplitudes and MWD parameters

## Slide 51
Sum of segment energy vs fold
segment id
segment id
Generate strong energy shifts proportional to the segment fold
After correction
Before correction
Data preparation to the PSA: cross-talk correction
Notes: Present in any segmented detector,

## Slide 52: Data preparation to the PSA: recovery of missing segment
45

## Slide 53
The 1332 keV peak as a function of crystal
depth (z) for interactions at r = 15mm
 corrected
CC r=15mm
SG r=15mm
April 2010
CC r=15mm
SG r=15mm
July 2010
Neutron-damage correction
Charge loss due to neutron damage 
proportional to the path length to the electrodes
Use PSA interaction points and modeling
of charge trapping to correct the effect
B.Bruyneel et al, Eur. Phys. J. A 49 (2013) 61

## Slide 54
uncorrected
corrected
Effect of the correction on energy resolution
Sum of segments: 5.9 keV  2.9 keV

## Slide 55
The nucleus is always full of surprises
Instrumentation advances ⇔ New Science