## Slide 2
SIS100
The Universe in the Laboratory
https://fair-center.eu/
FAIR- Facility for Antiproton & Ion Research
Notes: This is an artista view of how FAIR will look in a few years from know (2030?)
Upper left corner is the present GSI, and the rest is the future FAIR facility. (Berta showed you some photos on the status).
Inside this huge facility we have the NUSTAR facility

## Slide 3: FAIR - The Universe in the Laboratory
FAIR - The Universe in the Laboratory
https://www.youtube.com/watch?v=kbvK5AGg8oM
https://www.youtube.com/watch?v=wTCkZdeqI8I
Youtube movies
https://fair-center.eu/user/experiments/nustar/documents/technical-design-reports
NUSTAR

## Slide 4: Radioactive Beam Production
FAIR
(2028)
GSI
GANIL
SPIRAL
HIE –
ISOLDE
ISOLDE
2 GeV
1 GeV
50 MeV
10 MeV
0.06 MeV
High energy, large variety of species,
Short half-lives (ms), cocktail beam
Variable energy, high intensity, good beam qualities
Blanco
Haz
ISOL – Isotope Separation On Line
Beam Fragmentation

## Slide 5
Not-too-far future
Existing
Experiment facilities
Cave C
R3B
2028

## Slide 6: NUSTAR
The scientific user community of FAIR is organised in experimental collaborations, which are grouped in 4 scientific pillars:
APPA - Atomic, Plasma Physics and Applications
    BIOMAT - Biology and Material Science
    HED@FAIR - High Energy Density Science at FAIR
    SPARC - Stored Particles Atomic Research Collaboration
CBM - Compressed Baryonic Matter
NUSTAR - Nuclear Structure, Astrophysics and Reactions
    High Eenergy Branch R3B 2028
    Low Energy Branch HISPEC/DESPEC, MATS, LASPEC 2032
    Ring Branch ILIMA, ELISe, EXL 20xx
PANDA - Physics with High Energy Antiprotons
    Antiprotons produced by a primary proton beam  High Energy Storage Ring (HESR)  fixed target inside PANDA

## Slide 7: NUSTAR: NUclear Structure, Astrophysics and Reactions
What are the limits for existence of nuclei?
  Where are the proton and neutron drip lines situated?
  Where does the nuclear chart end?
How does the nuclear force depend on varying proton-to-neutron ratios?
  What is the isospin dependence of the spin-orbit force?
  How does shell structure change far away from stability?
How to explain collective phenomena from individual motion?
  What are the phases, relevant degrees of freedom, and symmetries of the nuclear many-body system?
How are complex nuclei built from their basic constituents?
  What is the effective nucleon-nucleon interaction?
  How does QCD constrain its parameters?
Which are the nuclei relevant for astrophysical processes and their properties?
  What is the origin of the heavy elements?
Notes: The Physics

## Slide 8
NUSTAR NUclear STructure & Astrophysis Research
Primary beam
from SIS100
Production of more than 4000 nuclear species
Olof TENGBLAD MASTER TEAFN
8
Notes: NUSTAR NUclear STructure & Astrophysis Research: includes many sub-collaborations
Specially we divide into Low EnergyBranch, Ring Branch and High Energy Branch=R3B.
The aim is the same but the methods differs, we all want to produce exotic nuclei and understand their structure.
The heart and common part is the Super Fragment Separator SFRS

## Slide 9: R3B: Reactions with Relativistic Radioactive Beams
CAD drawing of the new installation in High Energy Cave

## Slide 10: How does it work
FAIR (Facility for antiproton and ion research)
R3B
n
p
H
n
p
1. Accelerated beam impact on Production Target
2. Products are separated in SFRS
3. Separated isotopes directed to experiment
4. Isotope of interest impact on Reaction Target
5. Reaction fragments and gammas are detected
Notes: This animation illustrates how these experiments are performed..

## Slide 11
R3B: Reactions with Relativistic Radioactive Beams
BEAM 
Neutrons 
fragments 
protons
g p d
Magnet
Notes: Along the talk you will see different layouts of the R3B experimental hall. This is not only due to historical advances but the equipment although big si moved arround optimizing for each campaign.
R3B is a universal fixed target experiment for complete inverse kinematic reactions with radioactive beams in the energy range 300-15000MeV/u.
The concept is build ont he existing ALADIN-LAND set-up at GSI.
We will adress Nuclear Astrophysics, study exotic nuclei or nuclei at the extreme

## Slide 12: Key instrumentation
>20 meters
LH2 target

## Slide 13: LH2 target with Si-detector
1.5 cm 15 cm
Target cell diameter 42 mm
Three target length 15, 50 and 150 mm.
The cryogenic system operates in a closed loop.
The target is connected to a storage tank.
The tank is filled with 800 l of hydrogen at room temp.
After liquefaction the target hydrogen is at 20.3 K and 1041 mbar.
The target cell made of Mylar

## Slide 14
Reaction chamber: LH2-target, p-tracker, g-spec-calori-meter
Identify and track recoils emmitted at large angles
High angular resolution (better than 1 mrad)  very high segmentation
Low noise level  detection of MIP
Multi-layer sensors 50-100 mm for 1st layer  minimize multiple scattering or shadow g rays
Low threshold 25 KeV
Multi-hit capability
Further:
Closed geometry around the extended target 4p vertex reconstruction
Spark protection against ionising particles hit
Operate in the proximity of strong magnetic fields and vacuum
Dedicated electronics

## Slide 15: I+D para p-tracker  flexible pixelated Si-boards
flexible boards
2026/27
2024/25
2028/30

## Slide 16
Hybrid g/p spectrometer/calorimeter
Univ. Santiago de Compostela
TUDa - TUM – Lund

## Slide 17
A. Jungclaus
  R3B b > 80% c
  the intrinsic resolution not so important.
  we can go for scintillator
  Doppler broadening  high segmentation
B. Olaizola
  Scintillators are fast (CsI 420ns) but some are faster (LaBr3 18ns!)
   Forward endcap LaBr3 to avoid the pile-up
From the talks yesterday we learned
Design constrins

## Slide 18: Hybrid g/p spectrometer/calorimeter
Lorenz boost
0.5 – 1.5
Lorenz boost
2.5 -3
Lorenz boost
1.5-2.5
Coverage
35%
15%
Coverage
45%
b > 0.80
Ebeam= 700 MeV/u
Incoming beam @ 85% of c
 Reaction very much forward  g emitted in flight  Lorenz boost  at small angles g boosted up to 3x
 Highly segmented

## Slide 19: I+D para CALIFA

## Slide 20
Question to be answered:
Depth of first interaction
Depth @ 90% photopeak efficiency
How many neighbouring crystals are being hit?
Simulation codes
SRIM --- GEANT4 --- MCNPX Monte Carlo N-Particle eXtended code
@7 cm 70 % of incident beam is detected
gammas in Phoswich

## Slide 21: PROTONS in Phoswich: DE+ E
Protons: two DE-detectors one can determine the full proton energy with a resolution of <5%.
Gammas: Second detector placed to solve the ambiguity on the signal
Ep= 200MeV  20 mm LaBr  DE = 31 ± 1 MeV
200±10MeV
(sE/E=5%)
LaBr + LaCl
DE1 DE2
E = f( D E1 ) + g( D E2 )

## Slide 22: PROTONS in Phoswich: DE vs DE+ E
DE
DE + E
https://www.sciencedirect.com/science/article/pii/S0168583X19302228
https://www.sciencedirect.com/science/article/pii/S0168900212014416

## Slide 23: Endcap still in R&D!
8+7 cm
LaBr3
LaCl3
PM
3x4
As explained by Bruno
long funny shaped crystals
non-linear response
This is in CsI mitigated by LAPPING
In LaBr not easy…

## Slide 24
CALIFA barrel and forward endcap
(gamma/particle calorimeter)
9
CALIFA: Highly segmented
Thick detection volume
Inner radius 50cm
Barrel: Crystal length 15-20 cm
1952 crystals = 2 Ton
EndCap: 680 crystals = 1 Ton
https://iopscience.iop.org/article/10.1088/1742-6596/1667/1/012006

## Slide 26: GLAD - Large-Acceptance superconductingDipole magnet https://www.gsi.de/work/forschung/nustarenna/nustarenna_divisions/kernreaktionen/r3b_project_group/glad
Weight: 50 t
This is now reduced
to a few days

## Slide 27: NeuLAND - High-resolution neutron ToF spectrometer https://www.gsi.de/work/forschung/nustarenna/nustarenna_divisions/kernreaktionen/r3b_project_group/neuland
NeuLAND design goals:
>90% efficiency for 0.2-1.0 GeV neutrons
Multi-hit capability for up to 5n
invariant-mass resolution:
NeuLAND to target distance 35 m
∆E < 20 keV at 300 keV
x100 = one double-plane
NeuLAND detector parameters:
full active detector using RP/BC408
face size 2.50x2.50 m2
active depth 3m (30 double-planes)
3000 scintillator bars
6000 PM / readout channels (both ends)
32 tons
2024: 17 DP installed
2.5 m
https://www.sciencedirect.com/science/article/pii/S0168900221006860?via%3Dihub

## Slide 28
For full kinematic reconstruction & reaction channel ID we need to know
for incoming and outgoing fragments, beam, gammas
Energy loss  Nuclear charge Z
Time of Flight  Mass identification
Trajectory  Momentum
R3B tracking system

## Slide 29
C. Caesar and D. Savran
Scintillating Fiber Tracker
4d Tracking at High Rate with High Dynamic Range
Infrastructure upgrades
Square fibers 0.2x0.2 mm2
Number of fibers ~ 104 fibers
 60 mm resolution

## Slide 30: Many detectors, big distance, each with individual electronics and DAQ  But should work synchronized
R3B@FAIR
Notes: Secondary Target. (especially LH2 i.e. proton target)
CALIFA:m γ/p calorimeter-spectrometer Si-tracker: target recoil detector
GLAD: large acceptance dipole magnet tracking, DAQ, simulation, infrastructure
NeuLAND: neutron time-of-flight spectrometer
high-resolution spectrometer
I will go through some details in the following

## Slide 31: General outline of electronics and DAQ
1 detector
1 channel
several detectors
Many channels
Many detectors many channels + many systems  how to synchronize

## Slide 32: Synchronization and Coincidences to build event by event data . GSI-FAIR wide Time reference:
The R3B experiment is composed by several separate detector components that are spatially extended, running independent DAQ  stitch together in MAIN-DAQ
For the coincidence timing at R3B we have to be in time-correlation with all the detector-systems, with FRS and with the Machine timing of GSI-FAIR
Bunch Timing System (BuTiS) distribute high precision clock train (100 kHz ident pulse, 10 MHz sine).
White Rabbit is a fully deterministic Ethernet-based network for general purpose data transfer and synchronization. It can synchronize over 1000 nodes with sub-ns accuracy over fiber lengths of up to 10 km.
The distributed data acquisition system run in a time-synchronized distributed environment based on BuTiS and White Rabbit with timestamps of pico-second precision and 100 ps/km accuracy.
Individual detector triggers are stitched together event by event in the MAIN DAQ before storage.

## Slide 33: R3B Summary: Schedule and first experiments @ GSI in Cave C
2020 50% NeuLAND and 50% CALIFA & Si-Tracker + tracking detector prototypes
  Liquid Hydrogen target (LH2)
2019-25 Physics runs at GSI (Cave C) (phase 0)
2026 - 2027 Move to HEC- cave @FAIR
2028 1st R3B-NUSTAR experiment @FAIR
Experiments will make use of uniqueness of R3B:
Reactions at high beam energies up to 1 GeV/u
Tracking and identification capability for the heaviest ions
Multi-neutron tracking capability, high-efficiency calorimeter
Experiments possible for the first time:
4 neutron decays beyond the drip-line and for heavier n-rich isotopes
Kinematically complete measurements of quasi-free nucleon knockout reactions
Electric dipole and quadrupole response of Sn nuclei beyond N=82, and of neutron-rich Pb isotopes (polarizability, symmetry energy)
Fission barriers from (p,2p) reactions (  r-process)

## Slide 34: An example: S393 experiment
34
Study of light neutron-rich nuclei using kinematically complete measurements in inverse kinematics @ GSI
quasi-free scattering: 14B(p,2p)13Be
Study the precursor to the borromean nuclei 14Be
16B
Unbound
14Be
4.35ms
15B
9.93ms
14B
12.5ms
13Be
Unbound
18B
Unbound
19B
2.92 ms
17B
5.08ms
13B
17.3ms
12Be
21.5 ms
https://fnexp.iem.csic.es/reports/PhD_Theses/PhD-G_Ribeiro-2015.pdf

## Slide 35: Quasi-Free Scattering: Knockout reaction
14B(p,2p)13Be
Direct Reaction: quick and direct from initial to final states without intermediate compound state.
If both outgoing particles have the same masses, in the lab system:
(p,2p), (p,np)
16B
Unbound
14Be
4.35ms
15B
9.93ms
14B
12.5ms
13Be
Unbound
18B
Unbound
19B
2.92 ms
17B
5.08ms
13B
17.3ms
12Be
21.5 ms
35

## Slide 36: Experiment:Cave C
Primary beam 40Ar11+ @ 490 MeV/u
Intensity 6·1010 ions/spill.
Production target Be 4 mg/cm2
Reaction target H, C, empty
14B(p,2p)13Be

## Slide 37: Reaction channel Idenitifcation
Energy loss in the ToFW after the target  Identify the element after the reaction.
Identify the isotope from the ALADIN position deviation and beta of the fragment.
14B  12Be + n
37
12Be
Fragments from 14B
Be Fragments from 14B
Be Fragments from 14B & Neutrons
Incoming
Beam 14B
Outgoing Be
Be +n
Charge identification from energy loss
Mass identification from ToF tracking
Incoming
Beam 14B

## Slide 38: Relative Energy of 12Be + n:
1
2
3
4
2´
2´
2
3
1
4
13Be
Gamma Spectrum
Eg=2 MeV
https://journals.aps.org/prc/abstract/10.1103/PhysRevC.98.024603

## Slide 39: Experimentos de NUSTAR: pensar y recordar!
Acrónimos: FAIR NUSTAR SFRS R3B
Que método de producción se usa en experimentos de NUSTAR?
Cual es el haz primario, y de que origen normalmente?
Cual es el blanco de Producción?
Cual es el haz secundario? Cual es el blanco de Reacción?
Por que usamos varios blancos de reacción en el mismo experimento?
Por que cinemática inversa?
Que significa cinemática completa?
Como se selecciona el canal de reacción de interés del experimento?
Como se determina la carga, masa, la energía, el momento,
no olvides la importancia de medir las: g & neutrónes!

## Slide 40
250 Members
40 Institutes
15 Countries
Spokesperson: Lola Cortina IFIC
Technical Director 2014-24: O. Tengblad IEM

## Slide 41: España
Univ. Santiago de Compostela
Lola Cortina
Pepe Benlliure
Enrique Nacher
Enrique Casarejos
Carlos Parrilla
Olof Tengblad
María Borge
Christoph Rappold
Saúl Beceiro Novo
Jose Luis Rodriguez Sanchez
Hector Alvarez Pol
Diego Gonzales