## Slide 1
D. Attié
CEA/Irfu
Paris-Saclay University
RD51 – New Horizon in TPC
October 5th, 2020
Ions Backflow in TPCs: Simulations, Measurements and Suppression
Notes: I’m here to present a TPC review

## Slide 2: Outline
Introduction: Ion Mobility and Ion Backflow in Time Projection Chambers
Ion Backflow in Micro-Pattern Gas Detectors (GEM & Micromegas)
Studies: Simulations & Measurements
Ion Backflow Solutions
STAR TPC at RHIC

## Slide 3: Ions Mobility in Gases
Mobility: ratio of ion velocity and electric field
In gas mixture of n different gases, ions mobility is given by Blanc’s law:
Example: Ar-CH4, E=1kV/cm  =1.8 µm/s
S. C. Brown Basic Data in Plasma Physics (Wiley, New York 1959)
Gas | Ion | µ+ (cm²s-1V-1)
He | He+ | 10.2
Ar | Ar+ | 1.7
H2O | H2O+ | 0.7
CH4 | CH4+ | 2.26
Ar-CH4 | CH4+ | 1.87
CO2 | CO2+ | 1.09
Ar-CO2 | CO2+ | 1.72
Iso-C4H10 | Iso-C4H10+ | 0.61
Ar-Iso-C4H10 | Iso-C4H10+ | 1.56
    : concentration by volume of gas k
    : mobility of the ion of kind i in gas k
(NTP: 300K, 760 mmHg)

## Slide 4: Ion Backflow in Time Projection Chambers
Ion drift velocity is ~1-10 000 times lower than electron drift velocity
Ion backflow more problematic in MSGCs than MPGDs and depends of:
    Amplification structure at anode
    Field ratio (Ea/Ed)
    Gas mixture
IBF issues/solutions depend of:
    Beam time structure
    TPC length
October 5th, 2020
ILC
CEPC, EIC, FCC
Fbeam
Fbeam
time
time
anode
anode
cathode
cathode
    Disks of ions
    Energy resolution dE/dx
    Detector gain

## Slide 5: Ion Backflow in Time Projection Chambers
The positive ions have negligible diffusion (due to their high masses)
A part a secondary ions from amplification region can escape to drift region
  distortion of electric field
  modification of detector stable operation (margin <0.1%)
Ion backflow definition:
Field ratio and pitch dependence:
October 5th, 2020
    backflowing ions
    total ions from amplification
    FR: field ratio
    p: pitch of the holes
    : transverse diffusion
    GEM
    Miromegas mesh

## Slide 6: Ion Feedback Simulations
Most of simulations are based on open source softwares (Cern):
  Garfield: two- and three-dimensional drift chambers simulation
  Magboltz: electron transport properties in gas mixtures
  Heed: ionisation of gas molecules by particles in gaseous detector
  neBEM solver: electric field and potential in three-dimensional geometries
Field solver: Maxwell, Comsol Multiphysics (AC/DC), neBEM, …
Particle interaction in Garfield framework
  Detector/geometry modelling: Garfield
  Ionization: energy loss through ionisation of a particle crossing the gas and production of clusters (Heed)
  Transport and amplification: electron drift velocity and diffusion coefficients (longitudinal & transverse), Townsend and attachment coefficients (Magboltz)
  Detector response: charge induction using reciprocity theorem (Shockley-Ramo’s theorem), particle drift, charge sharing (pad response function), charge collection (Garfield)
Comparison of present numerical estimates with experimental results
October 5th, 2020

## Slide 7: Operational Conditions and Ion Backflow in ILC-TPC
T2K gas: Ar/CF4/iso-C4H10 95/3/2
Drift field: Edrift = 230 V/cm (Vdrift = 7.5 cm/µs)
Bulk Micromegas:
Gas gain: 2000-4000 (380-400V)
Eamplification/Edrift=EA/ED=130-135
IBF requirement: < 1% (for margin <0.1%)
Chart: Vmesh (V)
| 300 | 310 | 320 | 330 | 340 | 350 | 360 | 370 | 380 | 390 | 400 | 411 | 420 | 430 | 440 | 450 | 455
Après Viellissement | 160.2945 | 215.781 | 311.9577 | 447.5915 | 626.3815 | 896.416 | 1260.1612 | 1787.8999 | 2575.809 | 3491.9536 | 5006.1199 | 7768.117 | 10690.4086 | 16103.4299 | 24229.1269 | 39210.4954 | 48828.1641
Edrift=230 V/cm
  amplification gap: 128 µm
  hole pitch: 63 µm (400 lpi)
October 5th, 2020

## Slide 8: Micromegas: Intrinsic Suppresion of Ion Backflow
S1
In Micromegas, if the pitch hole is comparable to the avalanche size, only the fraction ~ S2/S1 = Edrift/Eamplification drift back to the drift space.
Others are neutralized on the mesh: optimally, the backflow fraction is as low as the field ratio
This has been experimentally thoroughly verified
ED drift field
EA amplification field
S2

## Slide 9: Ion Backflow: Measurement Principle
The ion backflow fraction is given by:
Determination of the primary ionisation from the drift current at low Vamp
Using equation (1) & (2) G is eliminated  IBF
Vamp
Vdrift
I2 (amplification)
I1 (drift)
X-ray gun
(1) primaries+IBF
(2) I1+I2 ~ G × primaries

## Slide 10: Ion Backflow in Single GEM or Micromegas
Single GEM
Micromegas
D. S. Bhattacharya, NIMA 861 (2017) 64–70
P. Bhattacharya, NIMA 870 (2017) 64–72
F. V. Böhmer, arXiv:1209.0482v1

## Slide 11: Ion Backflow with Micromegas
P. Colas et al., NIMA535(2004)226
Ar-CH4 97-3
EA/ED
1%
1%
5%
MWPC-TPC: IBF~30%
The ions backflow depends on avalanche spread (transverse diffusion) but cannot be smaller than the field ratio
The absence of effect of the magnetic field on the ion backflow suppression has been tested up to 2T
For a EA/ED ~100, IBF~1-5% depending on geometry (hole pitch)

## Slide 12: Ion Backflow in Bulk Micromegas
Micromegas for LC-TPC:
  (resistive) bulk technology
  128 µm gap
  woven mesh with pillars
  63 µm pitch (45 µm hole /18 µm wire )
  400 LPI
W. Wang, PhD Thesis (2013)

## Slide 13: Grid Geometry and Field Ratio
Study of IBF dependency with hole geometries and field ratios
20 µm hole pitch
32 µm hole pitch
45 µm hole pitch
58 µm hole pitch
Ingrid sample
  - p: hole pitch
  - : transverse diffusion, Dt (Dt: transverse coefficient)
  - FR:
M. Chefdeville, PhD Thesis (2009)

## Slide 14: Ion Backflow with Micromegas: Simulation
0.75
0.5
0.25
500 LPI
1000 LPI
1500 LPI
Mesh
t/p
Theoretical model
2D
3D
Sum of gaussian diffusions
l
Periodical structure
IBF calculation:
M. Chefdeville, PhD Thesis (2009)

## Slide 15: Grid Geometry and Fields
Gap (µm) | Hole pitch p (µm) | Hole d (µm) | σt /p
45 | 20 | 12 | 0.47
 | 32 | 23 | 0.30
 | 45 | 32 | 0.21
 | 58 | 21 | 0.16
58 | 20 | 9 | 0.58
 | 32 | 15 | 0.36
 | 45 | 34 | 0.26
 | 58 | 22 | 0.20
70 | 32 | 18 | 0.43
 | 45 | 32 | 0.30
 | 58 | 22 | 0.24
Fits using:
with y~1
45 µm gap
58 µm gap
70 µm gap
M. Chefdeville, PhD Thesis (2009)
EA/ED
EA/ED
EA/ED

## Slide 16: Ion Backflow in Bulk Micromegas
Bhattacharya et al. JINST 9 C04037 (2014)
IBF vs field ratio
  Gas mixture: Ar/Iso (90-10)
  Amplification gap: 128 m
  Pitch: 63 m
  Vmesh = 500 V
  Efield = 200 V/cm

## Slide 17: Ion Backflow in Bulk Micromegas
IBF vs amplification gap and hole pitch
  Gas mixture: Ar/Iso (90-10)
  Vmesh = 500 V
  Efield = 200 V/cm
Bhattacharya et al. JINST 9 C04037 (2014)
Gap: 128 m
Pitch: 78 m
Simulations
Measurements

## Slide 18: Possible Solutions to Reduce Ion Feedback
Two families of solutions: with or without gating grid
Solutions with gating grid (wires, GEM)
Solution without gating grid
  Trigger in asynchronous or synchronous modes
  Hybrid MPGDs (double/triple meshes, Quadruple GEMs, GEMs+Micromegas)
    Gating grid in MSGCs
    Trigger with asynchronous or synchronous modes

## Slide 19: Ion Feedback Reduction and Energy Resolution
Using gating:
  any multi-stage gain structure, a low gain stage makes irreducible contributions to gain fluctuations  no energy resolution loss
  First (early) stage(s) of G-G-G-G and G-G-MM must have low gain since they are coupled strongly to the gas
  The field ratio principle, larger low IBF, is independent of gain
  Passive structure generating a field ratio can lower IBF with little or no loss in energy resolution
Cylindrical holes gating
Wire mesh gating

## Slide 20: Possible Solution without Gating Grid
Micromegas with offset metal meshes (5 µm cooper):
Open questions:
- never used in TPC
- effect of magnetic field?
- large area?
F. Jeanneau et al., NIMA623(2010)94
10-5
50 m

## Slide 21: Possible Solution without Gating Grid
Micromegas using double meshes
Need higher amplification field
Reduce IBF by a factor of 2
P. Bhattacharya, JINST 10 (2015) P09017

## Slide 22: Ion Backflow in Triple GEM
P. Bhattacharya, NIMA 870 (2017) 64–72
H. Natal da Luz, et al. - arXiv:1803.09382v2

## Slide 23: Ion Backflow in Triple-GEM for ALICE-TPC
Ar/CO2 (90-10)
Ne/CO2 (90-10)
Ne/CO2/N2 (90-10-5)
Ne-CF4 (90-10)
Ball et al., JINST C04025 (2014)

## Slide 24: Ion Backflow in Quadruple-GEM for ALICE-TPC
Measurements of 55Fe energy resolution in quadruple GEMs
  Ne/CO2/N2 (90-10-5)
  GEM3 and GEM4 are adjusted to achieve a total effective gain of 2000
  The voltage on GEM1 increases for a given setting between 225 and 315 V from left to right
-drift = 400 V/cm
90-10 of Ne-CF4
Pad Plane
1
2
3
4
ΔV1
ΔV2
ΔV3
ΔV4
ΔV1
ΔV2
ΔV3
ΔV4

## Slide 25: TPC for EIC: requirements & R&D
BNL-Saclay-Yale team R&D Motivation: high rate TPC as a barrel tracker in EIC detector
Small TPC (~ 45-50 pad rows, ~100 cm drift distance), Bfield>1.5 T, beams interaction rate up to 500 kHz.
Needs: - Gain ~2000 - Good energy resolution: dE/dx < 12% - Lowest possible IBF
MM + GEM + MM, with ZZ-pad shape and R-protection promising configuration
Data taking in progress
A. Glaenzer

## Slide 26: TPC for EIC: Hybrid detectors MM + 2GEMs
- Edrift = 0.4 kV/cm - Etransverse = 2 kV/cm - Einduction = 0.075 kV/cm - Gain ~ 2000
Bfield: 1.5T.
vdrift = 8.2 cm/s
transverse = 58 m/√cm
-- w/o R-protection
-- w R-protection
VMM = 450 V
VMM = 480 V
P10+CF4(10%); Ne+CF4(10%)+CH4(10%)
Ne(90%) + CO2(10%) + N2(5%)
4GEMs, BNL-Yale
MMG+2GEMs, Yale
4GEMs, ALICE TPC upgrade
S. Aiola, NIMA 834 (2016) 149
4GEMs
MM + 2GEMs
Using setup with R-protection the MM mesh
HV PS reaction on sparks was tested
Am241 source (Vmesh ~ 670 V, C10 gas mixture).
In a case of spark (rate ~ 1/20 s) - HV drop ~ 0.4 V - Recovery time ~ 600 μs
For two voltages “stability” test was done with X-ray source Anode current : 10 nA/cm2, 7 hours runs,  no sparks
See Nikolai Smirnov’s talk

## Slide 27: Summary & Outlook
Micromegas and triple-GEMs offer intrinsic ion backflow suppression
  Micromegas: EA/ED~100  IBF~ 1-2%
  Triple GEMs with different pitches: IBF~ 1-2%
  Quadruple GEMs: IBF~ 1-2%
  Gain ~2000  ~20 ions for 1 primary (95% of space charge)
But not optimal for high rate experiment
Experimental and numerical studies show effects of different geometrical and electrical parameters on the ion backflow fraction
Measurements are still on-going (EIC, FCC) with different geometries

## Slide 28: Thank you