## Slide 1
The spherical proportional gaseous detector
and comparisons
Ioannis Giomataris, CEA-University Paris-Saclay
Short introduction
Recent developments
Dark matter project NEWS-G
at LSM and SNOLAB
Comparison with other gaseous detectors
OUTLINE

## Slide 2
5.9 keV 55Fe signal
20 s
Simple and cheap
Large volume
single read-out
Robustness
Good energy resolution
Low energy threshold
Efficient fiducial cut
Low background capability
A Novel large-volume Spherical Detector with Proportional Amplification read-out, I. Giomataris et al., JINST 3:P09007,2008
C≈ra= 1 mm < 1pF
rA = anode ball radius
rC = cathode radius
Radial TPC with spherical proportional counter read-out
Saclay-Thessaloniki-Saragoza

## Slide 3
Multi-ball ‘ACHINOS’ structure
Developed in Saclay in collaboration with University of Thessaloniki
Advantages
- Amplification tuned by the ball size:
1mm diameter for high pressure
-Volume electric field tuned by the size
of the ACHINOS structure
- Detector segmentation: 3D TPC like
Using 3D printer
Bakelite bias electrode
Graphite charged glue
copper charged glue
DLC layer (USTC-China)
It is fantastic technical solution:
Robust, stable, precise
Single ball

## Slide 4
Towards a radial field degrader
Concept
A conical resistive layer on top of metallic strips deposited on a kapton thin foil
creates a radial field by applying a high voltage
The foil is folded around the copper tube that holds the
sensor
HV
ground
HV
ground

## Slide 5
First home made demonstrator
using aluminum strips
A second has been recently build at CERN (Rui)
on top of thin chrome strips using resistive paste
A technical problem appeared during folding:
Some chrome have been slightly damaged
A second bunch of kapton foil with chrome strips sent to USTC (Yi)
to deposit DLC which must be the final solution

## Slide 6
Rise time (s)
Amplitude
 210Po
5.3 MeV
n capt on 3He
764 keV
 210Po
5.3 MeV
from 210Pb
@ Cu surface
Range = 15 cm
n capt on 3He
=> p + T
222Rn 218Po 214Po
1
2
3
Rate 400 capt/d
« Volume » alpha
Particle identification capability at MeV energy
Ar/CH4 + 3g 3He @ 200 mb SPC 130cm Ø @ LSM
PL
Point like
Tracks

## Slide 7
Low-energy calibration source Argon-37
Home made Ar-37 source: irradiating Ca-40 powder with fast neutrons 7x106neutrons/s
Irradiation time 14 days. Ar-37 emits K(2.6 keV) and L(260 eV) X-rays (35 d decay time)
Argon 37
First measurement
with Ar-37 source
Total rate 40 hz
in 250 mbar gas, 8 mm ball
240 eV peak clearly seen
A key result for light dark matter search
5.9.keV
2.4 keV
260 eV
Installation near the spherical detector

## Slide 8
80
4
Rate [Hz]
Date [s]
Polyethylene
30 cm
Lead
10 cm
Copper
5 cm
Decrease of factor 20 for
Energy range 1 – 200 keV
NEWS-LSM: Exploration of light dark matter search at LSM
Detector installed at LSM end 2012: 60 cm, Pressure = up to 10 bar
Gas targets: Ne, He, CH4
Effect of the cup

## Slide 9
Sensitivity with Neon at 3 bar
Data 40.5 days, threshold 30 eV
Q. Arnaud and al, Astropart. Phys. 97 (2018) 54–62

## Slide 10: NEWS-SNO with compact shield : data taking on 2021
140 cm Ø detector, 2 bars, Ne, He, CH4
Copper 1 mBq/kg
Compact lead –ancient- & PE shield solution
Lead shield
Shiped to SNOLAB
Canada

## Slide 11
NEWS-SNOLAB project sensitivity
DAMA
LUX
Xenon
DarkSide50-Ar
CDMS-Edelweiss
CDMS reanalysis
Edelweiss LE
CDMSLite2
CRESSTII
CRESST
DAMIC
COGeNT
CDMS_Si
CDMSLite1
NEWS-SNOLAB
H
He
Ne
2017

## Slide 12
Future projects with improved sensitivity

## Slide 13
E≈V/r2
≈V/ ra close to the ball
C ≈ ra < 1pF
Spherical Proportional Counter
Cylindrical Proportional Counter
E=V/ln(rc / ra)r L = length and a=radius of the wire, b = tube radius
C =2pL/ln(rc / ra)>> 10 pF
The electric field at the surface of the wire is weaker by a factor ln(rc / ra)
compared to the ball (applying the same voltage in both sensors)

## Slide 14
Spherical and cylindrical counter comparison
To compare the two concepts we consider large volume detector
as required for astroparticle physics (dark matter search, neutrino physics)
Total gas volume V=2m3
Spherical counter Cylindrical counter
rc = .8m ra=.5mm rc=.56m ra=15mm L=2m
The factor ln(rc / ra) = 10.5: a ball of rca= 150mm will provide equal electric field as a wire of
ra=15mm (at the anode surface applying the same high voltage)
Because of the longer avalanche path in the ball :
A ball of about a=.5mm will provide a roughly similar multiplication factor
depending of the gas mixture and pressure
robust 1mm ball instead of 30mm wire
High precision ball better than 1mm commercially available
Lower capacitance < 1pF
Small scale radial degrader 150 cm2 compared to 2x10,000=20,000 cm2
Sphere is better adapted to high pressure. Thinner vessel for equal pressure
Better energy resolution in avalanche mode FWHM = 1% with alpha particles
Very particle Identification thanks to radial field
Well adapted for high quality vacuum. It operates in seal mode
Advantages of the ball compared to wire

## Slide 15
LSM detector d=6 0 cm p=10 bar
University of Saragoza detector
University of Thessaloniki detector
Basic R@D detector in Saclay
Queens University test sphere
Grenoble Sphere
R2D2 Sphere CNBG Bordeaux
University of Birmingham detector
Boulby Mine neutron detector

## Slide 16
Bibliography
I Giomataris et al., JINST 3:P09007,2008,
I Giomataris and J.D. Vergados, NIMA530:330-358,2004,
I. Giomataris and J.D. Vergados, Phys.Lett.B634:23-29,2006.
I. Giomataris et al. Nucl.Phys.Proc.Suppl.150:208-213,2006.,
S. Aune et al., AIP Conf.Proc.785:110-118,2005.
J. D. Vergados et al., Phys.Rev.D79:113001,2009.,
E Bougamont et al., J. Phys.: Conf. Ser. 309 012023, 2011
Q. Arnaud and al, Astropart. Phys. 97 (2018) 54–62
I. Savvidis et al., Nucl. Instrum. Meth. A, vol. 877, 220–226, 2018.
I. Katsioulas et al., JINST, vol. 13, no. 11, p. P11006, 2018
Meregaglia et al., JINST, vol. 13, no. 01, p. P01009, 2018.
Q. Arnaud et al. Phys. Rev. D 99, 102003, 2019
Giomataris et al., arXiv:2003.01068
R. Bouet et al., arXiv:2007.02570

## Slide 17
THANK YOU

## Slide 18
Towards an overall radial field degrador
Degrador on
Degrador off

## Slide 19
Double beta decay project R2D2- 40bar Xe-136
KamLAND scintillator radio-purity:
232Th=5.2x10-17g/g
238U=3.5x10-18g/g
F. Suekane et al., Physics/0404071
60 cm
Vessel Copper activity mBq/kg:
Aurubis commercial 232Th= 1, 238U= 1
PNNL 232Th=.034, 238U=.13
NEW: Mitsubishi Cu x20 lower?