## Slide 1: The MARTA project in AugerPrime: RPCs to detect muons in the Pampa
pedro.assis@lip.pt

## Slide 3
Fluorescence Detector ↓
Water Cherenkov Detector ↓

## Slide 4
Depth of shower – Measured by FD
“number” of muons
Measured by tanks
Making precision measurements to shed light on what’s the muon content
The muons “problem”
simulations
data

## Slide 5
GAP2013-020
GAP2013-XXX

## Slide 6: Baseline configuration
4 x (1.5 m x 1.2 m) RPC
8x8 pads each RPC
Concrete precast : 20 cm thick (~50 g/cm2 )
2 x 1 mm gas gap RPC inside Al case

## Slide 7: Punch-through
“only muons reach the RPCs”
Some parts of the RPC are more “exposed”
  Segmented readout allows to create e.m. contamination maps
  Dynamically define a fiducial area (shower to shower, dependent on station-shower distance)
  Only pads with e.m. contamination below predefined threshold are used
  Allows for muon measurement with small bias from e.m. component
fiducial area
Total mass crossed g/cm-2

## Slide 8: MARTA EA

## Slide 9: The MARTA Engineering Array
FCT – FAPESP project
(Portugal – Brasil)
Results from a specific call FAPESP-FCT
RPC R&D
RPC technology @ Brasil
Build RPC detectors
Install EA (hexagon) in Auger
Install a unitary cell (hexagon)
In the infill area, in AMIGA tanks
Synergies with AugerPrime
RPC hodoscopes for testing SSD
Cross-calibration
Physics at E=10^17 eV

## Slide 10: The support structure
Precast structure built at the observatory
Transported to the field
Installed in a couple of hours
(Emptying/Filling the tank is more time consuming)

## Slide 11: The modules
4 modules of RPC to be installed in each station
Triggered by the WCD
The active medium

## Slide 12: Pads & Housing (first design)
Pads are defined in PCB boards. Routed with 2mm leaving ground between them

## Slide 13: RPC Module

## Slide 14: Read-out: Segmentation

## Slide 16: The MARTA module
Integration at São Carlos, Brazil
Each module contains:
  Sensitive volume
  Pickup system
  sensors
  Enclosure
  Annex:
    DAQ
    HV
    PSU
    Control Board
    Bubbler

## Slide 17: The MARTA module
RPC gaseous volume
(inside aluminum enclosure)
HV
Controllable by SW
64 coax cables from readout electrodes
DAQ board
Power and control
Gas
subsystem
DATA interface

## Slide 18: MARTA Readout System
Inputs
MAROC
FPGA
USB port

## Slide 19: RPC channel
RPC
MAROC
Th.
FPGA
Amp
pad
pad
pad
pad
“Pad is active”
64 x channels

## Slide 20: RPC channel
RPC
MAROC
Th.
FPGA
Amp
pad
pad
pad
pad
“Pad is active”
Charge memory
SLOW
ADC
64 x channels
Global control for charge acq.

## Slide 21
First field station

## Slide 22: Spin-offs
Hodoscopes to test other detectors
Telescopes for muon-graphy

## Slide 23: Thank you
www.lip.pt
pages.lip.pt/auger/

## Slide 24: Acknowledgements