## Slide 1: Radiobiology studies in proton therapy: range verification with Zn nanoparticles and studies of cell surveillance after irradiation with different LETs
IBÁÑEZ-MORAGUES, Marta; CHAMORRO, Natalia; FERNÁNDEZ-BARAHONA, Irene
OTEO, Marta; LAGARES, Juan Ignacio; ARCE, Pedro; LUJÁN-RODRÍGUEZ, Victor Manuel; RAMOS-MARTÍN, Fernando;
ESPAÑA, Samuel; FRAILE, Luis Mario;
AZCONA, Diego; MORCILLO, Miguel Ángel
Medical Applications of Ionizing Radiation Unit (CIEMAT)
IGFAE workshop on technologies and applied research at the future Galician proton-therapy facility

## Slide 2: Content
Medical Applications of Ionizing Radiation Unit (CIEMAT)
Proton therapy
A. Range verification with nanoparticles
Zinc-doped iron oxide nanoparticles as a proton-activable agent for dose range verification in PT
B. Biological optimization for protons
Development of a set-up for proton irradiation with different LETs in a clinical facility
LQM adjustment for cell surveillance measurements in 96-well cell culture plates
Conclusions

## Slide 3: Medical Applications of Ionizing Radiation Unit
Radioisotopes production and Radiopharmacy
PET/CT Molecular Imaging
Instrumentation and Simulation in Nuclear Medicine and Radiotherapy
Radiobiology
Morcillo, M. Á. et al. 2018
LINAC (CUN, Madrid)

## Slide 4: Protontherapy
Strategies:
Monte Carlo planning
Improvements in Image-Guided PT (IGPT)
Range verification
Radiobiological optimization for protons (LET/RBE)
Blanchard et al, 2017
Uncertainties:
Delineation
Positioning
Interfractional variation
Range calculation based on CT

## Slide 5: A. Range verification PRONTO-CM Project
Protoactivable NPs
Zn
66/68Ga
Nanoparticle
p+
Zn
PG
Range verification in vivo?
PET or PG from patient activation with the beam
Uncertainties
Paper in process

## Slide 6: Zinc-doped iron oxide nanoparticles as a proton-activable agent for dose range verification in PT a. Nanoparticle synthesis and characterization
Citrate
10 min
100ºC
240 W
N2 cooling
Fe oxide (38.8 %)
Zn oxide (61.2 %)
Sephadex PD-10 for purification
0.22 µm filter for sterilization
Microwave (CEM)
FeCl3
ZnCl2
Na3C6H5O7
N2H4
IONP@Zn-cit
67Ga citrate to chloride
Amicon (30K) for medium exchange
EX VIVO STUDIES
IN VITRO STUDIES
67Ga-IONP@Zn-cit
61 % Zn
39 % Fe
ICP-MS for quantification
TEM images

## Slide 7: Zinc-doped iron oxide nanoparticles as a proton-activable agent for dose range verification in PT b. IONP@Zn-cit Cytotoxicity
24h
MTT Proliferation Kit I (Roche)
Absorbance measurement
(570-690 nm)
IONP@Zn-cit
U251 cell line

## Slide 8: Zinc-doped iron oxide nanoparticles as a proton-activable agent for dose range verification in PT c. Influence of IONP@Zn-cit on X-Ray radiation-induced clonogenic cell death
Cell culture flasks used to perform clonogenic assays with NPs.
Farmer Ionization chamber (model NE-2571) as monitoring chamber.
X-Ray irradiator (Philips MCN 321 X-Ray tube, CIEMAT).
Formation of a 50 cell-colony
(5-6 divisions)
Survival Quantification
0Gy
100 cells seeded
10Gy
1000 cells seeded
Linear-Quadratic Model (LQM):

## Slide 9: Zinc-doped iron oxide nanoparticles as a proton-activable agent for dose range verification in PT c. Influence of IONP@Zn-cit on X-Ray radiation-induced clonogenic cell death
Results for U251 cell line and parameters to study NP effect:
α: probability of lethal damages to DNA (linear part of the curve)
β: probability of sub-lethal damages (quadratic part of the curve)
Matsui et al. 2019; Ahmad et al. 2020; Rajaee et al. 2019; Subiel et al. 2016
[IONP@Zn-cit] (µgZn/ml) | α (Gy-1) | β (Gy-2) | SF2Gy | D10% (Gy) | MID
0 | 0.747 ± 0.331 (44.3) | -0.025 ± 0.035 (143.2) | 0.277 ± 0.164 (59.3) | 3.60 ± 1.37 (38.2) | 2.78 ± 0.60 (21.5)
1 | 0.085 ± 0.118* (139.2) | 0.041 ± 0.019* (46.9) | 0.729 ± 0.148* (20.2) | 6.73 ± 1.07* (15.9) | 4.25 ± 0.83 (19.5)
10 | 0.408 ± 0.129 (31.6) | 0.007 ± 0.016 (222.2) | 0.436 ± 0.082 (18.8) | 5.15 ± 0.56 (10.8) | 3.52 ± 1.13 (32.0)
*p-value<0.05
= 5.04 (1.38;2.84) and 3.2 (1.03;1.56) for
1 and 10 µg Zn/ml NPs
Radioprotective effects at low NP doses???

## Slide 10
IONP@Zn-cit water solutions (red) were irradiated with 10-MeV proton beam and prompt gamma were measured. Zn foil sample (blue)/powder (pink) and water (green) were used as positive and negative controls, respectively.
10 mg/mL in this set-up
Set-up of CMAM irradiations with four LaBr detectors (in blue) for prompt gamma measurements.
Zinc-doped iron oxide nanoparticles as a proton-activable agent for dose range verification in PT c. Proton irradiation of IONP@Zn-cit d. Biodistribution and pharmacokinetic studies of 67Ga-IONP@Zn-cit
Center for Microanalysis of Materials
(CMAM, Madrid)
Possible improvements:
Active targeting
More detectors
Add Oxygen-10
U251 cell line
SC injection
159,7 µg Zn/ratón
67Ga-IONP@Zn-cit
Tumor Radioactivity |  | 67Ga- IONP@Zn-cit Concentrarion | 
%ID/g | SD | µg Zn/g | µg Fe/g
0.79 | 0.13 | 1.26 | 0.82
0.95 | 0.08 | 1.51 | 0.98
0.92 | 0.17 | 1.46 | 0.95
0.61 | 0.02 | 0.97 | 0.63
Pellico et al, 2016

## Slide 11: B. Radiobiological optimization for protons (LET/RBE)
Limitations -> Research facilities and reproducibility
PTCOG60

## Slide 12: Radiobiological optimization for protons (LET/RBE) a. Development of a set-up for proton irradiation with different LETs in a clinical facility
P1
P2
P3
P4
P5
P6
LET | %PDD | PMMA Thickness (mm)
P1 | 30 % | 23,46
P2 | 70 % | 31,19
P3 | 100 % | 32,11
P4 | 70 % | 32,6
P5 | 30 % | 32,96
P6 | 10 % | 33,23
Proton Irradiation, Hitachi (CUN, Madrid)

## Slide 13: Radiobiological optimization for protons (LET/RBE) a. Development of a set-up for proton irradiation with different LETs in a clinical facility
Proton Irradiation, Hitachi (CUN, Madrid)

## Slide 14
Radiobiological optimization for protons (LET/RBE) b. LQM adjustment for cell surveillance measurements in 96-well cell culture plates
V79 cell line
6. Dilution with Abs methanol
7. Absorbance measurement
(570-BKG nm)

## Slide 15: Take home message
IONP@Zn-cit produce prompt-gamma at a certain concentration and the biological characterization was performed successfully, obtaining results about what could be our next steps in this topic.
The set-up for proton irradiation in a clinical facility built allows irradiations at different LETs with uncertainties measured below 9 %.
The new method of cell surveillance is giving results comparable with the gold standard used in radiobiology, the clonogenic assay in which colonies are counted.
Our Unit is interested in continuing with this research and further more…
  Endpoints (ferroptosis, ROS, study of DNA damage…)
  Radiotherapy in combination with immunotherapy
  FLASH radiotherapy

## Slide 16: Acknowledgments...
Protontherapy and nuclear techniques for oncology (PRONTO-CM) - B2017/BMD­3888
Members of the Biomedical Applications on Ionizing Radiation Unit
marta.ibanez@ciemat.es
Marta Ibáñez
Radiobiology of proton therapy. Rationale for combining proton radiation and immunotherapy (RADPROTIM) - PID2019-104558RB-I00
THANKS FOR YOUR ATTENTION!
@RadioBiomed_CIEMAT
@CIEMAT_OPI
Clínica Universidad de Navarra (CUN)
Members of Nanomedicine and Molecular Imaging Group

## Slide 17: Timescale of the effects of radiation exposure